## Slide 1: LHC RF signals
P. Baudrenghien BE/RF

## Slide 2: Numerology
For each ring:
  The 400 MHz RF defines 35640 buckets, spaced by one RF period, and numbered from 1 to 35640
  Bucket 1 is the first bucket after the 3 ms long abort gap (defined from bucket 34442 to 35640)
  Bunches in bucket 1 of the two rings collide in IP1 (and IP5)

## Slide 3: Bunch Numbering
Convention: bunches in bucket 1 of the two rings collide in IP1
FAQ
  Q: Bunches in bucket 1 of both rings meet in IP1 (and IP5). Can this be changed ?
  A: No but when we want to have single bunch collisions in another IP we inject in a different bucket of ring 2. For example for collision in IP2: Inject pilot in bucket 1 ring 1, and pilot in bucket 1 + 35640/4 = 8911 ring 2 .
By delaying the ring 2 injection bucket by ¼ turn we displace the collision point by 1 octant

## Slide 4: Revolution Frequency or Orbit
For each ring:
  It is equal to the RF divided by the harmonic number, that is the number of RF periods per turn (h=35640)
  At a given place in the machine, and at a given beam energy (that is fixed RF frequency) the delay between the pulse and the passage of a bunch in bucket 1 is fixed from run to run

## Slide 5: Bunch Clock
For each ring:
  It is 1/10 the RF frequency
  At a given place in the machine, and at a given beam energy (RF frequency) the delay between the edge of the Bunch Clock and the passage of a bunch will be fixed from run to run

## Slide 6: Drifts
  Drift during the ramp: during the acceleration ramp due to the difference between signal transmission delay and the beam time of flight. For protons we have 6.5 ps/km, for ions 41.25 ps/km. Hopefully not a problem
  Drift during the year. Large drift (> 1 ns) caused by thermal effects on fiber SR4-CCR-ATLAS/LHCb/Alice. Shorter link SR4-CMS
  During a fill: small drifts due to thermal effects in SR4, luminosity optimization (crossing angle), and tides?

## Slide 7: Drifts during fill: comparison BPTX DT ALTLAS (green) and CMS (violet) Fill 3299, ~ 30 ps pk-pk
Data from J.P. Ochoa and G. Mikenberg

## Slide 8: SR4 upgrade. More stable temp/humidity in 2015
LLRF racks in SR4 before and after renovation

## Slide 9: Synchrotrons RF frequency swing (proton)
  The acceleration ramp is defined in momentum (unit eV/c)
  We have
    Injection: 400.788 860 MHz (+- 10 Hz)
    4 TeV/c: 400.789 710 MHz
    6.5 TeV/c: 400.789 730 MHz
  The Bunch Clock is the RF divided by ten. The orbit (revolution frequency) is the RF divided by 35640 (h)

## Slide 10: Synchrotrons RF frequency swing (ions)
  The acceleration ramp is defined in proton-equivalent momentum peq (unit eV/c), i.e. the momentum of proton in the same magnetic field
  In a given magnetic field we have
  With Pb20882+ , we have 2.51742798
    Injection: 400.784 220 MHz (+- 50 Hz)
    4 TeV/c: 400.789 660 MHz
    6.5 TeV/c: 400.789 700 MHz

## Slide 11: B1 references vs. B2 references
RF p
RF Pb
@ 3.5 Z TeV/c
we had 76 Hz difference @ 400.8 MHz
For p-p and Pb-Pb, the two RF are locked from injection -> can use B1 reference only
Por p-Pb, the lock is done at flat top only. B1 ref OK in collision but need to use both references for tracking during filling and ramping.