## Slide 1: BT technology R&D
M. Atanasov, M.J. Barnes, J. Borburgh, L. Ducimetière, B. Goddard, T. Kramer
FCC Dump System meeting, January 29th

## Slide 2: FCC Extraction: BT-Systems
System Interfaces
Extraction Septa
Fast Pulsed Extraction System
Electronics & Controls
Functional Extraction System Design
Risk-, Safety and Reliability Engineering
Beam Dilution and AUX Magnets

## Slide 3: Remark: System design
Presented hardware considerations are currently stand alone feasibility studies based on preliminary optics considerations.
The actual extraction system design is finally to be conducted on the basis of safety-, risk- and reliability analysis. -> To be covered in future studies.
Injection systems also interesting with different challenges – to present another time.

## Slide 4: Preliminary Identified HW Requirements
 |  | Kickers | Septa | Bumpers
B.dl | T.m | 3.3 - 50 | 22 - 334 | 7.7 - 120
Available system length | m | 100 | 300 | 50
Rise time | µs | 10 | - | -
Flat top length | µs | >340 |  | 
GFR* h/v | mm | 18/18 | 18/18 | 18/18
*important to quantify early, with collider accelerator physics team

## Slide 5: Extraction Septa: Scaled System
FCC extraction septa: Scaled LHC system |  | 
Technology |  | Lambertson Septa
# units (magnets) |  | 108
B.dl | T.m | 400
Magnetic length | m | 442.3
System length | m | 540
Deflection | mrad | 2.4
Inductance | H | 6.16
Peak current for nominal field | A | 880
Rise/fall time | µs | -
Flattop length | µs | DC
Gap | mm | 44
Hole for circulating beam | mm | 64
Septum thickness | №units/mm | 36/6, 36/12, 36/18
R&D Effort: Small
Innovation: Little
Large number of systems
System length does not match requirements

## Slide 6: Extr. Septa: Conservative case
Increased field (~1.4T) normal conducting Lambertson septa.
Inversed principle w.r.t LHC (septum bump).
  Less critical constraints in field free region
  Main field not needed for extraction(?).
  However challenging main field constraints (also dynamic behavior is important).
R&D Effort: Moderate
Innovation: Moderate

## Slide 7: Extr. Septa: Innovative case
Massless septa
  No TCDS needed but challenging collimation system downstream.
High field Lambertson septa (2T)
Direct drive superconducting septa
R&D Effort: High
Innovation: Big

## Slide 8: FCC Extraction Kicker: Scaled System
FCC extraction kicker system: Scaled LHC system |  |  | 
 |  | FCC MKD | LHC- MKD
# units (magnets) |  | 54 | 15
Technology |  | LHC Magnet, Free wheel + compensation | Free wheel + compensation
Magnetic length | m | 72 | 20
System length | m | 94 | 26
Kick | mrad | 0.275 | N/A
System impedance | W | 1.5 | 1.5
Operation voltage | kV | 30 | 30
B.dl | T.m | 46 | 6.37
Rise/fall time | µs | 10 | 3
Flattop length | µs | 340 | 90
# generators |  | 54 | 15
 | LHC magnet aperture 73 mm for 56 mm free passage: |  | 
 | FCC magnet aperture assumed to be 36 mm |  | 
 | Scaling factors : T.m and aperture –> 7.2*0.5 = 3.6 |  | 
R&D Effort: Small
Innovation: Little
Scaled system seems feasible and could just fit the requirements.
High number of units

## Slide 9: Kicker: Conservative case:
MKD upgrade:em
10 µs abort gap almost solves the di/dt issue.
Decreasing aperture (56mm to 36mm? - improves field strength (~factor 1.5)).
Lowering system impedance would increase current (18 -> 55kA -> ~factor 3).
Target: factor 4 in integrated field strength (~1.2 T.m/m) -> (30 1.5m long magnets for 55T.m within ~45-50m)
Saturation effects to be quantified.
R&D Effort: Moderate
Innovation: Moderate

## Slide 10: Kicker: Innovative case
Completely new magnet + pulsed power facility
Based on lumped inductance magnet powered by extremely high current pulses (several 100kA). Aim at 1.6-2.0 T?
Switches on magnets – no transmission lines
Will only work with large abort gap (di/dt).
Could massively save on beam line length, number of systems (or provide more kick angle).
However: Currently also needs huge cavern to house the capacitor banks.
R&D Effort: High
Innovation: Big

## Slide 11: Beam Dilution
Conservative case:
  Scaled & updated MKB
  “FPS”-optimized dilution pattern
Innovative case:
  Superconducting Quad
  Modified pulsed high field “solenoids”
  Gas pressurized dump line (N2)
  …
R&D Effort: High
Innovation: Big
R&D Effort: Moderate
Innovation: Moderate
Effort and strategy depends highly on acceptable energy density at dump. -> to be evaluated.

## Slide 12: Electronic & Controls
Profits from longer abort gap and trev
However:
Increased complexity
Largely distributed systems
Synchronization
Fault Tolerance, redundancy
Maintenance
Main challenges:
Safety,
Availability,
Reliability
R&D Effort: High
Innovation: Moderate

## Slide 13: R&D Conclusions
A scaled LHC septa system will not fulfill the requirements and the needed high number of units impacts on the cost side. R&D efforts for the conservative case are valid, the feasibility of innovative solutions needs to be further investigated and seen together with machine protection issues.
The development of a pulsed very high current/high field kicker magnet is an interesting option. It however seems that increasing the B.dl of the present MKD by a factor 3-4 is also possible and would just fit the requirements. Although it gives a large system it is possibly the most cost efficient solution with low technology risks.
Pulsed high field solenoid technology and SC dilution quads could be investigated together with other options for beam dilution in an innovative case. The number of units needed for a scaled MKB system seems to support the R&D efforts for an innovative solution.