## Slide 1: VeloPix: The Pixel ASIC for the LHCb VELO Upgrade
Kurt Rinnert (University of Liverpool)
On behalf of the LHCb VELO group
5.6.2015
VERTEX 2015, Santa Fe, NM, USA

## Slide 2: Outline
Introduction
VeloPix vs Timepix3
Readout Architecture
GWT Serializer
Summary

## Slide 3: Introduction
VeloPix: Hybrid pixel detector Readout ASIC for the LHCb VELO upgrade
The ASIC reads out all bunch crossings at 40 MHz
Artistic impression of
new VELO [1]
VeloPix
ASICs
The VELO upgrade:
Approx. 2.85 Tbit/s
26 module pairs
624 ASICs
41 Mpixels

## Slide 4: VeloPix ASIC module (12 ASICs)
Highly non-uniform radiation dose:
8 x 1015 to 2 x 1014 neq/cm2
Module of 12 VeloPix ASICs [1]:
Sensor
Sensor
Peak rates:
Hottest chip 15.1 Gbits/s
hottest module: 61.2 Gbits/s
ASIC
ASIC
ASIC
ASIC
ASIC
ASIC
Track rates for module [2]:
See Sophie Richards’ overview of the VELO upgrade:
“LHCb VELO Upgrade”

## Slide 5: VeloPix ASIC specifications
Feature | VeloPix | Timepix3 [2]
Readout type | Continuous, trigger-less, binary | Continuous, trigger-less, ToT
Timing resolution/range | 25 ns, 9 bits | 1.5625 ns, 18 bits
Power consumption | < 1.5 W cm-2 | < 1.0 W cm-2
Pixel matrix, pixel size | 256 x 256, 55 um x 55 um | 256 x 256, 55 um x 55 um
Radiation hardness | 400 Mrad, SEU tolerant | -
Peak hit rate | 900 Mhits/s/ASIC 50 khits/s/pixel | 80 Mhits/s/ASIC 1.2 khits/s/pixel
Sensor type | Planar silicon, e- collection | Various, e- and h+ collection
Max. data rate | 20.48 Gbps | 5.12 Gbps
Technology | 130 nm CMOS | 130 nm CMOS
> x 10
x 4

## Slide 6: Timepix3 Test Beams
Timepix3 DUT
8x Timepix3 telescope
SPIDR readout
Mechanics: CERN
Several successful test beams with different DUTs.
See [4] for more about Timepix3.

## Slide 7: VeloPix Architecture
Super pixel:
2x4 pixels to
reduce the data
rates
30% reduction
vs. single-pixel
super pixel logic
128 double columns (14.08 mm)
256 rows (14.08 mm)
SP63
SP62
SP61
SP0
SP1
SP2
SP63
SP62
SP61
SP0
SP1
SP2
SP63
SP62
SP61
SP0
SP1
SP2
SP63
SP62
SP61
SP0
SP1
SP2
PixelHit
Processor
SP0
SP63
SP62
SP61
EoC
EoC
EoC
EoC
EoC
router
serial
serial
serial
serial
DACs
PLL
SLOW CONTROL
TIMING, FAST CTRL
2-3 mm

## Slide 8: VeloPix Pixel Schematic
Global threshold
Front-end (Analog)
Leakage
Current
compensation
Preamp
Input
pad
1 pixel
TpA
TpB
TestBit
Counters
&
Latches
4-bit Local
Threshold
~43 mV/ke-
(Cdet = 50 fF)
MaskBit
Front-end (Digital)
Synch.
&
Clock
gating
ToT
Threshold
6-bit
LFSR
clock
(40MHz)
Super pixel (Digital)
Common for 8 pixels
9 bits
Data node
To next
node
23 bits
handshake
8
Valid
event
FIFO
23 bits
handshake
23 bits
BX ID
CLOCK
manager
3 fF

## Slide 9: Packet Format
Packet:
BX ID 9b
SP addr 13b
Hitmap 8b
30 bits
BX ID = bunch crossing ID/
time stamp/time-of-arrival
No ToT!
Grouping 8 hits into one packet
Range obtained
from simulations
Identify 2x4
SP region
(6 bits at column level)
30% data reduction from sharing the BX ID and super pixel address
among multiple pixels.

## Slide 10: Analog Front-End Amplifier Response
Input charges:
2 ke-
10 ke-
16 ke-
50 ke-
~225 ns @ 16 ke-
175 ns

## Slide 11: Analog Front-End Pile-Up
Up to 1.6% losses
Front-end efficiency (x 100%)
Rates up to 50 kHz per pixel

## Slide 12: Double Column Architecture
Chart: FIFO dead time (ns)
| 0 | 25 | 50 | 75 | 100 | 125 | 150 | 175 | 200 | 225 | 250 | 275 | 300 | 325 | 350 | 375
Buffer Depth 1 | 0.16 | 0.325 | 0.546 | 0.765 | 0.974 | 1.837 | 2.672 | 3.305
Buffer Depth 2 | 0.072 | 0.073 | 0.073 | 0.074 | 0.076 | 0.09 | 0.113 | 0.139
Buffer Depth 3 | 0.072 | 0.072 | 0.072 | 0.072 | 0.072 | 0.072 | 0.072 | 0.073
FIFO
Node
Node
FIFO
FIFO
Node
Node
FIFO
64 FIFOs
0 1
Register
Arbiter
Previous
Node
FIFO
Data
Size = 2
Up to 13.3
Mpackets/s
Rate: Up to 305 kHz
Next
Node
See [5] for more
details.
8 digital
Front-ends
8 analog
Front-ends
Sensor

## Slide 13: Simulation: Latency & BX ID Length
Chart: Latency (clock cycles @40MHz)
Simulation results:
Efficiency: 99.99%*
Hit rate: 840 Mhits/s
Packet rate: 505 M/s
Data rate: 16.2 Gbps
Hits per packet: 1.66
9-bit BX ID
(512 clocks)
sufficient!
Peak at 64 (highest
hit rate in SP 63)
Trigger-less architecture:
Latency must be < BX ID range. Otherwise
ambiguities in BX identification.
*No analog pile-up included.

## Slide 14: End-of-Column (EoC) Data Fabric
64 EoCs
64 EoCs
Architecture equalizes data
traffic in column direction!
Left
Data Fabric
Right
Data Fabric
Center
Node
Pixel Matrix
FIFO
19.20
Gbps
Data Node
Router/
Output logic
4.8 Gbps per bus

## Slide 15: GWT : a 60-mW 5.12 Gbps Serializer/Transmitter
Serialized data
@ 5.12 Gbps
MUX
16 phases
Reg <0:7>
data
8bit @ 320MHz
Reg <8:15>
data
8bit @ 320MHz
Driver
100 Ω
1m
low-mass
flex cable
∆U =
± 450mV
negedge
posedge
clock
(320MHz)
pre-emphasis
16 x 195ps
= 1 / 320MHz
Multi-phase DLL
Edge-
combiner
ph_0
ph_1
ph_2
ph_3
ph_14
ph_15
sel_0
sel_1
sel_15
45 mW
2mW
0.05mW
0.05mW
0.6mW
10mW
PLL
320MHz → 5.12GHz
Reg <0:15>
Sel
D0
Q0
MUX
D1
Q1
MUX
D2
Q2
MUX
D3
Q3
MUX
D4
Q4
MUX
D14
Q14
MUX
D15
Q15
data_out
1bit @ 5.12GHz
Shift Register
…as opposed to GBTX with shift register, which uses much more power

## Slide 16: Velo_GWT Test Chip in 130nm CMOS Technology
1 mm x 2 mm test chip in 130 nm CMOS technology
Power : 5.12 Gbps serializer: 15 mW, wireline driver: 45 mW
Eye diagram: +/- 200 mV is 60 ps (pseudo-random pattern)
SEU tests performed with different ions (Nickel, Argon, Neon)
Tested simple patterns: 01010101, 000FFF
Analysis pending, results coming soon

## Slide 17: Simulation: Data transfer efficiency
Chart: Packet rate (Mpackets/s)
| 419.55239999999998 | 459.33920000000001 | 499.3544 | 539.57119999999998 | 580.05240000000003 | 590.59280000000001 | 619.95600000000002 | 625.32839999999999 | 630.39200000000005 | 635.40719999999999 | 637.84680000000003 | 660.03200000000004 | 661.90840000000003 | 663.09479999999996 | 663.8904 | 665.60640000000001 | 666.53639999999996 | 667.84 | 670.47519999999997
Efficiency | 1 | 1 | 1 | 1 | 1 | 1 | 0.99997 | 0.99992 | 0.99968 | 0.9984 | 0.9965 | 0.90888 | 0.90009 | 0.89467 | 0.89113 | 0.88338 | 0.87878 | 0.87307 | 0.86135
Latency | 850 | 850 | 850 | 850 | 875 | 875 | 950 | 975 | 1025 | 1150 | 1275 | 4350 | 4575 | 4700 | 4800 | 5000 | 5100 | 5225 | 5525
The VELO upgrade
expected rate
*no front-end pile-up
taken into account
GWT x4
maximum
7-bit
BX ID
0.99

## Slide 18: Downstream Data Flow
Header
Packet 0
Time Ordering (FPGA)
Packet 2
4 x 30 bits = 120 bits
Packet 3
8 bits (4 parity bits)
BX ID 9b
SP addr 13b
Hitmap 8b
Packet 1
Event Builder (PC)
Software Event Filter
VELO tracking
budget 2 ms

## Slide 19: Diversion: Pixel Clustering
8-way flood fill algorithm as
commonly used in computer
graphics applications. [6]
Clustering on CPU was deemed too slow.
FPGA implementation very complex.
In fact, CPU clustering is feasible:
  Algorithm well known in graphics applications.
  Optimize for isolated Super Pixels flagged by FPGA.
About 10% of VELO tracking

## Slide 20: Power Consumption
Block | P (mw) | #Blocks | Total power
Analog front-end | 0.014 | 65536 | 917.5
Digital front-end | 0.002 | 65536 | 131.1
SP column (avg) | 3.6 | 128 | 460.8
Slow control | 50 | 1 | 50*
EoC block | 2 | 128 | 256*
Periphery clock tree | 100 | 1 | 100*
EoC fabric | 300 | 1 | 300*
PLL | 5.5 | 1 | 5.5*
GWT | 60 | 4 | 240
 |  | Total (mW): | 2460.9
 |  | W/cm^2 | 1.09
Chart: 
| Analog front-end | Digital front-end | SP column (avg) | Slow control | EoC block | Periphery clock tree | EoC fabric | PLL | GWT
 | 917.504 | 131.072 | 460.8 | 50 | 256 | 100 | 300 | 5.5 | 240
*estimated/budgeted

## Slide 21: Summary
Trigger-less readout ASIC architecture
Design driven by rate and power requirements
  Reads out > 900 Mhits/s/ASIC
  consuming < 1.5 W/cm2
VeloPix builds on expertise learned during the Timepix3 design
GWT serializer (5.12Gbps/60mW) demonstrated to work, SEU tests to be analyzed

## Slide 22: References
[1] LHCb VELO Upgrade TDR. CERN LHCC 2013-021. 2013.
[2] L. Eklund, “The LHCb VELO Upgrade”, ICHEP 2014
[3] T. Poikela. “Design and Verification of Digital Architecture of 65K Pixel Readout Chip for High-Energy Physics.”, 2010.
[4] T. Poikela et al. “Timepix3: a 65K channel hybrid pixel readout chip with simultaneous ToA/ToT and sparse readout”, 2014
[5] T. Poikela et al. “Digital column readout architectures for hybrid pixel detector readout chips“, 2014.
[6] "Recursive Flood Fill 8 (aka)" by André Karwath aka Aka - Own work. Licensed
under CC BY-SA 2.5 via Wikimedia Commons -
http://commons.wikimedia.org/wiki/File:Recursive_Flood_Fill_8_(aka).gif#/media/File:Recursive_Flood_Fill_8_(aka).gif

## Slide 23: Why 2x4 super pixel?
Binary encoded packets (no ToT) |  |  | 
Super Pixel Geometry | Data rate (Gbps) | Packet size (#bits) | Reduction (%)
256 x 256 | 14.785 | 28 + N x 16 | 38.179
4 x 4 | 16.477 | 28 + N x 4 | 31.105
2 x 4 | 16.806 | 28 + N x 3 | 29.729
2 x 4 | 16.945 | 33 | 29.148
1 x 4 | 17.758 | 30 | 25.748
2 x 2 | 17.857 | 30 | 25.335
1 x 4 | 18.283 | 28 + N x 2 | 23.553
2 x 2 | 18.373 | 28 + N x 2 | 23.177
4 x 4 | 18.661 | 40 | 21.973
1 x 2 | 19.703 | 29 | 17.616
1 x 2 | 19.878 | 28 + N x 1 | 16.884
 | 23.916 | 28 | 0.000
Chosen format
No super pixel
grouping
Table: Data rates for different super pixel dimensions:
N = number of pixel hits in a packet

## Slide 24: Super Pixel Power Estimation
Chart: SP Packet Rate (Mpackets/s)
| 0 | 0.25 | 1 | 2.5 | 5 | 8 | 10 | 13.333333333333334
Before custom CG | 0.0815 | 0.083 | 0.0871 | 0.098 | 0.108 | 0.122 | 0.136 | 0.154
Custom CG | 0.01482 | 0.01885 | 0.03091 | 0.05469 | 0.09449 | 0.1427 | 0.1719 | 0.1979
Chart: SP Packet Rate (Mpackets/s)
| 0 | 0.25 | 1 | 2.5 | 5 | 8 | 10 | 13.333333333333334 | 20
Power (mW) | 0.01482 | 0.01785 | 0.02585 | 0.041 | 0.0661 | 0.09876 | 0.1196 | 0.1536 | 0.1634
Power for SP hitmap buffers:
Target rate approx. 300 kHz
Power approx. 20 uW
Hand-crafted clock gating (CG) works!
Power for transporting the packets:
Target rate 5 MHz
Power 66 uW
128 x 64 = 8192 Super pixels
per chip!!