## Slide 1: HOM: Assessment of Thermo-Mechanical Performance
M. Garlaschè
on behalf of CRAB Collaboration

## Slide 2: HOM Calculations
Thermal:
Coax Cable Heat Losses
Quench Power Limits
Thermo-Structural:
Resistance to loads & maximum deformation in cool-down & working condition
Modal performance

## Slide 3: Thermal Calcs: Coaxial Line

## Slide 4: Thermal Calcs: Coaxial Line
Inner tube ∅_E | 17.4 mm
Outer tube ∅_E | 40 mm
Tube thickness | 0.3 mm
Copper coating | 5 μm
Length_coax | ~1600mm
DQW & RFD: common configuration
Semi-analitical evaluation:
Heat Losses to He Bath (Static & Dynamic)
T distribution
Hp: PRF=1kW @ 1GHz
A (=300K)
B (=2K)

## Slide 5: Thermal Calcs: Coaxial Line
Inner Intercept (e.g. Al2O3)
Thermal Intercepts (1x÷2x)
Outer Intercept
Total losses (@ 2K):
Static ~ 0.2 W
Dynamic ~ 1.9 W
~2W / line
Different Cases studied:
No Cooling
Outer H.Intercept
Inn. & Out. H.Intercept
Heat Loss [W]
2.5
0
200
440
Cable Length [mm]
TOTAL
DYN.
STAT.
CASE: 1x Outer Heat Interc.
@ 26%
!!!
For lengths 1600mm...

## Slide 6: Properties for Coax Line Calc.
Temperature values along Inner tube [K]
0
400
0.3 m
CASE:
1x Outer Heat Intercept @ 26%
300mm length

## Slide 7: Helium Heat Evacuation
Aim: determine minimum cross section for heat evacuation via HOM He cooling line
Hp: all coax line heat (~2W) goes to HOM line
[1]
~2W

## Slide 8: Thermal Calcs: HOM
  Aim: determine HOM thermal performance w.r.t. quench
PHOM

## Slide 9: Thermal Calcs: DQW HOM
Nb properties as function of Temperature

## Slide 10: Thermal Calcs: DQW HOM
  Iterative lumped calculation HFSS/ANSYS, to assess HOM temperature distribution
  RsNb = f(T) ; λNb = f(T)
  Initial DQW geometry
    No active cooling inside stem
Temp. Gradient
Courtesy S.Verdu Andres
T0
TMAX

## Slide 11: Thermal Calcs: DQW HOM
T0 [K] | RS , λNb | RRR | TMAX [K] | P_RF [mW] | 
2 | Const | - | 3.1 | 5 | 
2 | f(T) | 380 | 3.4 | 9 | 
2 | f(T) | 40 | X |  | 
4 | f(T) | 300 | 4.8 |  | 35
NEXT... Current Design:
QRF= 17mW
Active He cooling @ 2K, 100 mm distance from tip
Few configurations studied
Cu option not viable
RRR > ~250, for acceptable λNb
Temp. Gradient
Courtesy S.Verdu Andres
T0
TMAX

## Slide 12: Thermostruct. Calcs: HOM
Two Geometries: w. & w/o Bellow

## Slide 13: Thermostruct. Calc: Load Cases
 | Load Value | Verification criteria
Normal Operation (Load Case #1) | No pressure Thermal Contraction: 300K → 2K Coax Line: 20 N | Displacement of the hook (wrt the flange). Total budget 0.5 mm
Maximum Stress (Load Case #2) | Internal pressure: 0.18 MPa Thermal Contraction: 300K → 2K Coax Line (w/ margin): 50 N | Yield strength at 2K
Maximum Stress (Load Case #3) | Internal pressure: 0.18 MPa Coax Line (w/ margin): 50 N | Yield strength at 300K
Constrained Displacement in the bolt holes of the horizontal flange. Deformable option activated
(allows thermal contraction)
No constraint on the vertical flange.
Further Assumptions:
Nb-316LN welds not modeled (bonded contact in the flange internal cylinder).
Uniform temperature.
Neglected temperature dependence of Elastic modulus and Poisson’s ratio.

## Slide 14: With Bellows - Load Case #1
Nominal gap = 3 mm Deformed gap = 2.9 mm
0.1 mm

## Slide 15: With Bellows - Load Case #2
Component | σEQ_MAX [MPa] | σYield/1.5 [MPa]
SS | 44 | 570[5]
Bellows | 174 | 320 [6]
Nb | 45 | 320[5]

## Slide 16: With Bellows - Load Case #2
35x magnification

## Slide 17: With Bellows - Load Case #3
Component | σEQ_MAX [MPa] | σYield/1.5 [MPa]
SS | 28 | 190[5]
Bellow | 126 | 160[6]
Nb | 49 | 50[5]

## Slide 18: NO Bellows - Load Case #1
0.07mm

## Slide 19: NO Bellows - Load Case #2
Component | σEQ_MAX [MPa] | σYield /1.5 [MPa]
SS | 260 | 570[5]
Nb | 179 | 320[5]

## Slide 20: NO Bellows - Load Case #2
35x magnification

## Slide 21: NO Bellows - Load Case #3
Component | σEQ_MAX [MPa] | σYield/1.5 [MPa]
SS | 58 | 190[5]
Nb | 37 | 50[5]

## Slide 22: Modal
1st mode: 62 Hz
(both w/ or w/o bellows)
 | Load Value | Verification criteria
Modal (Load Case #3) | - | > 50 Hz
Displ. Gradient

## Slide 23: HOM Calculations: Remarks
Thermal
COAX: internal & external cable Intercepts ~2W
Active He Cooling inside stem, able to evacuate PCOAX+PHOM
HOM: Thermal calcs to be updated, no criticality expected
RRRmin= 250
Thermo-Structural
HOM design is compliant with the specified strength and deformation limits
Max 0.1mm relative displacement in the most critical area @ working condition

## Slide 25: References
[1]“RF Superconductivity”, H. Padamsee, pag. 53
[1] Cryogenie, B.Hebral et al., pag. 11
[2] D. Vaucoret, Materials and Ansys Library for Design Office, EDMS 1291793.
[3] Tensile tests
[4] H. Kaiser, Ge. Meyer, H.B. Peters, and G. Weichert, “Helium Vessel for the TTF Cavity,” TESLA Collaboration Report 94–26, October 1994.
[5]Information provided by Ignacio Aviles Santillana.
[6] “Fatigue life prediction…bellows at cryogenic temperatures” B. Skoczenet al. , LHC Project Note 012
[7] CERN specification for 1.4435 (316L) for bellows : EDMS 790771

## Slide 27: Coaxial Lines

## Slide 28: Thermostruct. Calc.
 |  | Niobium | Stainless Steel 316LN | 316LN Sheets
300 K | Poisson’s ratio | 0.38 | 0.27 | 
 | Elastic modulus (GPa)[2] | 103 | 196 | 
 | Yield strength Rp0.2 (MPa) | 70 [3] | 280 | 240
Properties | Integrated thermal contraction[4] |  |  | 
 | Coefficient of thermal contraction (1/K) |  |  | 
2 K | Yield strength Rp0.2 (MPa)[5] |  |  | 478
 | Yield with safety factor Rp0.2/1.5 | 320÷347 | 567÷700 | 320
 |  | Niobium | Stainless Steel 316LN | 316LN Sheets
300 K | Poisson’s ratio | 0.38 | 0.27 | 
 | Elastic modulus (GPa)[2] | 103 | 196 | 
 | Yield strength Rp0.2 (MPa) | 70 [3] | 280 | 240
Properties |  |  |  | 
2 K | Yield strength Rp0.2 (MPa)[5] |  |  | 478
 | Yield with safety factor Rp0.2/1.5 | 320÷347 | 567÷700 | 320
Material Properties

## Slide 29: Thermostruct. Calc: Mesh
Element size minimized in the Nb-316LN interfaces
Shell elements in the bellow
Mapped mesh in regular geometries (e.g. cylinders)
Large elements in the hook (only deformation is critical)
Defeaturing of small details (e.g. flange knife)

## Slide 30: Thermostruct. Calc: Mesh

## Slide 31: With Bellows - Load Case #2

## Slide 32: Current Tests
SPL HOM: OFE Cu prototype
2.2
16.048
+0.05
0.2
Nonconformities
Notes: HOM metrology EDMS: 1481124

## Slide 33: Further Images