## Slide 1: HOM Review: Mechanical design overview
LARP Review of the HOM couplers
Teddy CAPELLI
on behalf of CRAB Collaboration

## Slide 2: INTRODUCTION TO CRYOMODULES
HOM inside cryomodules
Design constraints
HOM coax lines overview
HOM review – Feb 2015
CERN – EN-MME

## Slide 3: DQW - Cryomodule
HOM (3 HOMs/Cavity)
Helium tank
Cavity

## Slide 4: RFD - Cryomodule
H-HOM (1 pce/Cavity)
V-HOM (1 pce/Cavity)
Helium tank
Cavity

## Slide 5: Design constraint
Limited space available inside cryomodules
DQW – Cryomodule – Cavities after insertion
DQW – Cryomodule – Cavities insertion
HOM review – Feb 2015
CERN – EN-MME
RFD – Cryomodule – H-HOM Limited height
Space beetween H-HOM feedthrough and thermal shielding < 50 mm

## Slide 6: HOMs overview
Filter
Feed Through
Coaxial line
RFD
DQW

## Slide 7: HOMs overview
RFD
DQW
Filter
Feedthrough
Coaxial line
H-HOM
Filter
Feedthrough
Coaxial line
V-HOM

## Slide 8: HOM FILTER DETAILS
Geometry
Design details
Cooling circuit
Materials
HOM review – Feb 2015
CERN – EN-MME

## Slide 9: Geometry definition
HOM review – Feb 2015
CERN – EN-MME
RF parameters
  2K
  After BCP
Extraction of surfaces from parameters
  2K
  After BCP
Conversion to 300K
  300K
  Before BCP
Definition of parts
  300K
  Before BCP

## Slide 10: Design details - DQW
Bellows (st. Steel)
(only for CERN prototype)
Centering step
UHV Conflat flanges
knife edge flanges with copper seal for UHV applications
not mandatory (but used for CERN prototyping)
gives flexibility for the st.steel welding / assembly
increases the positioning accuracy (female step on cavity)
maximum gap beetween the two steps: 0.05mm (radial)
St. Steel body
1.5 mm thick plate rolled/welded

## Slide 11: Design details - RFD
Centering step
UHV Conflat flange
Knife edge flanges with copper seal for UHV applications
increases the positioning accuracy (cavity equipped with female centering step)
maximum gap beetween the two steps: 0.1 mm
St. Steel body
1.5 mm thick plate rolled/welded
UHV Conflat flanges
Niobium body
3 mm thick

## Slide 12: Cooling circuit
Helium cooling circuit
He Supply
He Supply
DQW - HOM
RFD – H-HOM
Ø20mm
Section : ~500mm²

## Slide 13: Materials
H-HOM (RFD)
V-HOM (RFD)
DQW
Copper*
St. steel*
St. steel*
Niobium*
Ceramic*
St. steel*
Niobium*
*All materials used to manufacture HOMs
shall be compliant with CERN specification n°1389669

## Slide 14: (for CERN prototype)
HOM review – Feb 2015
CERN – EN-MME
HOM – DQW: assembly sequence

## Slide 15: DQW – HOM Assembly sequence (CERN prototype)
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 16
Assembly sequence: step 1
Hook / Cylinder welding (EBW)
*Welding thickness : 4mm
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 17
HOM review – Feb 2015
CERN – EN-MME
Assembly sequence: step 2
Hook re-machining: removal of welding extra thickness

## Slide 18
Assembly sequence: step 3
Niobium welding
Welding thickness : 2mm
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 19
Assembly sequence: step 4
Brazing of DN63 flange with Niobium part
Cu Brazing
The knife of UHV flange must be machined after brazing
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 20
Assembly sequence: step 5
Horizontal rod welding
EBW
Welding thickness : 1mm
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 21
Assembly sequence: step 6
Hook and Niobium cylinder welding
EBW
Welding thickness: 2mm
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 22
Assembly sequence: step 7
Stainless steel welding
Welding thickness: 1.5mm
TIG or EBW
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 23
Assembly sequence: step 8 & 9
Stainless steel welding
Welding thickness : 1.5mm
TIG or EBW
TIG or EBW
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 24
Assembly sequence: step 10
Brazing of DN40 flange on Niobium part
Cu Brazing
Knife of UHV flange must be machined after brazing
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 25
Assembly sequence: step 11
Bellows welding
Welding thickness : 1.5mm
TIG or EBW
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 26
Assembly sequence: step 12
Niobium welding
Welding thickness : 2mm
EBW
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669

## Slide 27
Assembly sequence: step 13 & 14
Final stainless steel welding
HOM review – Feb 2015
CERN – EN-MME
All welds shall be compliant with CERN specification n°1389669
TIG or EBW
TIG or EBW

## Slide 28: Current Tests
SPL HOM: OFE Cu prototype
2.2
16.048
+0.05
0.2
Nonconformities
Notes: Mention That Weld Test is ongoing
HOM metrology EDMS: 1481124

## Slide 29: Further Images

## Slide 30: FEEDTHROUGH § COAXIAL LINE
HOM review – Feb 2015
CERN – EN-MME

## Slide 31
FEEDTHROUGH
Shape and RF Calculation under progress.
(E.Montesinos – CERN)
RFD - H-HOM
DQW
UHV Conflat flanges
316LN Stainless steel
Ceramic – 10mm thick
Copper
HOM review – Feb 2015
CERN – EN-MME

## Slide 32: COAXIAL LINES (RFD § DQW)
Dimensions:
External pipe diameter : 40mm
Internal pipe diameter : 17.4mm
Material:
Stainless steel 0.3mm thick + Copper coating 5 µm
Length:
Minimum 500mm
Maximum 1600mm
Operating conditions : insulation vacuum
Cryomodule side
flexible connexion
Cavity side
Flexible connexion to HOM feedthrough
Thermal intercept
Outer pipe
Sliding/flexible connexion
Centering ring
§ thermal conductor
Inner pipe
Cooling pipe
32
HOM review – Feb 2015
CERN – EN-MME