## Slide 1: Thermal modelling DQW
G. Burt

## Slide 2: Preliminary simulations Scaling
Temperature difference scales with Rs linearly (in simulation not in reality) (simulations were at 5 mOhm)
Scales with V^2 (simulations were at 2 MV)
Coupler design has changed since these simulations to penetrate futher, temperature rise is approximately twice as large now.

## Slide 3: No cooling channel but with LHe jacket 2 MV, 400 MHz (5 nOhm)
@3 MV, 10 nOhms, DT=138 mK
Note simulations were at 1.8K instead of 2 K

## Slide 4: Inner conductor actively cooled
@3 MV, 10 nOhms, DT=66 mK

## Slide 5: Only cooling at base below gasket
@3 MV, 10 nOhms, DT=146 mK

## Slide 6: Thinner walls
@3 MV, 10 nOhms, DT=166 mK

## Slide 7: New simulations vs preliminary results
HOM coupler now penetrates in substantially further
Simulations have been run at a higher mesh (although I have had to use a hexahedral mesh as the tetrahedral mesher crashed on the imported surfaces)
Preliminary results were at 2 MV rather than 3 MV.
Preliminary results used a surface resistance of 5 nW new results use 50 nW

## Slide 8: Final coupler design
2.165 K @ 10 nW. This gives a limit to magnetic field on the HOM coupler and cleanliness

## Slide 9: HOM
We study the 0.58 GHz accelerating mode (R/Q=40, Q=1750).
V ~ I*R/Q*Q ~ 35 kV (which is more than the 1 kW spec)
I have used 10 nOhms

## Slide 10: HOM (10nW 35 kV)
Temperature rise due to a the 580 MHz HOM at 35 kV with Rsurf=10nW is 0.01K
If we have 10 HOMs of similar size the total rise is 0.1 K which is similar to the operating mode
Note that now most of the heat is on the gasket.