## Slide 1: Detectors for Future Linear Colliders
Lucie Linssen, CERN
Intro to Boston students, February 5th 2015

## Slide 2
Introduction

## Slide 3: from discovery to precision
electron
positron
proton
p-p collisions | e+e- collisions
Proton is compound object Initial state not known event-by-event Limits achievable precision | e+/e- are point-like Initial state well defined (√s / polarisation) High-precision measurements
High rates of QCD backgrounds Complex triggering schemes High levels of radiation | Cleaner experimental environment trigger-less readout Low radiation levels
High cross-sections for colored-states | Superior sensitivity for electro-weak states
LHC
CLIC
Notes: While the LHC is a perfect discovery machine, and reaches already a remarkable precision for the studies, a different type of accelerator can even do better.
This is because the LHC collides protons, which are composite particles. When you collide electrons with their antimatter twins positrons, this opens the door for much higher precision in the physics analysis.

## Slide 4: history of proton and electron colliders
1 GeV
1 TeV
10 GeV
100 GeV
10 TeV
100 TeV
pp and e+e- provide
complementary
information

particle physics needs both !
1940 1960 1980 2000 2020
proton collider
electron collider
historically,
electron colliders
lag behind in energy
(see later in this talk)
energy
starting
year

## Slide 5: circular or linear collider ?
many magnets, few accelerating cavities
beam circulates for a long time (at 11000 turns/sec in LHC)
high energy → strong magnets needed more synchrotron radiation loss
few magnets, many accelerating cavities
beam passes only once
high energy → high accelerating gradient needed
high luminosity → high beam power (high bunch repetition)
source
main linac
N
S
N
S
accelerating cavities
Synchrotron radiation
Energy4/Mass4Radius
Circular Collider
Linear Collider
proton mass
electron mass
≈ 2000

## Slide 6: ILC and CLIC in just a few words
Linear e+e- colliders
Luminosities: few 1034 cm-2s-1
CLIC
ILC
2-beam acceleration scheme, at room temperature
Gradient 100 MV/m
√s up to 3 TeV
Physics + Detector studies for 350 GeV - 3 TeV
Superconducting RF cavities
Gradient 32 MV/m
√s ≤ 500 GeV (1 TeV upgrade option)
Focus on ≤ 500 GeV, physics studies also for 1 TeV

## Slide 7
the CLIC accelerator

## Slide 8: CLIC two-beam acceleration scheme
Two Beam Scheme:
Drive Beam supplies RF power
12 GHz bunch structure
low energy (2.4 GeV - 240 MeV)
high current (100A)
Main beam for physics
high energy (9 GeV – 1.5 TeV)
current 1.2 A
Accelerating gradient: 100 MV/m

## Slide 9: CLIC layout at 3 TeV

## Slide 10: CLIC staged implementation
~100 m depth near collision point
Collision energy (GeV) | Site length (km) | Luminosity (cm-2s-1) | # Higgs events in ~4 yrs
350 | 11 | 1.5×1034 | 90000
1500 | 27 | 3.5×1034 | 430000
3000 | 48 | 6×1034 | 920000
staged operation

optimal for physics
Note: #Higgs is without enhancement from polarisation

## Slide 11
a detector for CLIC

## Slide 12: particle detection (1)
photon γ
electron e±
muon μ±
proton p± / pion π±
neutron n
neutrino ν
tracker
EM
hadronic
muon detector
calorimeters
Particles make small changes in the material they traverse
  ionisation, atomic effects, nuclear effect <= all very small !
Particles differ in the way they interact with material
  We can use it to identify particle types !
very light !
very heavy !
magnetic
field
passive/active sandwich structures

## Slide 13: particle detection (2)
Many of the elementary particles we know have very short life times
W, Z, Higgs (!) and many more
We only see the products of their decay
quarks cannot be observed, as they hadronise in to “jets” of particles
reconstructing the original particles
from the visible decay products
=> key ingredient of particle detection
~5
mm
Secondary vertex, sign of b-quark
jet
~1.5 m

## Slide 14: CLIC detector concept (2014)
ultra low-mass
vertex detector
with ~25 μm pixels
main tracker, silicon-based (large pixels and strips)
fine grained (PFA) calorimetry, 1 + 7.5 Λi,
strong solenoid
magnet, 4 Tesla
return yoke (Fe) with detectors
for muon identification
complex forward region with final beam focusing
6.5 m
Combining high precision + beam conditions at CLIC
e-
e+

## Slide 15: Pixel detector
1 m
(calorimeter)
pixel
detector
tracker
Flavour tagging capabilities drive the design of the pixel detector
has to be extremely accurate and light !
2 billion pixels
3 μm single point accuracy
25*25 μm2 pixels (25 times smaller pixel area than at LHC)
  Pulse height measurement
  Time measurement to 10 ns
Ultra-light => 0.2%X0 per layer
  Very thin materials/sensors
  Low-power design, power pulsing, air cooling
  Aim: 50 mW/cm2
  Radiation level 104 lower than LHC
high-tech R&D
covering several disciplines

## Slide 16: pixel detector R&D
thin silicon sensor
electronics chip (65 nm)
thin electronics + sensor assembly
HV-CMOS sensor + CLICpix
interconnect technology
signal simulations
power delivery + pulsing
thin supports
air cooling simulations/tests

## Slide 17: detector technology => “very heavy”
calorimeter
magnet coil
muon
detector
1.5 m
π- at 210 GeV in tungsten-DHCAL
tungsten analog HCAL
calorimeters
“electromagnetic + hadronic”
particles interact with heavy material => showers
make a sandwich ~60 layers
heavy absorbers + fine-grained detectors
extremely heavy and compact
80 million readout channels (400* larger than LHC)

## Slide 18
Snapshot of physics at CLIC

## Slide 19: CLIC physics programme…
sparticles in SUSY example scenario (not excluded by LHC results)
Example of energy staging
(with an example SUSY model)
CLIC: e+e- collider, staged approach
350 – 375 GeV, 500 fb-1 : precision Higgs and top physics
~1.4 TeV, 1.5 ab-1 : targeted at BSM physics, precision Higgs
~ 3 TeV, 2 ab-1 : targeted at BSM physics, precision Higgs
Exact energies of TeV stages will depend on LHC results

## Slide 20
Higgs physics (1)
probability
energy
Higgs production at CLIC
Very clean process
Can “see” Higgs by
looking at Z only !
μ+
μ-
b
b
Z => μμ recoil
350 GeV
500 fb-1
Model-independent Higgs measurement !
can also “see” invisible Higgs decays: <1% accuracy

## Slide 21: Higgs coupling to mass
model independent
much more accurate than HL-LHC
similar accuracy as HL-LHC
combining all
Higgs information
production
+
decay
Higgs self-coupling H=> HH
Gives access to understanding the Higgs field
Requires high energies => coupling gHHH to 24% at 1.4 TeV, 10% at +3 TeV
Note: contrary to (HL-)LHC, CLIC results are model-independent

## Slide 22: snapshot of other physics at CLIC
CLIC physics potential:
Accurate measurement of known physics:
  Higgs
  Top quark
Searching for New Physics:
  Direct searches
  Indirect searches
top mass
threshold scan
near 350 GeV
Additional
heavy Higgs
Δm/m = 0.3%
Δm < 100 MeV

## Slide 23
  How to contribute

## Slide 24
Possible participation in Linear Collider Detector project
Physics
Mechanical engineering
Electronics engineering
e+e-  Hνν  Zγνν
-
-
-
Welcome to join!
  http://clicdp.web.cern.ch/
Projects:
Vertex (pixel) detector R&D
test beam analysis, laboratory tests, engineering
Calorimeter R&D
laboratory tests (optical)
Detector optimisation
simulation of detector layout variants
Physics benchmarking
simulation and analysis

## Slide 25
SPARE
SLIDES

## Slide 26: CLIC machine environment CLIC machine environment
Beam-beam background at IP:
Small beams => very high E-fields
  Beamstrahlung
    Pair-background
      High occupancies
    γγ to hadrons
      Energy deposits
    (19TeV/train @ √s 3TeV)
Beamstrahlung  important energy losses
right at the interaction point
E.g. full luminosity at 3 TeV:
5.9 × 1034 cm-2s-1
Of which in the 1% most energetic part:
2.0 × 1034 cm-2s-1
Most physics processes are studied well above production threshold => profit from full luminosity
3 TeV
√s
energy spectrum

## Slide 27: CLIC physics aims => detector needs
impact parameter resolution:
e.g. c/b-tagging, Higgs BR
jet energy resolution:
e.g. W/Z/h di-jet mass separation
angular coverage, very forward electron tagging
momentum resolution:
e.g. Smuon endpoint
Higgs recoil mass, Higgs coupling to muons
W-Z
jet reco
smuon
end point
(for high-E jets)
+ requirements from CLIC beam structure and beam-induced background

## Slide 28: CLIC experimental conditions
Drives timing
requirements
for CLIC detector
 | CLIC at 3 TeV
L (cm-2s-1) | 5.9×1034
BX separation | 0.5 ns
#BX / train | 312
Train duration (ns) | 156
Rep. rate | 50 Hz
Duty cycle | 0.00078%
σx / σy (nm) | ≈ 45 / 1
σz (μm) | 44
very small beam size
- not to scale -
CLIC
1 train = 312 bunches, 0.5 ns apart
20 ms
156 ns

## Slide 29: CLIC conditions => impact on detector
CLIC conditions => impact on detector technologies:
High tracker occupancies => need small cell sizes
(beyond what is needed for resolution)
    Small vertex pixels
    Large pixels / short strips in the tracker
Bkg suppression => need high-granularity calorimetry
Bkg suppression => overall need for precise hit timing
    ~10 ns hit time-stamping in tracking
    1 ns accuracy for calorimeter hits
Low duty cycle
    Triggerless readout
    Allows for power pulsing
      => less mass and high precision in tracking
      => high density for calorimetry

## Slide 30: comparison CLIC  LHC detector
In a nutshell:
CLIC detector:
High precision:
  Jet energy resolution
    => fine-grained calorimetry
  Momentum resolution
  Impact parameter resolution
Overlapping beam-induced background:
  High background rates, medium energies
  High occupancies
  Cannot use vertex separation
  Need very precise timing (1ns, 10ns)
“No” issue of radiation damage (10-4 LHC)
  Except small forward calorimeters
Beam crossings “sporadic”
No trigger, read-out of full 156 ns train
LHC detector:
Medium-high precision:
  Very precise ECAL (CMS)
  Very precise muon tracking (ATLAS)
Overlapping minimum-bias events:
  High background rates, high energies
  High occupancies
  Can use vertex separation in z
  Need precise time-stamping (25 ns)
Severe challenge of radiation damage
Continuous beam crossings
Trigger has to achieve huge data reduction

## Slide 31
e+e-  Hνν  bbνν
-
-
-
CLIC 1.4 TeV
same event before cuts on beam-induced background

## Slide 32
same event before cuts on beam-induced background
e+e-  ttH  WbWbH  qqb τνb bb
-
-
-
-
-
CLIC 1.4 TeV

## Slide 33: CLIC vertex detector R&D roadmap
CLICpix demonstrator ASIC
64×64 pixels, fully functional
65 nm technology
25×25 μm2 pixels
4-bit ToA and ToT info
Data compression
Pulsed power: 50 mW/cm2
Hybrid approach pursued: (<= other options possible)
Thin (~50 μm) silicon sensors
Thinned high-density readout ASIC (50 μm)
  R&D within Medipix/Timepix effort
Low-mass interconnect
Power pulsing
Air cooling
Very thin sensors !
Successfully tested at DESY test beam
(with existing Timepix ASIC)
1.6 mm
64×64 pixels

## Slide 34: Hybrid vertex detector with HV-CMOS
Hybrid option with HV-CMOS:
Capacitive Coupled Pixel Detector (CCPD)
HV-CMOS chip as integrated sensor + amplifier
Capacitive coupling to CLICpix readout chip
through layer of glue => no bump bonding
Pursuing an alternative readout option
CCPDV3
Status: successful initial beam tests in 2014
Further beam tests in 2015
HV-CMOS + CLICpix, AC coupled

## Slide 35: Vertex detector optimisation
Spiral disks
Single layers
Spiral disks
double layers
Using flavour tagging as a gauge
Test single vs. double layers
More realistic material (0.2% X0/layer)
Vary inner radius (for 4 T or 5 T B-field)
double layer better
single layer better
larger inner radius better
Inner radius 27 mm / 31 mm
0.1% X0/layer / 0.2%X0/layer
Single layers / double layers
more material better
1.
2.
3.
Work in progress !

## Slide 36: Main silicon tracker
all-silicon tracker optimisation ongoing
+
now starting a tracker hardware R&D
7 μm single point accuracy
time-stamping 10 ns
~5-6 tracking layers
Radius ~1.5 m, half-length ~2.3 m
High occupancies in certain regions:
Need for large pixels and/or short-strips
Very light => ~1%X0 per layer
  Requires very thin materials/sensors
  => compatible with charge sharing and 7μm accuracy?
  Power pulsing (?)
  Is air cooling feasible in a large tracker volume?
  Radiation level 104 lower than LHC

## Slide 37: calorimetry and PFA
Jet energy resolution and background rejection drive the overall detector design
=> => fine-grained calorimetry + Particle Flow Analysis (PFA)
Typical jet composition:
60% charged particles
30% photons
10% neutral hadrons
Always use the best info you have:
60% => tracker
30% => ECAL
10% => HCAL

What is PFA?
Hardware + software !

## Slide 38: PFA calorimetry at CLIC
Technology (CDR)
ECAL
Silicon (active) + Tungsten (absorber)
cell sizes ~25 mm2
30 layers in depth (~23 X0)
HCAL
Scintillator+SiPM (active)
Tungsten (barrel), steel (endcap)
cell sizes 9 cm2 (analog)
75/60 layers in depth
Total depth 7.5 Λi
simulated jet energy resolution
(no jet clustering, no background overlay)
many technologies pursued
CALICE collaboration
http://fcal.desy.de/

## Slide 39: Forward calorimetry
2 forward calorimeters: Lumical + Beamcal
Electron / photon acceptance to small angles
Luminosity measurement
Beam feedback
Absorbers: tungsten, 40 layers of 1 X0
Sensors: BeamCal GaAs, LumiCal silicon
Angular coverage:
BeamCal 10 - 40 mrad, LumiCal 38 – 110 mrad
Doses up to 1 Mgy
Neutron fluxes of up to 1014 per year
Very compact !
30 cm
LumiCal
LumiCal
BeamCal
FCAL collaboration
http://fcal.desy.de/

## Slide 40: CLIC detector optimisation
towards one CLIC detector model by mid 2015
include lessons learnt so far
include experience from hardware R&D
In parallel:
Major improvements of simulation and reconstruction software
With new geometry description (DD4hep) and new track reconstruction
Already agreed working hypotheses:
Vertex: double layers
Vertex: spiraling disks
Tracker: all silicon
Tracker: radius 1.5 m, half-length 2.3 m
ECAL: 25 layers, 5×5 mm2 cell sizes
HCAL: steel absorbers
Solenoid field: 4 Tesla
Ongoing assessments:
Tracker layout and technology options
HCAL: cells sizes
Enhanced forward calo coverage
QD0 in detector or in tunnel
……..
Some examples in the following slides

## Slide 41: CLIC strategy and objectives
2013-18 Development Phase
Develop a Project Plan for a staged implementation in agreement with LHC findings; further technical developments with industry, performance studies for accelerator parts and systems, as well as for detectors.
2018-19 Decisions
On the basis of LHC data and Project Plans (for CLIC and other potential projects), take decisions about next project(s) at the Energy Frontier.
4-5 year Preparation Phase
Finalise implementation parameters, Drive Beam Facility and other system verifications, site authorisation and preparation for industrial procurement.
Prepare detailed Technical Proposals for the detector-systems.
2024-25 Construction Start Ready for full construction and main tunnel excavation.
Construction Phase
Stage 1 construction of CLIC, in parallel with detector construction.
Preparation for implementation of further stages.
Commissioning
Becoming ready for data-taking as the LHC programme reaches completion.

## Slide 42: European Strategy statements => 2006/2013 CLIC-related statements
2013 statement “d”:
2006 statement “4”:
pp or e+e-
 at high-energy frontier

## Slide 43: timeline: (HL-)LHC and future collider options