## Slide 1: Layout update in IR1/5
G. Arduini, R. De Maria, M. Fitterer, M. Giovannozzi
Thanks to S. Fartoukh, P. Fessia, C. Garion, C. Magnier, H. Prin, E. Todesco, B. Vasquez De Prada

## Slide 2: Introduction and outline
Layout changes
Optics changes
Aperture
Next activities
Summary

## Slide 3: Layout: V1.1 -> V1.2 in IR1 and IR5
Changes | by
Triplet gradient reduction. New length, position; D1 position changed by 2.35 m towards the arc. | WP3, WP15
TAXS moved towards the IP by 0.33 m (better integration) | WP2, WP8, WP15
D1/D2 integrated strength from 33.4 Tm to 35 Tm (reduced CC voltage) resulting in TAXN-D2-CRAB rigid shift (0.18 m towards the arc) | WP2
no D2/Q4 mask, more space between TCTs/TCLs | WP10, WP15
MCBRD – MCBYY length (1.5 m -> 1.8 m) for larger integrated strength | WP3, WP2, WP15
D2, Q4 and Q5 orbit corrector orientations | WP2, WP15
Q4-Q5 position re-optimized (reduced CC voltage) | WP2
Minor changes of all interconnection lengths | WP15
Changes implemented in optics files. TODO:
  BPM position to be iterated with Blanca
  TCL.6 (maybe even the TCTs) to be iterated with Collimation team
  Renamed TCT.5 in TCT.6 (S. Chemli)
  Wire space reservation (WP2)

## Slide 4: Optics V1.1 -> V1.2
Increase pre-squeeze β* 44 cm -> 48 cm (due to lower triplet gradient)
Increased peak β at constant β* by 5% (due to lower triplet gradient)
Typical ATS squeeze, injection, VDM updated
Provided alignment optics for BPM calibration
Offset knobs ± 2mm introduced due to recent requests from Experiments
Lumi scan knobs in the shadow of this knob with ~100 μm range
TODO:
  βx,y in Q4 tunability range
  IR8 ATS with β*< 3 m and IP longitudinal shift for LHCb new requests
  IR4 optics optimization for instrumentation and e-lens (received only generic optics specifications)
  IR6 optics optimization (no feedback yet LBDS constraints)
  Include D1/D2 transfer function correction if powered in series (not likely to happen)
  Exotic optics: no ATS (no IP phase constraint), ATS2 (suboptimal arc matching) to increase Q4 βx,y tunability range at the cost of chromatic correction and/or arc aperture.

## Slide 5: Squeezed optics
β* pre-squeeze: 44 cm -> 48 cm
Crab cavity: 12 MV needed for 590 μrad
New squeeze transitions needed for flat optics to have β*= 40 cm in the crossing plane.
Optics provided:
β* | 15 cm | 7.5 cm/30 cm | 20 cm | 10 cm/40 cm
Crossing angle | ± 295 μrad | ± 245 μrad | ± 255 μrad | ± 210 μrad
 | 12.5 σ | 14.5 σ | 12.5 σ | 14.5 σ
Separation | ± 2 mm | ± 0.75 mm | ± 2 mm | ± 0.75 mm

## Slide 6: Aperture margins
Layout and optics define nominal orbit and beam sizes.
Geometry of the vacuum system (e.g. beam screens inner dimensions with tolerances).
Operational tolerances on beam size are added to the actual beam size.
Alignment and fiducialization tolerances are subtracted from available aperture.
The difference in units of beam sigma is calculated and compared with the aperture protected by the collimation systems

## Slide 7: Aperture triplet region
Octagonal beam screens for triplets/D1 with tungsten shielding have been designed.
Expected straightness: 0.5 mm
Shape tolerance: ± 1 mm (C. Garion 12/06/2015 ), to be confirmed by the prototype.
The possibility of reducing the tungsten layer thanks to alternating crossing planes (F. Cerutti, S. Fartoukh) should be checked.
Triplet beam screens, C. Garion
shielding
cooling
Element | H or V gap [mm] | 45° gap [mm]
Q1 | 102-1.5 | 102-1.5
Q2-Q3-CP | 122-1.5 | 114-1.5
D1 | 122-1.5 | 114-1.5

## Slide 8: Aperture D2-Q4-Q5
New D2-Q4 octagonal beam screens have been designed, no tolerances given, yet.
Q5 beam screens (RectEllipse) oriented for collision optics aperture optimizations.
Same triplet tolerances removed from the mechanical dimensions.
D2
Q4
C. Garion, no tolerances included
Element | H or V gap [mm] | 45° gap [mm]
MBRD | 87.0-1.5 | 78.0-1.5
MQYY | 78.5-1.5 | 63.8-1.5
Q5 | 57.8, 48.0 | 

## Slide 9: Orbit corrector knobs
 | x-scheme [Tm] |  |  | cc alignment [Tm] |  |  | err [Tm] | arc [Tm] | lumi [Tm] | summary [Tm] |  | 
name | x | s | o | ccp | ccm | ccs | err | arc | lumi | tot | max | margin [%]
MCBX1 | 0.14 | 0.11 | 1.16 | 0.19 | 0 | 0 | 0.92 | 0 | 0 | 2.42 | 2.5 | 3.30
MCBX2 | 0.07 | 0.05 | 0.79 | 0.19 | 0 | 0 | 1.40 | 0 | 0 | 2.17 | 2.5 | 1.53
MCBX3 | 2.11 | 0.2 | 0.94 | 0.45 | 0.15 | 0 | 0.78 | 0 | 0 | 4.43 | 4.5 | 1.45
MCBRD4 | 2.97 | 0.09 | 0 | 0.28 | 0.15 | 0.52 | 0.11 | 0.35 | 0.27 | 4.60 | 4.5 | -2.89
MCBYY4 | 1.49 | 0.04 | 0.12 | 0.42 | 0.42 | 0.92 | 0 | 0.35 | 0.20 | 4.74 | 4.5 | -5.39
MCBY5 | 0 | 0 | 1.35 | 0.40 | 0.40 | 0.35 | 0 | 0 | 0 | 2.46 | 2.7 | 8.9
MCBY5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.7 | 0 | 0.7 | 2.7 | 26
MCBC6 | 0 | 0 | 0.46 | 0 | 0 | 0 | 0 | 0.7 | 0 | 0.46 | 2.8 | 83.4
MCBC7 | 0 | 0 | 1.40 | 0 | 0 | 0 | 0 | 0.7 | 0 | 1.40 | 2.8 | 50
IP crossing, separation, offset (x: ±295 μrad, , s: ±0.75 mm, o: ±2.0 mm)
beam based alignment of crab cavities: ccp, ccm (shift): ±0.5 mm, ccs (slope): ±0.25 mm
IT alignment and transfer function errors (err): ±0.5 mm transverse, ±10 mm longitudinal, ±2x10-3 relative gradient error, ±2x10-3 D2 relative field error.
orbit correction from the arc (to confirmed): arc 0.7 Tm;
lumi scan knobs (single beam IP shift for 100μm)
Studying re-sharing forces with new crossing and separation scenarios
  MCBRD/YY length increase 1.6 m -> 1.8 m needed

## Slide 10: Beam tolerances and collimation protection
Beam tolerances have been re-defined by:
Taking into account LHC Run I successful experience
Adding safety margins based on possible unknowns.
For collimation:
magnet protected by TCT: ≥ 12 σ
magnet not protect by TCT: 18 σ(2) or possibly less, pending dedicated studies (R. Bruce) .
Beam Tolerance | LHC DR Inj./Coll. | HL-LHC Inj./Coll.
Emittance [µm] (normalization only) | 3.75/3.75 | 3.5/3.5
β-beating [%] | 20/20 | 10/20
Orbit error [mm] | 4/3 | 4/2
Spurious Disp. [%] | 27.3/27.3 | 14/10
Dp/p [10-4] | 15/8.6 | 6/2
Target aperture [σ] | 8.4/8.4 | 9(1)/12 (18(2))
R. Bruce et al., CERN-ACC-2014-0044
Minimum aperture not protected by TCT in collision and aperture targets at injection should be confirmed by WP5(2) and WP14(1).

## Slide 11: Aperture vs optics for baseline
 | Round 15 cm | Round 20 cm | Flat 7.5 cm | Flat 10 cm
 | [σ] | [σ] | [σ] | [σ]
TAXS | 9.9 | 12.1 | 9.6 | 11.3
MQXFA.[AB]1 | 13.2 | 16 | 12.3 | 14.2
MQXFB.[AB]2 | 9.4 | 11.7 | 9.7 | 11.2
MQXFA.[AB]3 | 9.5 | 11.8 | 10 | 11.6
MBXF | 10.7 | 13.1 | 10.6 | 12.3
TAXN | 11.6 | 13.8 | 9.5 | 11.0
MBRD | 13.1 | 15.3 | 11.1 | 12.8
MCBRD | 16 | 18.7 | 13.7 | 15.4
MCBYY | 15.4 | 17.9 | 13.4 | 15.5
MQYY | 16.3 | 18.9 | 13.9 | 16.1
TCLMB.5 | 20.3 | 23.5 | 14.5 | 16.8
MCBY[HV].5 | 20.6 | 23.9 | 15 | 17.3
MQY.5 | 21.4 | 24.7 | 15.3 | 17.7
TCLMC.6 | 21.2 | 24.6 | 15 | 17.4
MCBC[HV].6 | 24.7 | 28.5 | 17.4 | 20.1
MQML.6 | 21.8 | 25.2 | 15.7 | 18.1
Aperture includes worst case scenarios for all knobs (IP crossing, separation, offset, crab cavity offset) assuming linear addition
Aperture in the triplets can be recovered by:
reducing crossing angle (round optics) and separation (flat optics) if one assumes that β* levelling is feasible
reducing beam screen/cold bore tolerances, shielding thickness (see US-LARP presentation)
This allows:
more aperture in the triplet at constant β* or
more performance if matching section keeps present margins.

## Slide 12: TAXS
TAXS aperture needs to be increased to 60 mm
Round
Flat

## Slide 13: Q1
Q1 OK
Round
Flat

## Slide 14: Q2
Q2 not OK, but options to improve it available
Round
Flat

## Slide 15: TAXN
Round
Flat
Left
Right
Aperture to be increased: 80mm to 85mm

## Slide 16: Q4 options
 | Coil aperture | Beam1 aperture | H,V2 full gaps | Round 15 cm | Round 20 cm | Flat 7.5 cm | Flat 10 cm
 | [mm] |  | [mm] | [σ] | [σ] | [σ] | [σ]
MCBYY | 90 | Octagon | 73.8,73.8 | 15.4 | 17.9 | 13.4 | 15.5
MQYY | 90 | Octagon | 73.8,73.8 | 16.3 | 18.9 | 13.9 | 16.1
MCBYY | 80 | Octagon | 63.8,63.8 | 11.6 | 13.5 | 10.1 | 11.7
MQYY | 80 | Octagon | 63.8,63.8 | 12.3 | 14.2 | 10.5 | 12.1
MCBY | 70 | RectEllipse | 57.8,48 | 11.8 | 13.7 | 8.4 | 9.8
MQY | 70 | RectEllipse | 57.8,48 | 13 | 15.1 | 9.2 | 10.6
Aperture includes worst case scenarios for all knobs: IP crossing, separation, offset, crab cavity offset (assuming linear addition).
We exclude the option MQY for robust flat optics operations.
MQYY at 80 mm is not sufficient to provide enough flexibility:
  Any improvement in triplet aperture would be useless if Q4 aperture is degraded.
  If Q4 needs to be pushed towards D2 more aperture is needed (about 0.7 σ).
  In case of operation at 6.5 TeV.
  The use of a Rectellipse beam screen can help recovering aperture, but only in specific cases: freezing optics constraints or crossing plane.
Impact of energy deposition needs to be re-evaluated in case of reduction of coil aperture

## Slide 17: Q4: MQY with 70 mm coils
Q4 with MQY not ok
Round
Flat
Left
Right

## Slide 18: Q4: MQYY with 80 mm coils
MQYY with 80mm coil not OK. RectEllipse option can help only for special cases.
Round
Flat
Left
Right

## Slide 19: Q4: MQYY with 90 mm coils
Q4 with MQYY: OK
Round
Flat
Left
Right

## Slide 20: Q5 options
 | Coil aperture | Beam1 aperture | H,V2full gaps | Round 15 cm | Round 20 cm | Flat 7.5 cm | Flat 10 cm
 | [mm] |  | [mm] | [σ] | [σ] | [σ] | [σ]
TCLMB.5 | 70 | RectEllipse | 57.8,48 | 20.6 | 23.9 | 15.0 | 17.8
MCBY[HV].5 | 70 | RectEllipse | 57.8,48 | 21.4 | 24.7 | 15.3 | 18.4
MQY.5 | 70 | RectEllipse | 57.8,48 | 21.2 | 24.6 | 15.0 | 17.6
TCLMB.5 | 56 | RectEllipse | 45.1,35.3 | 14.0 | 16.2 | 10.0 | 11.6
MCBC[HV].5 | 56 | RectEllipse | 45.1,35.3 | 13.8 | 16.0 | 10.1 | 11.7
MQML.5 | 56 | RectEllipse | 45.1,35.3 | 14.4 | 16.6 | 10.3 | 11.9
The RectEllipse shapes are oriented in opposite way w.r.t the LHC for both MQY and MQML options.
The choice of a new MQYY option for Q4 allows to re-use the MQY for Q5 including, which provides the two additional orbit correctors that are needed in Q5.
The MQY aperture is also needed for the present alignment optics at injection (not shown in the table).
The MQY aperture may avoid the need of a TCT protecting Q5.
Aperture includes worst case scenarios for all knobs: IP crossing, separation, offset, crab cavity offset (assuming linear addition).

## Slide 21: MQYY for Q5 in Q7+ optics
An additional Q7 and 2xMQYY in Q5 per side allow a substantial reduction of crab cavity voltage.
D2
Crabs
Q4
2xMQYY
Q5
Q6
Q7
2xMQM
MQYY
MQY
MQML
2xMQM
MQML
MQYY
2xMQM
 | V1.1 | Q7+
Crab voltage for 295 µrad | 12 MV | 8.8 MV
V1.1
Q7+
Ref: B. Dalena et al., Task 2.2, 24/10/2014
Voltage reach based on 90 mm aperture
without offset at the IP.
Without the additional Q7, it is difficult to make use of the large aperture margin provided by a MQYY in Q5. This option is therefore dropped.

## Slide 22: Next activities
Layout re-validation (Q4-Q5 position) | WP15, WP2
Wire space reservation | WP2
Review energy deposition | WP10
Confirm ground motion and fiducialization assumptions | Survey, WP3, WP8
Validation minimum protected aperture (collimation, injection, dump) | WP5, WP14
Validation aperture TAXS and TAXN with Experiments | WP8
Beam screen tolerances | WP12
Validation of dump (IR6), injection (IR2, IR8) optics constraints | WP14
Specification of optics constraints for IR4 | All requestors
Validation requirements orbit correction from the arc | WP2/OP

## Slide 23: Summary
New layout and optics increased β* value for the squeeze and pre-squeeze optics.
Critical revision of aperture, taking into account all constraints learnt from Run I experience.
Orbit correctors margins re-evaluated taking into account all known requests: additional strength needed (increased magnetic length). In addition, revision of the strength sharing on-going.
Q4 aperture: option of re-using MQY excluded. The current baseline is kept (90 mm), pending evaluation of benefits (magnet side) of slight aperture reduction (e.g., down to 85 mm).
Q5 aperture: critical review of aperture indicates the benefits of re-using the MQY (present Q4). This choice provides naturally also the needed two additional orbit correctors.

## Slide 24: Back-up

## Slide 25: Offset knob – 2mm

## Slide 26: Orbit corrector knobs - 1.5 m, 3T
 | x-scheme [Tm] |  |  | cc alignment [Tm] |  |  | err [Tm] | arc [Tm] | lumi [Tm] | summary [Tm] |  | 
name | x | s | o | ccp | ccm | ccs | err | arc | lumi | tot | max | margin [%]
MCBX1 | 0.14 | 0.29 | 1.22 | 0.19 | 0 | 0 | 0.92 | 0 | 0 | 2.63 | 2.5 | -5.2
MCBX2 | 0.07 | 0.14 | 0.55 | 0.19 | 0 | 0 | 1.4 | 0 | 0 | 2.54 | 2.5 | -1.42
MCBX3 | 2.11 | 0.54 | 0.94 | 0.45 | 0.15 | 0 | 0.78 | 0 | 0 | 4.43 | 4.5 | 1.45
MCBRD4 | 2.97 | 0.24 | 0 | 0.28 | 0.15 | 0.52 | 0.08 | 0.35 | 0.27 | 4.53 | 4.5 | -0.63
MCBYY4 | 1.49 | 0.12 | 1.12 | 0.42 | 0.42 | 0.92 | 0 | 0.35 | 0.2 | 4.81 | 4.5 | -6.98
MCBYS5 | 0 | 0 | 1.35 | 0.4 | 0.4 | 0.44 | 0 | 0 | 0 | 2.46 | 2.7 | 8.9
MCBY5 | 0 | 0 | 0.47 | 0 | 0 | 0 | 0 | 0 | 0 | 0.47 | 2.8 | 83.31
MCBC6 | 0 | 0 | 1.4 | 0 | 0 | 0 | 0 | 0 | 0 | 1.4 | 2.8 | 50
MCBC7 | 0.14 | 0.29 | 1.22 | 0.19 | 0 | 0 | 0.92 | 0 | 0 | 2.63 | 2.5 | -5.2
IP crossing, separation, offset (x: ±295 μrad, , s: ±2.0 mm, o: ±2.0 mm)
beam based alignment of crab cavities: ccp, ccm (shift): ±0.5 mm, ccs (slope): ±0.25 mm
IT alignment and transfer function errors (err): ±0.5 mm transverse, ±10 mm longitudinal, ±2x10-3 relative gradient error, ±2x10-3 D2 relative field error.
orbit correction from the arc (to confirmed): arc 0.7 Tm;
lumi scan knobs (single beam IP shift for 100μm)
Notes: Q4_8m/opt_presqueeze.madx

## Slide 27: Orbit corrector knobs – 1.8 m
 | x-scheme [Tm] |  |  | cc alignment [Tm] |  |  | err [Tm] | arc [Tm] | lumi [Tm] | summary [Tm] |  | 
name | x | s | o | ccp | ccm | ccs | err | arc | lumi | tot | max | margin [%]
MCBX1 | 0.19 | 0.28 | 0.88 | 0.19 | 0 | 0 | 0.92 | 0 | 0 | 2.27 | 2.5 | 9.04
MCBX2 | 0.09 | 0.14 | 0.14 | 0.19 | 0 | 0 | 1.4 | 0 | 0 | 1.9 | 2.5 | 24.06
MCBX3 | 2.29 | 0.54 | 0.41 | 0.45 | 0.15 | 0 | 0.78 | 0 | 0 | 4.08 | 4.5 | 9.37
MCBRD4 | 3.55 | 0.28 | 0 | 0.28 | 0.15 | 0.52 | 0.08 | 0 | 0.27 | 4.76 | 5.4 | 11.91
MCBYY4 | 1.07 | 0.08 | 2.1 | 0.42 | 0.42 | 0.92 | 0 | 0.7 | 0.2 | 4.96 | 5.4 | 8.24
MCBYS5 | 0 | 0 | 1.23 | 0.4 | 0.4 | 0.44 | 0 | 0 | 0 | 2.34 | 2.7 | 13.51
MCBY5 | 0 | 0 | 0.0 | 0 | 0 | 0 | 0 | 0.7 | 0 | 1.26 | 2.8 | 83.31
MCBC6 | 0 | 0 | 1.26 | 0 | 0 | 0 | 0 | 0 | 0 | 1.26 | 2.8 | 55.17
MCBC7 | 0 | 0 | 1.4 | 0 | 0 | 0 | 0 | 0 | 0 | 1.4 | 2.8 | 50
IP crossing, separation, offset (x: ±295 μrad, , s: ±0.75 mm, o: ±2.0 mm)
beam based alignment of crab cavities: ccp, ccm (shift): ±0.5 mm, ccs (slope): ±0.25 mm
IT alignment and transfer function errors (err): ±0.5 mm transverse, ±10 mm longitudinal, ±2x10-3 relative gradient error, ±2x10-3 D2 relative field error.
orbit correction from the arc (to confirmed): arc 0.7 Tm;
lumi scan knobs (single beam IP shift for 100μm)
Notes: Q4_8m/opt_presqueeze_1_8m_mcbrd_mcbyy.madx with cd2q4=0.3

## Slide 28: Effect of the knobs
 | Coil aperture | Beam1 aperture | H,V2full gaps | Sep. knob | Crossing Knob | Crab shift knob | Crab slope knob | Offset knob
 | [mm] |  | [mm] | [mm] | [mm] | [mm] | [mm] | [mm]
TAXS | 54 | Circle | 54, 54 | 0.8 | 6.1 | 0.0 | 0.0 | 2.0
MQXFA.[AB]1 | 150 | Octagon | 102, 102 | 0.8 | 11.2 | 0.0 | 0.0 | 2.4
MQXFB.[AB]2 | 150 | Octagon | 122, 122 | 1.2 | 16.7 | 0.2 | 0.0 | 3.6
MQXFA.[AB]3 | 150 | Octagon | 122, 122 | 0.8 | 16.6 | 0.4 | 0.0 | 2.8
MBXF | 150 | Octagon | 122, 122 | 0.5 | 15.5 | 0.5 | 0.0 | 2.4
TAXN | n/a | Circle | 80, 80 | 0.2 | 5.5 | 0.9 | 0.0 | 3.0
MBRD | 105 | Octagon | 87, 87 | 0.1 | 3.3 | 1.0 | 0.0 | 3.3
MCBRD | 105 | Octagon | 87, 87 | 0.1 | 1.7 | 1.0 | 0.1 | 3.4
MCBYY | 90 | Octagon | 73.8,73.8 | 0.0 | 0.1 | 1.0 | 0.5 | 4.0
MQYY | 90 | Octagon | 73.8,73.8 | 0.0 | 0.0 | 1.0 | 0.5 | 3.9
TCLMB.5 |  | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.4 | 0.2 | 3.7
MCBY[HV].5 | 70 | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.0 | 0.0 | 3.6
MQY.5 | 70 | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.2 | 0.1 | 3.5
TCLMC.6 | 56 | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.3
MCBC[HV].6 | 56 | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.1
MQML.6 | 56 | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.1
1Either Beam screen or beam pipe;
2 Rectellipse types are exchanges the H,V orientation depending on the polarity

## Slide 29: Effect of the knobs – 1.8 m
 | Coil aperture | Beam1 aperture | H,V2full gaps | Sep. knob | Crossing Knob | Crab shift knob | Crab slope knob | Offset knob
 | [mm] |  | [mm] | [mm] | [mm] | [mm] | [mm] | [mm]
TAXS | 54 | Circle | 54, 54 | 0.8 | 6.1 | 0.0 | 0.0 | 2.0
MQXFA.[AB]1 | 150 | Octagon | 102, 102 | 0.8 | 11.2 | 0.0 | 0.0 | 2.5
MQXFB.[AB]2 | 150 | Octagon | 122, 122 | 1.2 | 16.7 | 0.2 | 0.0 | 3.4
MQXFA.[AB]3 | 150 | Octagon | 122, 122 | 0.8 | 16.6 | 0.4 | 0.0 | 2.6
MBXF | 150 | Octagon | 122, 122 | 0.5 | 15.5 | 0.5 | 0.0 | 1.7
TAXN | n/a | Circle | 80, 80 | 0.2 | 5.5 | 0.9 | 0.0 | 3.1
MBRD | 105 | Octagon | 87, 87 | 0.1 | 3.3 | 1.0 | 0.0 | 3.4
MCBRD | 105 | Octagon | 87, 87 | 0.1 | 1.7 | 1.0 | 0.1 | 3.7
MCBYY | 90 | Octagon | 73.8,73.8 | 0.0 | 0.1 | 1.0 | 0.5 | 4.3
MQYY | 90 | Octagon | 73.8,73.8 | 0.0 | 0.0 | 1.0 | 0.5 | 4.2
TCLMB.5 |  | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.3 | 0.1 | 3.7
MCBY[HV].5 | 70 | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.0 | 0.0 | 3.6
MQY.5 | 70 | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.1 | 0.1 | 3.5
TCLMC.6 | 56 | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.3
MCBC[HV].6 | 56 | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.1
MQML.6 | 56 | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.1
1Either Beam screen or beam pipe;
2 Rectellipse types are exchanges the H,V orientation depending on the polarity
Notes: Q4_8m/opt_presqueeze.madx

## Slide 30: Alignment optics
Optics to align BPMs in the triplet at injection.
Compatible with injection strength, but aperture not exceptional in the arcs.