## Slide 1: WP3 UPDATES
E. Todesco
CERN, Geneva Switzerland
HI-LUMI TC, 6th October 2015

## Slide 2: LAST UPDATES
Triplet powering scheme
  We keep the two independent circuits as the baseline
  More time needed to get consensus on the one circuit solution
Q4 current
  Changed from 16 kA to 5 kA, using two layer cable
  Saving 8 power converters at 18 kA
Q4 length
  New operational gradient is 120 T/m, so magnetic length is 3.67 m
  Not yet in the intergration files, will be included in next iteration
D2 Q4 correctors
  Design change from 2 kA to 600 A – study in progress (we still do not the cable)
  Saving 32 2 kA power converters

## Slide 3: LAST UPDATES
Q6 temperature changed from 1.9 to 4.2 K
  See Herve talk – no need from beam dynamics
Current of the high order correctors is still at 120-150 A
  Studies to lower in order to be able to use the 120 A power converters, but no change of baseline yet
D1 and D2 in series
  In the hands of Felix, I put one circuit in the TDR
Important to have feedback on the need of doubling Q5 in IR6
  We should order the cryostats next year

## Slide 4: QUACO
European program QUACO
  Consortium of CERN, CIEMAT, CEA, Polish institute
  4.5 M to build two prototypes of Q4 in two different firms
  One procurement including conceptual design (short), engineering and tooling (1 y) and construction (2 y)
    3 Firms participating to conceptual and engineering, then reduced to 2 for construction
  Prototype ready by end 2019
    In line with the planning, also considering the recent 1 year shift of Q4 due to design change
  Complex proposal, but non negligible money
  Initial hypothesis of building one Q4 and one long corrector discarded (incompatible with planning)
  Program chaired by M. Losasso (CERN FP-KT)