## Slide 1: Status of the charge breeder upgrade
Fredrik Wenander, TSR workshop 27/4-2015
Outline
Revise goals
HEC2 path
MedEgun path
Notes: Programme since 2012
Time to deliver - present status

## Slide 2
Benefits of high charges states
  Rigidity TSR
  Storage lifetimes
  Cooling times
  Experiments
Ion | Z | q | A/q | Breeding time (ms)
7Be | 4 | 3 | 2.33 | 20
18F | 9 | 9 | 2 | 100
70Ni | 30 | 25 | 2.33 | 350
132Sn | 50 | 39 | 3.38 | 700 *
182Pb | 82 | 53 | 3.43 | 1000 *
182Pb | 82 | 64 | 2.84 | EBIS upgrade needed
REXEBIS charge breeding times
* to be tested
Some experiments might require:
* Fully stripped to Z~70
* Few-electron system, e.g. for Th/U
Tcool – horizontal cooling time for beam with large diameter
Light elements easiest to reach low A/q
Internal gas target
Notes: REXEBIS charge breeding times for a selection of elements of relevance for TSR@ISOLDE experiments
A/q<3.5 required for 10 MeV/u
 REXEBIS charge breeder capable of producing sufficiently low A/q (or beam rigidity for < 10MeV/u) for most elements

## Slide 3
Chart: Electron energy, [keV]
| 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150
Bare | 0.043211 | 0.10316 | 0.16177 | 0.21704 | 0.26812 | 0.31509 | 0.35822 | 0.39755 | 0.43356 | 0.46647 | 0.49663
H-like | 0.66536 | 0.67671 | 0.66689 | 0.64649 | 0.62118 | 0.59366 | 0.56567 | 0.53828 | 0.51179 | 0.48657 | 0.46273
He-like | 0.26822 | 0.20693 | 0.1632 | 0.13116 | 0.10707 | 0.088694 | 0.074262 | 0.062783 | 0.053606 | 0.046155 | 0.040004
 | TSR breeder | REXEBIS
Electron energy [keV] | 150 | 5
Electron current [A] | 2-5* | 0.2
Electron current density [A/cm2] | 1-2x104 | 100
Trap pressure (mbar) | ~10-11 | ~10-11
Ion-ion cooling needed | YES | NO
Extraction time (us) | <30 | >50
TSR@ISOLDE breeder design parameters
Capacity of 108 primary ions needs current Ie >3 A
Transverse acceptance ~ 34 μm (REXEBIS) needs Ie ~ 4-5 A
*
Chart: Current density required for 1 Hz rep rate
150 keV electron beam
Barium charge states

## Slide 4
High Energy Current and Compression (HEC2) electron gun project
HEC2 path

## Slide 5: Gun design
Very laminar electron flow,
high electrostatic compression
Matching two focusing systems
Electrostatic compression (~300)
Magnetic compression (~50)
anode
cathode
electron beam
Challenges
Require low B-field at cathode
Non-rippling electron beam
Mechanical tolerances
(Penning) discharges
magnetic field ‘grab’ the beam (~0.25 T)
A. Pikin, E. N. Beebe, and D. Raparia,
Rev. Sci. Instr. 84 033303 (2013)

## Slide 6: HEC2 gun and TestEBIS
Prototype gun design by BNL, built by CERN being tested at BNL by joint team at BNL TEBIS
Notes: External magnetic coil

## Slide 7: HEC2 prototype tests at BNL
Scenario | Ee, keV | Ie, A | Je, kA/cm2
HEC2 ultimate spec | 150 | 5 | >10
Test stand limit as is | 40 | 2.2 | 5
Achieved in 2nd run | 30 | 1.7 | tba
O7+
C5+
O6+
C4+
O5+
C3+/O4+
450 mA,
16.6 ms
C6+/O8+
H1+
Ions extracted, O6+/O5+ and C5+/C4+
give too big error bars to define Je
courtesy E. Beebe
Max current ramped to 1.7 A,
still limited by loss current
1V0.5A

## Slide 8
Chart: Electron beam energy, eV
| 5000
REX | 200
LLNL rep† | 5200
MSU rep* | 640
Titan est | 2000
CARIBU exp* | 750
HEC2 II | 10000
RHIC | 600
HEC2 low | 200
HEC2 up | 4000
HEC2 | 10000
Bubble size represents electron current
rep – reported
est – estimated - in commissioning phase
† - discontinued
Where we are on the map?

## Slide 9
Limiting factor – loss current
20 mA = 2% losses, too high for an EBIS.
20 mA x 12 kV = 240 W heating on the anode, too high for high duty factor and good vacuum.
In experiment – 20 mA trips the power supply.
Where 20 mA come from?

## Slide 10
Simplest answer is the wrong one
How do we know that?
Origin of loss current?

## Slide 11
Anode current strongly depends on
Drift tune voltages
Phase-coil current
Origin of loss current?

## Slide 12
Origin of loss current?
courtesy R. Mertzig
increasing B-field

## Slide 13
courtesy R. Mertzig
Wehnelt 0 V
Wehnelt 50 V
First two runs without Wehnelt.
At third test Wehnelt was shortcut.
Next HEC2 actions
Furthermore
a. Adjustment to compensate for
heat dilatation of cathode
b. Intercept reflected electrons
with a collimating tube
HEC2 design presently under revision
to reach specification of 3.5 A

## Slide 14
MedEgun path
Electron gun optimised for production of rapid C6+

## Slide 15
EBIST as 2nd generation IBT injector
Our suggestion:
EBIS with high-compression electron gun
+ Potentially very fast
+ Short ion pulses <5 us attainable for carbon ions
(aim for single-turn inj.)
+ 6+ ions out of the source
+ Very low beam contamination
Cyclinac ver. 2
MedEgun
MedEgun would require less electron current than proven, but a higher current density
C6+ per pulse

## Slide 16
 | TSR breeder | REXEBIS | MedEgun
Electron energy [keV] | 150 | 5 | 10
Electron current [A] | 2-5* | 0.2 | 1
Electron current density [A/cm2] | 1-2x104 | 100 | 1200
Trap pressure (mbar) | ~10-11 | ~10-11 | ~10-11
Ion-ion cooling needed | Yes | No | To be tested
Extraction time (us) | <30 | >50 | >50
Downscaling of HEC2 ultimate goal leads to IBT application
+ Less dependent on BNL constraints
+ More straightforward to implement (no need for a new SC magnet)
+ Funding available
? Efficiency unknown
How can TSR@ISOLDE benefit?
10 times faster than REXEBIS
No fully stripped heavy ions
fully stripped to Fe
Z=30 He-like
Z=40 He-like
Z=50 He-like
Z=60 O-like
Z=70 Na-like
Z=80 Na-like
Z=90 P-like

## Slide 17
Also use 3D electron beam simulations running on the CERN computing cluster
Investigate:
mechanical tolerances
electron beam back reflection
from gun-to-collector simulation
MedEGUN simulations
Latest state of the electron gun optimisation
2D Field Precision
3D CST

## Slide 18
Mechanical design
Present stage of the mechanical design
* integration study
* mechanical precision
superconducting magnet
drift tube structure
electron gun
gate valve
feedthrough flange
Notes: Two different mechanical implementations of the electron gun
Will start involving specialists from CERN group in June

## Slide 19
Test bench for electron gun
Functional EBIS available for tests:
magnet and vacuum chamber
electron collector
Focus entirely on the gun side
TwinEBIS setup in building 150
If successful -> could be implemented at REXEBIS
Possibly need to modify :
drift tube structure
collector to handle the larger current and deposited current
Approximate cost 200 kCHF

## Slide 20
2nd iteration
Manpower and budget request to KT fund (approved)
* Estimated hardware cost for technical support 90 kCHF
* Full-time fellow over 2 years with 50% coverage by the KT fund, remaining part elsewhere
Timeline and resources
Notes: Already started the development work, ahead of schedule for the moment
190 kCHF manpower+materials (CERN Knowledge Transfer grant)

## Slide 21
Conclusions
* Next HEC2 tests foreseen in May 2015
* HEC2 development continues + with or without CERN
  - fellow A. Shornikov’s continuation depends
on approval of ENSAR2
? HEC2 priority for BNL?
* In parallel MedEgun development started at CERN
partly funded by Knowledge Transfer fund at CERN
not aiming for heavy fully stripped ions
potentially very fast breeder
electron gun can be used in REXEBIS solenoid
intermediate stage to ultimate TSR charge breeder
Notes: HEC2 more difficult than BNL thought – maybe not me