## Slide 1: Bandwidth-sharing in LHCONE
an analysis of the problem
Insert title here…

## Slide 2: Spoiler…
Question:
  Can we use market-mechanisms (auctions etc) to address bandwidth-sharing at LHCONE?
Answer:
  Yes, with a caveat: market-mechanisms work well with real money, much harder with fake ‘budgets’

## Slide 3: Schedule, but how?
How to allocate bandwidth fairly & efficiently to users with different & time-dependent needs?
Candidate technologies, won’t discuss here
  Virtual circuits, multi-path flows
  Bandwidth guarantees can be hard or soft
Then you get a new problem: oversubscription
  Common to all successful middleware:
    phase 1: make it possible, phase 2: stop users abusing it!

## Slide 4: A good bandwidth-sharing system?
Automatic, lightweight
  Set up ‘circuits’ automatically, but only where needed
  Participation not mandatory (casual or low-load users)
Elastic, responsive
  Shares can grow & shrink on timescale of ~1 hour to follow needs
Efficient, fair
  Allows maximal use of bandwidth at all times
  Short-term & long-term: no starvation, no hogging
Fixed quotas

## Slide 5: High-level requirements: we want…
A way for users to tell LHCONE their needs
  At any time, across the whole of the LHCONE network
To resolve over-subscription, quickly & fairly
Technology to implement the shares
  (out of scope of this talk)
To avoid the possibility of ‘gaming the system’
One option, the Progressive Second-price Auction
  A.Lazar, N.Semret, Design, analysis and simulation of the progressive second price auction for network bandwidth sharing

## Slide 6: Second-price auctions
Highest bid wins, price set by the 2nd-highest bid
  Sounds odd, but is very common. E.g. Sothebys, Christies, the classic ‘English auction’
  Two bidders raise in increments until one drops out, the other then wins, but price set by the one who stops bidding
Key property: Best strategy is to bid the truth
  Bid too high: may win, but at unacceptable cost
  Bid too low: may lose at a price less than you are willing to pay
  C.f. first-price auction: best strategy is to guess other bids, then bid between that and your true value
  Useful when need to maximise ‘social utility’, not ‘profit’.

## Slide 7: How does the PSP work?
Network offers bandwidth Q on a given link
Bidders have a given budget (varies per bidder)
  Bidders specify quantity & unit-price: (qi,pi)
  PSP calculates allocations & total costs: (ai,ci)
  PSP sends all allocations/costs to all bidders
  Bidders revise their bids
Repeat until 3-6 until convergence
Convergence guaranteed for rational bidders

## Slide 8: Rationality, cost…
Rational bidders
  Economics: Law of Diminishing Marginal Returns
  The more b/w you have, the less you are willing to pay to get even more
Cost based on ‘exclusion compensation principle’
  Bidder i inconveniences other bidders, who lose a slice of bandwidth because they are outbid by i
  Cost to i set based on how much other bidders lose out because i exists

## Slide 9
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
Player with highest unit-price has their quantity subtracted from the total
Player with 2nd highest unit-price takes from what’s left
Bandwidth available for auction

## Slide 10
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
New bid ( qi, pi )

## Slide 11
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
New bid ( qi, pi )
How much does bidder i get?

## Slide 12
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
ai
How much does bidder i get?

## Slide 13
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
ai
How much does bidder i get?
How much does bidder i pay?

## Slide 14
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
ai
How much does bidder i get?
How much does bidder i pay?
ci =

## Slide 15
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
Bidder i’s ‘utility curve’
i’s optimal bid

## Slide 16: PSP on LHCONE?
PSP extends naturally to multiple links
  Decentralized, independent auction on each link
  Bidders have fixed global budget
  Can show that best strategy is to bid for same bandwidth on each link
  Bidder offers a price per link dependent on the competition for that link
  Still converges if bidders are rational
Repeat auction whenever conditions change
  After some ‘lease-time’, to prevent chaos - ~1 hour?

## Slide 17: Does that satisfy requirements?
Automatic, lightweight?
  Create circuits only where needed (i.e. where competition exists)
  May choose to not create circuits if natural performance satisfies requirements, trigger new auction if conditions change…
Elastic, responsive?
  Auction converges quickly, even for several tens of users
  Can make convergence faster with ‘reserve price’
Efficient, fair? Two sub-problems
  How to set budgets?
  How to cater for non-bidders/non-participants (casual users)?

## Slide 18: Practicalities: budgets…
Real world, real money
  Budgets set by bidders
  PSP guarantees the bidders converge on a solution
LHCONE, HEP experiments, fake budget
  Must ensure ‘fake money’ has real value in the auction
  How to set the budgets?
    One-time allocation not enough, auctions recur as conditions change
    Budget spent ~every time you win a slice of an auction, need to reset/adjust periodically, to keep the bidders solvent
    Similar problem to allocating batch quota on shared farms?

## Slide 19: How, and how often, to update budgets?
Reset budget per-auction?
  No incentive not to spend entire budget every time => create circuits where you don’t really need them
  Can bid to block opponents if you don’t need your full budget
Excess budget may be harmful
  Blocking tactics, bidding for a link you don’t need
  Some way to penalize for under-used circuits?
Carry-over of unspent budget?
  Budget-hoarding => undesirable/‘unfair’ outcomes
  Carry-over with exponential decay? Fixed ceiling?

## Slide 20: How, and how often, to update budgets?
Repeat auctions: possible learning of strategy
  Learn which links your opponent favours, and when
  May or may not be a problem, depends if result is co-operative or destructively competitive
Needs simulation, with various bidding strategies
  Budget adjustment must not destroy auction fairness
Initial budget, and refresh policy, decided by WLCG?

## Slide 21: How to represent LHCONE?
Topology: by individual service provider?
  PSP allows independent auctions, so each region can auction their part of the network separately
  Introduces another budget-related problem:
    With real money, the bidder decides how they are limited.
    With fake money, need to co-ordinate between independent auctions to ensure no bidder overspends their total budget
    i.e. with fake budgets, cannot truly decentralize the auction

## Slide 22: Casual users, non-bidders?
What fraction of b/w to auction per link?
  If offer 100%, can sell it all => excludes casual users
  If offer (e.g.) only 80%, casual users can fit into the other 20%
  But then: how can someone who wants 100% get it if nobody else is using it, but they’re only granted 80%?
  Soft-guaranteed b/w may help: allow giving more if no competition, less if competition arises from new users
    Can trigger a new auction if conditions change too much
    Casual users who use too much should ask for a budget

## Slide 23: Conclusion: principles
Bandwidth-allocation at LHCONE requires a mechanism which is fair, efficient, lightweight, responsive and automatic
The Progressive Second-Price auction offers this
  Users negotiate among themselves how much bandwidth they should get
    Repeat auction as needed, follow fluctuations automatically
  Network providers get clear statement of what users want at any point in time
    No negotiations between experiments & network providers

## Slide 24: Conclusion: practicalities
Fake budget complicates things
  Budget must have ‘real value’ to the bidders
  Bidding strategies can interact with long-term budget management
  Need to understand how, to keep the auction useful (truthful)
Network topology/representation?
  How to cater for casual users vs. the desire to use all of link?
  How to respond to less than total demand?
Needs more work, nonetheless, PSP shows promise as a bandwidth allocation mechanism for LHCONE