## Slide 1: 11T Dipole – New Baseline HL-LHC Parameter and Layout Committee 2015-03-12
F. Savary on behalf of the WP11 team
Input from V. Baglin, D. Ramos

## Slide 2: Outline
Background information
New baseline
By-pass cryostat for collimator integration
Recent news

## Slide 3: Background information
Interconnect
Collimator
11 T dipole magnet
Connection cryostat
15660 mm
Create space in the dispersion suppressor regions of LHC, i.e. a room temperature beam vacuum sector, to install additional collimators (TCLD), which are needed to cope with beam intensities that are larger than nominal, such as in the High Luminosity LHC (HL LHC)
Replace a standard MB by a pair of 11T dipoles (a pair of MBH’s)
Produce an integrated field of 119 Tm at 11.85 kA

## Slide 4: Two phases
Courtesy L. Rossi
TODAY
Graph showing nominal upgrade parameters - 3000 fb-1 would be reached in 2036
IP2: 2 cryo-assemblies for installation
1 spare assembly
IP7: 4 cryo-assemblies for inst.n
IP1-5: 4 cryo-assemblies
2 spare assemblies
1 spare assembly
New baseline

## Slide 5: Scope in numbers
 | Phase 1 - LS2 [all RRP] | Phase 2 – LS3 | Remark
Models | 4 single aperture / 1-in-1 2 double aperture / 2-in-1 | PIT (new X-section): 4 single aperture / 1-in-1 2 double aperture / 2-in-1 RRP (new X-section): 2 single aperture / 1-in-1 1 double aperture / 2-in-1 | New X-section is necessary for PIT conductor (suffering from excessive degradation when the current keystone angle is used)
Prototypes | P1: MBH_P001 | P2: MBH_P002 [PIT] P3: MBH_P003 [RRP] | 1 prototype cryostat
Series baseline | IP2 2 x (2 MBH__ + 1 BPC*) | IP7 4 x (2 MBH__ + 1 BPC) | 
Series spares | 1 x (2 MBH__ + 1 BPC) | 1 x (2 MBH__ + 1 BPC) | 
Option | - | IP1-IP5 Max. 8 x (2 MBH__ + 1 BPC) | Exact number and installation time t.b.d. later
*BPC stands for by-pass cryostat

## Slide 6: By-pass cryostat for collimator integration
Collimator support jacks
Cryostat support jacks
Cold mass enlarged to Ø750 on the collimator side
Constant LHC arc outer flange diameter: Ø1055
Flexible interconnects for alignment independency and thermal contraction
Interconnects use standard components and tooling despite the new compact layout
  Busbar routing is in the shadow of the beam screens and CWT!
Courtesy D. Ramos

## Slide 7: Beam vac. & Collimator length (1)
600 mm Collimator
Warm drift vacuum chamber
Transitions needed to allow installation of sector valves
Very tight integration
Courtesy D. Ramos

## Slide 8: Beam vac. & Collimator length (2)
Interconnects become longer because of the beam screens
Very compact cold line because of the sector valve RF shielding
Transitions avoided because there is no sector valve on the other beam line
Cold drift vacuum chamber – Preferred
650 mm Collimator
Courtesy D. Ramos
600 mm Collimator
Following the 51st Collimation Upgrade Specification Meeting held on Jan. 30, 2015
ColUSM #51
Work to make a mock-up
by-pass cryostat has started

## Slide 9: Recent news on the models @ CERN
Model # | Coil # | Status / plan
MBHSM101 | 101-105 | Tested [coil 101 made of copper]
MBHSP101 | 106-107 | Tested
MBHSP102 | 106-108 | Coils available, test in April/May 2015
MBHSP103 | 109-111 | Coils in production, test in June/July 2015
MBHDP101 | SP102-SP103 | Assembly to start in Sept. 2015, Test in Nov. 2015
MBHSP104 | 112-113 | Coil production to start in April/May 2015
MBHSP105 | 114-115 | 
MBHDP102 | SP104-SP105 | 
MBHSP106 | 202-203 | Coil production to start in second half of 2015
MBHSP107 | 204-205 | 
MBHDP103 | SP106-SP107 | 
RRP
PIT
Not an end here!
Collaring imminent

## Slide 10: Tooling for full-length MBH @ CERN
Start winding first low grade sc cable in the middle of April 15

## Slide 11: And on the side of FERMILAB
MBHSP03:
Bmax = 11.7 T at 1.9 K
97.5% of Bdesign = 12 T
no holding quenches
First two-in-one MBHDP01:
Bmax = 11.5 T at 1.9 K
after 36 quenches
Target current in LHC

## Slide 12: Thank you for your attention