## Slide 1: Calibration over more than one run
Marian Ivanov, Kai Schweda

## Slide 2: Use case: spatial distortions at high IR
Charging up of inner field cage observed on C - side
Depends on interaction rate x primary ionisation (Ar ≈ 2.0 x Ne)
Spatial distortions, i.e. Δrφ at vertex could reach 5mm in run 2
 Time dependent ! Clear structures within fill
Need time-dependent space point calibration, per fill
Use external detectors, i.e. ITS, TRD, TOF, for calibration
Fill starts
Fill ends

## Slide 3: Calibration per LHC fill
Cpass1 starts right after cpass0 finished for a run
(A) make cpass1 output for all runs of an LHC fill available
1 run might last as long as 1 LHC fill (up to 24h)
run1: 1 calibration object created per time interval, e.g. drift velocity each 15 min
(B) Issue: memory consumption  convert cluster-to-track residual histograms to distortion maps (each 30 min)
Model + fit to calibration output over 1 LHC fill  continuous space point correction
cpass0
cpass0
cpass0
cpass0
cpass0
cpass1
cpass1
cpass1
cpass1
cpass1
calls detector specific algorithm, interpolation, modeling, fit …

## Slide 4: Proposal
Goal: automated scheme for calibration
Lego train: manual intervention
Minimize usage of resources: (A) filling of cluster-residuals histos or trees in cpass1, O(104) jobs (B) creation of distortion maps O(101) jobs Run on grid (alien jobs) alternatively / interim solution as cron jobs at GSI

## Slide 5: Action items
In advance to data taking: ITS, TRD, TOF alignment with sufficient precision (interpolation error inside TPC < 200 mm, intrinsic tracklet resolution)
ITS-TRD-TOF interpolation method, available as macro, needs to be ported to TPCcalibration class
Define minimum granularity of residual histos, decide whether to use histos or trees depending on memory consumption vs CPU time

## Slide 6: Action items, cont’ed
Fit distortion maps with physics model to confirm understanding
distortion maps + linear interpolation in time for ultimate precision
Statistics required for 0.1mm target resolution: 180 bins in f x 10 bins in q x (3.5mm/0.2mm)2  5 x 105 tracks, 1 x 104 pp collisions @50 Hz  each 2000 s ≈ 30 min (for ITS-TOF)  TRD needs 4x less statistics, 8 min