## Slide 1
Tracking at the
Fermilab Test Beam Facility
Matthew Jones, Lorenzo Uplegger
April 29th 2015

## Slide 2
Fermilab Test Beam Facility (FTBF)
Beam

## Slide 3
Main Injector accelerates protons to 120 GeV
  Accelerating RF frequency: 53 MHz
  Ring circumference: 11.13 μs
Resonant extraction into electrostatic and magnetic septa
1.6 μs of one beam revolution is shaved off and split between MTest facility and SeaQuest experiment
Up to 800k protons per spill to test area over 4.2 seconds
Repeated every 60 seconds
Secondary beams including kaons, pions, electrons and muons
  Energies of 1-60 GeV possible (3% resolution)
Fermilab Test Beam Facility overview

## Slide 4
Availability

## Slide 5
Tracking systems at MTEST
At present 2 tracking telescopes are installed:
  The legacy pixel telescope built using leftover CMS modules
  The new strip based telescope
Pixel Telescope
Strip telescope

## Slide 6
Leftover modules from the FPIX production
PSI46 analog readout chip (ROC)
100x150 μm2 pixel pitch
Modules with 8 (2x4) or 6(2x3) ROCs

## Slide 7
Schematic view of the pixel telescope planes
8 modules tilted at 25o to
maximize charge sharing
Coverage area only 1.6x1.6 cm2
Resolution on the DUT of ~7um

## Slide 8
Silicon strip telescope station
The Silicon strip telescope has a coverage of ~3.8 x 3.8 cm2 which is almost 6 times than the current pixel telescope coverage.
Improved resolution with a 30 μm strip pitch
Minimal material in the path of the beam, using covers made of carbon fiber sheets
The software, firmware, hardware and DAQ have been developed in a very productive collaboration between Purdue University and Fermilab
20 stations have already been built but only 14 are currently installed
The 3.8x3.8 cm2
overlap area
Extra holes to allow a different mounting configuration for a total coverage of 7x7 cm2

## Slide 9
Sensor assembly

## Slide 10
0.25 μm CMOS process
128 analog inputs
8 programmable 8-bit thresholds
Independent BCO and readout clocks
Readout clock runs at up to 100 MHz
DDR serial output on 1,2,4,6 LVDS pairs
Data driven– no external trigger required
Data tagged with 8-bit bunch counter
“Fast-OR” trigger output
Originally developed for BTeV and gently given to us by Valerio Re of University of Bergamo
FSSR2 Readout Chip

## Slide 11
320 μm thick
639 strips
30 μm strip pitch
60 μm readout pitch
Sensitive area: 3.8 x 9.8 cm2
Fully depleted at ~100 V
Coverage area is then 3.8 x 3.8 cm2
Expected resolution on DUT ~3μm
Originally produced for DØ Run IIb upgrade
DØ Run IIb strip sensor

## Slide 12
The CAPTAN Data Acquisition board
DAQ based on the CAPTAN (Compact and Programmable daTa Acquisition Node) designed few years ago at Fermilab
Simple FPGA board with an Ethernet link

## Slide 13
The readout system

## Slide 14
The software is based on XDAQ which is the framework used by CMS and is basically a web server that allow to build a web based Graphical User Interface.
The Data Quality Monitor is also a XDAQ application based on WebGL and ROOTJS
The Data Acquisition software

## Slide 15
Silicon strip preliminary results
Pixel telescope
Strip telescope
We had to modify the alignment software (designed with pixels in mind) to accommodate the strip detectors
Already with this not optimal alignment we have a resolution at the center of the telescope of ~4 μm (to compare with 7 μm of the pixel telescope)

## Slide 16
Synchronizing a data driven ROC with a trigger
The FSSR2 transmits all data that are above threshold
Data are internally time-stamped in the chip with a running 8 bit counter called BCO
In order to correlate these data with a trigger, another counter, synchronous with the BCO counter of the FSSR, has been implemented in the CAPTAN FPGA. This counter is used to extend to 48 bits the native FSSR 8 bits counter but also to time-stamp the trigger coming from the scintillators.
Since the trigger is always registered in the FPGA with a fixed delay, then we can correlate the particle arrival and FSSR BCO with the constant delayed trigger counter latched in the FPGA.

## Slide 17
FSSR Data driven
PSI46 Triggered
Scintillator
FPGA
COUNTER 0
FPGA
COUNTER 0
TIME 0
BUILDER
TRIGGER – FSSR BCO
ALWAYS 4
FSSR DATA
BCO 1
PSI46 DATA
TRIGGER 1
TIME 1
FPGA
COUNTER 1
FPGA
COUNTER 1
Synchronizing a data driven ROC with a trigger

## Slide 18
FSSR Data driven
PSI46 Triggered
Scintillator
FSSR DATA
BCO 1
FPGA
COUNTER 2
FPGA
COUNTER 2
TIME 2
PSI46 DATA
TRIGGER 1
BUILDER
Synchronizing a data driven ROC with a trigger

## Slide 19
FSSR Data driven
PSI46 Triggered
Scintillator
FPGA
COUNTER 3
FPGA
COUNTER 3
TIME 3
PSI46 DATA
TRIGGER 1
BUILDER
FSSR DATA
BCO 1
Synchronizing a data driven ROC with a trigger

## Slide 20
FSSR Data driven
PSI46 Triggered
Scintillator
FPGA
COUNTER 4
FPGA
COUNTER 4
TIME 4
PSI46 DATA
TRIGGER 1
BUILDER
FSSR DATA
BCO 1
Synchronizing a data driven ROC with a trigger

## Slide 21
FSSR Data driven
PSI46 Triggered
Scintillator
FPGA
COUNTER 5
FPGA
COUNTER 5
TIME 5
PSI46 DATA
TRIGGER 1
BUILDER
FSSR DATA
BCO 1
Synchronizing a data driven ROC with a trigger

## Slide 22
FSSR Data driven
PSI46 Triggered
Scintillator
FPGA
COUNTER 5
FPGA
COUNTER 5
TIME 5
PSI46 DATA
BUILDER
TRIGGER 1 DATA
BCO 5
FSSR DATA
BCO 1
Synchronizing a data driven ROC with a trigger

## Slide 23
FSSR Data driven
PSI46 Triggered
Scintillator
FPGA
COUNTER 6
FPGA
COUNTER 6
TIME 6
PSI46 DATA
TRIGGER 1
BUILDER
TRIGGER 1 DATA
BCO 5
TRIGGER – FSSR BCO
ALWAYS 4
FSSR DATA
BCO 1
Synchronizing a data driven ROC with a trigger

## Slide 24
FSSR Data driven
PSI46 Triggered
Scintillator
FPGA
COUNTER 7
FPGA
COUNTER 7
TIME 7
BUILDER
TRIGGER 1 DATA
BCO 5
TRIGGER – FSSR BCO
ALWAYS 4
PSI46 DATA
TRIGGER 1
FSSR DATA
BCO 1
Synchronizing a data driven ROC with a trigger

## Slide 25
FSSR Data driven
PSI46 Triggered
Scintillator
FPGA
COUNTER 8
FPGA
COUNTER 8
TIME 8
BUILDER
TRIGGER 1 DATA
BCO 5
TRIGGER – FSSR BCO
ALWAYS 4
PSI46 DATA
TRIGGER 1
FSSR DATA
BCO 1
Synchronizing a data driven ROC with a trigger

## Slide 26
Why a tracking telescope
In the next 10 years the LHC will increase the beam intensity by a factor of at least 10
A new generation of sensors will be necessary to sustain the much higher level of radiation
The most promising technologies are: thin silicon, 3D silicon and diamond

## Slide 27
Test results on 3D sensors
You can see the 7 μm electrodes with the telescope when the sensors are hit by the beam

## Slide 28
Efficiency for irradiated 3D sensors

## Slide 29
Cell charge for 3D sensors
Non irradiated 3D sensor
Irradiated 3D sensor
FBK_11_37_01 (1x1015 neq/cm2)

## Slide 30
The Fermilab Test Beam Facility provides different beams available for detector studies
http://ppd.fnal.gov/ftbf/
Two tracking systems are currently available but we are hoping to resolve the remaining issues and remove the pixel tracker
The telescopes are available for experimenters’ that need tracking information extrapolated on their devices
Test results on 3D sensors