## Slide 1
The High-Luminosity Upgrade
of the CMS Tracker
Duccio ABBANEO
CERN
Focusing on the Outer Tracker

## Slide 2
Requirements for the High-Luminosity Upgrade
The Outer Tracker
Silicon sensors
pT modules
Electronics system
  Front-End hybrids
  Powering
Optimization of the detector layout
Mechanical structures and cooling
Performance
The Pixel detector
Main challenges

## Slide 3
Requirements for the High-Luminosity Upgrade
(1) From the LHC
Radiation tolerance up to 3000 fb−1
Keep the possibility to repair the pixel detector: the inner parts could be replaced if needed
Operate up to 200 <PU>
Maintain occupancy at the ~1% level ® much higher granularity

## Slide 4
Requirements for the High-Luminosity Upgrade
(2) From CMS
DAQ compatible with higher L1 rate and longer latency
100 kHz ® 750 kHz
3.2 ms ® 12.8 ms
Contribution to the Level1 trigger decision
pT modules in the Outer Tracker

## Slide 5
Requirements for the High-Luminosity Upgrade
(3) Extra commodities
Extended tracking acceptance
Up to h~4 (concerns mostly the pixel detector)
Main purpose: assign jets to primary vertices in the forward region
Reduce material in the tracking volume
If we can, as much as we can
The tracker material is a major limitation to the overall performance of CMS today

## Slide 6
Radiation tolerance
Radiation levels depend essentially on R, not on z
  The target is 10× present tracker
  Challenging for silicon sensors and electronics (notably in the pixel region)
2S modules
3.5E+14
PS modules
9.3E+14
Pixel 1st layer
2.0E+16
Pixel 2nd layer
5.8E+15
Pixel 4th layer
1.6E+15
Pixel service cylinder
1.0E+15

## Slide 7
Sensors for Outer Tracker
After heavy irradiation (~1015) charge from 320 μm thick sensors drops down to the same level as 200 μm
  More trapping
  In 200 μm the leakage current is smaller, and can be operated at smaller Vbias: mitigate requirement on cooling!
In p-in-n sensors observed spurious signals (random non-gaussian noise, a.k.a. Random Ghost Hits)
`

## Slide 8
Understanding RGH
T-CAD simulations show higher electric fields at the strip edges for irradiated p-in-n sensors than for p-type sensors with same geometry
  Suggests the occurrence of “micro-discharges” in p-in-n
Increasing oxide charge…
  increases max. electric fields in p-in-n, reduces max. electric fields in n-in-p
  Observation: rate of RGHs are smaller for neutron than for proton irradiation
    less ionization, less surface damage
F=1x1015cm-2 ; QF = 1.2x1012cm-2; U = 500 V; 5-trap model (Silvaco)
n-in-p
p-in-n
strip doping
aluminum
p-in-n

## Slide 9
Annealing
All thin p-type samples work well and show seed signals >8ke- at 600V until about 20w@RT
Can be used to reduce the leakage current by keeping the detector at RT for 2 weeks each year, e.g. during YETS
MCz material shows significantly better behaviour after long annealing time

## Slide 10
Sensor thickness
200 μm active thickness provides sufficient charge
  With smaller charge loss after irradiation
Adding (inactive) silicon thickness increases the mass
With larger active thickness the leakage current is larger
  … and most likely Vbias would be larger, eventually
® additional material for thermal management
≈ 30 g
≈ 34 g
≈ 40 g
Example for 2S modules

## Slide 11
Outer Tracker sensors summary
Polarity
  n-in-p is the selected option, as it offers robust performance (i.e. graceful degradation) after heavy irradiation
Material
  MCz is the preferred option
    Allows for long annealing times with no adverse effects
    Could be (eventually) operated at lower Vbias, mitigating the requirements on the cooling
Thickness
  200 μm active and physical thickness is the preferred option
    Sufficient charge, good annealing behaviour, lower Idark and Vbias
  200 μm active 320 μm physical is a good backup
  We can build a Tracker with sensors of 300 μm active thickness, but that would have a visible impact on the mass

## Slide 12
Tracker input to Level-1 trigger
  μ, e and jet rates would substantially increase at high luminosity
    Even considering other trigger upgrades
  Increasing thresholds would affect physics performance
    Performance of algorithms degrades with increasing pile-up
      Muons: increased background rates from accidental coincidences
      Electrons/photons: reduced QCD rejection at fixed efficiency from isolation
  Even HLT without tracking seems marginal
  Add tracking information at Level-1
    Move part of HLT reconstruction into Level-1
Goal for “track trigger”:
  Reconstruct tracks above 2 GeV
  Identify the origin along the beam axis with 1÷2 mm precision
    Enables vertex discrimination

## Slide 13
General concept
Silicon modules provide at the same time “Level-1 data” (@ 40 MHZ), and “DAQ data” (upon Level-1 trigger)
  The whole tracker sends out data at each BX
Level-1 data require local rejection of low-pT tracks
  To reduce the data volume, and simplify track finding @ Level-1
  Threshold of ~ 2 GeV ⇒ data reduction of ~ one order of magnitude
Design modules with pT discrimination (“pT modules”)
  Correlate signals in two closely-spaced sensors
  Exploit the strong magnetic field of CMS
Level-1 “stubs” are processed in the back-end
  Form Level-1 tracks, pT above ~2 GeV
  To be used to improve different trigger channels

## Slide 14
Working principle of pT modules
Sensitivity to pT from measurement of Δ(Rφ) over a given ΔR
  For a given pT, Δ(Rφ) increases with R
  In the barrel, ΔR is given directly by the sensors spacing
  In the end-cap, it depends on the location of the detector (tgϑ)
    End-cap configuration typically requires wider spacing, and yields worse discrimination
Optimize selection window and/or sensors spacing
  To obtain, ideally, consistent pT selection through the tracking volume
The concept works down to a certain radius
  20÷25 cm with the CMS magnetic field and a realistic 100 μm pitch
R
φ
“stub”
pass
fail
x
y
z
1 ÷ 4 mm
≤ 100 μm
ΔR
Δz = ΔR / tg ϑ
z
R
B
®
.
ϑ
B
®
.

## Slide 15
pT modules
2 Strip sensors
2×1016 Strips: 5 cm × 90 μm
2×1016 Strips: 5 cm × 90 μm
P ~ 5 W
~ 90 cm2 active area
For R > 60 cm
Pixel + Strip sensors
2×960 Strips: 2.5 cm × 100 μm
32×960 Pixels: 1.5 mm × 100 μm
P ~ 7 W
~ 45 cm2 active area
For r > 20 cm
accurate z coordinate
coarse z coordinate
2S
PS
2S
PS

## Slide 16
Module design
Two types of modules combined with different sensors spacing
  2S modules with 1.8 mm and 4.0 mm
  PS modules with (provisionally) 1.6 mm, 2.6 mm and 4.0 mm
Cooling requirement
  Silicon sensors at −20°C or lower, with full power and radiation damage, for cooling set point of −30°C
    Ensures that modules can be operated (no thermal runaway)
    Design cooling system capable of −40°C (the margin is on the cooling plant)
    Low operating temperature mitigates requirement on thermal management
      Notably on 2S modules
Additional requirements
  Low mass, good mechanical precision and stability, little deformations in cold, simple and reproducible assembly, affordable
Module design driven by Finite Element Analysis of thermal performance
  Minimize differences between different types and versions

## Slide 17
1
8
1
2
3
4
5
6
7
9
10
11
4
2S silicon sensors
Al-CF spacer
Al-CF tab
CF support
Al-CF spacer
CF stiffener
Al-CF short spacer
Service Hybrid
FE Hybrid
CBC
CIC
Mounting points / cooling contacts
2S module
Five mounting/cooling points – peripheral cooling
  Concept similar to modules of the present tracker
Al-CF spacers provide good thermal conduction, and enable simple, high-precision assembly with ~ no CTE mismatch
Hybrids are laminated on the CF supports by the company

## Slide 18
11
12
9
1
2
3
4
5
8
PS-s silicon sensor
PS-p silicon sensor
MPAs
Al-CF sensor spacer
CFRP base plate
FE Hybrid
Opto-Link Hybrid
Power Hybrid
SSA
CIC
Hybrid CF support
Al-CF Hybrid spacer
6
7
10
11
11
11
12
PS module
Heat dissipation in the MPA requires large area cooling contact
Cooling through CF base plate, glued on a cold surface on the supporting mechanics
Module assembly starts from the base plate
  Additional spacer under the Opto-Link Hybrid, wire-bonded to the FE Hybrids

## Slide 19
Al-CF composite
Property |  | Al-CF V2-4 | Al
Density [g cm-3] |  | 2.4 | 2.7
Thermal conductivity [W m-1 K-1] | In plane | 230 | 237
 | Through plane | 120 | 
CTE [ppm K-1] | In plane | 4 | 23
 | Through plane | 24 | 
Aluminium with embedded carbon fibers, randomly oriented in a plane
Excellent combination of mechanical and thermal properties
Easy to machine
Breakthrough in the design of pT modules!

## Slide 20
m-Tx
m-Rx
DTC
CTRL
TTC
DAQ
LV/HV PS
CBC
DC/DC
LP-GBT
CIC
FE-Hybrid
R
VTRx+
CBC
CIC
Service-Hybrid
2S Module
LV
HV
FE BE
FE-Hybrid
L
L1 Tk-Finding
TRIG
FPGA
AM
Process &
Route
stubs
GBT
FPGA
Process &
Route
Electronics architecture shown for 2S modules
  8 CBCs / side, 130 CMOS, bump-bonded on the flex hybrids together with the passive components
    800 bumps @ 250 μm pitch
    127×2 channels, performs top-bottom correlations
  Sensors wire-bonded to high-density FE hybrid
  Wire bonds from FE Hybrid to Service Hybrid
  FE hybrid implements all line routing (data, control, power)
    Sensors ® CBCs, CBCs ® CIC, CIC ® GBT on Service hybrids
    Power from Service Hybrid to all chips

## Slide 21
LP-GBT
CIC R
CIC L
CBC
5b + 5b
@ 320 Mb/s
5b
TRIG
CBC
1b
DAQ
5b
TRIG
1b
DAQ
@ 320 Mb/s
each CBC
4b
TRIG
1b
DAQ
@ 320 Mb/s
@ 320 Mb/s
4b
TRIG
1b
DAQ
FE-Hybrid R
Service-Hybrid
FE-Hybrid L
@ 320 Mb/s
each CBC
Data flow (2S modules)
  The Concentrator IC combines data from 8 CBCs and for 8 consecutive BX
    “Block synchronous” system. Efficient use of bandwidth with fixed latency
Based on a conservative assumption of 3.2 Gb/s available bandwidth in the LP-GBT
Most likely the real value will be higher
E.g. 3.84 Gb/s or 4.48 Gb/s, depending on error correction scheme chosen (specs under discussion now)
Option to use the high-speed version (2 × bandwidth) at the cost of some extra power
® Can be useful in the first layer of PS modules

## Slide 22
N.B. L1 tracking acceptance is limited at h~2.4
DAQ data @ 750 kHZ
L1 data @ 40 MHz
The L1 data output is disabled for modules located at low angle in the End Caps
(pT discrimination insufficient to achieve reasonable bandwidth and stub purity)
DAQ data @ 750 kHz

## Slide 23
Two different chips: Macro-Pixel ASIC (MPA) and Short Strip ASIC (SSA). TSMC 65 nm.
  Correlation in the MPA
  2×8 MPA per module, ~2000 bumps / MPA, ~30,000 macro-pixels
  Connectivity and data formats as for 2S modules
Service Hybrid split in two boards (readout and power) since the module is ½ length
  Sensors ® CBCs, CBCs ® CIC, CIC ® GBT on Service hybrids
  Power from Service Hybrid to all chips
System fully efficient in layers 2-3
Limited by bandwidth in layer 1 for the stub data
  If <PU> = 200 is confirmed as design goal, the 10 Gb/s version of the LP-GBT will be needed!
FE electronics for PS modules

## Slide 24
The requirements for the FE ASICs are calculated taking into account the effect of sensor irradiation and the specific functionality of pT modules
Measured
in the beam
The case of charge sharing sets the requirement on S/N to achieve full efficiency
Efficiency
  We aim at delivering a detector with ~99% initial efficiency, all effects combined
    Module dead area, faulty channels/chips/modules, faulty electrical connections, broken fibers…
  ® Each individual source of inefficiency should be at the 1 ÷ few ‰ level
Noise
  pT < 2 GeV particles are 98% at R=60 cm
  Stub rate for combinations of low-pT hits with noise hits 10% of rate of good particles
  ® Stub misid probability of 0.2% (0.2% ´ 50 = 10%)
Full Geant4 simulation of an irradiated module @ 60 cm,
200 mm active thickness, Lorentz angle, Vbias = 600 V, reduced CCE

## Slide 25
Before irradiation
Operability º max(inefficiency,misid)
  Operability < 0.2% means
  Both inefficiency and misid < 0.2%
  ® good!

## Slide 26
Good working point:
Threshold 3700e-
With noise < 1060 e-
After irradiation
Requirement for the CBC set to:
noise < 1000 e-

## Slide 27
High density flex hybrids
25 mm double-sided polyimide core layer, plus two single-sided 12.5 mm polyimide layers on either side. 25 mm coverlay on the bottom, solder mask on the top. Total thickness ~130 mm.
2S hybrid. Wirebonding pitch to sensor 90 mm ´ 2 sensors. Bump bonding pitch of CBC 250 mm,
800 bumps ´ 8 chips. High-density routing: thinnest line 30 mm with spacing 33 mm.
Prototype with Flat Flexible Connector (CIC not yet available).
Eventually will be wire bonded to the Service Hybrid.

## Slide 28
Front-End powering with on-board DC-DC converters
upFEAST
2nd stage
opto
ASICs
12 V
2.5 V
1.2 V
upFEAST
2nd stage
opto
ASICs
12 V
2.5 V
1.2 V
2nd stage
ASICs
0.8 V
2S module
PS module
DC-DC inside
The module is a self-contained functional unit
Individually connected to the back end with power lines and optical fibers for readout and control
upFEAST improved version of existing FEAST
2nd stage to be designed - technology chosen TSMC 130 nm

## Slide 29
Optimization of the detector

## Slide 30
Detector standalone modelling: tkLayout
Flexible tool to create 3D models of the tracker from simple configuration files and user-defined rules
Includes both active surfaces and inactive materials
Optimization of the detector

## Slide 31
Detector standalone modelling: tkLayout
Simple (semi-automatic) modelling of services
Material of sensitive elements
Dedicated volumes for supports and services

## Slide 32
Detector standalone modelling: tkLayout
Simple (semi-automatic) modelling of services
Material of sensitive elements
Dedicated volumes for supports and services
Automatic routing of outgoing services

## Slide 33
Detector standalone modelling: tkLayout
Implements estimates of tracking performance

## Slide 34
Detector standalone modelling: tkLayout
Provides:
  Estimates of the tracking precision including multiple scattering
    For both offline tracking and L1 tracking
  All useful summaries/statistics
    # of modules, active surface, # of channels, total power, total weight, etc etc….
  Radiation length and interaction length vs rapidity
  Map of leakage current in all modules after irradiation
    Input from FLUKA – used to optimize module cooling
  Stub pT resolution for each module location
    Used to optimize distribution of sensor spacing in the Tracker volume
  … and more…
Outputs:
  Mini web-site with full information
  Geometry files for CMSSW
  Module coordinate files for the 3D modelling of the detector structures
  Geometry files for FLUKA

## Slide 35
Some infos from tkLayout

## Slide 36
Acceptance window
Width 5÷15 channels in the barrel, 2÷12 in the endcap.

## Slide 37
Beyond baseline?
Variant of TBPS with progressively tilted modules
Short central section followed by groups of rings with same tilt
Same coverage and ~same tracking performance with a smaller number of modules

## Slide 38
Beyond baseline?
Variant of BPS with progressively tilted modules
Short central section followed by groups of rings with same tilt
Same coverage and ~same tracking performance with a smaller number of modules

## Slide 39
Variant of BPS with progressively tilted modules
Short central section followed by groups of rings with same tilt
Same coverage and ~same tracking performance with a smaller number of modules
Also Known As:
“The Dinosaur”

## Slide 40
Is it really a good idea???
Many tracking detectors have been designed and built by smart people…
… and they don’t look like that!

## Slide 41
Stub Finding logic efficiency results
X
V
Module A
Module B
Vertex
Z
Recovered
Without an interconnect technology (ex: TSV) between the two sides of the module, tracks crossing the middle will not be identified as stubs
Clashes of hybrids

## Slide 42
Stub Finding logic efficiency results
Vertex
Z
-Z
In reality even this is not achievable!

## Slide 43
PS-pixel sensor
MPAs
MPAs
Al-CF spacer
Al-CF spacer
CFRP base plate
PS-strip sensor
SSA
Al-CF spacer
CF support
flexible hybrid
CF support
SSA
Al-CF spacer
CF support
CF support
flexible hybrid
PS-pixel sensor
MPAs
MPAs
Al-CF spacer
Al-CF spacer
CFRP base plate
PS-strip sensor
SSA
Al-CF spacer
CF support
flexible hybrid
CF support
SSA
Al-CF spacer
CF support
CF support
flexible hybrid
Through-Silicon Vias would be required to achieve acceptable efficiency in the “flat” layout

## Slide 44
Stub Finding logic efficiency results
V
V
Module A
Vertex
Z
V
The tilted layout solves the problem (with a smaller the number of modules!)

## Slide 45
Three specific facts favour the tilted layout
Stub finding efficiency
Avoids needs of TSVs to interconnect the two halves of a PS modules
Avoids huge overlaps between consecutive modules in z
  Impossible to implement at the edge of the barrel anyway
Module length
(3) Modules only 5 cm long in the z direction because of technology limitations
Aggravates effects (1) and (2), but makes tilt possible!

## Slide 46
Tilted TBPS - performance
Less material, equal or better tracking performance, better stub coverage, no need of TSVs
Less modules, cost saving
  1200 modules, 10 m2 of silicon
Slightly degraded z0 resolution for L1 tracks
TBPS material
TK material
Flat
Tilted
Flat
Tilted
 1 GeV
 10 GeV
 100 GeV
pT resolution

## Slide 47
Mechanics
TB2S
TBPS
TEDD

## Slide 48
TBPS: How to construct the tilted geometry?
The current idea is to divide the assembly into following sub-structures:
Three layers as individual units
Each layer: Central flat section + 2 tilted sections
Central section: 2 end rings and module support plates
Tilted sections: module support rings
Longitudinal profiles join the sections and provide for services routing paths.
0.8 - 1 m
0.4 – 0.8 m
0.8 - 1 m
0.4 – 1.1 m

## Slide 49
Central flat section
4-6 mm thick module support & cooling plate
Space frame made of end rings
~0.5 mm high-conductivity carbon-fibre composite skins
Foam core
Diam ~2 mm cooling pipe, U-loop
Carbon foam or aluminium/carbon-fibre block next to cooling pipe
and longitudinal profiles
Modules attached with phase-change adhesive
Geometrically simple building blocks
Main challenges:
Precise and light plates with integrated cooling
Thermal and mechanical connections

## Slide 50
Modules supported by Rings
Rings joined by longitudinal bars.
Cooling supply pipes, wires and fibres routed along the bars.

## Slide 51
The Ring concept
Flat disk with cooling pipes and module supports on each side.

## Slide 52
The Ring
~5 mm thick sandwich structure with carbon-fibre composite skins and foam core
Cooling pipes on front and back side, with thermal contact pads in Al-CF composite
Module support / thermal contact plates in high thermal conductivity carbon-fibre composite
Ears for joining the Ring to the other Rings of the Layer
Inserts for module positioning

## Slide 53
Cooling
(… looks OK, but does the cooling actually work? … in progress….)

## Slide 54
Ring with modules

## Slide 55
Joining layers
2nd layer
3rd layer

## Slide 56
Additional rings for joining layers together

## Slide 58
TB2S
TB2S
TBPS
TEDD
Z overlap within one “ladder”
f overlap between consecutive ladders

## Slide 59
Two overlapping ladders
Full barrel length of L ~ 2.3 m
Ladder
L ~ 1.15 m

## Slide 62
Tracker End-Cap Double Disks (TEDD)
Modules mounted on four surfaces on two disks, each made of two dees
  φ overlap within disk, R overlap with next disk
Same rectangular modules as in the barrels
9 rings of PS modules + 6 rings of 2S modules
Cooling pipes embedded in the disk structure, wires and fibers running above and between the modules

## Slide 66
TEDD: sector-wise cooling loops
PS modules: C-foam pads
2S modules:
5 Al* inserts
*or Al-CF

## Slide 69
Overview of the system parts
Detector cooling
Cooling plant
Manifold
Main pipework
Detector transfer lines
Detector distribution
manifold
Detector
& on board
cooling loops
Connected to a commercial chiller

## Slide 70
Heat Transfer Coefficient higher than for liquid cooling
Limited temperature excursion on the detector
(isothermal evaporation – cooling exploits latent heat)
Chosen cooling technology: two-phase CO2
Advantages of evaporative cooling
Large latent heat of evaporation
Low liquid viscosity
Particularly high heat transfer coefficient
Very convenient fluid to work with (environmental friendly, not activated)
Convenient range of operating temperature −45°C to +25°C
Easier at low temperature
Advantages of CO2

## Slide 71
The 2PACL process
Capillaries
Ideal lines with no pressure drop

## Slide 72
In practice a quite complex system…
Detector loops must be properly sized (avoid dry out)
Flow distribution must be stable wrt to load changes
In reality there is pressure drop along the detector loops
Requires some pre-heating to ensure that the CO2 boils!
Higher operating temperature ® higher pressure rating
Electronics
Detector Inlet
Detector
Detector Outlet
Just started reflection on system parameters
Evaporation temperature −30° C, with operational margin to −40° C
Total power ~80 kW, about 50 cooling lines splitting to ~600 detector loops
On-detector pipes typically 2.0/2.2 mm (maybe larger in TEDD)
Realistic case: Pixel “phase-1”

## Slide 73
Some performance plots

## Slide 74
Stub finding performance
Muon stub finding efficiency in all layers (barrel, endcap)
Barrel layer 1 for muons, pion electrons
  Effect of interactions
Efficiency measured on DESY beam with 2-CBC2 module prototype
pT simulated with module tilt
Selected threshold equivalent to a nominal pT cut of 2.14 GeV @ 75 cm
Fit to data gives effective threshold of 2.2 ± 0.1 GeV

## Slide 75
Level-1 track finding
Track finding performance taken from “tracklet” method
  Estimates with AM track finding qualitatively similar
  N.B. Track finding not demonstrated in hardware
    Indication of the performance that could be achievable

## Slide 76
Offline tracking
Compare Phase-1 @ 50 PU with Phase-2 @ 140 PU

## Slide 77
Radiation tolerance is a major worry, not only for sensors but also electronics!
Huge ongoing effort in RD53 to qualify TSMC 65 nm technology
R&D on thin n-in-p planar sensors, 3D sensors
Rapidity extension
Main requirement is to match jets to vertices in the forward region
(Anything else is a bonus)
Recall: operate at 200 PU x 750 kHz
Maintain/improve single hit resolution and two-track separation
Rad tolerance requirements implies thinner sensors, less charge (100 ÷ 150 mm active thickness).
Achieve hit resolution with less charge sharing and smaller pixels.
Rectangular pixels give lower occupancy and mitigate requirement on pixel chip threshold
(around 1000 e-, under study)
The phase-2 pixel upgrade

## Slide 78
Service cylinders
200 PU x 750 kHz ® x 30 increased bandwidth wrt to phase-1
Huge increase of the cross section of electrical links
Optical converters can be integrated on the service cylinders
No option for module-level optical conversion…?
The service cylinders are completely inside the tracking volume

## Slide 79
Service cylinders
Even worse: higher power, with lower operating voltage
On-chip DC-DC conversion seems hard
And a factor of 2 would not be good enough
Inductor-based converters are bulky
Not suitable to be integrated on modules, away from modules don’t help much
Started to reconsider serial powering…!
The service cylinders are completely inside the tracking volume

## Slide 80
DC-DC conversion vs serial powering: the basics
ΔV
I×N
Parallel powering
No conversion
ΔV×R
(I×N)/R
Parallel powering
DC-DC converter
with ratio R
ΔV×N
I
Serial powering
Same current flows through all the loads in the chain
Each load works at a different potential!
DC-DC converter
Voltage regulator

## Slide 81
Service cylinders
In summary: a lot of interesting problems to solve!

## Slide 82
Questions?