## Slide 1: Initial thoughts on “PicoTDC”: Data framing Readout Architecture Data buffers and SEU Time offsets/parameters Configuration Monitoring Test
Jorgen Christiansen, PH-ESE

## Slide 2: Time measurement
Full time measurement:
  Course count (40MHz): 12 (cover LHC machine cycle)
  Fine count (2.56GHz): 6
  DLL interpolation: 5
  Resistive interpolation: 2
  Total TDC: 25
Edge lead/trail: 1
Channel ID: 4, 4 readout ports with 16 channels 6, 1 Readout port with 64 channels 5, 1 readout port with 32 channels
Data type field (minimum): 1
Total: 31bits - 33bits
Data packet: 32bits !
Channel (4-6)
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
Res int (2)
Edge (1)
Type (1)
31 - 33 bits

## Slide 3: 4 readout ports, 16 channels 1 readout port, 32 channels
16/32 channel mode: DEFAULT FORMAT
Channel (4+1)
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
Res int (2)
Edge (1)
Type (1)

## Slide 4: 1 readout port, 64 channels
(No type identifier: Exception , separate signal required to mark valid data ! )
No edge bit: If only measuring leading or trailing
No resistive interpolation:
Channel (6)
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
Res int (2)
Edge (1)
Channel (6)
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
Res int (2)
Type (1)
Channel (6)
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
0
Edge (1)
Type (1)
DEFAULT: One course count bit less:
Channel (6)
Coarse cnt (11)
Fine cnt (6)
DLL int (5)
Res int (2)
Edge (1)
Type (1)
POSSIBLE OPTIONS: To be define which ones to implement

## Slide 5: Leading + TOT
Packet Type: 1bit
Channel ID: 4 - 6 bits
Leading: >16 bits
  Large dynamic range
    16bit 3ps resolution: 200ns
    19bit 3ps resolution: 1600ns
  Programmable part of full 25bits leading TDC
  (Relative to trigger to be useable)
TOT (Relative to leading): >8 bits
  Short dynamic range:
    8bit 3ps resolution: 780ps
    11bit 3ps resolution: 6.1ns
  Programmable part of full 25bits TOT difference
    TOT assumed to be used for offline time-walk correction of leading.
Alternative: Readout of Individual Leading and Trailing edges with full range/resolution
  2x readout bandwidth
Channel (6)
Leading (16)
TOT(9)
Type (1)
1 readout port, 64/32 channels
Channel (4)
Leading (16)
TOT(11)
Type (1)
4 readout ports, 16 channels
Channel (4)
Leading (19)
TOT(8)
Type (1)

## Slide 6: Relative to trigger
Single edge with full/reduced coarse count
Leading + TOT with prog. Resolution
Channel (6)
Coarse cnt (11)
Fine cnt (6)
DLL int (5)
Res int (2)
Edge (1)
Type (1)
A: Triggered with relative time and reduced coarse count: Same as absolute
Channel (6)
Leading (16)
TOT(9)
Type (1)
B: Triggered with relative leading and TOT: Same as absolute Lead. + TOT
Channel (5)
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
Res int (2)
Edge (1)
Type (1)
Channel (4)
Leading (16)
TOT(11)
Type (1)
Channel (4)
Leading (19)
TOT(8)
Type (1)
1 readout port, 64 channels
4 readout ports, 16 channels or 1 readout port, 32 channels
4 readout ports, 16 channels
1 readout port, 64/32 channels

## Slide 7: Framing
Triggered
  Event header per trigger
  TDC measurements (relative to trigger)
    Single edge
    Leading + TOT
  (Errors, per event)
  (Debugging, per event)
  Event trailer
  Idle/no data
Non triggered
  TDC measurements (absolute)
    Single edge
    Leading + TOT
  (Errors, when they occur)
  (Debugging, when ?)
  (Counter overflow)
  Idle/no data

## Slide 8: Data frames
Header: Triggered
  Type: 1000
  Event ID: 12bit
  Bunch ID: 12 bit
Trailer: Triggered
  Type: 1001
  Event ID: 12 bit
  Status/error flags: 8bits
    Buffer overflows encountered.
    ?
  Number of hits or Check sum: 8bits
Errors: Triggered or non triggered (can be enabled/disabled)
  Type: 1010
  Status word with bit signalling what error
    Buffer overflows
    Hit error (time decoding)
    PLL loss of lock
    DLL loss of Lock
    SEU detect
    ?
  Error flags reset after having sent error status
  (error flags can also be read and reset via control/monitoring interface)
Monitoring/debugging: Triggered (can be enabled/disabled)
  Type: 1011
  Buffer occupancy: 64 L1 buffers * 8bit + 8 Readout FIFOs * 8 bit = 576bits !
  (can also be read via control/monitoring interface)
Counter overflow
  Type: 1100
TDC measurements:
  Type: 0xxx (xxx part of channel ID)

## Slide 9: 32bit frames
Event ID (12)
Type (4)=1000
Bx ID (12)
Div(4)
Event header
Event ID (12)
Type (4)=1001
#Hits/check (8)
Flags(8)
Event trailer
Type (4)=1010
Error/status flags, TBC (28)
Errors/status
Type (4)=1011
Monitoring data, TBC (20)
Monitoring data, possibly with sub-types to read out all buffer occupancies
Type (4)=1100
TBC (28)
Coarse count overflow
TDC data (31)
Type (1)=0
TDC measurement
Type (4)=1111
Undefined
Idle/null (When using 8B/10B this is part of coding)
Sub-Type (8)

## Slide 10: Encoding
Byte lane using max 10 signals + clk. Encoding not required. Two options
  Data-valid strobe(s)
    Data valid
    First byte in 32bit frame
  8B/10B:
    Frames
    Idle
    Data lines NOT guaranteed to be DC balanced.
  Who drives Byte lane clock (40, 80, 160, 320M): TDC or GBT ?
    Normally GBT. Then we need to synchronize within the TDC
    TDC clock derived from ref clock normally coming from GBT
Serial: Encoding required
  DC balancing
  Embedded clock
  Byte, Frame alignment
  Idle
  8B/10B:
  25% overhead
  64B/66B encoding ?
  2 bit preamble
  64bit scrambled data
  3% overhead
  We have 32B frames and no 32B/34B coding exists

## Slide 11: Block diagram

## Slide 12: IO and Pins
Differential SLVS (LVDS on inputs)
Hits: 128
Clk: 2
Trigger, resets: 6
Readout: 80
Control: 6
  E-link: clk, Din, Dout
  (I2C ? ) Single ended, Voltage
Div test: 8
Power, GND: 40
  PLL: 4
  TDC: 8
  I/O 16
  Core: 8
Total: ~270 (17 x 17 FPBGA)

## Slide 13: Internal buffering
TDC time: 25bits
Edge: 1 bit
Channel ID:
  Latency buffer: 0bits, buffer per channel
  Readout FIFO: 4 Bits, buffer per 16 channels
Max TOT: 11bits
SEU detect: 1bit parity or Hamming
  Hamming for 32bit data: 6bit = 38bits
  Hamming for 26bits data: 5 bit = 31bits
  Extra parity bit to detect double errors (but not correct), (fits well for 26 bit data)
Latency buffer: Basic TDC measurements
  Full TDC time + edge
  Full Leading + TOT (or split across two words)
  SEU detect/(correct)
    SEU errors can seriously confuse trigger matching as hits may look like being out of time order
Readout FIFO: Data as it will be sent out on readout port
  Full TDC time + edge
  Required Leading + TOT
  Event separator: Header, (Trailer)
  Other: (error flags), (Monitoring)
  Final readout formatting can be done before or after readout FIFO, or as a combination
  SEU detect/(correct)
    SEU errors can corrupt/disturb readout data but not the TDC chip itself
Buffers: 32 bit wide or larger if required
  Latency buffer: 32 bit OK with 5+1 bit hamming if leading and trailing as separate words
  Readout FIFO: 32bit with 1 bit parity or 38/39 with hamming

## Slide 14: Latency buffer
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
Res int (2)
Edge (1)
Required TDC data:
Max_TOT(11)
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
Res int (2)
Edge (1)
SEU (5+1)
Full TDC data in 32bit with 5+1bit hamming (single bit correct and double bit detect)
26bits
11bits
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
Res int (2)
Max_TOT(11)
36bits
Full Leading + max TOT: 36bits
32bits
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
Res int (2)
Max_TOT(11)
43bits
SEU (6+1)
Full Leading + max TOT + 6+1bit Hamming: 43bits
Leading + TOT requires two consecutive memory locations
Not interesting to protect only coarse count (requires 5+1bit hamming code)

## Slide 15: Readout FIFO
Full TDC: 16/32 channel mode: DEFAULT READOUT FORMAT
Channel (5)
Coarse cnt (12)
Fine cnt (6)
DLL int (5)
Res int (2)
Edge (1)
Type (1)
Only 4 bit channel ID needed within channel group of 16
Room for 1 parity bit
Channel (4)
Leading (16)
TOT(11)
Type (1)
Leading + TOT: 4 readout ports, 16 channels
Channel (4)
Leading (19)
TOT(8)
Type (1)
No Spare bit for Parity
Full 6+1 bit Hamming on 32bit data: 39 bits
32bit readout data (32)
39bits
SEU (6+1)
Parity on 32bit data: 33 bits
32bit readout data (32)
33bits
Parity(1)

## Slide 16: SEU protection
Configuration data:
  TMR (or on purpose NOT as not to be classified rad hard)
  Parity, simple SEU detect
State machines, counters:
  TMR (or on purpose NOT as not to be classified rad hard)
  One-hot with error detect and self reset, Simple SEU detect as in HPTDC
Data memories
  Latency buffer:
    Full Hamming
    Hamming on course count (used for Trigger matching)
    Parity
  Readout FIFO:
    Hamming
    Parity
    None
Hit registers:
  Fine time: No SEU protection but data verification as possible (bubbles)
  Course, Fine count: Parity to the extent possible
Data pipeline registers:
  Parity
PLL: To extent possible (e.g. phase detector)
DLL: Not needed
Must not be classified as 100% rad hard !

## Slide 17: Time offsets/parameters
Coarse count offset: 12 bit
  Loaded with external BX-reset signal
  Not required every machine cycle as chip programmed to know LHC machine cycle.
Machine cycle period: 12 bit (Only support for LHC period)
  Must be taken into account:
    Coarse counter to zero
    Trigger counter to zero
    Channel offset
    TOT
    Comparison to trigger
    Relative to trigger
Per channel offset: 16 bit
Trigger latency: 12bit
Other ?

## Slide 18: Configuration
Interface: E-port and/or I2C
  E-port: Get E-port IP block (Sandro/Kostas)
  (I2C: Get I2C block (Ken ?). Problem with IO and voltage levels)
Configuration bits
  PLL: 16
  DLL: 16
  Global clocking: 16
  Channel enable: 64
  Leading/trailing/both: 2
  Channel dead time: 8
  Coarse count offset: 12
  Machine cycle: 12
  Trigger latency: 12
  Reject latency: 12
  Trigger window: 12
  Channel offsets: 16 x 64 = 1024
  Data formatting: 32
  Readout: 32
  Test selects: 32
  Total: ~1300
Must be possible to reload and read config while running.
TMR or Parity

## Slide 19: Monitoring
PLL status
DLL status
Div. status/error flags
SEU counts
Triggers
Buffer occupancies
Slow readout via control/monitoring path ?.
?

## Slide 20: Test features
Access to raw data/inject specific hits ?
Scan path ?
Boundary scan path ?
BIST of memories ?
DLL ?
PLL ?
Other ?

## Slide 21
Channel buffer: 1k
Counters
TDC channel
2.56GHz
320MHz
160MHz
80MHz
40MHz
40MHz
Ext ref.
2.56GHz
x16
Readout buffer: 1k
1/8/10bit 40,80,160,320M
Serial 2.56G
x10
40MHz
PD
Res. int.
40,80,160,320MHz
x10
x10
Channel buffer: 1k
TDC channel
x16
Readout buffer: 1k
1/8/10bit 40,80,160,320M
Serial 2.56G
x10
Trigger matching
Trigger matching
PLL
Trigger buffer 1k
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
D
Interpolation decoder
Hit register
x16
x16
x16
x16
Control,
Programming,
Monitoring
Hits
x64
Trigger,
Resets
E-port, (I2C)
Readout
1-40
Trigger interface