## Slide 1: WLCG Network and Transfer Metrics WG After One Year
Shawn McKee, Marian Babik
HEPiX Fall 2015 Meeting at BNL
13 October 2015

## Slide 2: Review of Working Group
After its first year, it is appropriate to review the WCLG Network and Transfer Metrics working group progress
Started in Fall 2014, it brings together network & transfer experts
  Follows up on the WLCG perfSONAR Task Force goals
Mandate
  Ensure all relevant network and transfer metrics are identified, collected and published
  Ensure sites and experiments can better understand and fix networking issues
  Enable use of network-aware tools to improve transfer efficiency and optimize experiment workflows
Membership
  WLCG perSONAR support unit (regional experts), WLCG experiments, FTS, Panda, PhEDEx, FAX, Network experts (ESNet, LHCOPN, LHCONE)
https://twiki.cern.ch/twiki/bin/view/LCG/NetworkTransferMetrics

## Slide 3: Overview of Work Areas
The working group has met on a monthly basis and made progress in a number of areas:
  Defining important use-cases
  Understanding slow transfers
  Providing a uniform way to define and access network metrics
  Integrating network metrics with the experiments
  Coordinating responses to network issues
  Baselining existing links; commissioning new links
We will cover these in the following slides

## Slide 4: Defining Important Use-Cases
The working group has assembled feedback about the use-cases foreseen for network and transfer metrics into a google document
  Participation from ATLAS, CMS and LHCb, and various middleware and application providers
  Details at https://docs.google.com/document/d/1OcggHH4DM6vhe1ydJteYazwc0WgOLcHU31H1X5vbq3I/edit and are summarized later in this presentation
We also have CHEP 2015 paper, detailing the working group, to be published soon. See abstract https://indico.cern.ch/event/304944/contribution/407.pdf
Notes: Link to the use case document https://docs.google.com/document/d/1OcggHH4DM6vhe1ydJteYazwc0WgOLcHU31H1X5vbq3I/edit
Details on particular use cases are shown later on in the presentation.
Summary of the WG was also presented at CHEP2015 with paper to be published soon

## Slide 5: Understanding Slow Transfers
Slow transfers can have many causes in complex end-to-end topologies
  Differentiating “network” issues from application, end-site and end-host issues can be difficult
A core task for the working group was perfSONAR deployment and commissioning to provide a source of network metrics to enable effective problem debugging
  245 active WLCG/OSG instances; 278 registered
  WG tracks issues in infrastructure and networks
  Supports problem debugging and resolution
Uses perfSONAR metrics to identify “network” causes for slow transfers; conversely can rule-out network issues where perfSONAR metrics show good networks.

## Slide 6: Providing Network Metrics
Working closely with the Open Science Grid (OSG) Network Area, the group has provided access to perfSONAR network metrics
  OSG Network Datastore is used to gather and store ALL WLCG/OSG perfSONAR metrics in a common API (Esmond).
  CERN hosts a Active Message Queue that OSG “publishes” all metrics to. End users can subscribe to any data they choose
The working has prototyped a proximity service to handle topology-related requests: closest perfSONAR server to storage element and vice-versa; closest perfSONAR to arbitrary end-host using GeoIP (eventually could use route data).
  Needs testing and further development but functional now:
  http://proximity.cern.ch/api/0.3/geoip/nearest?sonar=psum02.aglt2.org&count=10
  http://proximity.cern.ch/api/0.3/geoip/matrix?vo=atlas
Collaborating with ESnet on proximity service follow-on, an open-source configuration interface project and the deployment/debugging of perfSONAR toolkit.
Notes: You can also mention collaboration with ESNet (on e.g. open-source configuration interface project, possible proximity service follow up project, deployment/debugging cycles, etc.)
http://proximity.cern.ch/api/0.3/geoip/nearest?sonar=psum02.aglt2.org&count=10
http://proximity.cern.ch/api/0.3/geoip/matrix?vo=atlas

## Slide 7: Integrating Network Metrics
It is important to be able to utilize the network and transfer metrics we gather to support higher level services that rely upon the network
One example is the FTS study which used traceroute information from perfSONAR and FTS log details to analyze FTS performance versus various parameters (See later slides)
Ongoing pilot projects with ATLAS and LHCb providing pipelines of metrics for the experiments
  LHCb is processing perfSONAR stream and correlates it with the network and transfer metrics in DIRAC
  ATLAS processing perfSONAR data to create a network “cost-matrix” for use by PANDA with additional use cases in scheduled transfers and dynamic data access

## Slide 8: FTS Transfer Study Details (1/2)
Saul Youssef undertook a study of FTS transfer data augmented with perfSONAR traceroutes to analyze how transfers are working and if there are specific problematic links in our networks.
  The analysis uses the average transfer rate and assigns that rate to all the hops along the network transfer path for a given time-window
  The sum of all transfers in a time-window for a specific network hop can be used to infer a lower bound on its maximum transfer rate
  In this way hops with low maximum transfer rate are identified and can be checked to see if there are problems that need addressing
                Transfer rate bounded >= size(file1+2+3)/(end-start)
The study also identified a number of issues
  Number of streams may not be optimized
  Lots of SRM overhead impacting performance (esp. small files)
  CMS consistently getting better throughput than ATLAS

## Slide 9: FTS Transfer Study (2/2)
The details of the analysis and results are available at http://egg.bu.edu/LHC%7Binf:LHC%7D/gadget:FTS/section:history/fts/index.htm
This has become a collaboration among a number of people (including ATLAS, CMS, LHCb) and most recently the FTS developers / operators
This collaboration is now exploring the impact of a new way to optimize FTS transfers:
  Because of SRM overhead it is better to multiplex more transfers at lower number of streams each as opposed to using more streams and a smaller number of transfers
  Each end-site has only so many resources (Storage I/O, memory and network bandwidth). The algorithm needs a tunable limit (MAXBUFFER) which may vary by site.
  The number of TCP streams for best performance varies. Lower numbers may be better. In some cases 1 seemed optimal. The error rate (timeouts) with 1 TCP stream is only slightly higher than the rate with multi-TCP streams.
Looking forward to seeing how this new strategy works

## Slide 10: LHCb DIRAC bridge
Federico Stagni, Henryk Giemza and Stefan Roiser are working on the perfSONAR-DIRAC bridge
LHCbDIRAC provides information on transfer metrics such as
  number of files transferred
  “quality”, i.e. amount of successful/failed transfers
  throughput
Main use case is to correlate with perfSONAR and use it to better debug transfer issues
  prototype is being developed
Another one is to commission new links, determine capabilities of the new network links

## Slide 11: ATLAS Use Cases (Mario Lassnig)
ATLAS utilizes both scheduled and dynamic transfers
  Scheduled flows for Tier-0 Export, Analysis Output, Production Input/Output, Data Consolidation
  Dynamic for jobs brokered for remote access, local data access failure recovery and the event service
  Both could benefit from using network and transfer metrics
  We need better understanding of network infrastructure and characteristics for full performance and rely upon the working group to provide that information
ATLAS perspective: storage is expensive — make better use of the network
  Leads to more use of dynamic data access, less movement of files
  Depending on activity, only small parts of the files are needed — prime use case
Assumption: current network infrastructure is configured for long flows, big files — is this good for us in the long run?
  Need a dedicated study how an increase in short flows on our infrastructure will behave
  Can we do something on our side? Virtual switches with end-to-end traffic policing sound promising

## Slide 12: ATLAS Network Metrics Pipeline
Ilija Vukotic, Kaushik De, Rob Gardner and Jorge Batista are working with our WG to make perfSONAR metrics available to PANDA
Pipeline: OSG Network Datastore -> CERN Active MQ -> Flume -> ES -> PANDA
Prototype working and analytics being performed in Elastic Search to validate data
Plan is to create a network source-destination cost-matrix PANDA can use to evaluate options
  Actual interface details being discussed with PANDA team

## Slide 13: Coordinating Network Issue Response
The working group has created a support unit to coordinate responses to potential network issues
  Tickets opened in the support group can be triaged to the right destination
  Many issues are potentially resolvable within the working group
  Real network issues can be identified and directed to the appropriate network support centers
Documented at https://twiki.cern.ch/twiki/bin/view/LCG/NetworkTransferMetrics#Network_Performance_Incidents
Notes: https://twiki.cern.ch/twiki/bin/view/LCG/NetworkTransferMetrics#Network_Performance_Incidents

## Slide 14: Baselining Our Networks
The working group has defined a number of meshes with corresponding tests to measure the performance of our network paths
WLCG-wide meshes for latencies, traceroutes and throughput
  perform full mesh tests involving all WLCG sonars
Network provider meshes
  LHCOPN and LHCONE meshes to help debug weak links
Specific project meshes
  Dual-stack – compares throughput between IPv4 and IPv6 instances
  Belle II – covers the additional non-LHC sites in Belle II

## Slide 15: Next Steps
Main focus will be on the pilot projects in collaboration with experiments (ATLAS, CMS, LHCb)
Integration of the higher-level infrastructure services (such as MadAlert, PuNDIT, etc.)
Enabling easy integration with data analytics platforms (ES, Hadoop)
Finalize production deployment of the base infrastructure and follow up
perfSONAR 3.6 (release around summer 2016)

## Slide 16: Summary
The working group has made very good progress in all of its areas of responsibility
ATLAS, CMS and LHCb are all involved and should benefit from our pilot projects and the FTS study work.
We have had very successful (and continuing) collaboration with ESnet and OSG
Focus during the first year has moved from deployment debugging issues to use of the metrics, which is where we want to be.
QUESTIONS?
Notes: Mention successful collaboration between WLCG, ESNet and OSG
Mention pilot projects such as FTS, done in common for ATLAS, CMS and LHCb