## Slide 2: Status of tune integer change in the PS
R. Wasef, S. Gilardoni, M. Juchno, D. Schoerling, F. Sperati
Acknowledgements: A. Huschauer, S. Machida
HSS Meeting, 15/04/15

## Slide 3: The PS
Started operation in 1959
100 m radius
100 combined function magnets
Each magnet consists of 10 blocks: 5 F and 5 D (cell: FDODF)
Tunes are controlled with: - LEQ at low energy (2 families, different symmetry than lattice) - PFW at high energy (on main magnets, same machine periodicity)
Injection kinetic energy 1.4GeV (2 GeV after upgrade).
HSS Meeting, 15/04/15

## Slide 4: Coil system: main circuit and auxiliary coils
HSS Meeting, 15/04/15
Narrow circuit
B
B
Wide circuit
I8L
Thermographic inspection of PFW

## Slide 5: Coil system contributions
IFW
IDN
IFN
IDW
I8L
  Hyperbolic pole shape
  Only dipolar and quadrupolar field at low field level
  Iron saturation
  Sextupolar and higher order components at high field level
Main coil
Pole-face windings + and figure-of eight loop
  5-Current Mode
  Un-balanced N and W circuit current generate octupolar and higher components
  Non-linearities at high field (iron saturation)
  Field probably up to decapole
HSS Meeting, 15/04/15

## Slide 6: Magnetic Model (3D Opera)
Advanced 3D magnetic model available, so far only static solution performed.
Transient solutions are possible but will require long calculation times (several weeks per model).
All coils are implemented, auxiliary coils are approximated by linear pieces.
1
2
3
4
5
6
7
8
9
10
HSS Meeting, 15/04/15

## Slide 7: Working Point Control
In order to model the effect of the PFW, we measured the following matrices:
A similar matrix is measured using the magnetic model (calibrated to a reference point)
HSS Meeting, 15/04/15

## Slide 8: Limit of matrix
The matrix doesn’t agree with the measurement at all configurations
One has to be careful and specially for large changes.
Chart: p/p
| -0.0121069349310016 | -0.0111614923928439 | -0.0102074942282097 | -0.00927277393479932 | -0.00830030010984487 | -0.00749037789995776 | -0.00643201459801348 | -0.00549215713645348 | -0.00458703356058924 | -0.00365548516524864 | -0.0027150834725076 | -0.00182058641335231 | -0.000888618902479413 | -1.27666821499741E-5 | 0.00092049835205755 | 0.00181298298245221 | 0.00273455959803933 | 0.00355343103438087 | 0.00442328528573715 | 0.00526505567445194 | 0.00606850696759334 | 0.0069288818432378 | 0.00778047292829959 | 0.00857709482106454 | 0.00941527235861086 | 0.0102384567779539 | 0.0110564201613327 | 0.0119014787758639 | 0.012713346592081 | 0.0135131628436606
Horizontal measurement | 6.2591 | 6.2543 | 6.2494 | 6.2447 | 6.2401 | 6.2359 | 6.2321 | 6.2285 | 6.2253 | 6.2223 | 6.2195 | 6.217 | 6.2147 | 6.2126 | 6.2106 | 6.2087 | 6.207 | 6.2052 | 6.2034 | 6.2014 | 6.1993 | 6.1969 | 6.1941 | 6.1909 | 6.1873 | 6.1832 | 6.1786 | 6.1736 | 6.168 | 6.1621
Vertical measurement | 6.3676 | 6.3639 | 6.3598 | 6.3556 | 6.3514 | 6.3472 | 6.3423 | 6.3372 | 6.3322 | 6.3267 | 6.3211 | 6.3155 | 6.3099 | 6.3041 | 6.2986 | 6.2931 | 6.2871 | 6.2817 | 6.2765 | 6.2719 | 6.2674 | 6.2632 | 6.2591 | 6.2557 | 6.2525 | 6.2499 | 6.2478 | 6.2461 | 6.245 | 6.2442 | 6.2433 | 6.2426
Horizontal simulation | 6.1851 | 6.2018 | 6.215 | 6.2243 | 6.2297 | 6.2308 | 6.2274
Vertical simulation | 6.4846 | 6.4374 | 6.3933 | 6.3537 | 6.3196 | 6.2925 | 6.2735
HSS Meeting, 15/04/15

## Slide 9: Current Situation
The beam tune-spread is trapped between the Qv=6.25 and the integer resonances.
If one increases the vertical tune to avoid growth due to the integer, the losses increase because of the Qv=6.25 resonance
There are less losses with higher tune-spread because the proton population becomes smaller on the Qv=6.25 after compression.
The choice of the working point is a compromise between losses and emittance blow-up
Core of the beam
Halo particles
HSS Meeting, 15/04/15

## Slide 10: Qy=6.25 resonance
 Qy=6.25 resonance seems to be excited by space charge
Maximum detuning due to space charge:
Beam 1 : (-.22 ; -.4)
Beam 2 : (-.18 ; -.37)
Beam 3 : (-.08 ; -.07)
Beam 4 : (-.01 ; -.01)
Horizontal tune fixed at 6.23
Vertical tune: 6.24->6.3->6.24
6.24
6.3
HSS Meeting, 15/04/15

## Slide 11: Hypothesis
Structure resonance driven by Space Charge.
Structure h=50 (lattice 50xFDODF).
Driven by space charge because doesn’t exist at low brightness (Tune-diagrams).
Mitigation strategies:
  A partial compensation with magnets seems extremely challenging because of the difference in magnetic center.
  Change of the integer, would avoid the harmonic 50.
HSS Meeting, 15/04/15

## Slide 12: Mitigation of the problem
Nominal Optics
Optics (5,7)
 Significant improvement at the new integers
HSS Meeting, 15/04/15
Qv
time
Qp

## Slide 13
2Qy=10
4Qy=20
2Qx=10
4Qx=20
8Qy=50
3Qy=20
8Qx=50
3Qx=20
Qx+2Qy=20
2Qx-Qy=10
-Qx+2Qy=10
2Qx+2Qy=25
Qx+3Qy=25
-Qx+3Qy=10
2Qx+Qy=20
3Qx-Qy=10
3Qx+Qy=25

## Slide 14: Change of integers to (7,7)
Vertical Orbit
Horizontal Orbit
0.1 mm

## Slide 15: Change of integers to (7,7)
The beam is radially unstable due to the change of phase advance between the pickups of the radial loop.
The simulated matrix seems much closer. (The beam was not injected using the measured one!)
It is not possible to reach (7,7) without introducing octupolar component! An resonance compensation might be necessary (using octupoles)
 | Measured Matrix | Simulated Matrix | Measurement
Qx | 7.15 | 7.24 | 7.18
Qy | 7.18 | 7.28 | 7.24
ξx | 8 | -0.83 | -0.5
ξy | 0.5 | -1.12 | -0.5 : -1
HSS Meeting, 15/04/15

## Slide 16: Conclusions
The simulated matrix is a good cross-check/alternative to the measured one.
For large changes, a new matrix is needed.
Injection on (7,7) was only possible using the simulated matrix.
For the integers (7,7), the simulated matrix seems close to the measurement up to the 1st order chromaticity.
a new matrix is needed in order to make accurate changes (loss maps).
an octupolar compensation is needed .
HSS Meeting, 15/04/15