## Slide 1: Activities in Radio-Frequency Engineering
Erk Jensen

## Slide 2: CERN Accelerator Complex

## Slide 3: LHC RF Systems

## Slide 4: LHC Transverse Damper
Damping of injection oscillations,
Damping of oscillations driven by coupled bunch instability,
Important role in preservation of the beam’s transverse emittance
Injection and abort gap cleaning
Transverse blow-ups for loss-maps
Tune measurements
Characteristics:
Bandwidth , full kick strength , 10% at
16 x 35 kW tetrode amplifiers.

## Slide 5: PSB Digital LLRF & Finemet
The hardware
42 Motherboards (FMC-DSP-Carrier)
42 Rear-transition modules
23 Switch modules
(42 ADC, 30 DAC, 15 MDDS) FMCs
14 Cavity Control Interface modules

## Slide 6: Hadron Therapy Collaboration
Successfully delivered & contributed to commission Digital LLRF (PSB-style) + HLRF (Finemet®-based ) systems for MedAustron synchrotron.
  6 Nov ‘14: 10E8 protons extracted to IR3 @ 250 MeV
  31 Mar ‘15: Entering Clinical Qualification Phase
MedAustron synchrotron
Irradiation Room 3 (IR3)
MedAustron complex

## Slide 7: More digital LLRF
Switch&Limiter
Cavity Loops
f quadrupler
RF function generator
Clock distributor
FMC Carrier
RTM
VXS Switch
ADC FMC
SDDS FMC
MDDS FMC
SPS 800 MHz system upgrade!
PSB renovation & MedAustron LLRF systems

## Slide 8: Linac 4 – RFQ

## Slide 9: Linac 4 – DTL
6. August 2014: first beam through tank 1!
100% transmission
Success of drift tube alignment principle (over up to 7.3 m) < ±0.1 mm

## Slide 10: Linac 4 – CCDTL & PIMS
CCDTL (Cell-Coupled DTL, 3-50 MeV)
Assembly finished in 2013
4 out of 7 CCDTL modules are installed,
2 are fully conditioned, 2 more are presently being conditioned,
PIMS (PI-Mode Struct., 100 – 160 MeV)
First complete cavity assembled at CERN,
2nd cavity under assembly,10 to go…
Series production now in full swing.

## Slide 11: Linac 4 – High power RF

## Slide 12: Fundamental Power Couplers
2014 FPC results | 
SPL cylindrical | 1 MW TW – 600 kW SW
SPL disk | 1 MW TW – 1 MW SW
Linac4 window | 750 kW SW, 4/28 series done
HIE-Isolde | 15 couplers done
Crab Cavities | 2 different designs, under construction
SPS800 | Old spare couplers tested
Medical RFQ | Under study
ESRF | 300 kW CW
SOLEIL | 300 kW CW – 250 kW SW
APS | 300 kW CW
ILC | New ceramic without coating
SPL cylindrical
SPL disk
Linac 4
HIE-Isolde
SPS
Crab cavity

## Slide 13: CLIC Study

## Slide 14: X-band (12 GHz) RF components
‘’Simple” -60 dB directional coupler.
Pulse compressor

## Slide 15: X-band Accelerating structures
TD26
TD2 6CLEX
TD24 SiC

## Slide 16: X-band test facility Xbox-3

## Slide 17: SRF – SPL & HL-LHC
SPL 5-cell cavity in He vessel
HL-LHC Crab Cavity Prototypes

## Slide 18: SRF – HIE-ISOLDE
Cavities performances (last 2 prototype tests)
High-beta quarter-wave cavity, Nb-coating un Cu substrate
High-beta cryomodule
SM18, April 2015

## Slide 19: SRF – Infrastructures

## Slide 20: FCC Study – RF
e+ e- collider
Collision energy 90 to 350 GeV
Very high luminosity
Hadron collider
16 T  100 TeV for 100 km
20 T  100 TeV for 80 km
Compare: LEP (1995), 288 Cavities, 17 MW CW
FCC: >1000 cavities, 100 MW CW!
Frequency? (400 MHz & 800 MHz)
Technology? (Nb sputtered on Cu)
RF power – high efficiency!!
Major R&D programme started

## Slide 21: Thank you very much!