## Slide 1: HL-LHC Collimators and High Temperature Materials
HiLumi LHC Goes To Industry Workshop CERN, Geneva, Switzerland – 26 June, 2015
Alessandro Bertarelli, CERN (EN/MME)
On behalf of the LHC Collimation Team
(BE-ABP, EN-STI, EN-MME)

## Slide 2: Outline
Why Collimators in the (HL-)LHC?
What must they do?
Where are Collimators?
What is a LHC Collimator?
How is a Collimator made?
What is a Collimator Jaw made of?
HL-LHC Collimators

## Slide 3: High Energy Particle Accelerators Challenges
Beams circulating in last-generation accelerators can store very high energies (678 MJ for future HL-LHC)
Beam-induced accidents, beam losses and beam stability represent one of the most relevant issues for high power particle accelerators!
Collimators are one of the most critical systems when these issues are of concern
Why Collimators in HL-LHC?
What is HL-LHC Energy equivalent to?
160 kg TNT
30 kg Milk Chocolate
v = 210 km/h
TGV
v = 7 knots
USS Harry S. Truman
J. Wenninger (CERN)

## Slide 4: Beam Cleaning and Machine Protection
Why Collimators?
Primary Collimator
Secondary halo
p
p
e
p
Core
Unavoidable losses
Shower
Beam propagation
Impact parameter
≤ 1 mm
Primary
halo (p)
Secondary Collimator
e
p
Shower
p
Tertiary halo
Absorber
C/C
C/C
W
W
Super-conducting magnets
SC magnets and particle physics exp.
Absorber
The collimation system must satisfy 2 main functions:
Multi-stage Beam Cleaning, i.e. removing stray particles which would induce quenches in SC magnets.
Machine Protection, i.e. shielding the other machine components from the catastrophic consequences of beam orbit errors.

## Slide 5: Requirements for LHC Collimators
Collimators impedance/ LHC Impedance
Collimators are required to survive the beam-induced accidents to which they are inherently exposed given their vicinity to the beam
They must possess extremely accurate jaw flatness to maintain their beam cleaning efficiency
The collimation system is, by far, the highest contributor to accelerator EM impedance which may significantly limit machine performances: they must possess the lowest possible electrical resistivity
Their lifetime and efficiency should be conserved under long-term particle irradiation
Identifying collimator materials able to meet all requirements requires extensive R&D
What must they do?

## Slide 6: Collimation System for HL-LHC
Where are Collimators?
IR1 + IR5:
New tertiary collimators and
physics debris absorbers Completely new layouts
Novel materials
IR2 (Ion physics debris): DS collimators + 11T dipoles
IR7 : DS collimators + 11T dipoles
IR7: Low impedance collimators
New design, novel advanced materials
Total of 118 collimators presently installed
~10 different design!
108 Movable units
No less that 40 units to be replaced for HL-LHC
Final decision on installation to be taken based on Run 2 experience

## Slide 7: General Layout
What are Collimators?

## Slide 8: Horizontal Collimator Layout
Beam axis
Collimator assembly
Overall length: 1480mm
Tank width: 260mm
Plug-in system (integrates mechanical, hydraulic and electrical quick connections)
Adjustable (Horizontal) Stand
(Al Alloy)
What are Collimators?
Fixed Support
(Stainless Steel)

## Slide 9: LHC Secondary Collimator (TCSG)
The collimator and its jaws are expected to maintain their functionality after the impact of 288 SPS bunches at 450 GeV (1+ kg TNT)
What is a Collimator?
Actuation system
35 mm stroke
10 mm repeatability
High radiation compliant
Vacuum Vessel
Stainless steel
EB welded
Jaw Block (2D Carbon-Carbon)
1 m long
40 m flatness in operation
Jaw Assembly (1.2 m long)
Up to 15 kW per jaw in regular operation
Particle Beam
Jaw Cooling system
Cu-Ni Pipes
Notes: 9

## Slide 10: Jaw Assembly Designs
How is a Collimator made?
TCPP /TCSP
(LHC and HL-LHC)
TCSPM (HL-HLC)
TCTP (LHC and HL-LHC)
2D Carbon-Carbon
Tungsten Heavy Alloy (95 W - 3.5 Ni - 1.5 Cu)
R&D currently ongoing
(candidate materials: MoGr and CuCD
Glidcop (Dispersion Strengthened Copper)
Materials of the jaws are the critical component because of the tough requirements (robustness, geometrical stability, electrical conductivity, radiation resistance ...)
New advanced materials being investigated for HL-LHC

## Slide 11: Jaw assembly Design
Vacuum Brazing (Cu-Ni to Glidcop)
How is a Collimator made?

## Slide 12: TCSPM Jaw Prototype
How is a Collimator made?
BPM Button pickup
Molybdenum – Graphite Tapering
Copper – Diamond Blocks

## Slide 13: Actuation System Design
Hybrid Stepper motor
Return spring
To ensure auto-retraction
Mobile table
35 mm stroke
Fixed table
Roller screw assembly
2 mm lead/rev
Each jaw is actuated by two independent actuators and supported on two axles. Hybrid stepper motors are used to drive the system
The system must operate for ~20 years in a harsh environment (15 MGy) with virtually no maintenance
How is a Collimator made?

## Slide 14: Actuation System Design
How is a Collimator made?
Linear Ball Bearing
High precision
Radiation hard lubrication
Stainless steel shaft
Roller screw assembly
High efficiency
High precision (6 m/135 mm)
Radiation hard lubrication

## Slide 15: Summary
Given the very high stored energy of the HL-LHC, collimation is one of the most critical systems of the accelerator.
A complex system made of ~120 units is presently installed and fully operational.
To meet HL-LHC tougher requirements, a significant fraction of the current system is expected to be replaced/updated/complemented.
Intensive R&D is currently ongoing to develop novel materials particularly for low-impedance collimators
Turn-key units will be procured in the industry.
CERN will procure and provide to system contractor critical components: these include jaw materials (novel composites, carbon-based materials, refractory materials etc.), dispersion strengthened copper, lead screws, Cu-Ni pipes etc.
Motorization, electronics, diagnostics and control systems (not covered here) represent a procurement effort as important as mechanics.
Finally, collimation is more than collimators .. New challenging projects in the pipeline such as Hollow Electron Lens, Crystal Collimation …

## Slide 16: Summary
Hollow Electron Lens
Crystal Collimation

## Slide 17
Thank you for your attention!
The research leading to these results has received funding from the European Commission under the FP7 Research Infrastructures project EuCARD, Grant Agreement 227579 and EuCARD-2 Grant Agreement 312453
alessandro.bertarelli@cern.ch

## Slide 18: Collimation system for LHC RunII
Where are collimators?
Total of 118 collimators
~10 different design!
108 Movable units
Roughly 40 units to be replaced for HL-LHC
Dedicated insertions for betatron (IR7) and momentum (IR3) cleaning systems.
Cleaning of incoming beam in all experiments.
Physics debris collimation in the high luminosity IR1/5.

## Slide 19
0°
135°
90°
45°
Base support
Quick interconnection
Support
Collimator
5th axe (±10mm)

## Slide 20
(1) Jaw Bloc (C/C composite)
(2) Main support beam (Glidcop)
(3) Cooling-circuit (Cu-Ni pipes)
(4) Counter-plates (Stainless steel)
(5) Clamping plates (Glidcop)
(6) Preloaded springs (Stainless steel)
Jaw Bloc Assembly
(1)
(2)
(4)
(3)
(6)
(1)
(2)
(3)
(4)
(6)
TCSG Jaw Assembly

## Slide 21
Beam
Vacuum tank
Jaws
Actuation system
Jaws
40µm surface flatness on 1m
10µm positioning accuracy
Heat load: up to 30 Kw