## Slide 1: Superconducting RF Crab Cavities
Marco Garlaschè – CERN EN/MME
On behalf of the Crab Cavities Team
HiLumi LHC Goes To Industry Workshop CERN, Geneva, Switzerland – 26 June, 2015

## Slide 2: Crab Cavities: Why?
Collision Point
…the AIM…
to increase the number of collisions between the two LHC beams by reducing the crossing angle φ
2φ
Currently in LHC, at a given experiment…

## Slide 3: Crab Cavities: Why?
…the ANSWER…
Superconducting Radio-Frequency Cavities, a.k.a. CRAB Cavities

## Slide 4: Crab Cavities: Where & When?
LHC Point 1
Modules to be installed on each IP side & beam
LHC Point 5
Modules to be installed on each IP side & beam
SPS Test (before LS2)
2x Prototype Modules
SM18 Area (~2016)
Initial testing: CRAB cavities, clean room & handling facilities..

## Slide 5: Crab Cavities: What?
300 K > T > 80 K
2 K
2 K
BEAM
…a Module is…
Cryostat embedding
2x CRAB cavities
auxiliary systems
80 K > T > 2 K

## Slide 6: Bottom-Up View: Cavities
2x designs!
Highly non-axialsymmetrical Niobium cavities
RFD Cavity
DQW
Cavity
Technologies Involved:
Forming of 3÷4mm-thick Niobium sheets
  non axisymm. shapes, high aspect ratios, profile tolerance ~ 0.5mm
EB-welding (strict requirements …): Nb/Nb & Nb/NbTi
Brazing (or other) of Nb to S.Steel
900 mm
650 mm
Interest for
Suppliers
Needed
Not Needed
Much Welcome

## Slide 7: Manufacturing R&D with companies
CRABS Initial tests qualification of forming and RF
SPL Project forming & welding of Cu  Nb
CERN
Nb/SS CERN

## Slide 8: HOMs & FPCs1
Technologies Involved:
Mix turning + milling + assembly of Cu and Nb parts (assembly profile ~0.3mm)
Brazing of vacuum-air interfaces embedding Ceramic + Cu + S.Steel
Input/Output systems
for power management inside cavities
Cu
Al2O3
620 mm
200 mm
Nb
SS
Coaxial line
1 High Order Mode Dampers, Fundamental Power Couplers

## Slide 9: Magnetic Shieldings & He Vessel
Magnetic Shielding alloy:
Forming + assembly
Annealing treatment
TSHIELD= 2K
TSHIELD= 80K÷300K
Helium Vessel:
Machining (Titanium Gr.2)
Assembly + Titanium TIG welding
Supply of Titanium bellows
900 mm
Supply of raw Material (Nb, NbTi, Magn. Shielding, St. Steel, Titanium)

## Slide 10: Cryostat
Manufacturing of Cryostat and Auxiliary systems
Sheet metal working of tank (precision interfaces)
Cryo Line (welds tight at 2K)
Ti/S.Steel direct transitions (also @ 2K)
SS Bellows and vacuum equip.
Thermal shielding with Helium cooling + MLI
…
2900 mm
1700 mm

## Slide 11: Electronics and Power supplies
Courtesy E. Montesinos
SPS Test
Series

## Slide 12: Not Forgetting…
Passive/active Tuning System
(ref. Kurt Artoos)
FSI1 Alignment System
(ref. Mateusz Sosin)
1 Frequency Scanning Interferometry
Actuation

## Slide 13: Not Forgetting…
Active Alignment @ SPS Test: motorized & remotely-controlled supporting systems

## Slide 14
Accelerating Science and Innovation
Thank you for your attention!
Notes: 14

## Slide 15: Technology for SC RF cavities

## Slide 16: Magnetic Shieldings & He Vessel
DQW

## Slide 17: Thermal shield overview
Courtesy Andy May & STFC
1050 Aluminium shield
Aluminium alloy tubing
Removable side panels (fitted to frame during initial assembly)
Thermal shield “Window frame”
Flexures
Panel mass = 14Kg each at 6mm thick
Entire shield = 116Kg