## Slide 1: Investigations of Unidentified Lying Objects in the LHC
D. Mirarchi, R. Bruce, P. Hermes,
S. Redaelli, B. Salvachua, G. Valentino
On behalf of
the LHC Collimation Team
Special thanks to BE-OP for the support during measurements

## Slide 2: Introduction
Various dump of beam 2 triggered after ~10-15 min at flat top by BLMBI.15R8.B0T20_MBA-MBB
Main suspect: Multi-UFOs event
40 μs int. time
hadronic showers causing such losses should take place in the middle of MB.15R8.B2(FLUKA)
Beam screen of C15R8 warmed up of >70K for 2h the 18th of April
First ramp after (night of 19th of April) last for 4h without M-UFOs events
May be something frozen was creating “falling objects” and then fallen down for the warm up?
Initial local aperture measurements: aperture restriction were not found
New local aperture measurements show the presence of Unidentified Lying Objects (ULOs)

## Slide 3: Measurements procedure
Beam screen
No losses at B15
1st losses at B15
Local orbit bump: given that MQ.15R8.B2 is a focusing quadrupole
4 correctors bump in V plane
3 correctors bump in H plane
Q15
Q14
Q16
Q15
B15=1.14*Q15
B15=0.86*Q15
First fast scans performed the night of 18th April
First detailed scan performed the night of 20th April:
Beam shaped with IR7-TCPs (H & V)
Systematic probing of local aperture
Max excursion in H~±14mm, in V~±8mm (due to losses rising at Q14 and Q16)

## Slide 4: First scan 20-21/4/15
Cut applied with IR7-TCPs: 4σy and 3σx
Step of 2-3mm for H bumps, 1mm for V bumps (~1.4σy at MB15R8)
Safe aperture (last step before losses on MB15R8)
Physics aperture at MB.15R8
Aperture in units of σ
~-8.4mm
~12σy
Measurements performed at injection

## Slide 5: First scan 20-21/4/15
V bumps stopped when losses observed on BLMBI.15R8.B0T20_MBA-MBB
Each beam loss provoked about the same BLM signal and drop in intensity
Touched aperture
Physics aperture at MB.15R8
Aperture in units of σ
~-9.4mm
~14σy
Edge of aperture restriction found between ~ -8.4mm and ~ -9.4mm, i.e. ~12σy and ~14σy

## Slide 6: OP scans 22/4/15
Similar scan performed during the night shift of 22nd April by OP (B. Salvachua) at flat top
Cut applied with IR7-TCPs: 9.5σx and 5.4σy
Less positions probed, however:
First losses in C15R8 observed with: bump H=0mm, V= -1.7mm
Steps of ~200μm (~1σy at MB15R8) for V bump
Taking into account the beam dimensions of 5.4σy , and translating this at MB.15R8:
Edge of aperture restriction found between ~ -3.1mm and ~ -3.3mm, i.e. ~4.5σy and ~4.8σy

## Slide 7: Second scan 23/4/15
Cut applied with IR7-TCPs: 4σy and 2σx
Step of 2mm for H bumps, 0.5mm for V bumps (~0.7σy at MB15R8)
Safe aperture (last step before losses on MB15R8)
Physics aperture at MB.15R8
Aperture in units of σ
~8.4mm
~12σy
Measurements performed at injection

## Slide 8: Second scan 23/4/15
V bumps stopped when losses observed on BLMBI.15R8.B0T20_MBA-MBB
Tentatively each beam loss provoked same BLM signal and drop in intensity
Touched aperture
Physics aperture at MB.15R8
Aperture in units of σ
~-9.0mm
~13σy
Edge of aperture restriction found between ~ -8.4mm and ~ -9.0mm, i.e. ~12σy and ~13σy
The ADT was now operational, small blow up made after each beam loss

## Slide 9: Second scan 23/4/15
After measurements at injection for B2, performed also at flat top:
Unfortunately only one measurements (with bump H=0mm) was possible due to dump triggered by a UFO at our location
Probed also same location for B1 (at injection): aperture restrictions were not found
Cut applied with IR7-TCPs: 5σy and 5σx
Steps of 0.1mm for V bumps (~0.5σy at MB15R8)
Edge of local aperture restriction found with V bump of -7.9mm
Taking into account the beam dimensions of 5σy , and translating this at MB.15R8:
Edge of aperture restriction (at H=0mm) found at V ~ -9.91mm at flat top
Consistent with what found at injection for bump H=0mm: edge found with bump V=-6.0mm
Taking into account the beam dimensions of 4σy , and translating this at MB.15R8:
Edge of aperture restriction (at H=0mm) found at V ~ -9.60mm at injection

## Slide 10: Third scan 26/4/15
Beam screen of C15R8 warmed up again the 25th of April
Same measurements performed (bump steps and IR7-TCPs cuts) as in the second scan
Measurements performed at injection
Physics aperture at MB.15R8
Aperture in units of σ
~-5.6mm
~8σy
Edge of aperture restriction found between ~ -5.0mm and ~ -5.6mm, i.e. ~7σy and ~8σy

## Slide 11: More scans 26/4/15
After the previous measurement performed another two scans at injection with fresh beam
Only bump H=0mm was probed: edge aperture restriction found again with bump V=-6.5mm
(i.e. at V=~-9.6mm at MB.15R8, plus the beam dimensions of 4σy )
WHY??
Correlation with circulating intensity?
(scans of 20th and 23th pilot bunch, 22nd with nominal, and 26th after about 20min with nominal)
Injected nominal bunch and left in the machine for about 30min
edge aperture restriction found again with bump H=0mm at V=-6.5mm
(i.e. at V=~-9.6mm at MB.15R8, plus the beam dimensions of 4σy )
Measurement repeated right after using pilot bunch

## Slide 12: Were we where we though?
Measured beam position by BPM.15R8.B2 during third scan (26/4)
Distortions due to non-linearities at large displacements

## Slide 13: Beam 2 loss maps
No obvious activity seen in C15R8

## Slide 14: Conclusions
First (20/4 at injection) and second scan (23/4 at injection and flat top) made with pilot bunch:
OP scan (22/4 at flat top) made with nominal bunch:
Third scan (26/4 at injection) made with pilot bunch, but after about 20min with nominal bunch circulating in the machine:
“More scans” (26/4 at injection) made with pilot bunch after about 2 hours of measurements (third scan):
Correlation with circulating intensity seems also excluded
Various dump of beam 2 triggered after ~10-15 min at flat top by M-UFOs in MB.15R8.B2
Local aperture restriction were not found before beam screen warm up, while ULOs after
consistent results were found (restriction at H=0, -9mm < V < -10mm at B15R8)
restriction at H=0, -3.1mm < V < -3.3mm
restriction at H=0, -5.0mm < V < -5.6mm
restriction at H=0, -9.0mm < V < -9.5mm
No obvious activity seen in C15R8 during Beam 2 loss maps
More scans are yet to come,
any idea is welcome!
(Latest meas. tonight: >6mm)
More news at LMC by Stefano

## Slide 15: BACKUP

## Slide 16: Were we where we though?
Measured beam position by BPM.15R8.B2 during second scan (23/4)
Distortions due to non-linearities at large displacements

## Slide 17: Q' measurements
S. Redaelli

## Slide 18: Losses in physics in 2012
S. Redaelli

## Slide 19: Losses in physics in 2012
S. Redaelli