## Slide 1: Register-Like Block RAM: Implementation, Testing in FPGA and Applications for High Energy Physics Trigger Systems
Wu, Jinyuan
Fermilab
May. 2014

## Slide 2: Introduction
A basic building block for data storage is presented.
The block RAM operates as if it is a register, supporting:
  Single clock cycle booking
  Single clock cycle reading
  Single clock cycle refreshing
The RAM is organized in bins supporting multiple hits per bin.

## Slide 3: Contemporary Tracking Trigger Schemes
Detector hit data are partially used in Segment Finding block while full data are stored in Data Buffer.
Segment Finding block finds segments and output address of the hits in each segment.
Full hit data are read out and sent to Track Fitting block to calculate track parameters.
Segment
Finding
(AM,
Artificial Retina,
Kalman Filter)
Hit Addresses
Data Buffer
Data Buffer
Data Buffer
Data Buffer
Track
Fitting

## Slide 4: Block RAM in Trigger System
The RAM is organized in bins.
Hit data arrives along with bin numbers (e.g., hit coordinates).
Hit data are stored in corresponding bins.
Each bin may store multiple hits.
Hits in each bin are read out for fitting once addressed.
BIN_NB
DATA

## Slide 5: Fast Refresh between Events
The buffer operates event by event.
It is desirable to refresh the buffer, i.e., to clean up the contents, between two events.
The refreshing process should be as fast as possible, ideally in single clock cycle.
Event n
Event n+1
Refresh

## Slide 6: Typical Refreshing Process
The regular RAM devices are not resettable globally.
In order to refresh a memory buffer for next event, all locations are to be written with 0.
The process takes many clock cycles.
Event n
Event n+1
Refresh
RAM
0
Reset

## Slide 7: Global Refresh Scheme
An event ID counter EVID is kept and is written into RAM along with Payload Data.
The refreshing takes a single clock cycle to increase EVID (i.e., EVID++).
During readout, the EVID is checked to validate the output data.
RAM
QC
QD
DC
DD
A
WE
D Q
D Q
CNT
CE
A
B
A=B
RFRSH
DD
ADDR
WR
YD
EVID
Event ID
Payload
Data
Event ID
Payload
Data

## Slide 8: Event ID Rollover Issue
With finite number of bits storing the EVID, the counter will roll over.
The data from old events may be viewed ask new.
Event ID
Payload
Data
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
Event Number
EVID
EVID
8-bit EVID: Rolling Over every 256 events
16-bit EVID: Rolling Over every 64K events

## Slide 9: Overwriting Bins with EVID Rotationally
The RAM has 256 bins and a 9-bit EVID.
One bin is overwritten during each refreshing cycle.
All 256 bins are written within 256 events.
No bins containing EVID older than current event-256.
RAM
QC
QD
DC
DD
A
WE
D Q
D Q
CNT
CE
A
B
A=B
RFRSH
DD
ADDR
WR
YD
EVID

## Slide 10: Multiple Hits Per Bin
Each bin may store multiple hits.
A bin takes three steps to update:
  Reading out the bin contents
  Attaching new data
  Writing back to the bin
BIN_NB
DATA
1
2
3

## Slide 11: Read-after-Write (RAW) Hazard
If the same bin is to be booked in two adjacent clock cycles, a read-after-write (RAW) hazard will occur.
When the second data arrives, the bin has not been updated by the first data.
BIN_NB
DATA
1

## Slide 12: Read-After-Write (RAW) Hazard
D Q
K4
DV
RAM
Q
D
WA
WE
RA
D Q
D Q
+1
D Q
D Q
K1
K1
K0
K2
N1
Wrong!
Wanted to be N1+1
K0 | K1 | K2 | K1 | K4 |  |  |  | 
 | K0 | K1 | K2 | K1 | K4 |  |  | 
 |  | K0 | K1 | K2 | K1 | K4 |  | 
 |  |  | K0 | K1 | K2 | K1 | K4 | 
 |  |  | N0 | N1 | N2 | N1 | N4 | 
 |  |  |  | K0 | K1 | K2 | K1 | K4
 |  |  |  | N0+1 | N1+1 | N2+1 | N1+1 | N4+1

## Slide 13: Data Forwarding Scheme
A data forwarding unit is used to eliminate the RAW hazard.
The data forwarding is a scheme transplanted from micro-processor design method.
RAM
QA
QB
DA
AA
WEA
DB
AB
WEB
Refresh
Logic
Unit
Data
Update
Unit
Input Data Pipeline
Data Forwarding Unit
Forwarding Control
Refresh Counter Control & Pipeline
Refresh
Logic
Unit
RFRSH
WR
BIN_NB
DATA

## Slide 14: RAW Hazard Prevention: Data Forwarding
D Q
DV
RAM
Q
D
WA
WE
RA
D Q
D Q
+1
D Q
D Q
D Q
D Q
&&==
&&==
&&==
If any bin is to be re-hit before data is written back to RAM, it is forwarded to these registers.
Re-hit of a bin is detected.
K

## Slide 15: The Entire Design
The data, bin number and operation command are sent through a pipeline.
The are stored in RAM along with EVID.
RAM
QA
QB
DA
AA
WEA
DB
AB
WEB
Refresh
Logic
Unit
Data
Update
Unit
Input Data Pipeline
Data Forwarding Unit
Forwarding Control
Refresh Counter Control & Pipeline
Refresh
Logic
Unit
RFRSH
WR
BIN_NB
DATA

## Slide 16: Actual Implementation
Implemented in an EP3C25F324C6 device.

## Slide 17: Fast Book & Fast Reset Block Memory
The interface of the block.
The system clock is 250 MHz

## Slide 18: The Test Platform
Altera evaluation board.

## Slide 19: Operations (1)
In event 001, 6 data are written into 4 bins.
 |  |  |  |  |  | Mem Data |  |  | 
 | Raw Data | Op. Code | InData | Addr | EvtID | 3 | 2 | 1 | Valid
0 | 00000800000000 | 0: Read |  | 00 | 000 |  |  |  | <<<<
1 | 20000800000000 | 2: Refresh |  | 00 | 000 |  |  |  | ¦
2 | 1A1018010000A1 | 1: Write | A1 | 01 | 001 |  |  | A1 | ¦
3 | 1A20180100A1A2 | 1: Write | A2 | 01 | 001 |  | A1 | A2 | ¦
4 | 1A3038010000A3 | 1: Write | A3 | 03 | 001 |  |  | A3 | ¦
5 | 1A401801A1A2A4 | 1: Write | A4 | 01 | 001 | A1 | A2 | A4 | ¦
6 | 1A5058010000A5 | 1: Write | A5 | 05 | 001 |  |  | A5 | ¦
7 | 1A6068010000A6 | 1: Write | A6 | 06 | 001 |  |  | A6 | ¦
8 | 00000000000000 | 0: Read |  | 00 | 000 |  |  |  | ¦
9 | 00001801A1A2A4 | 0: Read |  | 01 | 001 | A1 | A2 | A4 | <<<<
10 | 00002000000000 | 0: Read |  | 02 | 000 |  |  |  | ¦
11 | 000038010000A3 | 0: Read |  | 03 | 001 |  |  | A3 | <<<<
12 | 00004000000000 | 0: Read |  | 04 | 000 |  |  |  | ¦
13 | 000058010000A5 | 0: Read |  | 05 | 001 |  |  | A5 | <<<<
14 | 000068010000A6 | 0: Read |  | 06 | 001 |  |  | A6 | <<<<
15 | 00007000000000 | 0: Read |  | 07 | 000 |  |  |  | ¦
16 | 20001801000000 | 2: Refresh |  | 01 | 001 |  |  |  | ¦
17 | 1B1078020000B1 | 1: Write | B1 | 07 | 002 |  |  | B1 | ¦
18 | 20002802000000 | 2: Refresh |  | 02 | 002 |  |  |  | ¦
19 | 1C1048030000C1 | 1: Write | C1 | 04 | 003 |  |  | C1 | ¦
20 | 1C20480300C1C2 | 1: Write | C2 | 04 | 003 |  | C1 | C2 | ¦
21 | 1C3018030000C3 | 1: Write | C3 | 01 | 003 |  |  | C3 | ¦
22 | 1C40180300C3C4 | 1: Write | C4 | 01 | 003 |  | C3 | C4 | ¦
23 | 1C504803C1C2C5 | 1: Write | C5 | 04 | 003 | C1 | C2 | C5 | ¦
24 | 00000000000000 | 0: Read |  | 00 | 000 |  |  |  | ¦
25 | 0000180300C3C4 | 0: Read |  | 01 | 003 |  | C3 | C4 | <<<<
26 | 00002002000000 | 0: Read |  | 02 | 002 |  |  |  | ¦
27 | 000030010000A3 | 0: Read |  | 03 | 001 |  |  | A3 | ¦
28 | 00004803C1C2C5 | 0: Read |  | 04 | 003 | C1 | C2 | C5 | <<<<
29 | 000050010000A5 | 0: Read |  | 05 | 001 |  |  | A5 | ¦
30 | 000060010000A6 | 0: Read |  | 06 | 001 |  |  | A6 | ¦
31 | 000070020000B1 | 0: Read |  | 07 | 002 |  |  | B1 | ¦
Event 001
A1
01
A2
01
A3
03
A4
01
A5
05
A6
06
A1
A2
A4
A3
A5
A6
BIN_NB
DATA
EVID
001
001
001
001

## Slide 20: Operations (2)
In event 002, 1 data is written into 1 bins.
 |  |  |  |  |  | Mem Data |  |  | 
 | Raw Data | Op. Code | InData | Addr | EvtID | 3 | 2 | 1 | Valid
0 | 00000800000000 | 0: Read |  | 00 | 000 |  |  |  | <<<<
1 | 20000800000000 | 2: Refresh |  | 00 | 000 |  |  |  | ¦
2 | 1A1018010000A1 | 1: Write | A1 | 01 | 001 |  |  | A1 | ¦
3 | 1A20180100A1A2 | 1: Write | A2 | 01 | 001 |  | A1 | A2 | ¦
4 | 1A3038010000A3 | 1: Write | A3 | 03 | 001 |  |  | A3 | ¦
5 | 1A401801A1A2A4 | 1: Write | A4 | 01 | 001 | A1 | A2 | A4 | ¦
6 | 1A5058010000A5 | 1: Write | A5 | 05 | 001 |  |  | A5 | ¦
7 | 1A6068010000A6 | 1: Write | A6 | 06 | 001 |  |  | A6 | ¦
8 | 00000000000000 | 0: Read |  | 00 | 000 |  |  |  | ¦
9 | 00001801A1A2A4 | 0: Read |  | 01 | 001 | A1 | A2 | A4 | <<<<
10 | 00002000000000 | 0: Read |  | 02 | 000 |  |  |  | ¦
11 | 000038010000A3 | 0: Read |  | 03 | 001 |  |  | A3 | <<<<
12 | 00004000000000 | 0: Read |  | 04 | 000 |  |  |  | ¦
13 | 000058010000A5 | 0: Read |  | 05 | 001 |  |  | A5 | <<<<
14 | 000068010000A6 | 0: Read |  | 06 | 001 |  |  | A6 | <<<<
15 | 00007000000000 | 0: Read |  | 07 | 000 |  |  |  | ¦
16 | 20001801000000 | 2: Refresh |  | 01 | 001 |  |  |  | ¦
17 | 1B1078020000B1 | 1: Write | B1 | 07 | 002 |  |  | B1 | ¦
18 | 20002802000000 | 2: Refresh |  | 02 | 002 |  |  |  | ¦
19 | 1C1048030000C1 | 1: Write | C1 | 04 | 003 |  |  | C1 | ¦
20 | 1C20480300C1C2 | 1: Write | C2 | 04 | 003 |  | C1 | C2 | ¦
21 | 1C3018030000C3 | 1: Write | C3 | 01 | 003 |  |  | C3 | ¦
22 | 1C40180300C3C4 | 1: Write | C4 | 01 | 003 |  | C3 | C4 | ¦
23 | 1C504803C1C2C5 | 1: Write | C5 | 04 | 003 | C1 | C2 | C5 | ¦
24 | 00000000000000 | 0: Read |  | 00 | 000 |  |  |  | ¦
25 | 0000180300C3C4 | 0: Read |  | 01 | 003 |  | C3 | C4 | <<<<
26 | 00002002000000 | 0: Read |  | 02 | 002 |  |  |  | ¦
27 | 000030010000A3 | 0: Read |  | 03 | 001 |  |  | A3 | ¦
28 | 00004803C1C2C5 | 0: Read |  | 04 | 003 | C1 | C2 | C5 | <<<<
29 | 000050010000A5 | 0: Read |  | 05 | 001 |  |  | A5 | ¦
30 | 000060010000A6 | 0: Read |  | 06 | 001 |  |  | A6 | ¦
31 | 000070020000B1 | 0: Read |  | 07 | 002 |  |  | B1 | ¦
Event 002
B1
07
001
A1
A2
A4
001
001
001
A3
A5
A6
BIN_NB
DATA
EVID
002
B1

## Slide 21: Operations (3)
In event 003, 5 data is written into 2 bins.
 |  |  |  |  |  | Mem Data |  |  | 
 | Raw Data | Op. Code | InData | Addr | EvtID | 3 | 2 | 1 | Valid
0 | 00000800000000 | 0: Read |  | 00 | 000 |  |  |  | <<<<
1 | 20000800000000 | 2: Refresh |  | 00 | 000 |  |  |  | ¦
2 | 1A1018010000A1 | 1: Write | A1 | 01 | 001 |  |  | A1 | ¦
3 | 1A20180100A1A2 | 1: Write | A2 | 01 | 001 |  | A1 | A2 | ¦
4 | 1A3038010000A3 | 1: Write | A3 | 03 | 001 |  |  | A3 | ¦
5 | 1A401801A1A2A4 | 1: Write | A4 | 01 | 001 | A1 | A2 | A4 | ¦
6 | 1A5058010000A5 | 1: Write | A5 | 05 | 001 |  |  | A5 | ¦
7 | 1A6068010000A6 | 1: Write | A6 | 06 | 001 |  |  | A6 | ¦
8 | 00000000000000 | 0: Read |  | 00 | 000 |  |  |  | ¦
9 | 00001801A1A2A4 | 0: Read |  | 01 | 001 | A1 | A2 | A4 | <<<<
10 | 00002000000000 | 0: Read |  | 02 | 000 |  |  |  | ¦
11 | 000038010000A3 | 0: Read |  | 03 | 001 |  |  | A3 | <<<<
12 | 00004000000000 | 0: Read |  | 04 | 000 |  |  |  | ¦
13 | 000058010000A5 | 0: Read |  | 05 | 001 |  |  | A5 | <<<<
14 | 000068010000A6 | 0: Read |  | 06 | 001 |  |  | A6 | <<<<
15 | 00007000000000 | 0: Read |  | 07 | 000 |  |  |  | ¦
16 | 20001801000000 | 2: Refresh |  | 01 | 001 |  |  |  | ¦
17 | 1B1078020000B1 | 1: Write | B1 | 07 | 002 |  |  | B1 | ¦
18 | 20002802000000 | 2: Refresh |  | 02 | 002 |  |  |  | ¦
19 | 1C1048030000C1 | 1: Write | C1 | 04 | 003 |  |  | C1 | ¦
20 | 1C20480300C1C2 | 1: Write | C2 | 04 | 003 |  | C1 | C2 | ¦
21 | 1C3018030000C3 | 1: Write | C3 | 01 | 003 |  |  | C3 | ¦
22 | 1C40180300C3C4 | 1: Write | C4 | 01 | 003 |  | C3 | C4 | ¦
23 | 1C504803C1C2C5 | 1: Write | C5 | 04 | 003 | C1 | C2 | C5 | ¦
24 | 00000000000000 | 0: Read |  | 00 | 000 |  |  |  | ¦
25 | 0000180300C3C4 | 0: Read |  | 01 | 003 |  | C3 | C4 | <<<<
26 | 00002002000000 | 0: Read |  | 02 | 002 |  |  |  | ¦
27 | 000030010000A3 | 0: Read |  | 03 | 001 |  |  | A3 | ¦
28 | 00004803C1C2C5 | 0: Read |  | 04 | 003 | C1 | C2 | C5 | <<<<
29 | 000050010000A5 | 0: Read |  | 05 | 001 |  |  | A5 | ¦
30 | 000060010000A6 | 0: Read |  | 06 | 001 |  |  | A6 | ¦
31 | 000070020000B1 | 0: Read |  | 07 | 002 |  |  | B1 | ¦
Event 002
003
001
001
001
A3
A5
A6
EVID
002
B1
C1
04
C2
04
C3
01
C4
01
C5
04
BIN_NB
DATA
002
C3
C4
003
C1
C2
C5

## Slide 22: Event ID Updating
More than several thousands events are fed through the RAM block.
The Event ID for each bin is updated as expected.

## Slide 23: Future Improvement (1) Boundary Coverage
For each detector layer, once a bin is addressed, the actual hit data may be found in up to 4 bins to ensure correct boundary coverage.

## Slide 24: Future Improvement (2) Hidden Refreshing Process
The refreshing process can be hidden during the event transition.
Totally no dead time between two events.
Event n
Event n+1
Refresh

## Slide 25: Summary
The block RAM operates as if it is a register. It supports:
  Single clock cycle booking
  Single clock cycle reading
  Single clock cycle refreshing
The RAM is organized in bins supporting multiple hits per bin.

## Slide 26: The End
Thanks