## Slide 1
Design and test of a GBTx based board for the upgrade of the ALICE TOF readout electronics
P. Antonioli, C. Baldanza, D. Falchieri, F.M. Giorgi, A. Mati, C. Tintori
INFN Bologna, INFN & University of Bologna, CAEN S.p.A
SIU
TTCrq
CONET
A1500
VME
SSRAM
Actel APA
GBTx test board
Igloo2
GBTx
VME
A1500
CONET2
VTRx
SSRAM
DRM2
DRM1

## Slide 2: GBTx test board: picture
VTRx
GBTx
IGLOO2
E-Links
4.8 Gbps
CONET2
NI USB pod
8451
USB

## Slide 3: GBTx loopback tests
eye diagram of the GBTx TX output
GBTx tested in loopback while transmitting fixed patterns (0xAAABBB…) at 4.8 Gbps and no errors were found.
GBTx
VTRx
TX
RX
multi-mode fiber
Measured BER lower than 10-14
Igloo2
GBTx
LVDS
LVDS, SLVS
SLVS
40 diff pairs @ 80 Mb/s
40 diff pairs @ 80 Mb/s

## Slide 4: Conclusions
Good testbench for testing the Igloo2 – GBTx – VTRx system
Very good BER (as low as 10-14)
Already used in connection to a PCIe C-RORC board for data acquisition on a PC
200 KHz trigger rate
270 MB/s throughput

## Slide 5: Backup

## Slide 6: GBTx test board: scheme
FPGA IGLOO2
GBTx
VTRx-VTTx
M2GL90T
JTAG
ETH
A1500
mezzanine
USB
PXL_*
40
SSRAM
SFP
clock
SERDES
clock
I2C+SC
clock
debug
58
80+80
CY7C1350G 133AXC
ALICE C-RORC