## Slide 1: Beam Synchonous Timing (BST)
Short Description
Status
New Design
Future ….

## Slide 2: BST - Short description
Broadcast timing signals & messages required to synchronize acquisition systems with beam.
Use the 40MHz & Orbit Turn-clock provided by the RF system.
A message is produced by BST-Master every revolution period.
Distribution to the experiments and BI over optical networks by using TTC components. (TTCex, TTCvx, TTCtx, TTCrx)
The BST Receiver (BOBR) is the interface to the end users installed in each VME beam instrumentation crates .

## Slide 3: BST - Master
3 x VME Crates:
LHC Ring 1
LHC Ring 2
SPS

## Slide 4: BST - Optical Distribution
End Users:
( EA, BI, Labos )
LHC 1 = 157
LHC 2 = 156
SPS = 22
+ pre-pulse
by cable!

## Slide 5: BST - Receiver (BOBR)
Installation: E.A.= 10
B.I. = 160
Spare = 40
2 Channels (LHC 1 & 2)
40 MHz Bunch-Clock > P0+FP
Delayed Turn-Clock > P0+FP
Message > DP RAM.
2 x Trigger bytes > P0
8 x Bunch selector > P0
IRQ on specific bytes.
….
P0 BUS
VME-BI
Crate
ONLY !
To be plug into VME-BI crate pos 12:
VME64x Board
2 x TTCrm:

## Slide 6: BST- New Design: BSTR implementation in the VFC
SFPGA
FLASH CONFIG
AFPGA
BSTR
Application Firmware
P2 Extension Module
CDR
BST Optical network
.
SFP
IF Wiener Crate
P0
BST Signals From BOBR
  Clock + Data + Status
New Acquisition Board :
VFC ( VME FMC CARRIER)
BST Optical network
Use one of the 2 x SFPs
( Small Formfactor Pluggable)
BSTR: VHDL package to be put into the Application FPGA.
>> Same functionality as the BOBR module
1:16 Optical Splitter
P0
P2
Up to 16 VFC
ADN2814
CDR
Interface

## Slide 7
TTC Frame >> Clock & Data Recovery
BST- New Design:
LHC : Protons & Ions > OK
SPS : Protons > OK (Except Injection pre-pulse)
SPS : Ions > Problem during injection phase !
Biphase Mark TTC Frame
( Sync with the 40 MHz x 4)
160 MHz Recovered Clock
160 Mb/s Recovered Data

## Slide 8
BST- New Design:
SPS : Ions > Problem during injection phase !
SPS Super Cycle with Ions
CDR Loss of Lock syncro @ RF switching
=> No BST Message for few ms. when no beam !
SPS Super Cycle
Time interval when the CDR is not locked!
Why? : The RF 200M is active only 12.5 µs over the 23 µs of the SPS rev.
The other 12.5 µs the RF switches to a default freq. (~198 MHz)
=> No BST Message !
=> Bunch-Clock & Turn-Clock from local osc. (not syncro with beam)
Possible solution: Do not use the 40 M clock directly from the RF 200M / 5
=> Modification at the BST Master level ?
Ions injection period

## Slide 9: BST – Future …
BST-Master (BE-CO)
      CPU replacement
      SPS Message restructuration (if needed)
      SPS synchro for ions ?
      New design ?
TTC (Sophie)
      Support (TTCex, vx ,tx, rx)
      New design ?
Optical Network (JJ,Eva, EL-CF)
BST Receiver
    - BOBR (JJ, after 2014 ?)
- New design (JJ, Andrea)