## Slide 1: discussion issues*
Miniweek WG5 June 2015
Hans Muller CERN/RD51
* probably not complete

## Slide 2: Functionality issues
Z-suppression for APV ( common mode addition)
SRU Readout bandwidth (10 GBE -> DAQ disk )
clock&trigger timing (common via SRU/CTF)
Max trigger rates APV, VMM ( 10 kHz, 1 MHz)
SRS in Magnetic fields ( crates =NO, hybrids = YES)
APV at low temperature ( is this an issue? )
APV non linearity (is this an issue ?)
add more

## Slide 3: Procurement/availability issues
CERN store (only team account, only local delivery, no RFF )
RFF (billed purchase from external teams: large administrative overhead, intermediate account loan, shipment issues)
Restricted APV hybrids ( Compliance Letter and Federal Regulations http://www.ecfr.gov )
FEC6 and FEC3 ( FEC 6 new on CERN store, replaces FEC V3)
Panasonic connectors ( production stopped, second source found)
Commercial SRS sales ( SRS licence: EicSys, Samway, … )
Classic SRS vs. SRS ATCA (small systems vs medium / large systems)
Price / channel ( 2012 : 2Eu/ APV channel, 2015: 2.5 Eu/APV ch)
VMM2 hybrids (2 protos produced last week, 14 more for sponsor teams)
VMM3 hybrids ( expect as from 1Q 2015, no embargo, commercial )
DCards for VMM readout ( revised for triple power consumption of VMM )
SRU, CTF ( commercial availability to be set up )
APIC Trigger pickup boxes ( PCB revision before commercial mini-series )
OCX boxes (delayed, expect 10 inhouse protos 3Q 15, prior to commercial )
add more

## Slide 4: Firmware / Software
SVN repository ( binaries, docs, ticketing )
WG5 web download ( binaries, docs)
SRS source code (Memo procedure)
SRS DAQ software (DATE, MMDAQ.. )
SRS slow controls ( SDC, scripts, …
Data Analysis ( Root , Amore )
Test system software (Labview )
add more

## Slide 5: Frequent questions
Which type of SRS system do I need (ask us)
CERN store SRS purchase template (SCEMs + prices)
Crate power limit F(#ch, APV/VMM )
power per channel (APV 4mA, VMM >10 mA)
How to update FEC, SRU binaries (Dongle)
Crate compliance (US Labs better use ATCA minicrates)
220V/110V options ( automatic in last Crates)
Grounding, noise, sparc-protection ( …deserves care)
add more

## Slide 6: SRS architectures
Small Systems ( Minicrates, < 2 k channels)
Medium-sized < 16 k ch ( Eurocrates, ATCA )
Large systems > 16 k ch ( ATCA )
CTF = mini-SRU ( ommon clock and trigger )
SRU vs. networkswitches (DTCC vs UDP only)
triggered systems (APV needs low lat. trigger )
self triggered systems ( VMM = provides its own)
add more

## Slide 7: SRS MANPOWER (major vacancies)
Work on specific technical issues ( trigger, power, connectors, cables, new SRS devices )
SRS firmware ( SRU BW , Z-Suppression, VMM integration)
SRS controls for APV and VMM
user assistance for standard SRS DAQ software ( i.e DATE )
small system user support ( i.e Labview )
CERN purchase consultancy ( team accounts, RFF )
SRS innovation issues ( VMM , Dcards, optical SRS, TPIC )
Hotline (nothing works, SRS got broken, need firmware ..)
add more