## Slide 1: ILC Calorimeters FCCee Calorimeters
Imad Laktineh
Institut de Physique Nucléaire de Lyon, France

## Slide 2
Outline
ILC detectors philosophy
ILC calorimeters options :
SiD, ILD
ILC calorimeters for FCCee
Examples: SDHCAL, Si-W ECAL

## Slide 3
Philosophy of the ILC detectors
Detectors should be precision and discovery
tools beyond the LHC scope.
Relevant Physics phenomena in the TeV
energy range are associated to multi jet
final states  Jet energy measurement
is the most important item.
Particle Flow Algorithm is adopted in both
SiD and ILD concepts. PFA: Construction of individual
particles and estimation of their energy/momentum
in the most appropriate sub-detector.
PFA requires the different sub-detectors including calorimeters to be highly granular.
PFA uses their granularity to separate neutral from charged contributions and exploits
the tracking system to measure with precision the energy/momentum of charged particles.

## Slide 4
Philosophy of the ILC detectors
Detectors should be precision and discovery
tools beyond the LHC scope.
Relevant Physics phenomena in the TeV
energy range are associated to multi jet
final states  Jet energy measurement
is the most important item.
Particle Flow Algorithm is adopted in both
SiD and ILD concepts. PFA: Construction of individual
particles and estimation of their energy/momentum
in the most appropriate sub-detector.
PFA requires the different sub-detectors including calorimeters to be highly granular.
PFA uses their granularity to separate neutral from charged contributions and exploits
the tracking system to measure with precision the energy/momentum of charged particles.

## Slide 5
Charged tracks resolution ∆p/p ~ few10-5
Photon(s) energy resolution ∆E/E ~ 12% / E
Neutral hadrons energy resolution ∆E/E ~ 45% / E
Ejet = Echarged t + E + Eh0
fraction 65% 26% 9%
Why tracking is so important?

## Slide 6
Philosophy of the ILC detectors : Requirements
Vertex detector : excellent resolution
sIP(rf) = 5+10/(p sin2/3(q)) mm
b-tag, c-tag,… for H  bb, cc, tt studies
Tracker : excellent precision measurement of pt
s(1/pt) =10-5 GeV-1
H mass recoil, e+ e-  H Z m+ m- + anything
Calorimeters : highly granular but still providing
good measurement of neutrals
sE/E = 30%/E
The whole detector should be hermitic, compact
with moderate power consumption
30%/E

## Slide 7
Power-Pulsing
Important feature of ILC detectors to reduce power consumption and heating for highly-granular detectors
Electronics switched on just before the bunches train and off after
A factor 100-200 power reduction could be achieved.
2820 bc by train
337 ns separating two bc.

## Slide 8
ILD SiD

## Slide 9
)

## Slide 10
ILD SiD
Precision vertex detectors
CMOS MAPs, FPCCD, DEPFET 3D, chronopixel,DEPFET, MAPs
Tracker
TPC (GEM,MMEGAS,MAPs) Silicon
many measurement points Few points but very precise
Calorimeters
ECAL: Si-W, Sc-W ECAL: Si-W
AHCAL: Sc-Steel, SDHCAL-GRPC,.. DHCAL-GRPC
Size&Magnet
Large size, 3.5 Tesla Compact, 5 tesla

## Slide 11
Technologies proposed for ILD&SiD calorimeters
ECAL for SiD
X-talk to be reduced by better shielding
New scheme to have rectangular sensor (modified cells on the edge)
Mechanical structure study needed
1024 KPiX ASIC
Power-pulsed
TB scheme : 9 layers SiW
3-electron event

## Slide 12
Technologies proposed for ILD&SiD calorimeters
HCAL for SiD
40 layers of 2 cm stainless steel interleaved with
planes made of Glass RPC and their embedded readout 1-bit electronics allowing a lateral segmentation of 1 cm2
An advanced physical (embedded electronics) prototype of 54 was built and successfully run.
Other options with GEM and micromegas detectors are also proposed as active layers for the SiD HCAL
Several layers of mm were built and tested using 2-bit readout electronics. Few GEM planes are also in preparation.
Scintillator tiles is an option.
Dual readout is also an option for both ECAL&HCAL
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation

## Slide 13
Technologies proposed for ILD&SiD calorimeters
ECAL for ILD
30 layers of tungsten (24X0) interleaved with
-Pixellated Silicon of 5x5 mm2,
A physics prototype (1x1 mm2 cell size) with a deported electronics was built and successfully tested.
A technological prototype fulfilling the ILD DBD requirement is being developed :
Self-supporting structure (alveolar)
Embedded power-pulsed electronics
Large surface detector
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
Energy resolution =
16.5/sqrt(E)+1.1%
Linearity <1%
Several TB took place at DESY

## Slide 14
Technologies proposed for ILD&SiD calorimeters
ECAL for ILD
30 layers of tungsten (24X0) interleaved with
of 5x45 mm2 scintillator strip with alternating direction
layers (X&Y)  equivalent of 5x5 mm2 (SSA)
Read out by SiPM
A physics prototype with a deported electronics was built and successfully tested
A technological prototype is being developed with
Scintillator shape that optimizes light collection and reduces dead zones : rectangular, wedge, tapered..
SiPM more compact with higher linearity range
and less noise (MPPC 10000 ch in 1x1mm2)
Electronic board to host ASIC on one side
and scintillator plane on the other.
A first plane with the new technology was tested
in 2014.
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
Linearity <1.5%
Energy resolution
12.8%/E ⊕ 1.0%

## Slide 15
Technologies proposed for ILD&SiD calorimeters
HCAL for ILD
48 layers of 2 cm stainless steel interleaved with
planes made of 3x3 cm2 tiles, read out directly by SiPM
and embedded electronics.
A physical prototype of 38 layers of 1 m2, totalizing
(5.3 lI) accompanied by a tail catcher (6 lI) with
deported electronics was built and successfully tested
A technological prototype fulfilling the ILD requirements is being developed :
Optimized tile shape for direct readout
Embedded, power-pulsed readout electronics
Large plane with tiles assembled in a way to reduce
dead zones
Self-supporting mechanical structure
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
Several planes of different sizes were made and successfully tested in 2014

## Slide 16
Technologies proposed for ILD&SiD calorimeters
HCAL for ILD
48 layers of 2 cm stainless steel interleaved with
planes made of Glass RPC and their embedded readout 2-bit electronics allowing a lateral segmentation of 1 cm2
A technological prototype of 48 fulfilling almost all the ILD requirements of compactness and power consumption was built with a self-supporting mechanical structure. It ws successfully tested with
Triggerless mode
Power-pulsing mode
Last step is to build very large GRPC and equip them with the last generation of the readout electronics
The GRPC was also successfully tested in a magnetic field of 3 T using the power-pulsing mode
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation

## Slide 17
Technologies proposed for ILD&SiD forward calorimeters
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
LumiCal: Precise luminosity measurement (10-3) at 500 GeV.
BeamCal : Instantaneous luminosity measurement, beam diagnostics
but very high radiation load (up to 1MGy/ year)
LHCaL: Extends the calorimeter measurements to small polar angles
LumiCal (31 -77 mrad)
Two Si-W sandwich EM calo at ~ 2.5 m from the IP (both sides).
30 tungsten disks of 3.5 mm thickness. Si sensor pitch of 1.8 mm
Two tracking layers in front are envisaged to improve angle
measurement and separate e/g.
BeamCal (5 – 40 mrad)
similar W-absorber as for the LumiCal but radiation hard sensors
(GaAs, CV Diamond, Sapphire, Si).
Segmentation is being worked out,
new ideas on the sensor orientation

## Slide 18
Technologies proposed for ILD&SiD forward calorimeters
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
non-linearity<1%
Ebeam
electron data (2006)
MOKKA (geant4) simulation
LumiCal chip in 130 nm.
● 8 channel (preamp, shaper Tpeak ~ 60 ns,~9 mW channel);
● 8 channel pipeline ADC, ~1.2 mW/MHz;
● FPGA based data concentrator and further readout.
4 layers are realized and tested in TB
Mechanical structure studied and prototyped
BeamCal
Choice of the sensor will depend on the T-506 studies at SLAC
BeamCal is sensitive above 50 GeV. At 50 GeV the fake rate due to beamshtrahlung is 0.5% for R>7 cm,
energy resolution = 10%, at 200, 4% at 500
GeV 4%

## Slide 19
For ILC the high-granularity calorimeters concept is possible thanks to the power-pulsing mode. This mode allows a reduction of power consumption of a factor of 100-200. Cooling is still needed but is limited to the outer surface.
For FCCee and similar accelerators (CEPC) the power-pulsing is not possible
and one should extract the heat produced by the embedded electronics in
efficient way.
Some studies have been initiated in the case of SDHCAL and SiW ECAL.
From ILC to FCCee

## Slide 20: Example1: ILD SDHCAL
1 m
Max ~3.0m
Chambers are 91.6 cm in width, maximum length 290 cm
Embedded front-end Hardroc electronics cover the whole area
Active cooling essential if no power-pulsing : 70 106 channels
Power of each channel : 1 mW

## Slide 21
12 x 12 matrix for SDHCAL prototype → 144 Hardroc / m2
For longest chambers in ILD design: 1m x 3m → 432 hardroc
Power (no power-pulsing): ~10 W / m2 (1 mW/chan, 64 chans / Hardroc)
ILD-SDHCAL : 70 kW
SDHCAL technological prototype
6mm(active ara) + 5mm(steel) =
11 mm thickness
144 ASICs= 9216 channels/1m2

## Slide 22
 ‘In-chamber’ routing
  -Attempt to make thermal contact between cooling pipes and all Hardrocs (not easy)
  -Embed pipes in cassette cover (cover thickness 2mm: very small pipe diameters)
 ‘In-absorber’ routing
  -Embed pipes in absorber
  -Convective heat transfer in air gaps between Hardrocs and cassette, and cassette and
  absorbers
  -Larger pipe diameters possible
  -Caveat: degradation of physics performance as diameters increase!
 Outside edge of absorber (between HCAL and cryostat) or full circumference of absorber
  -As for ‘in-absorber’ routing, but much longer heat transfer paths through absorber to cooling
  pipe.
Active cooling scenarios

## Slide 23: In-chamber’ cooling: possible pipe configurations
In
In
Out
Out
Longest pipe ~3m
Disadvantage: many joints/welds
Length ~36m
Disadvantage: high Δp
x12
x12
3m
1m

## Slide 24: Pressure drops for water and 2-phase CO2
Heat capacity: 4.18 J/g/K
Kinematic viscosity: 1.0 * 10-6 m2/s
Assume ΔT of 2°C
Then needed mass flow = 11 kg/hr
ΔP for 1 mm pipe ~175 bar
For L = 3m, ΔP = 15 bar
Global assumptions:
Pipe length = 36 m (single pipe option)
Power to evacuate = 30 W
Heat of evaporation: 574 J/g
Kinematic viscosity: 0.1 * 10-6 m2/s
Needed mass flow = 0.25 kg/hr
ΔP for 1 mm pipe ~0.2 bar*
*Friedel method
Water (single phase)
CO2 (two phase)
Conclude: single pipe OK for CO2, water needs parallel pipes

## Slide 25: Two-phase CO2 cooling
2-Phase Accumulator Controlled Loop (2PACL)
(NIKHEF)
‘Accumulator’

## Slide 26: CO2 cooling - Background in HEP
Attractions:
  -High latent heat (low flow) + low viscosity → Small Δp
  -Small Δp → small pipe sizes
  -Small pipe sizes → low mass
  -High heat transfer coefficient
  -Radiation hard
  -Low global warming potential
Disadvantage: High pressures (60 bar at room temp), components expensive
Running systems:
  -AMS tracker (150 W)
  -LHC-b VELO vertex detector (2x 750W)
  -CMS pixel Phase 1 upgrade (2x 15 kW, system fully tested)
Proposed for: CMS and ATLAS silicon trackers

## Slide 27: 1 kW Test system at IPN-Lyon
Accumulator
Pump
HEX
Developed for CMS Phase-2 TK testing
Operation at -30°C
Could also operate at, say, 20°C
→ Test-bed for SDHCAL system?
-30
-40
~2.5 hours
(Pipe diam. 1.4 mm)
T spread from Δp along 5.5 m pipe

## Slide 28
Example2: ILD Si-W ECAL

## Slide 29
Average surface of one active layer 1.5 m2, pixels of 0.5x0.5 cm2
SKYROC ASIC is used (64 channels)
Power : 10 mW/ch if no power-pulsing
For one layer 60000 x 10 mW = 600 W
ILD-SiW ECAL 1400 kW

## Slide 30: Géométrie
Cooling Tube
PCB
Silicon
Chip
100µm Epoxy
H composite
Tungsten
Two-Phase CO2 cooling for Si-W ECAL active layer

## Slide 31
Ideal case:
By requiring a temperature of 20°c at in the heat exchanger tube, the temperature map of one active layer shows that variation is 2°c
A demonstrator for the HGCAL is being built to confirm the simulation results.

## Slide 32
Rate &Timing
Time information could be a big asset for FCCee calorimeters when contamination by delayed neutron and pile-up become an issue.
Some ILC calorimeters like SDHCAL could achieve excellent time resolution by replacing single gap RPC by multigap RPC to reach resolution better than 100 ps. Their rate capability could also be enhanced using new low-resistivity material (rate capability of 100 kHz/cm2). Calorimeters become not only trackers but also TOF.
FCCee groups interested to work on these topics are welcome to join the efforts initiated by IPN-Lyon and recently joined by GWNU.

## Slide 33
Conclusion
ILC Calorimeters are PFA-based detectors that could be used in other projects (CLIC, FCCee, CEPC,…).
Technical issues related to power consumption and consequently heating and cooling problems are being addressed. Demonstrators are to be built soon.
Timing in FCCee calorimeters could be an asset that needs to be carefully investigated.
Collaboration on e+ e- is always welcome.

## Slide 34
ILD PFA performance