## Slide 1: A novel technique at the leading Penning trap mass spectrometer ISOLTRAP
Andree Welker
28.10.2015
8th Gentner Day

## Slide 2: Outline
Motivation
Setup
Overview of ISOLDE
ISOLTRAP-Tools:
    Multi Reflection Time-of-Flight Separator/Spectrometer (MR-ToF)
  Precision Penning-Traps
New technique
Phase Imaging-Ion Cyclotron Resonance Technique (PI-ICR)
First results
Conclusion
1
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 3
ISOLTRAP@ISOLDE@CERN
2
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 4
ISOLTRAP@ISOLDE@CERN
2
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 5
ISOLTRAP@ISOLDE@CERN
ISOLTRAP
1.4-GeV protons
from PSB
Radioactive beams
HRS
GPS
3
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 6
Nuclides
4
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
K.Blaum

## Slide 7
Table of Nuclides
Nucleonica.net
4
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 8
Masses help to understand:
Table of Nuclides
Crab Nebula
Our Sun
Evolution of Universe
Shell structure of Nuclides
Possible Neutrino masses
CKM matrix element calculation
5
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
Nucleonica.net
sdo.gsfc.nasa.gov

## Slide 9
1987
1994
1999
2010
M. Mukherjee et al., Eur. Phys. J. A 35, 1 (2008), S. Kreim et al., Nucl. Instrum. Methods B 317, 492 (2013).
ISOLTRAP@ISOLDE@CERN
6
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 10
F. Herfurth et al., NIM A 469, 254 (2001).
R. N. Wolf et al., Int. J. Mass Spectrom 313, 8 (2012).
G. Savard et al., Phys. Lett. A 158, 247 (1991).
M. König et al., Int. J. Mass Spectrom. 142, 95 (1995).
Tools of ISOLTRAP
7
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 11
F. Herfurth et al., NIM A 469, 254 (2001).
R. N. Wolf et al., Int. J. Mass Spectrom 313, 8 (2012).
G. Savard et al., Phys. Lett. A 158, 247 (1991).
M. König et al., Int. J. Mass Spectrom. 142, 95 (1995).
Tools of ISOLTRAP: MR-ToF
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
8

## Slide 12
F. Herfurth et al., NIM A 469, 254 (2001).
R. N. Wolf et al., Int. J. Mass Spectrom 313, 8 (2012).
G. Savard et al., Phys. Lett. A 158, 247 (1991).
M. König et al., Int. J. Mass Spectrom. 142, 95 (1995).
Tools of ISOLTRAP
9
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 13
Eigen motions:
2,5 cm
Three harmonic oszillators:
+ : Magnetron frequency
- : Modified Cyclotron
z : Axial frequency
B
Tools of ISOLTRAP: Penning trap
z
y
x
Penning trap: Storage of ions by the superposition
of electric and magnetic fields
Hyperbolic
Penning trap
10
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 14
F. Herfurth et al., NIM A 469, 254 (2001).
R. N. Wolf et al., Int. J. Mass Spectrom 313, 8 (2012).
G. Savard et al., Phys. Lett. A 158, 247 (1991).
M. König et al., Int. J. Mass Spectrom. 142, 95 (1995).
Tools of ISOLTRAP: Penning trap
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
11
First ToF-ICR of 130Cd+

## Slide 15
R. Wolf et al. IJMS 349-350 (2013) 123-133
S. Eliseev et al. Appl. Phys. B, 13 (2013)
20
50
Limits of different ICR techniques
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
12

## Slide 16: Position sensitive detector
Active diameter | 42 mm
Channel diameter | 25 mm
Open area ratio | >50 %
Position resolution | 70 mm
Max. B-field | a few mT
Time resolution | ~ 10 ns
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
13
Mounted on top of ISOLTRAP

## Slide 17: Position sensitive detector
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
14
X1
X2
Y1
Y2
Side view:
Back view (Delay lines):
MCP
Ion

## Slide 18: Position sensitive detector
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
14
Signal answer of the detector and the delay lines
X1
X2
Y1
Y2
Side view:
Back view (Delay lines):
MCP
Ion

## Slide 19
Phase Clock:
.
Need some “raw assumption”
of the mass
2 ions are enough
to determine a mass
No. of detected ions
Only a small effort of information is needed:
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
15
Phase Imaging- ICR (PI-ICR)

## Slide 20: Phase Imaging- ICR (PI-ICR)
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
16
Projecting:
B
- Ions follow the magnetic
field lines
- Hit the detector
afterwards
B

## Slide 21: Phase Imaging- ICR (PI-ICR)
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
16
Projecting:
B
- Ions follow the magnetic
field lines
- Hit the detector
afterwards
B

## Slide 22: Phase Imaging- ICR (PI-ICR)
B
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
16
Projecting:
- Ions follow the magnetic
field lines
- Hit the detector
afterwards
B

## Slide 23
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
17
Phase Imaging- ICR (PI-ICR)
129In
129Cd
g: T1/2 = 242 ms
m: T1/2 = 104 ms
11/2-
3/2+
β-
β-
m: isomer
g: ground state
Unseparable with ToF-ICR
Example of the limit of ToF-ICR:

## Slide 24
Resolving differences in ToF-ICR and PI-ICR:
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
18
Unseparable with ToF-ICR
Phase Imaging- ICR (PI-ICR)
Easy separable with PI-ICR

## Slide 25: First results: Beam time
First use in a beam time to suppress the background noise low ion yields:
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
19
New detector makes the 34Al beam time possible:
  5 ions/h and 5 ions/h dark counts
Position [mm]
ToF [us]
Position [mm]
Frequency [Hz]

## Slide 26: First results: Beam time
First use in a beam time to suppress the background noise low ion yields:
19
New detector makes the 34Al beam time possible:
  5 ions/h and 5 ions/h dark counts
Position [mm]
ToF [us]
Position [mm]
Frequency [Hz]
Position [mm]
Position [mm]
ToF [us]
Frequency [Hz]
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 27: First results: Beam time
First use in a beam time to suppress the background noise low ion yields:
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
20
New detector makes the 34Al beam time possible:
  5 ions/h and 5 ions/h dark counts

## Slide 28: First result: PI-ICR
First result of an image:
After some effort, we have good starting conditions, but still a long way to go.
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
21

## Slide 29: Summary
Setup:
Presented the ISOLTRAP setup and possibilities.
Technical part:
Compared the main different image cyclotron resonance techniques.
Showed some interesting physic cases which will be accessible for the first time with the PI-ICR technique.
Outlook:
The setup and the position sensitive detector will be configured, that we might be to use the new technique in the beginning of 2016.
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
22

## Slide 30: Acknowledgements
N. Althubiti, P. Ascher, G. Audi, D. Atanasov, D. Beck, K. Blaum, G. Bollen, Ch. Borgmann, M. Breitenfeldt, R. B. Cakirli, T. Cocolios, S. Eliseev, T. Eronen, S. George, F. Herfurth, A. Herlert, D. Kisler, M. Kowalska, S. Kreim, J. Kluge, Yu. A. Litvinov, D. Lunney, V. Manea, E. Minaya-Ramirez, M. Mougeot, S. Naimi, D. Neidherr, M. Rosenbusch, A. de Roubin, L. Schweikhard, F. Wienholtz, M. Wang, A. Welker, R. Wolf, K. Zuber, S. Schwarz
ISOLDE Target
and Technical Group
Grants No.:
05P12HGCI1
05P12HGFNE
http://isoltrap.web.cern.ch
Thank you very much for your attention

## Slide 31
Backup

## Slide 32
Applied filters:
André Welker for ISOLTRAP, EuNPC 2015, Groningen, 31.08.2015
2
Table of Nuclides

## Slide 33
Rb
Sr
Cr
3
André Welker for ISOLTRAP, EuNPC 2015, Groningen, 31.08.2015
Why neutron-rich nuclides?

## Slide 34
Beam purification:
200-300 ms trapping
for m/Δm =104-105
Beam purification:
1 s trapping for
m/Δm =105-106
Measurement of cyclotron frequency:
100 ms – 1 s trapping for σm/m = 10-6-10-8
Beam purification:
30 ms trapping
for m/Δm = 105
F. Herfurth et al., NIM A 469, 254 (2001).
R. N. Wolf et al., Int. J. Mass Spectrom 313, 8 (2012).
G. Savard et al., Phys. Lett. A 158, 247 (1991).
M. König et al., Int. J. Mass Spectrom. 142, 95 (1995).
Tools of ISOLTRAP
6
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015

## Slide 35
Mass determination:
relative precision better than 10-6
Result: mass of 54Ca
mass
separator
2
André Welker for ISOLTRAP, EuNPC 2015, Groningen, 31.08.2015
mass
spectrometer
Wollnik & Przewloka, Int. J. Mass Spectrom. Ion Proc. 96, 267 (1990)
Wolf et al., IJMS 349-350, 123 (2013)
Wienholtz et al., Nature 498, 346-349 (2013)
Contamination suppression (with BNG):
mass resolving power
fast separation
Result: mass of 82Zn
The MR-ToF MS

## Slide 36
F. Herfurth et al., NIM A 469, 254 (2001).
R. N. Wolf et al., Int. J. Mass Spectrom 313, 8 (2012).
G. Savard et al., Phys. Lett. A 158, 247 (1991).
M. König et al., Int. J. Mass Spectrom. 142, 95 (1995).
Tools of ISOLTRAP: MR-ToF
7
Andree Welker, 8th Gentner Day 2015, CERN, 28.10.2015
102Sr,102Rb measurement
Hints for nucleus deformation,
impact in theory

## Slide 37
Beam purification:
200-300 ms trapping
for m/Δm =104-105
Beam purification:
1 s trapping for
m/Δm =105-106
Measurement of cyclotron frequency:
100 ms – 1 s trapping for σm/m = 10-6-10-8
Beam purification:
30 ms trapping
for m/Δm = 105
F. Herfurth et al., NIM A 469, 254 (2001).
R. N. Wolf et al., Int. J. Mass Spectrom 313, 8 (2012).
G. Savard et al., Phys. Lett. A 158, 247 (1991).
M. König et al., Int. J. Mass Spectrom. 142, 95 (1995).
2
André Welker for ISOLTRAP, EuNPC 2015, Groningen, 31.08.2015
First ToF-ICR of 2014
Tools of ISOLTRAP

## Slide 38
1987
1994
1999
2010
ISOLTRAP@ISOLDE@CERN
M. Mukherjee et al., Eur. Phys. J. A 35, 1 (2008).
S. Kreim et al., Nucl. Instrum. Methods B 317, 492 (2013).

## Slide 39
1987
1994
1999
2010
ISOLTRAP@ISOLDE@CERN
!
2013

## Slide 40
Motions:
16
Hyperbolic
Penning-Trap
2,5 cm
Three eigenmotions:
- : Modified Cyclotron/
+ : Magnetron frequency
z : Axial frequency
Penning-Trap
K. Blaum
André Welker, Group Meeting, IKTP Dresden, Oct. 25, 2014
B

## Slide 41: Penning-Trap
Function:
16
Hyperbolic
Penning-Trap
2,5 cm
K. Blaum
André Welker, Group Meeting, IKTP Dresden, Oct. 25, 2014

## Slide 42
Motions:
16
Hyperbolic
Penning-Trap
2,5 cm
Three eigenmotions:
- : Modified Cyclotron/
+ : Magnetron frequency
z : Axial frequency
Penning-Trap
K. Blaum
André Welker, Group Meeting, IKTP Dresden, Oct. 25, 2014

## Slide 43
Motions:
16
Hyperbolic
Penning-Trap
2,5 cm
Three eigenmotions:
- : Modified Cyclotron/
+ : Magnetron frequency
z : Axial frequency
Penning-Trap
K. Blaum
André Welker, Group Meeting, IKTP Dresden, Oct. 25, 2014
B

## Slide 44
Motions:
17
Penning-Trap
André Welker, Group Meeting, IKTP Dresden, Oct. 25, 2014
With cooling gas in trap
-
+
-
+
-
-
+
+

## Slide 45
Motions:
18
Penning-Trap
André Welker, Group Meeting, IKTP Dresden, Oct. 25, 2014
Without cooling gas in trap
-
+
-
+
-
-
+
+

## Slide 46
Motions conversion:
18
Penning-Trap

## Slide 47
129Cd, 130Cd – Mass measurement
≈6300 ions/s from ISOLDE; 1539 ions
4 ToF-ICR resonances
  1 normal, 3 Ramsey
 Δm/m≈1.2E-7
≈625 ions/s from ISOLDE; 588ions
130Cd/cont. ≈ 0.2; only R ≈ 15k needed
3 ToF-ICR resonances
  1 normal, 2 Ramsey
Δm/m≈1.6E-7
129Cd Ramsey-type resonance
20ms – 160ms – 20ms
130Cd Ramsey-type resonance
10ms – 80ms – 10ms
129Cd, T1/2=242(8)ms
130Cd, T1/2=162(7)ms
Frank Wienholtz NUSTAR 2015