IPv6 Hands-on
pre-GDB IPv6 workshop
7th of June 2016
edoardo.martelli@cern.ch

---
Set up IPv6 connectivity
on your client

---
IPv6 at CERN
CERN uses DHCPv6
MAC addresses must be registered to get a lease
RAs (Router Advertisements) only used for default gateway and prefix length

---
MS Windows

---
MS Windows 7
DHCPv6 on by default
Issue:
DHCPv6 requests may be sent with the MAC address of another interface
Solution:
Register all the MAC addresses

---
MS Windows 8.x, 10
DHCPv6 on by default
Issue:
DHCPv6 requests may be sent with a DUID not containing the MAC address
Solution:
See next page

---
Set up DUID in Windows
- Open the Registry Editor
- Navigate to HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\services\TCPIP6\Parameters
- Right click and edit the entry named Dhcpv6DUID
- Write a DUID based on Link-layer Address Plus Time (DUID-LLT) where the last 6 digits contain the MAC address of the connected interface. For example if the MAC address is b4:b5:4d:83:03:19, then write 00-01-00-01-57-57-57-57-b4-b5-4d-83-03-19 (the first 4 pairs of digits should be 00-01-00-01, the second group of four pairs of digits is a date)
- Save and reboot the computer (rebooting is mandatory, renewing the DHCP lease is not sufficent)

---
MS Windows Vista
DHCPv6 off by default
Get the interface number:
  netsh int ipv6 show int
Disable Router Discovery:
   netsh int ipv6 set int [index] routerdiscovery=disabled
Enable Managed Address:
  netsh int ipv6 set int [index] managedaddress=enabled
After enabling Managed Address, you may need to run the following commands to delete the existing IP address and renew the DHCP assigned IPv6 address:
netsh int ipv6 delete address [index] <static IPv6 address>
ipconfig /renew6 [index]
Disclaimer: not verified

---
MS Windows XP
No DHCPv6 client
In case of SLAAC, IPv6 needs to be enabled manually:
1. Open Network Connections
2. Right-click any local area connection, and then click Properties.
3. Click Install.
4. In the Select Network Component Type dialog box, click Protocol, and then click Add.
5. In the Select Network Protocol dialog box, click Microsoft TCP/IP version 6, and then click OK.
6. Click Close to save changes to your network connection.

---
MS Windows 7: check settings

---
MS Windows 7: check routing

---
Windows: terminal commands
Check interface configuration:
ipconfig
Check routing table:
netstat -rn
netsh interface ipv6 show route
Manual configuration
Address:
netsh interface ipv6 add address "Local Area Connection" 2001:1458:201:1::C
Default gateway:
netsh interface ipv6 add route ::/0 "Local Area Connection" 2001:1458:201:1::1
DNS servers:
netsh interface ipv6 add dnsserver "Local Area Connection" 2001:1458:201:1000::5

---
Apple MacOS

---
MacOS: enable IPv6
Enable IPv6 in System Preference, Network, Advanced:

---
MacOS X: command line
mac$ ifconfig
en1: flags=8863<UP,BROADCAST,SMART,RUNNING,SIMPLEX,MULTICAST> mtu 1500
ether e4:ce:8f:0a:66:08
inet6 fe80::e6ce:8fff:fe0a:6608%en1 prefixlen 64 scopeid 0x5
inet 128.141.237.155 netmask 0xffffff00 broadcast 128.141.237.255
inet6 2001:1458:202:180::101:3602 prefixlen 64
nd6 options=1<PERFORMNUD>
media: autoselect
status: active
mac$ netstat -rn
$ netstat -rn
[...]
Internet6:
Destination Gateway Flags Netif
default fe80::215:60ff:feed:ce00%en1 UGc en1
::1 ::1 UHL lo0
2001:1458:202:180::/64 link#5 UC en1
2001:1458:202:180::1 a:0:30:b0:78:1 UHLWI en1
2001:1458:202:180::101:3602 e4:ce:8f:a:66:8 UHL lo0
fd01:1458:201:127d::/64 link#5 UC en1

---
Linux

---
Linux: enable IPv6
- SLC5: IPv6 may be disable. Edit the file /etc/modprobe.conf and remove the lines disabling ipv6 (#alias ipv6 off, #options ipv6 disable=1); then reboot
- Others: on by default

---
Linux: useful commands
marit> ifconfig
eth0 Link encap:Ethernet HWaddr 00:22:4d:83:03:19
        inet addr:137.138.32.137 Bcast:137.138.32.191 Mask:255.255.255.192
        inet6 addr: fe80::222:4dff:fe83:319/64 Scope:Link
        inet6 addr: 2001:1458:201:b459::100:a/128 Scope:Global
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
marit> ip -6 route
2001:1458:201:b459::100:a dev eth0 proto kernel metric 256
2001:1458:201:b459::/64 dev eth0 proto kernel metric 256
fd01:1458:204:1a::/64 dev eth0 proto kernel metric 256
fe80::/64 dev eth0 proto kernel metric 256
default via fe80::215:60ff:feed:ce00 dev eth0 proto ra metric 1024

---
Linux: useful commands
Static configuration:
ip -6 addr flush scope global dev eth0
ip addr add FEC0::1:0:0:0:21/64 dev eth0
ip route add 0::/0 via 2001:1458:ef10::56
NDP
ip -6 neighbor
Delete a neighbor entry:
ip -6 neighbor delete 2001:1458:201:b459::1 dev eth0
Trigger neighbor discovery:
ping6 -c2 -I eth0 ff02::1
Solicit RAs:
rdisc6 eth0
Disable SLAAC address, but keeps RAs info:
sysctl -w net.ipv6.conf.all.autoconf=0

---
iOS and Android

---
Mobiles
iOS
v6: no DHCPv6 client, SLAAC OK
v7 and following : DHCPv6 on by default, SLAAC OK
Android
v6.x: no DHCPv6 client yet, only SLAAC

---
Final checks

---
Check IPv6: http://ipv6-test.com

---
Check IPv6: http://test-ipv6.com

---
Questions?
edoardo.martelli@cern.ch