Muon Cooling for a Neutrino Factory and Muon Collider
Step IV Physics Paper Readiness
C. T. Rogers
ASTeC Intense Beams Group
Rutherford Appleton Laboratory

---
Step IV Papers
- For quick release (these are papers):
  - Description of MICE Step IV
  - First observation transverse emittance reduction
- Slower boil, worthy of a publication, maybe not one per bullet
  - Diagnostics
    - Global track fitting
  - Magnetics
    - Measurement of optical emittance growth and non-linearities
    - Direct measurement of the transfer map including higher order terms
  - Absorber
    - Energy loss
    - Multiple scattering
    - Angular momentum
    - Beam (de)polarisation
    - Wedge
  - “Cooling Channel”
    - (Long, probably following end of Step IV with all results in) Observation of transverse emittance reduction
    - Emittance exchange with wedge

---
Step IV Papers
- For quick release (these are papers):
  - Description of MICE Step IV
  - First observation transverse emittance reduction
- Slower boil, worthy of a publication, maybe not one per bullet
  - Diagnostics
    - Global track fitting
  - Magnetics
    - Measurement of optical emittance growth and non-linearities
    - Direct measurement of the transfer map including higher order terms
  - Absorber
    - Energy loss
    - Multiple scattering
    - Angular momentum
    - Beam (de)polarisation
    - Wedge
  - “Cooling Channel”
    - (Long, probably following end of Step IV with all results in) Observation of transverse emittance reduction
    - Emittance exchange with wedge

---
Description of MICE Step IV
- Detectors and Diagnostics
  - Reconstruction efficiencies
  - Reconstruction residuals – u/s versus d/s
  - Validation of Particle ID routines
- Description of incoming beam/beamline
  - Match through diffuser to tracker
  - Beam impurity
- Description of magnets
  - Magnet mapping
  - Beam-based alignment
- Cooling channel optics
  - Measurement of beam upstream and downstream

---
First Observation of Emittance Reduction
- Measurements all with LiH
  - Dependence on optical beta function
  - Dependence on momentum
  - Dependence on emittance
  - Change in particle amplitude
- Basic analysis
  - Beam selection
  - Errors – pid
  - Errors – phase space vector
- Data taking
  - Real run settings
  - Analysis tools
- To Do List

---
Reminder of Terms - 2D
px
σ(px)
ɛγ
σ(x)
Area ɛ
“emittance”
ɛβ
Area A “amplitude”
x
Muon with (x, px) = u

---
Basis for run settings
Aim is to explore the “emittance reduction” formula
  - Dependence on optical beta βᚆ
  - Dependence on energy - Eμ and β
  - Dependence on input emittance εn
  - (Dependence on material - LR and dEμ/ds)
- Plan to:
  - Scan about the centre on each variable with ~ 10 points
  - Large statistics run at center of parameter space
  - Check corners of the parameter space
- Consider accessible phase space as:
  - 140 MeV/c < P < 240 MeV/c
  - ε < 10 mm; difficult to get below ~ 3-4 mm (but we should try)
  - Β < 1000-2000 mm; difficult to get below ~ 200 mm

---
Measurements - Beta function scan
Flip Mode
β at the absorber
εn = 6 mm
P = 200 MeV/c
Linear model
- At 200 MeV/c – wide range of available optics
  - Smallest βᚆ 218 mm (flip mode)
  - Is it worth scanning with constant FC current?
- Tighter focussing is available at 140 MeV/c
  - dp/p is greater here
  - May find more cooling at 140 MeV/c

---
Measurements – Momentum scan
Focus Coil = 141 A
Flip Mode
β at the absorber
εn = 6 mm
β = 420 mm
Linear model
- At different momenta we get different cooling performance
  - Can we hold beta constant at different momenta?

---
Measurements – Dependence on Emittance
β = 420 mm
P = 200 MeV/c
Linear model
- Show dependence on emittance
- Find zero crossing “equilibrium emittance”
  - Tough for lower beta functions; the beamline cannot deliver

---
Measurements – Particle Amplitude
MICE Step VI
Errors are purely statistical
- Sit at a single optics and momentum
- Take data covering a large portion of phase space
- Calculate change in particle amplitudes over this phase space

---
Comment on “Corners”
- Seek to take good statistics in the “corners” of the parameter space
  - i.e. min/max emittance, momentum, beta
- This is useful for checking MC code
  - But I do not anticipate a massive MC exercise to be a part of this paper i.e. we report cooling performance with little comparison to MC
  - Comparison to MC comes later
- May be able to make some amplitude plots

---
Beam Weighting - Voronoi
- For each particle, find the region nearest to that particle
  - Nearest neighbour algorithms are well-known
  - I choose Voronoi algorithm, which is fast enough and accurate
- Calculate the volume ci of that region
  - Not quite straightforward in higher dimensions
- Calculate the desired pdf fi at that point
- Assign a statistical weight given by
  - wi = cifi

---
Beam Weighting - Moments
- Estimate the phase space density by calculating beam moments
- Weight using a polynomial f(u) in phase space vector coordinates u
  - wi = f(ui)
  - Linear relationship exists between input moments, output moments and polynomial coefficients for the weighting
- Issue:
  - Weights can be positive and negative
- To do:
  - Find a set of basis functions that are always positive
Old beamline simulation
“Ideal” beam
Weighted beam
MICE Step VI
MICE Step VI

---
Error analysis – Phase Space
- Beam RMS ellipse can be deduced from
  - Vmeasured = Vtrue + C + R + RT
  - V is the matrix that describes the beam ellipse
  - C is the matrix that describes the errors
  - R is the matrix that describes correlations between the true phase space vectors and the errors
  - We know R is significant e.g. we know pz errors are large for small pt
- Questions:
  - Can we deduce the error matrices from the measured Kalman fit errors?
  - What is the effect of known misalignment on track fit? Can recon cope?

---
Error analysis – PID Speculation
- 4D emittance is related to particle amplitude by
  - ε = <A>/4
- Effect of mis-PID depends where in phase space the mis-identified particles are
  - Probably PID is worst at high amplitude
- Upstream
  - μ identified as e/π only effects sampling efficiency
  - π identified as μ - guess – look like larger upstream emittance
    - They will probably decay to π by downstream detectors
  - e identified as μ – guess – look like too much scraping
    - They will probably be identified correctly downstream
- Downstream
  - μ identified as e will look like too much scraping
  - e identified as μ will look like not enough scraping, larger downstream emittance
- To do:
  - Make this quantitative, rather than speculative

---
Data taking - settings
- Beamline settings
  - We have reasonable set of beamlines (J. Pasternak)
  - Further optimisation is in progress
- Cooling channel optics
  - Ideal settings shown above
  - PRY → Holger is developing non-linear scaling from ideal currents to real currents
    - Preliminary analysis indicates scalings are <= 5 %
  - Near to Virostek plates, a field map may be needed
  - Misalignments will need to be understood; may feed into run settings

---
Data taking – analysis tools
- Physics shifter tool
  - Physics shifter tool is now automatically checking for new data sets and performing checks every hour
  - Would like to fold in “online reconstruction” plots but run against the offline reconstructed data set
- Online analysis tool
  - An event display has been foreseen for many years with beam envelopes etc superimposed
  - Some prototype code exists but is not ready for deployment to MLCR

---
To Do List
- Determine run settings
  - Optics studies for basic magnet settings
  - Tracking studies for momentum acceptance
  - Tracking studies for dynamic aperture checks
  - Tracking studies for cooling performance
  - Fold in “real world“ effects – windows, iron, misalignments ...
- Improve online/offline “data quality” tools
- Get a better grasp on errors

---
Conclusions
DATA
- Physics goals have been outlined
- Status of Step IV analysis preparation has been discussed
- Plan for June/July has been presented
- Planning for subsequent runs discussed
- Plan for analysis group support of Step IV operations was described