## Slide 1
How does a synchrotron radiation source work?
Rolf Landua
CERN

## Slide 2
Main chapters of my talk
What is SESAME?
Production of synchrotron light
SESAME components
Synchrotron light spectrum for experiments
Later today:
SESAME - Status/Prospects (Chris Llewellyn-Smith)
CERN-SESAME parallels and differences (Herwig Schopper)

## Slide 3
What is SESAME?
Production of synchrotron light
SESAME components
Synchrotron light spectrum for experiments

## Slide 4
SESAME is an ‘electron synchrotron’
Very intense beams of X-rays*, infrared and UV light (billion times brighter than Sun)
Allows to study objects that are much smaller than 1 µm (~ cell size)
Energy = 2.5 GeV
Circumference = 133.2 m
Magnet strength = 1.455 T
Max. current = 400 mA (3·1012 e)

## Slide 5
http://www.sesame.org.jo/sesame/
Synchrotron Light for Experimental Science and Applications in the Middle East
A “CERN” in the Middle East

## Slide 6
Dead
Sea
SESAME on ‘Google Earth’

## Slide 7
SESAME on ‘Google Earth’

## Slide 8
SESAME building

## Slide 10
Chris Llewellyn-Smith
President SESAME council
Former CERN DG
Herwig Schopper
Former president SESAME council
Former CERN DG

## Slide 11
http://mag.digitalpc.co.uk/fvx/iop/esrf/sesamepeople/
SESAME people: who is already working there?

## Slide 12
Comparison of synchrotron light sources world-wide
SESAME

## Slide 13
What is SESAME?
Production of synchrotron light
SESAME components
Synchrotron light spectrum for experiments

## Slide 14
Synchrotron
Synchrotron light: artificial and natural sources
Crab nebula (neutron star)
Notes: Synchrotron radiation is the name given to the radiation which occurs when charged particles are accelerated in a curved path or orbit. Classically, any charged particle which moves in a curved path or is accelerated in a straight-line path will emit electromagnetic radiation. Various names are given to this radiation in different contexts. For example, when is occurs upon electron impact with a solid metal target.
The Crab pulsar is slowing at the rate of about 10-8 sec per day, and the corresponding energy loss agrees well with the energy needed to keep the nebula luminous. Some of this luminosity takes the form of synchrotron radiation, requiring a source of energy for accelerating charged particles.

## Slide 15
Two important concepts about electromagnetism
e-
+
-
Electric force on electron (with charge q) in the direction of
the electric field E
F = q · E (Coulomb force)
e-
N
S
Magnetic force on electron (with charge q) is perpendicular
to the direction of the magnetic field B
F = q · v · B (Lorentz force)
Electric fields increase kinetic energy
Magnetic field change the direction

## Slide 16
And what about accelerated charges ?
Whenever a charged particle accelerates it emits electromagnetic waves
Principle of radio station / antenna

## Slide 17
Electrons in a synchrotron emit radiation
SESAME: 𝛾 ~ 5000
Acceleration by magnetic dipole field

## Slide 18
How to increase synchrotron radiation intensity ?
Array of magnets
Lateral deflection of electrons
Broad and incoherent emission spectrum
Higher intensity and energy than
inside a bending magnet
Wiggler

## Slide 19
Undulator
Less powerful magnets —> gentler undulations
Match transverse motion to transit speed:
      constructive interference !
Frequency tuneable (alter gap between magnets)
Narrow and coherent emission spectrum

## Slide 20
Overview: Dipole magnet, Wiggler, Undulator

## Slide 21
What is SESAME?
Production of synchrotron light
SESAME components
Synchrotron light spectrum for experiments

## Slide 22
Schematic overview of a Synchrotron Radiation Source

## Slide 23
Environmental science
Archeology
Physics
Bio-medical
Material science
Layout of the SESAME complex
Microtron
Booster
Storage Ring

## Slide 24
Electrons are generated in an electron gun (like cathode ray tubes in old TVs)
Main steps of SESAME
Acceleration in three steps:
Microtron (= linear accelerator, up to 22 MeV)
Booster synchrotron (22 - 800 MeV)
Storage ring (800 - 2500 MeV)
t
Energy
22 MeV
800 MeV
2500 MeV
Booster
SESAME Storage Ring
Microtron

## Slide 25
Overview: Synchrotron light source animation

## Slide 26
Step 1a - electron gun

## Slide 27
Step 1b : the Microtron (up to 22 MeV)
linear accelerator
Bending magnet
Bending magnet

## Slide 28
Step 2 : the Booster (up to 800 MeV)
Booster = BESSY I 0.8 GeV synchrotron
decommissioned at BESSY, Berlin, Germany in 1999
donated to the SESAME project

## Slide 29
Step 2 : the Booster (up to 800 MeV)
Mr. Salameh, Mayor of Salt City, Jordan, and Herman Winick (SLAC)

## Slide 30
Step 3 : the Storage Ring (up to 2500 MeV)
16 Dipole magnets (CERN)
CESSAMAG project: European Union grant €5 million
CERN supplies magnetic system allowing for the completion of the main ring
CERN is the main contractor, coordinates the delivery of the magnet system.
+ 64 quadrupole magnets
+ 64 sextupole magnets

## Slide 31
Other important components
RF cavities
(compensate for lost energy)
Vacuum pumps
(no scattering)

## Slide 32
What is SESAME?
Production of synchrotron light
SESAME components
Synchrotron light spectrum for experiments

## Slide 33
Animation: emission of synchrotron radiation

## Slide 34
Synchrotron light is very, very bright
x 1,000,000,000

## Slide 35
Brilliance (“concentration”) of SESAME light

## Slide 36
Synchrotron “light” covers a wide range of wavelengths
WIDE RANGE OF EXPERIMENTS:
Material science
Molecular biology
Archeology
Medicine
Environmental studies
AND MANY OTHERS

## Slide 37
Advantages of synchrotron light sources

## Slide 38
… incredibly detailed pictures

## Slide 39
(Talk by H. Abualrob)
World-class tool for many fields of science