## Slide 1: Energy calibration in FCC-ee based on polarization I. Koop, BINP, Novosibirsk
CERN, Geneva, 12.06.2015

## Slide 2: Outline
Energy calibration concept
Longitudinal Compton Backscattering Polarimeter
Free precession frequency measurement approach
Spin precession de-phasing rates
Spin tracking results for various FCC-ee beam parameters
Discussion
Conclusion

## Slide 3: Energy calibration concept
1. Production of polarized electrons from a laser photocathode.
2. Production of polarized positrons in a small energy damping ring
(1-2 GeV), with polarization time in the order of 10 min (wigglers).
3. Acceleration of polarized beams via linac, SPS (?) and finally in the
booster storage ring (100 km) using Siberian Snakes.
4. Injection of polarized bunches into the collider rings with the
horizontal spin orientation and measuring turn by turn free
precession frequency using the longitudinal Compton polarimeter.
5. Number of polarimeters should be large (4-12). Then one can
measure the spin precession phase advances per every arc. This
paves a way to validate the saw-tooth energy distribution model,
constructed on the full data set, such as RF-voltage/ RF-phases, plus
orbit data from BPMs, plus geodesy data, plus many other.

## Slide 4: Energy calibration concept, cont.
Measuring the beam energy in several points (about 4-12), using
the magnetic spectrometer, based on Compton scattering of a
laser light on an electron beam (N. Muchnoi proposal).
Absolute calibration of such spectrometric system will be done by
measurement of the spin precession phases per arc segments.
Spin coherence time depends strongly on the value of
synchrotron modulation index: χ = σδν0/νs (ν0=γa). It should be
chosen not too large: acceptable is χ < 1.8 (νs ≈ 0.1-0.2 is
required). Examples will be shown at several slides.
9. Resonance depolarization is not excluded, but did not work near
integer resonances. In contrast, the free precession method works
everywhere!
10. Shall measure, suppress and account spin resonances in a broad
energy interval. Only after that can claim true energy value!

## Slide 6: Compton scattering of a laser light
Detection of the
scattered electrons
instead of photons
provides selection of
events with maximal
momentum loss!
Let’s utilize the
highest value of the
analysing power!
0.746

## Slide 7: Spin tracking oscillogram. 125 test-particles. E=45.5 GeV, σδ=0.0005, νs =0.15, τs =1320 turns
Loss of polarization degree due to de-phasing is small thanks to high enough νs.

## Slide 8: Spin precession spectrum. Number of turns 8192. E=45.5 GeV, ν0=103.25, σδ=0.0005, νs =0.15, χ=0.35
χ = σδν0/νs = 0.35 – synchrotron modulation index.

## Slide 9: Spin tracking oscillogram. 125 test-particles. E=45.5 GeV, σδ=0.0005, νs =0.035, τs =1320 turns

## Slide 10: Spin precession spectrum. Number of turns 8192. E=45.5 GeV, ν0=103.25, σδ=0.0005, νs =0.035, χ=1.48
We want: χ < 1.7. With χ > 1.7 peaks will disappear!

## Slide 11: Spin tracking oscillogram. 125 test-particles. E=80 GeV, σδ=0.001, νs =0.15, τs =243 turns

## Slide 12: Spin precession spectrum. Number of turns 8192. E=80 GeV, ν0=181.55, σδ=0.001, νs =0.15, χ=1.21

## Slide 13: Spin tracking oscillogram. 125 test-particles. E=80 GeV, σδ=0.001, νs =0.10, τs =243 turns
Fast de-phasing due to slow synchrotron motion!

## Slide 14: Spin precession spectrum. Number of turns 8192. E=80 GeV, ν0=181.55, σδ=0.001, νs =0.10, χ=1.82
Same results one gets with doubled both: energy spread and synchrotron tune.

## Slide 15: Spin tracking oscillogram. 125 test-particles. E=120 GeV, σδ=0.001, νs =0.20, τs =72 turns
Fast de-phasing! Synchrotron modulation index is too high: χ=1.36.

## Slide 16: Spin precession spectrum. Number of turns 8192. E=120 GeV, ν0=272.325, σδ=0.001, νs =0.20, χ=1.36
Same results one gets with scaled both: energy spread and synchrotron tune.

## Slide 17: Discussion
Spin dephasing rate is governed by the synchrotron
frequency modulation index χ. It should be low enough:
χ < 1.7 at least. Collision with the half-intensity bunch will
reduce σδ, may help? Special polarization runs with high νs,
to calibrate the Compton based spectrometers!?
VEPP-4 team performs just now the experiment “Pulsar” which, hope, will validate free spin precession technique.

## Slide 18: Conclusion
Free precession approach provides extremely fast
method of spin frequency measurement.
It is limited only by the energy spread averaging rate, provided by the synchrotron oscillations. This is expressed via synchrotron modulation index. It should not exceed a factor x < 1.7 or lower. This, in general, leads to choice of high synchrotron tunes.
FCCee-CW parameters do not satisfy this requirement: νs≈ 0.015-0.05. So, special calibration runs with high νs are needed from time to time, then calibrated Compton magnetic spectrometers shall continuously monitor beam energy during normal runs.

## Slide 19: Plans for future work
Incorporate into the ring the 900 spin rotator insertions for experiments with longitudinally polarized beams at Z-peak. Required additional space could be shared with RF.
Make numerical simulations of the saw-tooth energy model reconstruction code.
Develop/understand the acceleration chain for polarized beams.
Simulate tools for suppression of spin resonances.
Consider technical aspects of Compton polarimeter and Compton magnetic spectrometer. Combine them in one?
Think on resonance depolarization technique, as an alternative to free spin precession method.
There are more experts at BINP for these tasks! Polarization is our specialty since 70-th!