Calet in GEANT4 Electron benchmark Proton benchmark Conclusion
Implementation and
validation of CALET
flight model in
GEANT4 simulation
Presentation by
Lorenzo Pacini
25/06/2015
Title

---
Calet in GEANT4 Electrons benchmark Protons benchmark Conclusion
CALET - Technical Int. Meeting
June 25 2015 - Pisa, Italy
Contents
Calet flight model in GEANT4
Benchmarks with electrons
Benchmarks with protons
Conclusion
Contents

---
Calet flight model in
 GEANT4
Lorenzo Pacini
Nicola Mori
Calet in GEANT4

---
We developed the Calet flight model in GEANT4
Shape and size of the supporting structures have been extracted from Epics config. files and replicated in details in the Geant4 geometry description.
Some simplifications have been introduced (e.g.: honeycomb) as we did with FLUKA:
1) honeycomb → homogeneous aluminum material,
density = 0.3856g/cm3
2) IMC and TASC lateral panel → single aluminum box
Calet in GEANT4

---
Calet simplified geometry: no supports and mechanical structures.
Calet new geometry
(figures are not in scale)
Calet in GEANT4

---
Vacuum
Legend:
Aluminum (7075)
Scintillator
Carbon fiber
Honeycomb
Vacuum
Aluminum structures: lateral, base, top panel and PMT box in CHD and IMC
Carbon fiber and honeycomb supports for scintillator (CHD, IMC, TASC)
Scintillators and tungsten layers (also present in the simplified geometry).
Calet in GEANT4

---
CHD top panel, IMC lateral and base panel
IMC lateral and base panels
CHD top panel and PMT box
Geom. details

---
IMC and TASC layers
Legend:
Tungsten
Scintillator
Carbon fiber
Honeycomb
Vacuum
In IMC: the supports are thin carbon fiber layers and big honeycomb structures
In TASC: The supports are carbon fibers (no honeycomb)
Geom. details

---
Calet flight model
benchmark
Lorenzo Pacini
Caterina Checchia
Francesco Palma
Paolo Maestro
Nicola Mori
Benchmark

---
To validate the new GEANT4 geometry we performed common benchmarks with FLUKA end EPICS:
Proton and Electron @ 10, 100,1000,10000 GeV
Future works: 12C and 56Fe @ 10, 100,1000,10000 GeV/n kinetic energy
Particle:
Normal incidence
Generated in 4x4 cm2 area on top of CHD at the center of the detector
Interesting quantities for this presentation:
Energy deposited in CHD, IMC and TASC.
High energy trigger efficiency.
We also investigated the energy deposited in TASC, IMC layers, in IMC single fibers and TASC logs.
Introduction

---
Software versions
GEANT4-09-06-patch-02
physics lists: FTFP_BERT
EPICS9.167 Calet Cad model rev. 21 (COSMOS 7.645)
hadronic interacting model: DPMJET-III
FLUKA 2011.2c.0
hadronic interacting model: DPMJET-III
Introduction

---
All electrons @ 10 GeV.
Total energy in TASC.
H.E triggered electrons @ 10 GeV.
Total energy in TASC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 87.1% EPICS 85.3%
FLUKA 86.4%
Electrons 10GeV

---
All electrons 10 @ GeV.
TASC lateral distr.
All electrons @ 10 GeV.
TASC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Electrons 10GeV

---
All electrons @ 10 GeV.
Total energy in IMC.
H.E triggered electrons @ 10 GeV.
Total energy in IMC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Electrons 10GeV

---
All electrons @ 10 GeV.
IMC lateral distr.
All electrons @ 10 GeV.
IMC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Electrons 10GeV

---
All electrons @ 10 GeV.
Total energy in CHD.
H.E triggered electrons @ 10 GeV.
Total energy in CHD.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Electrons 10GeV

---
Electrons @ 10 GeV results
TASC total energy: very similar distributions, difference between bins with the highest energy deposit is 1-2 %
TASC lateral and longitudinal distributions: good agreement around the maximum of the distributions; difference of order 10% in the low energy tails.
IMC total energy: the shape of the distributions are very similar. The maximum position is about 10% higher in Epics and Fluka with respect to Geant4.
IMC lateral and longitudinal distributions: quite good agreement, with discrepancies only in the low energy tails.
CHD total energy: very similar distributions, the shape of the distributions are very similar.
Electrons 10GeV

---
Electrons @ 100 GeV results
The results from the comparison of the three simulations are similar to the 10 GeV case (plots and tables are in the backup slides)
TASC total energy: very similar distributions, difference between bins with the highest energy deposit is about 0.7 % for EPICS with respect to GEANT4 and FLUKA
TASC lateral and longitudinal distributions: large differences (10%) only for layers with low energy deposited
IMC total energy: distributions have similar shapes,, difference between maximum energy bins is about 20 % for EPICS with respect to GEANT4 and
IMC lateral and longitudinal distributions: large difference (20%) only for layers with low energy deposited
CHD total energy: very similar distributions, difference between maximum energy bins is about 2%
Electrons 100GeV

---
Electrons @ 1 TeV results
TASC total energy and distributions: similar results to the ones obtained at 10 and 100 GeV (plots and tables are in the backup slides) .
IMC total energy: the shape of the EPICS distributions is remarkably different with respect to the GEANT4 and FLUKA ones; the difference between the maximum energy bin is about 30% with respect to GEANT4 and FLUKA (see next slides)
CHD total energy: the shape of the EPICS distributions is remarkably different with respect to the GEANT4 and FLUKA ones; the difference between the maximum energy bin is about 30% with respect to GEANT4 and FLUKA (see next slides)
Electrons 1TeV

---
All electrons @ 1 TeV.
Total energy in IMC.
H.E triggered electrons @ 1 TeV.
Total energy in IMC.
EPICS distributions are not in agreement with GEANT4 and FLUKA.
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 99.9% EPICS 99.9%
FLUKA 99.9%
Electrons 1TeV

---
All electrons @ 1 TeV.
Total energy in CHD.
H.E triggered electrons @ 1 TeV.
Total energy in CHD.
EPICS distributions are not in agreement with GEANT4 and FLUKA.
H.E. triggered
particle table:
Electrons 1TeV

---
In order to understand these large differences in CHD (and IMC) distributions we have studied the energy deposited in the CHD paddle directly hit by the primary particle.
The single bar distribution is in agreement with the MIP energy release, (mean ~ 2-3 MeV)
The CHD total energy is bigger then the MIPs energy release in the crossed bars ( 20 MeV vs. 4-6 MeV )
CHD single paddle
CHD total energy
Electrons 1TeV

---
A possible explanation of these differences are:
The total energy released in CHD (IMC) includes both the energy deposited by the primary particle in the two crossed paddles	(fibers), and the signals due to backscatter particles in the nearby bars (fibers).
The latter is expected to increase with the primary particle energy.
The lower total energy deposited in IMC and CHD observed with Epics might be related to a different treatment of the backscatter particles with respect to GEANT4/FLUKA.
Electrons 1TeV

---
Electrons @ 10 TeV results
The results from the comparison of the three simulations are similar to the 1 TeV case (plots and tables are in the backup slides) .
TASC total energy and distributions: similar results to the ones obtained at 10, 100 and 1000 GeV
IMC total energy: the shape of the EPICS distributions is remarkably different with respect to the GEANT4 and FLUKA ones; the difference between the maximum energy bin is about 44 % with respect to GEANT4 and FLUKA
CHD total energy: the shape of the EPICS distributions is remarkably different with respect to the GEANT4 and FLUKA ones; the difference between the maximum energy bin is about 42 % with respect to GEANT4 and FLUKA (see next slides)
Electrons 10TeV

---
Proton benchmark
The TASC energy distributions of the three simulations are in good agreement at all the energy (see Maestro's presentations at the last TIM in Waseda)
IMC and CHD show large discrepancies, especially for triggered proton.
I will show the plots for protons @ 1TeV. The other energies are in in the backup slides.
Protons

---
All protons @ 1 TeV.
Total energy in TASC.
H.E triggered protons @ 1 TeV.
Total energy in TASC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 27.1	% EPICS 24.3%
FLUKA 27.4%
Protons 1TeV

---
All protons @ 1 TeV.
TASC lateral distr.
All protons @ 1 TeV.
TASC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Protons 1TeV

---
All protons @ 1 TeV.
Total energy in IMC.
H.E triggered protons @ 1 TeV.
Total energy in IMC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Protons 1 TeV

---
All protons @ 1 TeV.
IMC lateral distr.
All protons @ 1 TeV.
IMC longitudinal distr.
Very big differeces in IMC for EPICS simulation with respect to FLUKA and GEANT4
Protons 1TeV

---
All protons @ 1 TeV.
Total energy in CHD.
H.E triggered protons @ 1 TeV.
Total energy in CHD.
GEANT4 blue
EPICS red
FLUKA black
Protons 1TeV

---
Summary plots
In order to summarize electrons and protons results I will show you some plots with the differences of EPICS and FLUKA with respect to GEANT4:
Maximum energy bins deposited in TASC vs Energy, for H.E. triggered protons and electrons
Maximum energy bins deposited in IMC vs Energy, for H.E. triggered protons and electrons
Maximum energy bins deposited in CHD vs Energy, for H.E. triggered protons and electrons
Trigger efficiency vs Energy, for H.E. triggered protons and electrons
Conclusion

---
Electrons: difference in IMC total energy maximum
Electrons: difference in TASC total energy maximum
The shape of the distributions for EPICS is very different compared to GEANT4 and FLUKA ones.
Conclusion

---
Electrons: difference in
High Energy trigger efficiency
Electrons: difference in CHD total energy maximum
The shape of the distributions for EPICS is very different compared to GEANT4 and FLUKA ones.
Conclusion

---
Protons: difference in IMC total energy maximum
Protons: difference in TASC total energy maximum
The shape of the distributions for EPICS is very different compared to GEANT4 and FLUKA ones.
Conclusion

---
Protons: difference in
High Energy trigger efficiency
Protons: difference in CHD total energy maximum.
The shape of the distributions for EPICS is very different compared to GEANT4 and FLUKA ones.
Conclusion

---
Conclusion
Good agreements among the three simulations about the energy deposited in TASC and trigger efficiency
As far as CHD and IMC response is concerned, we notices a quite good agreement between FLUKA and Geant4.
Instead there are significant differences between GEANT4 and EPICS, more and more pronounced as the primary particle energy increases.
Because of the good agreement between FLUKA and GEANT4, we can consider the new GEANT4 CALET flight model validated.
Discrepancies with EPICS need to be investigated accurately.
Conclusion

---
Possible explanations
1) Different implementation of some volumes of the CALET Flight model in FLUKA/GEANT4 with respect to EPICS?
The most important simplification is Honeycomb..
2) Possible differences in the simulation of the back scattering particles?
It seems that in Epics the amount of backscatter in CHD and IMC is lower.
To check the conjecture 1) we also simulated electrons and protons with FLUKA, EPICS and GEANT4 using the Calet simplified geometry (Pisa model).The results of this simulations are shown in Caterina's presentation.
Conclusion

---
End Of Presentation
Any questions?
End Of Presentation

---
Backup slides
End Of Presentation

---
Calet High energy trigger
This is the main trigger mode for CALET
By requiring a large energy deposit in the middle of the detector,
Energy in last 2 X layers of IMC > 7.5 MIPs
Energy in last 2 Y layers of IMC > 7.5 MIPs
Energy in the first X layers of TASC > 55 MIPs
Questa slide può essere utile ma non è strettamente necessaria. La tolgo?
Trigger in Calet

---
Electrons plots and
tables: 10, 100, 1000,
10000 GeV
Electron plots and tables

---
All electrons @ 10 GeV.
Total energy in TASC.
H.E triggered electrons @ 10 GeV.
Total energy in TASC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 87.1% EPICS 85.3%
FLUKA 86.4%
Electrons 10GeV

---
All electrons 10 @ GeV.
TASC lateral distr.
All electrons @ 10 GeV.
TASC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Electrons 10GeV

---
All electrons @ 10 GeV.
Total energy in IMC.
H.E triggered electrons @ 10 GeV.
Total energy in IMC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Electrons 10GeV

---
All electrons @ 10 GeV.
IMC lateral distr.
All electrons @ 10 GeV.
IMC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Electrons 10GeV

---
All electrons @ 10 GeV.
Total energy in CHD.
H.E triggered electrons @ 10 GeV.
Total energy in CHD.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Electrons 10GeV

---
All electrons @ 100 GeV.
Total energy in TASC.
H.E triggered electrons @ 100 GeV.
Total energy in TASC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 99.7% EPICS 99.7%
FLUKA 99.7%
Electrons 100GeV

---
All electrons @ 100 GeV.
TASC lateral distr.
All electrons @ 100 GeV.
TASC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Electrons 100GeV

---
All electrons @ 100 GeV.
Total energy in IMC.
H.E triggered electrons @ 100 GeV.
Total energy in IMC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Electrons 100GeV

---
All electrons @ 100 GeV.
IMC lateral distr.
All electrons @ 100 GeV.
IMC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Electrons 100GeV

---
All electrons @ 100 GeV.
Total energy in CHD.
H.E triggered electrons @ 100 GeV.
Total energy in CHD.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Electrons 100GeV

---
All electrons @ 1 TeV.
Total energy in TASC.
H.E triggered electrons @ 1 TeV.
Total energy in TASC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 99.9% EPICS 99.9%
FLUKA 99.9%
Electrons 1 TeV

---
All electrons @ 1 TeV.
TASC lateral distr.
All electrons @ 1 TeV.
TASC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Electrons 1 TeV

---
All electrons @ 1 TeV.
Total energy in IMC.
H.E triggered electrons @ 1 TeV.
Total energy in IMC.
EPICS distributions are not in agreement with GEANT4 and FLUKA.
H.E. triggered
particle table:
Electrons 1TeV

---
All electrons @ 1 TeV.
IMC lateral distr.
All electrons @ 1 TeV.
IMC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Electrons 1 TeV

---
All electrons @ 1 TeV.
Total energy in CHD.
H.E triggered electrons @ 1 TeV.
Total energy in CHD.
EPICS distributions are not in agreement with GEANT4 and FLUKA.
H.E. triggered
particle table:
Electrons 1TeV

---
All electrons @ 10 TeV.
Total energy in TASC.
H.E triggered electrons @ 10 TeV.
Total energy in TASC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 99.9% EPICS 99.7%
FLUKA 99.9%
Electrons 10TeV

---
All electrons @ 10 TeV.
TASC lateral distr.
All electrons @ 10 TeV.
TASC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Electrons 10TeV

---
All electrons @ 10 TeV.
Total energy in IMC.
H.E triggered electrons @ 10 TeV.
Total energy in IMC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Electrons 10TeV

---
All electrons @ 10 TeV.
IMC lateral distr.
All electrons @ 10 TeV.
IMC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Electrons 10TeV

---
All electrons @ 10 TeV.
Total energy in CHD.
H.E triggered electrons @ 10 TeV.
Total energy in CHD.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Electrons 10TeV

---
Protons plots and
tables: 10, 100, 1000,
10000 GeV
Electron plots and tables

---
All protons @ 10 GeV.
Total energy in TASC.
H.E triggered protons @ 10 GeV.
Total energy in TASC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 2.4% EPICS 1.3%
FLUKA 1.8%
Protons 10GeV

---
All protons @ 10 GeV.
TASC lateral distr.
All protons @ 10 GeV.
TASC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Protons 10GeV

---
All protons @ 10 GeV.
Total energy in IMC.
H.E triggered protons @ 10 GeV.
Total energy in IMC.
Low
Numbers of triggered
protons
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Protons 10GeV

---
All protons @ 10 GeV.
IMC lateral distr.
All protons @ 10 GeV.
IMC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Protons 10GeV

---
All protons @ 10 GeV.
Total energy in CHD.
H.E triggered protons @ 10 GeV.
Total energy in CHD.
Low
Numbers of triggered
protons
GEANT4 blue
EPICS red
FLUKA black
Protons 10GeV

---
All protons @ 100 GeV.
Total energy in TASC.
H.E triggered protons @ 100 GeV.
Total energy in TASC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 25.5% EPICS 19.4%
FLUKA 21.4%
Protons 100GeV

---
All protons @ 100 GeV.
TASC lateral distr.
All protons @ 100 GeV.
TASC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Protons 100GeV

---
All protons @ 100 GeV.
Total energy in IMC.
H.E triggered protons @ 100 GeV.
Total energy in IMC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Protons 10GeV

---
All protons @ 100 GeV.
IMC lateral distr.
All protons @ 100 GeV.
IMC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Protons 100GeV

---
All protons @ 100 GeV.
Total energy in CHD.
H.E triggered protons @ 100 GeV.
Total energy in CHD.
GEANT4 blue
EPICS red
FLUKA black
Protons 100GeV

---
All protons @ 1 TeV.
Total energy in TASC.
H.E triggered protons @ 1 TeV.
Total energy in TASC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 27.1% EPICS 24.3%
FLUKA 27.4%
Protons 1TeV

---
All protons @ 1 TeV.
TASC lateral distr.
All protons @ 1 TeV.
TASC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Protons 1TeV

---
All protons @ 1 TeV.
Total energy in IMC.
H.E triggered protons @ 1 TeV.
Total energy in IMC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Electrons 10GeV

---
All protons @ 1 TeV.
IMC lateral distr.
All protons @ 1 TeV.
IMC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Protons 1TeV

---
All protons @ 1 TeV.
Total energy in CHD.
H.E triggered protons @ 1 TeV.
Total energy in CHD.
GEANT4 blue
EPICS red
FLUKA black
Protons 1TeV

---
All protons @ 10 TeV.
Total energy in TASC.
H.E triggered protons @ 10 TeV.
Total energy in TASC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
H.E.trigger efficiency
GEANT 37.1% EPICS 31.4%
FLUKA 34.2%
Protons 10TeV

---
All protons @ 10 TeV.
TASC lateral distr.
All protons @ 10 TeV.
TASC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Protons 10TGeV

---
All protons @ 10 TeV.
Total energy in IMC.
H.E triggered protons @ 10 TeV.
Total energy in IMC.
GEANT4 blue
EPICS red
FLUKA black
H.E. triggered
particle table:
Protons 10TeV

---
All protons @ 10 TeV.
IMC lateral distr.
All protons @ 10 TeV.
IMC longitudinal distr.
diff = EPICS/GEANT4 - 1 (rosso)
diff = FLUKA/GEANT4 - 1 (nero)
Protons 10TeV

---
All protons @ 10 TeV.
Total energy in CHD.
H.E triggered protons @ 10 TeV.
Total energy in CHD.
GEANT4 blue
EPICS red
FLUKA black
Protons 10TeV