## Slide 2
How precisely can we control our magnets? Experience and impact on the expected control of machine parameters (tune and chromaticity)
Thanks to: M.Lamont, M. Schaumann, E.Todesco, J.Wenninger
M.Solfaroli
BE department
OP group

## Slide 3: Outline
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
The FiDeL model and its implementation
Tune: injection and snapback
Q’: injection, snapback, ramp and squeeze
b3 to Q’ “conversion”

## Slide 4: The FiDeL model
Decay
“The decay of harmonics at constant current is driven by current redistribution on superconducting cables, which results in a net decrease of the average dc magnetization of the cables and of its contribution to the total field”
N. J Sammut et al., Phys. Rev. ST Accel. Beams 9
Snap back
rapid reestablishment of magnetization after decay. The field bounces back to its pre-decay level once the current in the magnet starts to ramp up
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
FiDeL dynamic component has been studied and modeled based on a massive set of magnetic measurements

## Slide 5: The powering history dependency
The magnitude of the decay depends on the powering history, both on the waveform of the powering cycle as well as waiting times, and has memory of previous powering cycles, thus making this effect non-reproducible from cycle to cycle.
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli

## Slide 6: The FIDEL model implementation
* *
IFTnom, tFTnom, tPREnom , Tinj
PH normalization factors
dectau, decd, decdelta
fitting parameters
decay
PH dependency (reduced for Q)
decay normalization (b3 only)
IFT, tFT, tPRE
Powering History (PH)
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli

## Slide 7: The snapback
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
N. J. Sammut et al., Mathematical formulation to predict the harmonics of the superconducting Large Hadron Collider Magnets. II. Dynamic field changes and scaling laws. PRSTAB 10, 082802 (2007)
The amplitude A depends on length of injection plateau & powering history
Measurements show that the snap-back to the hysteresis curve in the first part of the ramp follows an exponential law in current. As the current at the start of ramp is parabolic, the snapback is Gaussian in time

## Slide 8: Tune injection decay
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
Example of bare tune decay at injection with corresponding exponential fit
Synchrotron Sidebands (?)
(Those lines decay with the tune already in the raw data. 50Hz lines have slightly smaller spacing but stay at constant frequency)

## Slide 9: Tune injection decay – PH dependency
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
To exclude dependence on preparation time, select only cycles with tpre<800s
Although there is no much reproducibility in the data (especially for pre-cycles), thus the fit isn’t good, a dependency of the decay amplitude with Flat-top time (tFT) is visible
No pattern of dependency of decay amplitude on preparation time (tpre)
A dependency of decay amplitude on tFT has been implemented in the online correction system in 2015
Control is important, though not extremely critical as tune is always visible and can be corrected
Flat-Top
Flat-Bottom

## Slide 10: Tune snapback
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
If the correction incorporation is not good enough, it can be difficult for the QFB to keep the tunes constant and large tune excursions can occur at the beginning of the ramp with the risk of control loss
Example of snapback-like incorporation for Q implemented in Run2 to limit the load on the QFB

## Slide 11: b3 injection decay
About 0.46 b3 units (~20 Q’ units) decay in 1 hour
Operationally difficult to inject in the very first part of the injection plateau
Good fit, but few units will always “leak” into lattice sextupole correction
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
As expected, decay amplitude is about 40% larger than at 4 TeV
B1H
B1V
B2H
B2V

## Slide 12: b3 injection decay compensation
Horizontal
Vertical
The present compensation of b3 injection decay makes Q’ flat
(in within ±0.5 units)
Measured Q’
Decay compensation
Corrected Q’
The precision of the correction over several fill depends on the quality of the powering history dependency model
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli

## Slide 13: Snapback - Horizontal
sec
Q’H
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
b3
sec
Q’ corrections
Measured Q’
Natural Q’
b3 correction is fully incorporated in ~30 sec
(depending on the intensity)…consistent with measurements!

## Slide 14: Snapback - Vertical
sec
Q’V
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
b3
sec
Q’ corrections
Measured Q’
Natural Q’
b3 correction is fully incorporated in ~30 sec
(depending on the intensity)…consistent with measurements!

## Slide 15: Ramp
Q’ along the ramp is well controlled (±2 units)
Small imperfection in the persistent currents model <3 kA, but still very good control considering the 8 units swing (300 Q’ units) of b3
No visible effect from the missing RCS (compensation split on the other 7 circuits)
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
B1H
B1V
B2H
B2V

## Slide 16: Ramp
b3 evolution during ramp (~8 units -> 300 Q’ units)
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
Typical sextupole correction
Vertical
Horizontal
Bare Q’ along the ramp
(lattice sext corrections removed):
Precision of the model above 3 kA is ±5 Q’ units
~1 unit of uncorrected b3 below 3 kA
In addition, about 15 Q’ units error (positive in both planes)…on ~300 Q’ swing

## Slide 17: Decay @flat-top
Horizontal
Vertical
sec
sec
Q’
Q’
Expected to be negligible is indeed very small!
b3 compensation knob
Q’ decay
~2 units in H
~1.5 units in V
Example of Q’ measurements at flattop after compensation
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
~0.05 b3 units

## Slide 18: Squeeze
Q’ stable in within ±2 units
Noisy signal (V especially) => measurements not fully reliable
Some feed-forward could be done (fine tuning)
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
B1H
B1V
B2H
B2V

## Slide 19: Reproducibility – B1 Horizontal
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
Fill 4534 on Oct 25th
Fill 4307 on Sept 5th
In Fill 4534 we enter the ramp with ~2 Q’ units more

## Slide 20: Reproducibility – B1 Vertical
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
Fill 4534 on Oct 25th
Fill 4307 on Sept 5th
Fed-forwarded peak
In Fill 4534 we enter the ramp with ~2 Q’ units more

## Slide 21: b3 to Q’ measurement
Run1 assumption:
1 b3 unit =
43 Q’ units in H
-35 Q’ units in V
New measurements
1 b3 unit =
B1
H ~ 42.6 Q’ unit
V ~ -35.3 Q’ unit
B2
H ~ 42 Q’ unit
V ~ -35 Q’ unit
0.03 b3 units swing in 10 steps
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli
B1H
B1V
B2H
B2V
Very good agreement

## Slide 22: Conclusions
Tune
  Tunes at injection are under control, although decay isn’t fully reproducible
  Once the ramp starts the tunes are controlled by the QFB
Chromaticity (measured with pilot)
  b3 injection decay is correctly compensated for operational purpose (it would be a plus to verify the powering history dependency)
  Good control and reproducibility during squeeze, ramp and snapback (±2 units)
  Small imperfection in the persistent current model below 3kA
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli

## Slide 23: Q’ knob check
Knob measurements
2 steps of 5 units
B1
H -> 2 to 12
V -> 15 to 5
B2
H -> 2.2 to 12.2
V -> 14 to 4
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli

## Slide 24: OP without RCS.A78B2
INJECTION
b3 decay
RAMP
Snapback
b3 variation (momentum change)
FLATTOP
b3 decay
B2 compensation is calculated as for B1 then multiplied to a 8/7=1.14 factor
The RCS.A78B2/B3 function has been equally distributed on the other circuits
The B2 global_b3 knob has been multiplied by a 8/7=1.14 factor
(effect of about 0.2 Q’ units)
RCS.A78B2/B3
sec
b3
Q’
min
sec
b3
~7/8 b3 units
Example of H corr
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli

## Slide 25: Ramping w/o RCS.A78B2
First ramp:
At about 800 sec the B2Q’V starts growing and B2Q’H goes down then passes negative…B2 is dumped around 1080 sec after the ramp start
Third ramp:
Both beams survive!
Q’ (re-)measured along the ramp (small corrections implemented) and at flattop
Second ramp:
Both beams survive the ramp, but are dumped about 30 sec after flattop is reached (electrical glitch caught by FMCM RD1.LR5)
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli

## Slide 26: Online Q’
Worked very reliably for several fills
Next improvement steps:
  Q’ trace (e.g. to observe evolution during ramp)
  Feed Forward
  Error Estimation
K.Fuchsberger
5th Joint HiLumi LHC-LARP Annual Meeting – M.Solfaroli