## Slide 1: INTERACTION REGION MAGNETS
E. Todesco
CERN, Geneva, Switzerland
With the contribution of
B. Auchmann, P. Fessia, P. Fabbricatore, F. Toral, G. Volpini, D. Wollman,
CERN, 27th October 2015

## Slide 2: OUTLOOK
We started the protection work favoring the energy extraction option
  Having seen the overhaed for operation and the risk/faults associated to quench heaters
After cost and schedule review we decided to remove the energy extraction for the high current (>10 kA) system because of their cost (millions)
Panorama of protection systems in LHC given by B. Auchmann in WP3 meetings
  Many different solutions according to the zoo
For the intermediate current (single aperture orbit correctors, at 2 kA) designers would prefer avoid quench heaters
For the high order correctors we explore the options of self protection (power converter crowbar, with a 50 V max)

## Slide 3: OUTLOOK
General feature: HL LHC has independently powered magnets with few exceptions
For the intermediate current (single aperture orbit correctors, at 2 kA) designers would prefer avoid quench heaters
  Preliminary simulations in CIEMAT
For the high order correctors we explore the options of self protection (power converter crowbar, with a 50 V max)
  Ongoing work in LASA
For the D2 Q4 correctors we just decided to change from Rutherford cable 2 kA to a ribbon cable with 500 A, so we have not yet estimates
  We have to wait for final design of ribbon to know inductance, etc and see how to protect

## Slide 4: MAIN MAGNETS
D1, D2, Q4
  No dump resistor to save money on the switches
  Energy density on the coil between 0.040 and 0.070 J/mm3, values similar to typical Nb-Ti magnets
Quench heaters on the outer layer
  D1, D2 are single layer so even more efffective than in the LHC dipoles
  Q4 has double layer but heaters will work as well
    If switches are available consider extraction ?
CLIQ a viable option
  Cost to be estimated
  D1 and D2 in series to be considered

## Slide 5: ORBIT CORRECTORS
Two lengths, and two circuits (V and H) so four cases
Protection with energy extraction and 500 V looks easy
Possibility of relying on the power converter: resistor can tolerate at max 80 V
  This solution seems beyond our target
  This is a first estimate, iteration with PC needed
  Simulations including quench propagation needed, work to be ddone in CIEMAT and CERN

## Slide 6: NONLINEAR CORRECTORS
With 50 V, protection possible for short magnets
  Sextupole octupole decapole, skew dodecapole
For normal dodecapole and skew quadrupole larger stored energy and inductance
  Estimates ongoing

## Slide 7: CONCLUSIONS
D1, D2, Q4
  Quench heaters is the baseline
  CLIQ option to be studied and estimated
    If cost and risks are not larger then heaters, I would go for it
Orbit correctors
  Protection on the PC looks difficult, more simulations needed
High Order correctors
  Protection on the PC looks viable for sex, oct, dec, and skew dod
    Lowering the current to match the 120 A PC must be assessed
  Skew quadrupole is a big beast and may need extraction
  Probably also normal dodecapole should follow the same strategy