## Slide 1
Research Areas of LINAC and NNP Groups
at the Institute for Applied Physics Frankfurt
LINAC Group
H. Podlech, F. Schneider, M. Busch, F. Dziuba, M. Schwarz, M. Basten et al
NNP Group
K. Schulte, M. Droba, O. Meusel et al
in close coordination and collaboration with
G. Franchetti
CERN, Geneva
June 18th, 2015
From Ion Sources to High Power Linacs

## Slide 2
Goethe University Frankfurt
Founded in 1914
16 Departments
3 Campus areas
45000 Students (# 3 in Germany)

## Slide 3
Department of Physics at Goethe University (FB13)

## Slide 4
Plasma-Physics
Prof. Dr. J. Jacoby
Accelerator Physics
Prof. Dr. O. Kester
Prof. Dr. H. Podlech
Prof. Dr. U. Ratzinger
Nuclear Astro-Physics
Prof. Dr. R. Reifarth
Institute for Applied Physics (IAP)

## Slide 5
Accelerator Physics at IAP
Superconducting RF cavities
Space Charge Lenses
Room temperature RF cavities
RFQ accelerators
Beam Dynamics and Code development
Ion sources
Beam diagnostics
Laser-Plasma acceleration
Plasma stripper
Magnet design (rt)
LEBT Sections
Magnetic storage ring

## Slide 6
Projects
HLI
CH0
CH1
CH2
CH3
CH4
CH5
CH6
Buncher
Hochladungs-Injektor
CH7
CH8
CH9
CH10
CH-cavity demonstrator
1.4 AMeV
6 AMeV
FRANZ @ IAP
sc cw linac @ GSI
100% RF duty factor
RFQ-structures
rt DTL-structures
sc DTL structures
17 MeV p-Injector for MYRRHA

## Slide 7
Frankfurt Neutron Source FRANZ
2 MeV Protons  7Li as Target  Neutrons 0-500 keV
2 mA cw
50-200 mA pulsed, t=50 ns, rep. rate 250 kHz  RF cw
Next stage: Bunch compressor

## Slide 8
MYRRHA Project
600 MeV Protons, 4 mA, cw
Demonstration of large scale transmutation

## Slide 9
MYRRHA Project 17 MeV Injector
rt CH-cavities
100% duty cycle, high reliability, excellent beam quality
4-rod RFQ
rt CH-cavities
sc CH-cavities

## Slide 10: Advanced Demonstrator for GSI-SHE-Linac
HLI
CH0
CH1
CH2
CH3
CH4
CH5
CH6
Buncher
High Charge Injector
CH7
CH8
CH9
CH10
CH-cavity demonstrator
1.4 AMeV
6 AMeV
2 identical CH-cavities per cryomodule
Constant beta
Warm quadrupoles in inter-tank sections
Superconducting cw operated heavy ion linac
for the production of superheavy elements

## Slide 11
RFQ Structures
RFQ structures using electric RF quadrupole fields
 Strong electric focusing

## Slide 12
Parameter | SARAF | FRANZ | MHYRRA | Unit
RF Structure | 4-Rod | 4-Rod | 4.Rod | ---
Frequency | 175 | 175 | 176.1 | MHz
Beam current | 2 | 2-50 | 5 | mA
Duty factor | 100 | 100 | 100 | %
Eout | 1.5 | 0.7 | 1.5 | MeV
Rp | 67 | 77 | 77 | kWm
RF Power | 240 | 110 | 108 | kW
Specific power | 60 | 60 | 25 | kW/m
Voltage | 65 | 65 | 44 | kV
Length | 4 | 1.7 | 4 | m
A. Bechtold, NTG
175 MHz 4-Rod SARAF
RFQ Development for cw Operation

## Slide 13
175 MHz cw Prototype RFQ

## Slide 14
Philosophy of Cooling Concept
As much as possible
Temperature distribution as homogeneous as possible

## Slide 15
175 MHz cw Prototype RFQ

## Slide 16
Philosophy of Cooling Concept
300 kW cw
Amplifier

## Slide 17
Conditioning

## Slide 18
RF Power Test
Pth=116 kW/m
U=94.5 kV
Ep=29 MV/m

## Slide 19
FRANZ RFQ
175 MHz, 700 keV, 1-50 mA, cw, 60 kW/m: Delivered 12.6.2015
Notes: Spaltkonfiguration
Beschleunigungsgradiente und Vergleich
Design-Kriterium war ein elektrisches Oberflächenpeakfeld von E_p <30 MV/m.
Wichtig: mechanische Steifigkeit
Durchgehende Stützen
Verzicht auf Rippen (auf B_p ~50 mT)
Sternförmig angeordnete Versteifungsklammern, Verschiebung der Enddeckel minimieren.

## Slide 20
RFQ-Injection
RFQ-accelerators are very sensitive to input beam parameters  often poor transmission
Systematic investigation of RFQ performance for variation of LEBT parmeters
Many effects: Field errors, misalignment, space charge compensation, residual gas pressure, lens parameter
Planned: Investigation (Theor.+Exp) at FRANZ, MYRRHA, HSI

## Slide 21
The Family of H-Mode Drift Tube Cavities
Room temperature
IH-DTL
Room temperature
CH-DTL
Superconducting
CH-DTL
H11(0)
H21(0)
H21(0)

## Slide 22
The Family of H-Mode Drift Tube Cavities

## Slide 23
rt CH-Cavity Program
Duty factor 100%
FRANZ, MYRRHA
P/L≈30 kW/m
RF simulations
Thermal/structural mechanical simulations
Tuning

## Slide 24
Rt CH-Cavity Programme

## Slide 25
Worldwide the first superconducting multi-cell cavity for the low and medium energy range
Cavity | CH-Mode
Length (mm) | 1048
Diameter (mm) | 280
Cells | 19
b =v/c | 0.1
Frequency (MHz) | 360
Material | Niob
Quality factor | 7·108
H. Podlech et. al, Phys. Rev. ST Accel. Beams, 10, 080101 (2007)

## Slide 26
Bellow Tuners
Helium Vessel
Coupler Flanges
Static Tuners
b | 0.155
Frequency (MHz) | 325.224
Cells | 7
Length bl-def (mm) | 505
Diameter (mm) | 350
Ea (MV/m) | 5
Ep/Ea | 5.1
Bp/Ea [mT/(MV/m)] | 13
G (W) | 66
Ra/Q0 (W) | 1248
RaRs (W2) | 80000
325 MHz CH-Cavity

## Slide 27
Dynamic Tuning of sc CH-Cavities
Bellow tuner
Niobium, cooled
No longitudinal space needed
±1 mm (slow tuner, stepper motor)
± 5 mm (fast piezo tuner)

## Slide 28
Development of Power Couplers

## Slide 29
Testing Superconducting CH-Cavities
2 cryogenic RF labs at IAP

## Slide 30
Linde L140 liquifier, 90 l lHe/hr @ 4K

## Slide 31
Test Results 325 MHz CH-Cavity
Ep=72 MV/m
Bp=182 mT

## Slide 32
Gap Voltages and Residual Resistance

## Slide 33
Helium out
Helium vessel
Tuner flange
Helium in
Dynamic bellow tuner
Static tuner
Preparation
flange
Inclined
end stem
217 MHz SC CH-Prototype
PARAMETER | UNIT | 
Beta |  | 0.059
Frequency | MHz | 216.816
Gap number |  | 15
Total length | mm | 691
Cavity diameter | mm | 409
Cell length | mm | 40.82
Aperture | mm | 20 / 18
Ua | MV | 3.369
Energy gain | MeV | 2.97
Accelerating gradient | MV/ m | 5.1
Ep/ Ea |  | 6.3
Bp/ Ea | mT/ (MV/m) | 5.7
R/ Q | Ω | 3240
Static tuner |  | 9
Dynamic bellow tuner |  | 3
HLI
CH0
CH1
CH2
CH3
CH4
CH5
CH6
Buncher
High Charge Injector
CH7
CH8
CH9
CH10
CH-cavity demonstrator
1.4 AMeV
6 AMeV

## Slide 34
Production of the 217 MHz CH-Prototype

## Slide 35
Horizontal Cryo Module for cw Linac

## Slide 36
The cw LINAC Demonstrator Project at GSI
The HLI will be used as an injector
for the cw LINAC demonstrator
A full performance test of the demonstrator in 2016 is one important milestone on the way to a new sc cw LINAC at GSI
sc 217 MHz CH cavity
sc 9.5 T solenoid
LN / LHe reservoir
Demonstrator
3000 l
LHe reservoir
IH-DTL
RFQ
ECR source
Control room, RF amplifiers

## Slide 37: Advanced Demonstrator for GSI-SHE-Linac
CH-1/2
HLI
CH0
CH1
CH2
CH3
CH4
CH5
CH6
Buncher
High Charge Injector
CH7
CH8
CH9
CH10
Call for tender finished
Cryo module design

## Slide 38
„BABY“ - Prototype
„HERO“ – High Field Gabor Lens
„HERBERT“ – Gradient Density Gabor Lens
Space Charge Lenses for E-Cloud Confinement
160 mT
35 kV
12 mT
6 kV

## Slide 39
Scheme of Gabor Plasma-Lenses
Longitudinal and transversal confinement of an electron cloud by magnetic and electric fields
Homogeneous electron density leads to linear forces (at least in the ideal world)
Focusing and space charge compensation

## Slide 40
RF-pick up
beam
e-column
Investigation of Frequency Spectrum Emitted by the Undisturbed Electron Column
antenna
RF Probe Diagnostics of E-Cloud Response to Bunch Impact

## Slide 41
Emitted Bremsstrahlung Spectra
 Loss mechanism
Dependence on Anode Potential
Dependence on Magnetic Field
Objectives:
study of loss channels
determination of loss rates
B=9,7 mT, p=3,4e-7 hPa
B=11,8 mT
p=1,7e-7 hPa
Dt=120 s
F=22 kV
p=5,1e-7 hPa
Dt=300 s
X-Ray Spectroscopy for Investigation of Electron Loss Characteristics
Some electrons have higher energy as expected  Plasma instabilities

## Slide 42
Measured Ion Current
Measured Intensity of
Light Density Distribution
Time-Resolved Measurement of an Instabilty
Arising instability seems to be a result of a difference in the local electron density distribution and the electron temperature in transverse and longitudinal direction.
F=3400V
B=12 mT
p=7,9-4 hPa (He)
Datei: 18072011
Time-Resolved Measurements of E-Cloud Instabilities
Diacotron-instability

## Slide 43: Shaping of Phase Space Distribution by Stably Confined E-Clouds
Ion Beam Transport and Space Charge Compensation Strategies
measurement
FA= 9.8 kV
Bz= 10.8 mT
erms,n= 0.236 p mm mrad
measured light density
distribution
FA= 9.8 kV
Bz=10.8mT
measured light density
distribution profile
measurement
erms,n= 0.170 p mm mrad
measured beam current
profile
measured beam current
profile
IB=35 mA
Notes: 97% Emittanz ist zu sehen im Vergleich zur Simualtion

## Slide 44: Superconducting Gabor Lens for XHV Applications
Gabor Lens Filling Scheme under XHV - Conditions
Ion Beam
SC – Cavity (DTL)
SC – Gabor Lens
Beam optics for SC LINACs
Reduced risk of quenching due to reduced magnetic field strength
Cold emitter as an e-source
Collaboration with INFN Catania and Bologna
CNT
Courtesy of F. Odorici

## Slide 45
Gabor Lens
Ion sources
& LEBT‘s
merging
Neutralized Merging of Bunch Trains by Gabor Lens
Shift of beam axis behind electron column at t = 75 ms
Crossover under full space charge w/o e-column
Two separted bunch trains at the exit of the RFQ
y
x
y
x
bunching and acceleration
merging
matching
two beam RFQ
ion sources
& LEBTs
deflector
Gabor lens

## Slide 46
bender
  3D PIC code, kinetic description
  ionization of residual gas and secondary electrons on surfaces implemented
  built-up and decay time of e-clouds
State of the plasma column after 140 μs, U=9.8 kV, B=10.8 mT, 1e-3 Pa Ar+
GaborM
  fluid description
  steady state
GabLensM2
  3D PIC code
  kinetic description
  dynamic processes
Numerical Simulation of E-Cloud Dynamics

## Slide 47
Summary
Capabilities at IAP
Test stands for sc cavities
Vertical cryostat Ø 900 and 600 mm
RF amplifiers 4 W-300 kW and
from 50-1000 MHz
Test stands for rt cavities
RFQ design, RFQ tuning, testing
IH/CH design, tuning, testing
Beam diagnostics
RF control systems
He-Liquifier
Proton/Ion sources
Tuner systems
LEBT sections
Beam dynamics codes
Parmteq, LORASR, TraceWin
Bender, GaborM, GabLensM2
RF Simulations
Thermal simulations
Structural mechanics simulations
Broad research portfolio in accelerator physics

## Slide 48
Bolivia 2014
Pomerape 6250 m

## Slide 49
RF Power Test

## Slide 50
Water cooling

## Slide 52
RFQ Structures
Mechanical modulation on electrodes
 Longitudinal field components for bunching and acceleration

## Slide 53
RFQ Structures
More than 60 4-Rod RFQs have been built at IAP