## Slide 1: IR6 squeeze for layout HLLHCV1.2
M. Fitterer, R. De Maria
Acknowledgments: R. Bruce, S. Fartoukh, J. Uythoven, M. Fraser

## Slide 2: Outline
IR6 optics – aperture optimization at injection
IR6 constraints from ABT and collimation
IR6 squeeze (round, flat, flathv)

## Slide 3: IR6 constraints from ABT + collimation
Constraints derived from V1.0 squeeze analysis and RunII optics
(M.A. Fraser, J. Uythoven, R. Bruce):
maximize β-functions at dump in order to ensure a sufficient distribution of the beam energy
        Beam 1: βx > 5012 m, βy > 3955 m
      Beam 2: βx > 5052 m, βy > 3698 m
    Limits taken not to decrease nominal LHC ones.
    -> Can they be relaxed to minimum over both beams ?
    -> What is the true minimum on the β in one plane, what is the minimum on sqrt(βx*βy) ? -> FLUKA simulations needed (Jan)
MQY.4L6.B1 and MQY.4R6.B2 constant in order to ensure enhancement of the MKD kick (1% gradient error acceptable)
dispersion smaller than 0.5 m in straight section (educated guess)

## Slide 4: IR6 constraints from ABT + collimation
Constraints derived from V1.0 squeeze analysis and RunII optics
(M.A. Fraser, J. Uythoven, R. Bruce):
asynchronous dump:
    phase advance of π/2 between MKD and TCDQ to ensure protection by TCDQ in case of asynchronous dumps -> 10% relative error tolerable
    Δμx (MKD->TCDQ) = 0.5*π ± 0.025*π
    maximize β-functions at TCDQ in order to ensure a sufficient distribution of the beam energy (hor. less critical as already diluted by horizontal kick)
    βx/y (TCDQ) > 160 m (= nominal LHC)
in addition: aperture limit at 7 TeV =βIR6 < βarc + 20 m, e.g. flat βarc=1150 m

## Slide 5: Injection β*=6m - optics
TCDQ (black/red)
MKD

## Slide 6: Injection β*=6m - aperture
layout | βx/y* [m] | minimum n1, Beam 1 |  | minimum n1, Beam 1 | 
 |  | element | value | element | value
LHC, RunI | 11 | MQ.11R6.B1 | 9.54 | MQML.10R6.B2 | 9.49
LHC, RunII* | 11 | MQ.11R6.B1 | 9.49 | MQML.10R6.B2 | 9.47
HLLHCV1.0 | 6 | MQ.11R6.B1 | 9.42 | MQML.10R6.B2 | 9.50
HLLHCV1.1 | 6 | MQML.10L6.B1 | 9.28 | MCBV.12R6.B2 | 9.40**
HLLHCV1.2 | 6 | MQ.11R6.B1 | 9.24 | MQML.10R6.B2 | 9.25
aperture degraded in order to meet ABT+collimation constraints
+ n1>9.4 in straight section
relaxation of βx/y (TCDQ) or βx/y (dump) would improve aperture at injection (see V1.1 optics)
*injection with MQT for adjustment of WP (beta-betating), strength unchanged
**aperture for b1 worse in order to fulfill βx/y(TCDQ)>160 m, for beam 2 dump constrained is not fulfilled
βx/y(dump, V1.1)=3538 m < 3955 m

## Slide 7: Injection β*=6m - aperture
9.4
(real target to be defined)
HLLHCV1.0
HLLHCV1.2

## Slide 8: Squeeze round: 0.48 m -> 0.15 m
not possible to remove
(origin kq10.l6b1)
no change of slope

## Slide 9: Squeeze flat: 0.48 m -> 0.075/0.30 m
round
flat 0.40/0.10 m
very difficult to remove
-> small change results in large impact on other quadrupoles
results in change of slope in kq4.r6b1
no change of slope

## Slide 10: Squeeze flathv: 0.48 m -> 0.30/0.075 m
induces strong change of slope in kq4.l6b2
round
flat 0.10/0.40 m
induces strong changes of slope in kq5.l6b1, kq9.r6b1,kq10.r6b1, kq10.l6b1, …
Notes: 1) compare squeeze 41 and 42

## Slide 11: Summary
injection aperture could be improved if βx/y (TCDQ) or βx/y (dump) are relaxed
round, flat and flathv meet ABT/collimation constraints (MQY4 strength for kick enhancement, maximum beta at dump and TCDQ for dump and asynchronous dump protection, dispersion)
smoothness of flat and flathv could be improved by squeezing both planes equally fast. Each change in the squeeze causes “steps”. Ideal squeeze x/y-ratio for β*-leveling to be defined.

## Slide 13: beta @ MKD and TCDQ
layout | βx/y* [m] | MKD.H5[LR]6.B[12], β [m] |  |  |  | TCDQA.A4[LR]6.B[12], β [m] |  |  | 
 |  | x, b1 | y, b1 | x, b2 | y, b2 | x, b1 | y, b1 | x, b2 | y, b2
LHC, RunI | 0.6/0.6 | 382 | 356 | 377 | 355 | 495 | 165 | 500 | 165
LHC, RunII* | 0.8/0.8 | 382 | 356 | 377 | 355 | 484 | 161 | 488 | 162
HLLHCV1.0 | 0.15/0.15 | 195 | 460 | 269 | 350 | 966 | 129 | 697 | 168
HLLHCV1.1 | 0.15/0.15 | 232 | 438 | 281 | 273 | 814 | 133 | 667 | 216
HLLHCV1.2 | 0.15/0.15 | 258 | 363 | 239 | 362 | 732 | 161 | 788 | 162
HLLHCV1.2 | 0.075/0.3 | 380 | 327 | 349 | 318 | 497 | 181 | 540 | 185
HLLHCV1.2 | 0.3/0.075 | 270 | 320 | 280 | 204 | 700 | 185 | 673 | 289
*injection with MQT for adjustment of WP (beta-betating), strength unchanged

## Slide 14: Injection β*=6m - aperture
9.4
(real target to be defined)
HLLHCV1.1
HLLHCV1.2

## Slide 15: Squeeze round with V1.1 injection endpoint
Notes: 1) compare squeeze 41 and 42