## Slide 2: Simulation of Transient Effects in Accelerator Magnets Tools for Magnet Protection and Circuit Modeling
B. Auchmann, L. Bortot, M. Maciejewski, M. Prioli, A.M. Navarro, A. Verweij with M. Baveco, D. Paudel, E. Ravaioli, who recently left.

## Slide 3
Goals, Strategy, Tactics
c
Common Workflow
December
January
2015
Co-Simulation
FEM Solvers
Network Solvers
STEAM: Summary and Overview

## Slide 4
Accuracy and performance
Fast reaction times upon incidents
Flexibility for long-term evolution by multiple developers (student projects)
Guaranteed (low) long-term maintenance
Goals

## Slide 5
Combination of a limited number of tools.
Each tool is applied within its specific domain of competitive advantage.
We become specialists in the optimal use and flexible coupling of tools.
We produce recipes and workflows that can be passed on to other teams/labs without software-maintenance and support efforts.
Strategy

## Slide 6
Minimalistic software-development to create code-coupling interfaces and automated workflows.
Clean code (conventions), that is versioned, reviewed, and regularly tested for long-term sustainability.
Maintained and documented model library.
Persistency-policy for input/output of modeling activities.
Tactics

## Slide 7
Workflows under development | tools we currently use | Status
COMSOL 1D for longitudinal quench propagation | QP3 | done
PSpice netlists for circuit simulations | PSpice GUI | done
PSpice + COMSOL 2D co-simulation for CLIQ | TALES | on-going
PSpice + COMSOL 3D for quench simulation | ROXIE | 
Co-simulation
COMSOL
MATLAB/ Simulink
…
PSpice
Work Ongoing

## Slide 8: Overview Common Workflow Network Solvers FEM Solvers Co-Simulation

## Slide 9
,,
Code repository Code review Wiki documentation
Daily stand-up meetings @10AM
New section website, one drive cloud, indico: http://cern.ch/te-mpe-pe | June 2015
Clean code development workshop, jointly with MS | 9 July 2015
Object oriented programming workshop, jointly with MS | 13 Aug 2015
Workflow improvements – our conventions

## Slide 10: Overview Common Workflow Network Solvers FEM Solvers Co-Simulation

## Slide 11
A netlist is a textual description of the circuit elements (VI characteristics) and interconnections (topology)
Recently, much effort has been dedicated to the migration of the PSpice RB circuits from the GUI format to the netlist format
  Implementation of circuit libraries
Maurice Baveco, "Lumped element modelling of superconducting circuits with SPICE"
GUI
* source
X_X1 N00174 N000402 1 2N6405
R_R2 N03745 N000402 8 TC=0,0
V_V2 N00174 0
+SIN 0 10 1 0 0 0
R_R1 0 1 1 TC=0,0
I_I3 N00174 N03745 DC 0Adc AC 0Aac
+PULSE 0 0.5A 0.1 0.001 0.001 0.2 2
Netlist
Netlist.cir
Circuit libraries.lib
Results.txt
Post
processing.m
FPA
data.csv
Data
processing.m
Model
validation
Solver
  OOP
Model Description
Workflow Description
PSpice netlist

## Slide 12
Low maintenance as compared to GUI based tools
  Netlist is a general description of a modelled circuit
Simplified extension to other circuits
  Thanks to the library structure and to protocols that define how to develop it
Easy versioning and code sharing
  Also considering the GitLab repository
The final goal is a quick fault analysis
  Minimum set of measures to identify a fault (support to the ELQA Team)
  Identification of the fault location from the available measurements
Examples
  RQ.A78, Earth failure on 13 Oct 2015, fault position detected in 24h
  RCS.A78B2, intermittent short to ground, first on 16 Jul 2015
PSpice netlist: motivations

## Slide 13
For a FPA @ 2kA, 10A/s the model has been validated against
  Previous results: E. Ravaioli et al., Modelling of the Voltage Waves in the LHC Main Dipole Circuits, IEEE Trans. on Applied Superconductivity, 22(3), 2012 (not shown here)
  New FPA data obtained on Oct 2014: the moving average filter of the nQPS is applied to the following traces
Simulation
Measurements
— Simulation
X, X Measurements
PSpice netlist: model validation at 2kA
missing
data

## Slide 14
For a FPA @ 10kA, 10A/s the model has been validated against
  New FPA data obtained on Oct 2014: the moving average filter of the nQPS is applied to the following traces
The model provides accurate predictions also at this current level
  The impact of the nonlinear effects on the voltage oscillations is limited
Simulation
Measurements
— Simulation
X, X Measurements
PSpice netlist: model validation at 10 kA
missing
data

## Slide 15
In Oct 2014 dump crowbars were installed on the output filter of the PC
  Eliminate voltage oscillations due to the LC filter
PSpice netlist: changes in the RB circuit
Simulated, w/o dump crowbars
Simulated, with dump crowbars
The model needs to be re-validated starting from new experimental data
X. Genillon, H. Thiesen, "Installation of Dump Crowbars on the LHC Main Dipole Power Converters"

## Slide 16
For a FPA @ 10kA, 10A/s the model has been validated against
  New FPA data obtained on Feb 2015: the moving average filter of the nQPS is applied to the following traces
The model provides accurate estimates also after the installation of the dump crowbars
  Their impact on the voltage oscillations across magnets is evident
Simulation
Measurements
— Simulation
X, X Measurements
PSpice netlist: model validation at 10 kA, dump crowbars
missing
data

## Slide 17
This project has to be imported in GitLab to improve cooperation and allow an effective versioning
  Two different branches can be created: simulation and experimental data processing
Development of the model for the HL-LHC 11T dipole magnets
  A preliminary model has been already developed but requires further work
The PSpice netlist approach has to be applied to the other circuits of the LHC
PSpice netlist: next steps

## Slide 18
MATLAB/Simulink framework for quench-protection and fault-cases studies
M. Maciejewski, "Automated Object-Oriented Simulation Framework for Superconducting Magnets Modelling
at CERN", Technical University of Lodz, Lodz, 2014
hcable
wcable
lcoil
dstrand
2D Electro-thermal lumped-element model including
- Inter-Filament and Inter-Strand Coupling Losses
Three-layer architecture
Model Description
Workflow Description
Transient Analysis with Lumped Elements of Superconductors

## Slide 19
Model validation (experiments) | HL-LHC | FCC
HQ02b | D1-D2 (standalone and in a chain) | HD2
MQXC | MQXF | 
MB | 11 T dipole | 
MQY | Q4 | 
RCS chain | HT | 
MB
MB
HD2
Users:
Emmanuele
Alejandro
Jonas
Michał
Lorenzo
TALES – use cases

## Slide 20: Overview Common Workflow Network Solvers FEM Solvers Co-Simulation

## Slide 21
D. Paudel, "Quench Simulation of Superconducting Magnets with Commercial Multiphysics Software", Aalto University, Espoo, 2015
Approximation fun. order
QP3 - Linear
ANSYS - Linear (was used)
Requires discretization in the scale less than 1 mm
In COMSOL Convergence achieved with discretization scale of 1 cm (Cubic order approximation )
n = 1000 Linear, Computation time = 110 s (QP3 )
QP3 like 1D strand model
Model Description
Single 1D 1 m long turn model of heat transfer in coil turn with nonlinear helium. I = 150 A , B = 2.88 T, T = 1.9 K
Notes: Physical model

## Slide 22
Coil Geometry
CAD
ROXIE
Turn2turn Mapping
1D FEM Thermal Model
Physics
Coil | Helium
Solver





Single 1D 2.25 km long line model representing heat propagation in the LHC dipole magnet. I = 4200 A , B = 2.88 T
Model Description
Workflow Description
1D FEM Coil Model Development Workflow

## Slide 23
Equivalent cable magnetization model:
No need to model in detail the cable internal structure;
Eddy-currents magnetization is related directly with magnetic flux change
Laws of Faraday-Lenz and Ampere are combined with a-priori knowledge about eddy currents path.
Flux density [T]
Flux change [T/s]
Equivalent
magnetization [A/m]
Induced currents [A/m^2]
Transient analysis:
dI/dt = 10 [A/s]
t = 10 [s]
Model Description
FEM Feasibility study: D1 magnet

## Slide 24
Magnet Features:
Geometry
Materials
OOP application for model creation:
Geometry
Materials
Physics
Mesh
Studies
.mph model
Comsol server:
Model dynamic repository
Interface
Tasks allocation
Comsol engine(s)
Comsol GUI
Post processing
*Optional cluster
352 different domains to be defined:
Geometry
Materials
Physics
Post-processing
Therefore, the process has to be automated
Workflow Description
FEM Feasibility study: D1 magnet

## Slide 25
Coil Geometry
CAD
ROXIE
Automatic detection of thermal contacts
3D FEM Model
Unstructured | Structured
Physics
Heat Exchange| Magnet, Helium
Solver
Additional elements
Heaters
Central Post
Wedges
Mid-plane insulation
Interlayer insulation
Entire cold-mass
Water Heat Exchange
Coil geometry
Winding direction
#1 How to adaptively mesh 3D to get 1D performance?
#3 Performance optimisation
#2 Tips on how to read geometry from CAD
Meeting with Sven Friedel at COMSOL HQ Switzerland in Zurich – 7 Sep 15
(COMSOL API) MATLAB/Java
3D FEM Coil Model Development Workflow

## Slide 26: Overview Common Workflow Network Solvers FEM Solvers Co-Simulation

## Slide 27
Meeting with Prof. Sebastian Schoeps at TU Darmstadt on 23-27.03.15
Electrical part
L1
R1
Lif,y,1
iif,y,1
Lif,x,1
iif,x,1
i1
Mif,y,1,1
Mif,x,1,1
Rif,x,1
Rif,y,1
REE=0.06Ω
Thermal part
PC
kHe,b
THe
cth,b
Q_ifcl
Heat load
calculation
i1
B1
Q=q*Q_ohmic+(1-q)*Q_ifcl,
q = 1 if quenched, otherwise 0
Q
R=f(T)
1 ms time window,
10 ms after quench
1 ms time window,
1 ms after quench
Co-simulation of a single strand with MpCCI
Model Description

## Slide 28
Thermal model B:
Electrical model A:
2) ib; Qifcl
dim 1x1
4) dim 1x1
3)
5)
MpCCI serial simulation coupling
6)
1)
7)
8)
9)
10)
Code B: Matlab electrical network should be simulated to obtain current ib, magnetic field Bb and AC losses – Qifcl
ib, magnetic field Bb, and Qifcl are passed to the Code A.
Code A: COMSOL receives appropriate signals from Code B and runs a simulation for certain time span. The result is a temperature distribution in the 1D turn that allows calculating resistance value at each node.
The sum of resistances Rb (turn is a series connection of nodes) is then passed to the Code B that will include it in the electrical network calculations as a lumped resistance.
Repeat 1)
Co-simulation: weak coupling with 1D COMSOL
Workflow Description

## Slide 29
LEM-FEM approach:
PSPICE performs electrical network analysis;
COMSOL takes care about solving the electro-thermal problem.
Benefits:
Full electro-thermal dynamic phenomena;
Full electro dynamic circuit analysis;
Nodal structure suitable for parallelism.
Flux density [T] - D1 magnet
Co-simulation: LEM-FEM codes for RB model

## Slide 30
Meeting with Prof. Sebastian Schoeps at TU Darmstadt on 23-27.03.15
Co-simulation: theoretical description of interdomain coupling

## Slide 31
Electro thermal
Electromagnetic
Electrical
PSpice
Simulations Coupling (MpCCI, Java)
Electro thermal
CAD
ROXIE
Computational Fluid Dynamics Helium Modelling
Open Foam
Coil geometry
Winding direction
Collaboration with Fraunhofer Institute and MpCCI trial.
Co-simulation: scheme for 3D simulations
Domain decomposition

## Slide 32
Future FEM Simulations
The Canted-Cosine-Theta Dipole (CCT) For LBNL High Field Magnet Program
Coil Minimum Symmetry

## Slide 33: R&D Topics with External Partners
Topic | Action
Multi-rate domain decomposition and high performance computing (TEMF, TU Darmstadt) | Meeting 13/14.01.2016 at CERN
Port-Hamiltonian analysis of consistent coupling strategy (LAGEP, Uni Lyon) Port-Hamiltonian School in Berlin Port-Hamiltonian Workshop in Berlin | Meeting 20.01.2016 in Valance 4-6.04.2016 7-8.04.2016
1st School on Numerical Modeling for Applied Superconductivity | 20-24.06.2016
Fraunhofer Institute (MpCCI) collaboration on co-simulation interfaces | tbd
COMSOL support | on-going