## Slide 1
Nb-Ti Strand and 2D magnet coil
Deepak Paudel
March 2015, Geneva
Supervisor:
Bernhard Auchmann

## Slide 2
Normal zone propagation modelled correctly for Adiabatic and single regime analysis
Nb-TI strand; ANSYS vs QP3 Model
ANSYS
QP3

## Slide 3
Error Anaysis
Different time steps;
Fixed, 20 µs (ANSYS)
Adaptive, smallest 3 µs (QP3)
Different regime changing algorithms.
No possibility to fall back once it has been to the higher regime (ANSYS)
No possibility to fall back to transient regime once it has been to higher regime (QP3)
Nb-TI strand: ANSYS vs QP3 Model;

## Slide 4
Time steps:
Fixed, 3 µs (ANSYS)
Adaptive, smallest 3 µs (QP3)
Same regime changing scheme
Nb-TI strand: ANSYS vs QP3 Model;

## Slide 5
Nb-Ti strand models
Element Switching
Heat conduction along conductor, 1D thermal element.
Heat conduction along Helium,1D thermal element.
Non-linear heat transfer, 5 contact elements.
nkap = float/integer
Mass element and HTC
Heat conduction along conductor, 1D thermal element.
Helium as mass element
Non-linear heat transfer, (
nkap = Integer
Source and Sink
Heat conduction along conductor, 1D thermal element.
Helium cooling (negative heat generation load)
nkap = float/Integer
Nb-Ti Strand
He-Mass
Helium cooling
Joule heating
1
2
i
n

## Slide 6
Element Switching

## Slide 7
Q(()
Mass element and HTC

## Slide 8
1
2
i
n
Source and Sink

## Slide 9
PERFORMANCE ANALYSIS
QP3
Adaptive time stepping
Min Δt = 3e-5 s
Max Δt = 1e-4 s
ANSYS
Fixed time step
Δt = 3e-5 s
21350 steps
Chart: Computation time (Minute)
| HTC | Element Switching | Source and Sink
QP3 | 0.75 | 0.75 | 0.75
ANSYS | 251 | 350 | 167
Total simulation time 0.064 s

## Slide 10
PERFORMANCE ANALYSIS
Chart: Computation time (second)
| Adiabatic
QP3 | 242.5
ANSYS | 66.88
QP3
Adaptive time stepping
Min Δt = 5e-5 s
Max Δt = 1e-4 s
ANSYS
Adaptive time stepping
Min Δt = 1e-5 s
Initial Δt = 1e-5 s
Max Δt = 1e-3 s
Total simulation time 0.2 s

## Slide 11
2D AND 3D MODEL OF THE MAGNET COIL; GEOMETRY
ANSYS APDL
Macros and algorithms builds the geometry
Parametrisation
ANSYS Workbench
Import CAD file/ construct via GUI
Limited Parametrisation
Easy
Simplify
CAD file SMC 11T

## Slide 12
2D AND 3D MODEL OF THE MAGNET COIL
Length = 1 m
Nb-Ti, Rutherford cable
Kapton= contact elements
Thermal resistance defined through contact elements
Length =1 m
Parametric construction

## Slide 13
Computation time; ̴ 3 min (800 Elements )
Computation time; ̴ 1 hour (20,000 Elements)

## Slide 14
2D AND 3D MODEL OF SMC 11 T
Nb3Sn, Rutherford cable
G10
̴ 300 mm
Imported CAD file
Simplified model

## Slide 15
Computation time: 4 minute, Discretization: 0.75 mm (1400 elements) minimum Δt: 1e-5s
QUENCH PROPAGATION

## Slide 16
QUENCH PROPAGATION
Computation time: 4 hour, Discretization: 280,000 elements minimum Δt: 1e-5s

## Slide 17
HOTSPOT TEMPERATURE
Computation time: 4 hour, Discretization: 280,000 elements minimum Δt: 1e-5s