## Slide 1: Beam losses in the triplet due to AC-dipole excitation
V. Chetvertkova

## Slide 2: Contents
27 May, 2.11 am: Sequence of events
Concerns
MAD-X simulations
Conclusions

## Slide 3: Sequence of events
Optics measurements
Beam:
  6 bunches at 6.5 TeV
  intensity ~7e9 (SMP: present, safe)
Beam setup/ squeeze
BSTAR: 0.8 / 10 / 0.8 / 3 m
Half-gap of the collimators:
  TCP.D6R7 (vert.): 4.5 mm
  TCP.C6R7 (hor.): 6 mm
  TCTPV.4R5: 15 mm
  TCTPH.4R5: 15 mm
The beam was excited by AC dipole (MKQA.6L4)

## Slide 4: Sequence of events
Beams were dumped due to 10ms RS by a BLM at IP5:

## Slide 5: Sequence of events
Beams were dumped due to 10ms RS by a BLM at IP5: BLMQI.02L5.B2E22_MQXB
  Beam losses were observed during ~15ms, with peaks every ~3ms
BPM ORBIT:
Frequency of the AC dipole trimmed too close to the tune value

## Slide 6: Sequence of events

## Slide 7: Sequence of events

## Slide 8: Concerns
Why was the triplet at IP5 first hit by beam losses? Is this the general aperture limitation?
The TCT in IR5 did not protect the triplet, why?
What should be the position of the TCT to protect the triplet?

## Slide 9: MAD-X simulations
V6.503 sequence
0.8 / 3 / 0.8 / 3 m optics
3.5 mm·mrad – normalized emittance
Task:
Check where the losses occur when MKQ has
  Tune frequency (Qy = 59.32)
  Nearly tune frequency (Qy-0.001; Qy-0.01)
Check the aperture size at the bottlenecks
0.8 / 10 / 0.8 / 3 m optics was not yet available at the time of event

## Slide 10: MAD-X: Comparison of sigmas
 |  | RUN 1 : 0.8 / 3 / 0.8 / 3 |  |  |  |  |  |  | RUN 2: 0.8 / 10 / 0.8 / 3 |  |  | 
NAME | S, m | Aperture-X, mm | Aperture-Y, mm | SIGMA-X, mm | SIGMA-Y, mm | Aperture-X, sigma | Aperture-Y, sigma |  | SIGMA-X, mm | SIGMA-Y, mm | Aperture-X, sigma | Aperture-Y, sigma
TCTPV.4R5.B2 | 13183.95 | 40 | 15 | 0.74 | 0.47 | 53.93 | 31.86 |  | 0.74 | 0.47 | 54.02 | 31.64
TCP.D6R7.B2 | 6460.043 | 40 | 4.5 | 0.28 | 0.20 | 141.19 | 22.63 |  | 0.28 | 0.20 | 141.75 | 22.54
TCP.C6R7.B2 | 6462.043 | 6 | 40 | 0.28 | 0.20 | 21.76 | 195.61 |  | 0.27 | 0.21 | 21.85 | 194.80
MQXA.3R5 | 13282.32 | 28.9 | 24 | 0.86 | 1.13 | 33.48 | 21.17 |  | 0.98 | 1.01 | 29.58 | 23.77
MQXB.B2R5 | 13290.74 | 28.9 | 24 | 1.22 | 0.73 | 23.77 | 32.99 |  | 1.24 | 0.65 | 23.37 | 36.93
MQXB.A2R5 | 13297.24 | 28.9 | 24 | 1.16 | 0.60 | 24.87 | 40.11 |  | 1.03 | 0.60 | 28.18 | 39.78
MQXA.1R5 | 13306.32 | 28.9 | 24 | 0.69 | 0.63 | 42.12 | 38.15 |  | 0.58 | 0.58 | 50.05 | 41.56
MQXA.1L5 | 13358.62 | 28.9 | 24 | 0.63 | 0.69 | 45.94 | 34.98 |  | 0.63 | 0.85 | 45.95 | 28.16
MQXB.A2L5 | 13366.84 | 28.9 | 24 | 0.60 | 1.16 | 48.30 | 20.65 |  | 0.63 | 1.23 | 45.84 | 19.54
MCBXV.2L5 | 13367.31 | 28.9 | 24 | 0.64 | 1.23 | 45.18 | 19.48 |  | 0.64 | 1.23 | 45.19 | 19.47
MQXB.B2L5 | 13373.34 | 28.9 | 24 | 0.73 | 1.22 | 39.73 | 19.74 |  | 0.85 | 1.12 | 34.00 | 21.40
MQXA.3L5 | 13382.62 | 28.9 | 24 | 1.13 | 0.86 | 25.49 | 27.80 |  | 1.16 | 0.82 | 24.81 | 29.23
The tracking simulations were done with available Run 1 optics.
To be checked with actual Run 2 optics, however no significant differences are expected.

## Slide 11: MAD-X: Comparison of the loss patterns in case of various MKQ kicks
If the MKQ frequency is equal to
Qy
Qy-0.001
Losses are mostly observed in MCBXV.2L5
If the difference with tune is 0.01 (Qy-0.01)
– no losses are observed

## Slide 12: Conclusions
In case of AC dipole vertical excitation with the frequency close to that of the tune, the aperture bottleneck is located not in the triplet (not in the quadrupole), but in the corrector magnet in between two quadrupoles within the triplet.
In order to intercept the losses in the triplet-region, the TCT should be moved to <19 sigma.