## Slide 1: From 10-12 TeV to 1016 TeV Introduction to accelerator physics and technology: The Large Hadron Collider Rüdiger Schmidt KIT Workshop Freudenstadt 2015

## Slide 2: To accelerate a particle to very very high energy …
Particle energy about 2*1010 TeV

## Slide 3
To accelerate particles to much lower energy
….… 6.5 TeV for a proton, for an ion >500 TeV Energy stored in the entire proton beam = 2*1015 TeV

## Slide 4
LHC pp and ions
7 TeV/c – up to now 6.5 TeV/c
26.8 km Circumference
CERN Main Site
Switzerland
Lake Geneva
France
LHC Accelerator
(100 m down)
SPS Accelerator
CERN-Prevessin
CMS, TOTEM
ALICE
LHCb
ATLAS

## Slide 5: LHC: A long story starting in the distant past
First ideas to first protons: from 1984 to 2008
Tears of joy…. first beam in 2008
Tears of despair (and hopefully last) accident in 2008
The story of the champagne bottles

## Slide 6: Overview
Accelerator physics and LHC crash course - DONE
Energy and Luminosity
What is accelerator physics?
Acceleration and deflection of charged particles
Energy and Luminosity Challenges
Short Accelerator Physics Course
Particle Energy and Superconducting Magnets
Understanding LHC operation
Challenges for high intensity beams operation
Preparing for the next 20 years: HL-LHC…..
Preparing for the next 50 years: FCC study…..

## Slide 7: Energy and Luminosity

## Slide 8: Energy and (integrated) Luminosity
Particle physics requires an accelerator colliding beams with a centre-of-mass energy as high as possible
The event rate is determined by cross-section and luminosity
In order to observe events with low cross-section, the luminosity should exceed 1034 [cm-2s-1]
The time available for data-taking with high luminosity is important

## Slide 9: Integrated Luminosity and Availability
The total number events is proportional to the Integrated Luminosity:
It has the unit of [cm-2] and is expressed in Inverse Picobarn or Inverse Femtobarn
The availability of the accelerator plays an essential role: all systems must work correctly, very challenging for such complex machine

## Slide 10: The LHC: just another collider ?
 | Start | Type | Max proton energy [GeV] | Length [m] | B Field [Tesla] | Lumi [cm-2s-1] | Stored beam energy [MJoule]
TEVATRON Fermilab Illinois USA | 1983 | p-pbar | 980 | 6300 | 4.5 | 4.3 1032 | 1.6 for protons
HERA DESY Hamburg | 1992 | p – e+ p – e- | 920 | 6300 | 5.5 | 5.1 1031 | 2.7 for protons
RHIC Brookhaven Long Island | 2000 | Ion-Ion p-p | 250 | 3834 | 4.3 | 1.5 1032 | 0.9 per proton beam
LHC CERN | 2008 | Ion-Ion p-p | 7000 Now 6500 | 26800 | 8.3 | 1034 Now 7.7× 1033 | 362 now 180
Factor |  |  | 7 | 4 | 2 | 50 | 100

## Slide 11: What is Accelerator Physics ?

## Slide 12
thinking, thinking, thinking …. and predicting the results
....sometimes correctly!
Peter Higgs

## Slide 13
…building the detectors and
analysing the results
Experimental Physicist
F.Gianotti Person of the year

## Slide 14: The hierarchy in physics
19/7/2012
citing Mike Lamont (Head of CERN accelerator operation):
Among physicists there is a hierarchy: » On top are the theorists, then the experimental physicist, then us, the machine people.«
German original: Und unter den Physikern gebe es eine Hierarchie: »Ganz oben stehen die Theoretiker, dann kommen die Experimentalphysiker und dann wir, die Maschinenleute.«

## Slide 15
…building very long, exceptionally cold and extremely complex machines …
Accelerator Physicist
Plumber of the year

## Slide 16: What is accelerator physics … and technology?
The physics and engineering required to plan, develop, construct and operate particle accelerators
Electrodynamics
Relativity
Particle physics, nuclear physics and radiation physics
Thermodynamics
Mechanics
Quantum Mechanics
Physics of nonlinear systems
Material science, solid state physics and surface physics
Vacuum physics
Plasma physics and laser physics
Plus: mechanical engineering, electrical engineering, computing science, metrology, civil engineering
Plus: Management, reliability engineering and system engineering
What does he need to know?
A fairly clever plummer is needed

## Slide 17: Acceleration and deflection of charged particles How to get to high energy? How to make many collisions (~109/s)?

## Slide 18: Lorentz Force
The force on a charged particle is proportional to the charge, the electric field, and the vector product of velocity and magnetic field:
For an electron or proton the charge is:
Acceleration (increase of energy) only by electrical fields – not by magnetic fields:

## Slide 19: Particle acceleration
  Acceleration of elementary particles to high energy in an electrical field, e.g. 1 GeV => 1 GV
    No constant electrical field above some Million Volt (break down)
    => Use of time dependent electrical field
1 MeV requires U = 1 MV

## Slide 20: Particle acceleration with RF cavity
LHC RF frequency 400 MHz (typical frequency for an accelerator)
Time varying field
Maximum field about 30-40 MV/m
Beams are accelerated in bunches (no continuous beam)

## Slide 21: RF systems: 400 MHz
400 MHz system:
16 superconducting cavities (copper sputtered with niobium) for 16 MV/beam, built and assembled in four modules

## Slide 22: 400 MHz RF buckets and bunches
E
time
RF Voltage
time
LHC bunch spacing = 25 ns / 50 ns = 10 / 20 buckets  7.5 m / 15 m
2.5 ns
The particles are trapped in the RF voltage:
this gives the bunch structure
RMS bunch length 11.2 cm 7.6 cm
RMS energy spread 0.031% 0.011%
450 GeV 7 TeV
The particles oscillate back and forth in time/energy
RF bucket
2.5 ns

## Slide 23
To collide particles at very high energy
Linear collider versus Circular collider

## Slide 24: Linear accelerator: use accelerating structure once
Accelerating beams to high energy in a linear collider:
The beams are accelerated during one passage and the perticles are colliding only once at the center of the experiment
Experiment
Accelerating structures
Accelerating structures
  Acceleration of particles with time-varying electrical field
    Limit 30-40 MeV/m with superconducting cavities
    Limit about 100 MeV/m with other technologies, not yet used (CLIC)
    Some 100 GeV … ~TeV conceivable for e+e- colliders
    Reaching an energy of 14 TeV c.m. (such as LHC) would require an accelerator with a length > 400 km (with 40 MV/m)
    Long-term: acceleration in a plasma … not ready for a HEP collider

## Slide 25: Circular accelerator: re-use accelerating structure
Accelerating structure
Magnets around the accelerator to bring the beam back to the accelerating structure
Accelerating beams to high energy in a synchrotron
Beam are injected into the accelerator
The particles make many turns
The magnetic field is slowly increased, and particles are accelerated when travelling through the accelerating structure
The beams can be extracted, or stored for many hours at top energy, bunches collide each turn
Major limitations: emission of synchrotron radiation and strength of the magnetic field
Experiment
Today achieved particle momentum of 6.5 TeV/c at LHC

## Slide 26: Synchrotron – circular accelerator
LHC circular machine with energy gain per turn ~0.5 MeV
acceleration from 450 GeV to 6.5 TeV takes about 20 minutes
Experiment
Experiment

## Slide 27: Operational cycle of a synchrotron
Time
Magnetic field
26 GeV
Injection
450 GeV
Cycle ~20 s
CERN - SPS
Injection
Beam intensity
Injection at low energy
Ramping of magnetic field and acceleration by RF field
Operation (collisions) at top energy
Can be extended

## Slide 28
Particle Energy challenge

## Slide 29: Major limitation: Synchrotron Radiation
Electromagnetic radiation is emitted when charged particles are accelerated radially: synchrotron radiation.
Power of synchrotron radiation for one particle with the energy and the mass in a deflecting field with the bending radius assuming the charge :
LEP with electron-positron beams at 100 GeV/c: 16000 kW
LHC with proton-proton beams at 7000 GeV/c
and about 100 times more particles: 2.2 kW

## Slide 30: Major limitation: Strength of deflecting field
The force on a charged particle is proportional to the charge, the electric field, and the vector product of velocity and magnetic field given by Lorentz Force:
Momentum of a particle in a magnetic field:
z
x
s
v
B
F
  Example for LHC
  Radius = 2805 m fixed by LHC (former LEP) tunnel
  Magnetic field B = 8.33 Tesla (NbTi magnets) with high field superconducting magnets
  Maximum momentum 7000 GeV/c

## Slide 31: LEP / LHC in tunnel with a length of 27 km
Particles | Momentum [GeV/c] | Energy loss per turn [GeV] | Energy loss per turn [%] | Energy loss [MeV/m] | Bending field [T]
e+e- | 102.00 | 3.22 | 3.16 | 0.172 | 0.12
p | 7000.00 | 6.29E-06 | 0.00 | 0.000 | 8.30
p | 187232.00 | 3.22 | 0.00 | 0.000 | 222.00
e+e- | 7000.00 | 71385649.93 | 1019795.00 | 3818950.942 | 8.30
e+e- | 175.00 | 27.89 | 15.93 | 1.492 | 0.21

## Slide 32: LEP / LHC tunnel: limitations for protons
Particles | Momentum [GeV/c] | Energy loss per turn [GeV] | Energy loss per turn [%] | Energy loss [MeV/m] | Bending field [T]
e+e- | 102.00 | 3.22 | 3.16 | 0.172 | 0.12
p | 7000.00 | 6.29E-06 | 0.00 | 0.000 | 8.30
p | 14000.00 | 1.02E-04 | 0.00 | 0.000 | 16.60
p | 187232.00 | 3.22 | 0.00 | 0.000 | 222.00
e+e- | 7000.00 | 71385649.93 | 1019795.00 | 3818950.942 | 8.30
e+e- | 175.00 | 27.89 | 15.93 | 1.492 | 0.21
Protons with synchrotron radiation loss GeV/turn as electrons in LEP: magnetic field more than one order of magnitude above what is possible today (14 TeV could possibly be conceived)

## Slide 33: LEP / LHC tunnel: limitations for e+e-
Particles | Momentum [GeV/c] | Energy loss per turn [GeV] | Energy loss per turn [%] | Energy loss [MeV/m] | Bending field [T]
e+e- | 102.00 | 3.22 | 3.16 | 0.172 | 0.12
p | 7000.00 | 6.29E-06 | 0.00 | 0.000 | 8.30
p | 14000.00 | 1.02E-04 | 0.00 | 0.00 | 16.60
p | 187232.00 | 3.22 | 0.00 | 0.000 | 222.00
e+e- | 7000.00 | 71385649.93 | 1019795.00 | 3818950.942 | 8.30
e+e- | 175.00 | 27.89 | 15.93 | 1.492 | 0.21
Electrons with same magnetic field as protons in LHC: energy loss in a few cm.
……. and with a large reduced field, but somewhat higher than LEP, still much too high

## Slide 34
Luminosity challenge
How to make many collisions (~109/s)?

## Slide 35: How to get to many many many many collisions ?

## Slide 36: Luminosity parameters for a circular collider
Head-on crossing: L =
N … number of protons per bunch
… revolution frequency
… number of bunches per beam
… beam dimensions at interaction point

## Slide 37: LHC Luminosity: parameters for head on collisions
Beam size 16 m,
for  = 0.5 m ( is a function of the lattice)
Beam size given by injectors and by space in vacuum chamber
Number of protons per bunch 1.11011 (limited to about 31011 due to the beam-beam interaction and beam instabilities)
f = 11246 Hz
~2800 bunches (every 25 ns one bunch) L = 1034 [cm-2s-1]
L = = 1, one bunch)
Watch out for another limitation: Event pile-up

## Slide 38
The price of the high luminosity with fewer collisions: for each bunch crossing there are up to ~35 interactions.
2010: ~ 2 events/x-ing
2011: ~ 10 events/x-ing
2012: ~ 20 events/x-ing

## Slide 39: Crossing parameters with many bunches
Illustration drawing
Large beam size in adjacent quadrupole magnets
Crossing angle to avoid additional collision points
Separation between beams needed, about 10  ( = rms beam size)
Limitation with aperture in quadrupoles
Quadrupole
Quadrupole
Collision point in experiment
~ 80m
Parasitic crossing
Parasitic crossing

## Slide 40: Experimental long straight sections
The 2 LHC beams are brought together to collide in a ‘common’ region
Over ~260 m the beams circulate in one vacuum chamber with ‘parasitic’ encounters (when the spacing between bunches is small enough)
Total crossing angle of about 300 mrad

## Slide 41: Event pile up in LHC experiments
Assuming nominal parameters, for one bunch crossing, the number of colliding proton pairs (events) is given by:
L =

## Slide 42: Challenges for high luminosity operation
Large beam intensity => Energy stored in beams
Dumping the beam in a safe way in case of failure
Avoiding beam losses, in particular in the superconducting magnets (beam induced magnet quenching (for LHC, when 10-8-10-7 of beam hits magnet at 7 TeV/c)
Radiation, in particular in experimental areas from beam collisions (beam lifetime is dominated by this effect)
Beam dynamics
Instabilities and Electron Cloud
UFOs
Beam-beam effects

## Slide 43: Energy stored in the beam
362 MJoule: the energy stored in one LHC beam corresponds approximately to…
90 kg of TNT
8 litres of gasoline
15 kg of chocolate
It’s how ease the energy is released that matters most !!
The energy of an 200 m long fast train at 155 km/hour corresponds to the energy of 362 MJoule stored in one LHC beam
For LHC at 7 TeV/c the energy stored in the beam is equal to 362 MJ

## Slide 44: Some essential parameters for accelerators
Particle type (e+, e-, p, antiproton, ion, …)
Energy / momentum of a particle
Beam intensity / beam current
Beam size => beam emittance
Trajectory / closed orbit
Betatron oscillations
Betatron tune (Q value)
L =

## Slide 45: Short Accelerator Physics Course How to transport particles in an accelerator?

## Slide 46: CERN accelerator complex
?
?
?
?
High intensity beam from SPS to LHC at 450 GeV via TI2 and TI8, LHC accelerates to 7 TeV

## Slide 47: SPS, transfer line and LHC
Beam is accelerated in the SPS to 450 GeV (stored energy of 3 MJ)
Beam is transferred from SPS to LHC
Beam is accelerated in the LHC to 6.5 TeV (stored energy of some 100 MJ)
Scraping of beam in SPS before transfer to LHC
1 km
Transfer line 3km
LHC
SPS
6911 m
450 GeV / 400 GeV
3 MJ
Acceleration cycle of ~10 s
CNGS Target
IR8
Switching magnet
Fast extraction kicker
Injection kicker
Transfer line
Injection kicker
IR2
Fast extraction kicker

## Slide 48: Beam transport
Need for getting protons on a circle: dipole magnets
Need for focusing the beams with lenses:
Particles with different injection parameters (angle, position) separate with time
  Assuming an angle difference of 10-6 rad, two particles would separate by 1 m after 106 m. At the LHC, with a length of 26860 m, this would be the case after 50 turns (5 ms !)
Particles would „drop“ due to gravitation
The beam size must be well controlled
  At the collision point the beam size must be tiny
Particles with (slightly) different energies should stay together

## Slide 49: Force by quadrupole magnets
Here: a particle with positive charge travels in s-direction, into the table
z
x
x
z
s
z
s
x
Side view: focusing
View along particle path
Top view:
defocusing
From Maxwell’s
equations

## Slide 50: Focusing by two quadrupole magnets, thin lenses
d = 50 m
Horizontal plane
Vertical plane

## Slide 51: Phase Space of an ensemble of particles
X
X’
X
X’
X

## Slide 52: Phase Space of an ensemble of particles
X
X’
X
X’
X

## Slide 53: Phase Space of an ensemble of particles
X
X’
X
X’
X

## Slide 54: Phase Space of an ensemble of particles
Many particles, same „normalised“ amplitude
Real beam: many particles, different amplitudes
X
X’
X’
X
This conservation law: phase space volume occupied by a collection of systems evolving according to Hamilton's equations of motion is preserved in time

## Slide 55: Betatron oscillations for many particles
K.Wille
Beam size at longitudinal position s
The emittances x and z are statistical values.
decreases proportional to the particle energy during acceleration (adiabatic damping).
for each plane x and z

## Slide 56: Light and particle sources

## Slide 57: Particle stability and magnets
Particle oscillations in quadrupole field (small amplitude)
Harmonic oscillation after coordinate transformation
Circular movement in phase space
All particles in a circular accelerator oscillate around a trajectory in the accelerator: the closed orbit
With correct coordinate transformation, these betatron oscillations have sinusoidal shape
This is exactly true for a system with linear fields (only quadrupolar fields), and only approximately true for non-linear field

## Slide 58: Magnets and beam transport
Dipole magnets
  To make a circle around LHC
Quadrupole magnets
  To keep beam particles together
  Particle trajectory stable for particles with nominal momentum
Sextupole magnets
  To correct the trajectories for off momentum particles
  Particle trajectories stable for small amplitudes (about 10 mm)
Multipole-corrector magnets
  Sextupole - and decapole corrector magnets at end of dipoles
Particle trajectories can become instable after many turns (even after, say, 106 turns)

## Slide 59: A (F0D0) cell in the LHC arcs
SSS
quadrupole
MQF
sextupole
corrector
(MCS)
decapole
octupole
corrector
(MCDO)
lattice sextupole (MS)
lattice sextupole
(MS)
lattice sextupole
(MS)
orbit corrector
special corrector (MQS)
special corrector (MO)
special corrector (MO)
quadrupole
MQD
quadrupole
MQF
main
dipole
MB
orbit corrector
orbit corrector
main
dipole
MB
main
dipole
MB
main
dipole
MB
main
dipole
MB
main
dipole
MB
LHC Cell - Length about 110 m (schematic layout)
Vertical / Horizontal plane
(QF / QD)
Quadrupole magnets controlling the beam size „to keep protons together“ (similar to optical lenses)
10000 magnets powered in 1700 electrical circuits

## Slide 60: Particle stability and magnets
Particle oscillations in quadrupole field (small amplitude)
Harmonic oscillation after coordinate transformation
Circular movement in phase space
Particle oscillation assuming non-linear fields, large amplitude
Amplitude grows until particle is lost (touches aperture)
No circular movement in phasespace

## Slide 61: Visualising bunch oscillation in accelerator

## Slide 62: Particle energy and superconducting magnets …….the magnetic field strength determines the beam energy

## Slide 63: Superconducting magnets in LHC tunnel
  Deflection by 1232 superconducing dipole magnets

## Slide 64: Dipole magnets for the LHC
1232 Dipole magnets
Length about 15 m
Magnetic Field 8.3 T for 7 TeV
Two beam tubes with an opening of 56 mm
plus many other magnets, to ensure beam stability (1700 main magnets and about 8000 corrector magnets)

## Slide 65: Coils for Dipolmagnets

## Slide 66: Dipole magnet cross section
Beam tubes
Supraconducting coil
Nonmagetic collars
Ferromagnetic iron
Steelcylinder for Helium
Insulationvacuum
Supports
Vacuumtank
16 mBar cooling tube

## Slide 67: Coils: dipole and quadrupole magnets
Quadrupolemagnet

## Slide 68: Operating temperature of superconductors (NbTi)
The superconducting state only occurs in a limited domain of temperature, magnetic field and transport current density
Superconducting magnets produce high field with high current density
Lowering the temperature enables better usage of the superconductor, by broadening its working range
T [K]
B [T]
J [kA/mm2]

## Slide 69: Operational margin of a superconducting magnet
Bc
Tc
9 K
Applied Magnetic Field [T]
Bc critical field
1.9 K
QUENCH
Temperature [K]
quench with fast loss of ~5 · 106 protons
8.3 T
0.54 T
quench with fast loss of
~5 · 109 protons
Tc critical
temperature

## Slide 70: Dipole magnets from surface to tunnel

## Slide 71: LHC energy evolution
Energy (TeV)
7 TeV
Design
5 TeV
Magnet de-training after installation
2007
2008
2009
2010
2011
2012
2013
2014
2015
Decided to start operating at 5 TeV …..never got there

## Slide 72: September 10th 2008
A brief moment of glory

## Slide 73: September 19th 2008
On 19th September magnet interconnections became the hot topic for more than 1 year

## Slide 74: Incident September 19th 2008
Arcing in the interconnection
53 magnets had to be repaired
An interconnect was not ok and opened. An electrical arc provoked a He pressure wave damaging ~700 m of LHC, polluting the beam vacuum over more than 2 km
Over-pressure
Magnet displacement
(not so) Proud to present the:
LHC Horror Picture Show

## Slide 75: More problems on the joints
The copper stabilizes the bus bar in the event of a cable quench (=bypass for the current while the energy is extracted from the circuit).
Protection system in place in 2008 not sufficiently sensitive.
A copper bus bar with reduced continuity coupled to a badly soldered superconducting cable can lead to a serious incident.
During repair work, inspection of the joints revealed systematic voids caused by the welding procedure.
X-ray
Energy limitation for Run 1 !!
bus
U-profile
bus
wedge
Solder
No solder

## Slide 76: LHC energy evolution
Energy (TeV)
7 TeV
Design
5 TeV
Magnet de-training after installation
2007
2008
2009
2010
2011
2012
2013
2014
2015
3.5 TeV
Joint problems,
incident
1.18 TeV
Consolidation delays

## Slide 77: LHC is back !
20th November 2009: after 14 months of repair
3 weeks later

## Slide 78: LHC energy evolution
Energy (TeV)
7 TeV
Design
5 TeV
Magnet de-training after installation
2007
2008
2009
2010
2011
2012
2013
2014
2015
3.5 TeV
Joint problems,
incident
1.18 TeV
Consolidation delays
3.5 TeV
Operation after installation of new protection system
4 TeV
6.5 TeV
Interconnect improvements

## Slide 79: Understanding LHC operation
Filling
Ramp
Squeeze
Adjust
Stable beams
Pilot beam
Batches
Closed orbit
Beta function
Betatron tunes
Emittance
Impedance

## Slide 80: From first year to first fb-1
2008
First beam in LHC
2010
First fb-1

## Slide 81: …..to 2012

## Slide 82: 2015: arriving at 13 TeV cm energy

## Slide 83: Fill 2195 - start of the fill about 1 h (2011)
Start injection
End injection
Start energy ramp
End energy ramp
3.5 TeV
~1 hour

## Slide 84: Excellent fill (2011)
A nice long fill of about 18 hours……
For physics, the most interesting quantity is the integrated luminosity
Injection and ramp
Stable beams
Beam dump

## Slide 86: Challenges for high beam intensity operation Machine Protection and Collimation Electron clouds Instabilities UFOs Damage of components by em fields from beam

## Slide 87
LHC Layout
eight arcs (sectors)
eight long straight section (about 700 m long)
IR4: RF + Beam instrumentation
IR5:CMS
IR1: ATLAS
IR8: LHC-B
IR2: ALICE
Injection
Injection
IR6: Beam dumping system
IR3: Moment Beam Cleaning (warm)
IR7: Betatron Beam Cleaning (warm)
Beam dump blocks
Detection of beam losses with >3600 monitors around LHC
Signal to kicker magnet
Beams from SPS

## Slide 88: Hydrodynamic tunnelling
In case that the beam is accidentally deflected into a magnet, each bunch will heat the material.
The pressure will build up and the density is reduced.
The following bunches will penetrate deeper into the material.
A controlled experiment was performed at the SPS with a 1 MJ beam, demonstrating hydrodynamic tunnelling.
The penetration for the full beam at the LHC is expected to be around 30 m.
A single bunch at top energy could drill a hole in the vacuum chamber.
Target damaged by the SPS beam, after penetrating 60 cm of solid copper (~0.5% LHC beam energy)
F.Burkart, N.Tahir et al
Notes: 88

## Slide 89: Beam losses, machine protection and collimation
89
Continuous beam losses
Collimation prevents too high beam losses around the accelerator (beam cleaning)
A collimation system is a (very complex) system installed in the LHC to capture mostly halo particles
Such system is also called (beam) Cleaning System
Accidental beam losses
“Machine Protection” protects equipment from damage, activation and downtime
Machine protection includes a large variety of systems
Notes: 89

## Slide 90: Layout of beam dump system in IR6
Beam 2
Beam dump block
Kicker magnets to paint (dilute) the beam
about 700 m
about 500 m
15 fast ‘kicker’ magnets deflect the beam to the outside
To get rid of the beams (also in case of emergency!), the beams are ‘kicked’ out of the ring by a system of kicker magnets send into a dump block !
Septum magnets deflect the extracted beam vertically
quadrupoles
The 3 ms gap in the beam gives the kicker time to reach full field.
Ultra-high reliability system !!

## Slide 91: Beam dump line

## Slide 92: Beam dump with 1380 bunches
Beam spot at the end of the beam dumping line, just in front of the beam dump block

## Slide 93
RF contacts for guiding image currents
Beam spot
2 mm
View of a two sided collimator
about 100 collimators are installed in LHC
Ralph Assmann, CERN
length about 120 cm

## Slide 94: Betatron beam cleaning
Cold aperture
Cleaning insertion
Arc(s)
IP
Circulating beam
Illustration drawing
Arc(s)
Primary collimator
Secondary collimators
Tertiary beam halo + hadronic showers
Shower absorbers
Tertiary collimators
SC Triplet

## Slide 95: Beam Loss Monitors
Ionization chambers to detect beam losses:
  Reaction time ~ ½ turn (40 s)
  Very large dynamic range (> 106)
There are ~3600 chambers distributed over the ring to detect abnormal beam losses and if necessary trigger a beam abort !
Very important beam instrumentation!

## Slide 96: BLM system: beam losses before collisions
CMS Experiment
ATLAS Experiment
LHCb Experiment
ALICE Experiment
MomentumCleaning
RF and
BI
Beam
dump
Betatron Cleaning

## Slide 97: Continuous beam losses during collisions
CMS Experiment
ATLAS Experiment
LHCb Experiment
ALICE Experiment
MomentumCleaning
RF and
BI
Beam
dump
Betatron Cleaning

## Slide 98: Accidental beam losses during collisions
CMS Experiment
ATLAS Experiment
LHCb Experiment
ALICE Experiment
MomentumCleaning
RF and
BI
Beam
dump
Betatron Cleaning

## Slide 99: Accidental beam losses during collisions

## Slide 100: Limits to the bunch population
High bunch population and tight bunch spacing make the beams prone to instabilities related to impedances i.e. to self-generated fields
s
Orbit (pipe axis of symmetry)
Vacuum chamber
Induced (or ”image”) currents
”Source” particle
Direct EM interaction → ”direct space-charge”
EM interaction through the chamber wall→ ”impedance”
x
”Test” particle
s
V
~r.m.s 8 cm
~15 m
~1.6×1011 p

## Slide 101: Limits to the bunch population
High bunch population and tight bunch spacing make the beams prone to instabilities related to impedances i.e. to self-generated fields
s
Orbit (pipe axis of symmetry)
Vacuum chamber
Induced (or ”image”) currents
”Source” particle
Direct EM interaction → ”direct space-charge”
EM interaction through the chamber wall→ ”impedance”
x
In 2012 instabilities have become critical due to higher bunch intensity and tighter collimators settings  larger impedance. Cures:
  Transverse feedback
  Non-linear magnetic fields (sextupoles, octupoles, beam-beam) that produce a frequency spread among particles – kill coherent motion
We are far away from a full understanding!
”Test” particle

## Slide 102: Wake fields and Impedances Challenge
Intense bunches generate electromagnetic fields when passing inside a structure (in particular Carbon collimators – opening of ~1 mm!!!)
→ results in an EM force, called wake field in time domain coupling with the beam
Avoid the abrupt transition for the beam fields at the location of the beam passage (taper)
Reduce the resistivity of the material
Abrupt transition
With taper
B. Salvant

## Slide 103: Electron cloud challenge
In high intensity accelerators with positively charged beams and closely spaced bunches, electrons liberated on vacuum chamber surface can multiply and build up a cloud of electrons.
The cloud triggers vacuum pressure increases and beam instabilities!
Electron energies are in the 10 to few 100 eV range.
N
e-
Bunch N liberates e-
++++++
N+1
e-
Bunch N+1 accelerates e-,
multiplication at impact
++++++
N+2
e-
Process repeats for Bunch N+2 …
++++++
Beam screen

## Slide 104
Electron cloud effects
Possible consequences:
  instabilities, emittance growth, desorption, vacuum degradation, background
  excessive energy deposition in the cold sectors
Electron bombardment of a surface has been proven to reduce secondary electron yield (SEY) of a material as a function of the delivered electron dose. This technique, known as scrubbing, provides a mean to suppress electron cloud build-up.
Secondary emission yield [SEY]
SEY>SEYth  avalanche effect (multipacting)
SEYth depends on bunch spacing and population
G. Iadarola, G. Rumolo

## Slide 105: Electron cloud mitigation
Strong reduction of e-clouds with larger bunch spacing:
With 50 ns spacing e-clouds are much weaker than with 25 ns !
 One of the main reason to operate in 2012 with 50 ns spacing
Remedy: conditioning by beam-induced electron bombardment (“scrubbing”) leading to a progressive reduction of the SEY (Secondary Electron Yield).
  Done at 450 GeV where fresh beams can be injected easily.

## Slide 106: From 2012 to 2015 …and beyond 2012: high intensity proton operation at 4 TeV 2013: few weeks for ion operation 2013-2015: consolidation (interconnects, others) 2015…..2017: proton and ion operation at 6.5 TeV Operate with 25 ns bunch spacing (50 ns spacing not favoured due to event pile-up) Maximize the integrated luminosity Small focusing – β* as small as possible Highest possible efficiency

## Slide 107: Dipole training campaign
The 1232 main dipole magnets had to be trained for 6.5 TeV operation.
  2-3 training quenches could be performed for each sector in 24 hours, limited by the recovery time of the cryogenic system.
  About 150 training quenches were required.
The large spread in number of quenches between the eight sectors (arcs) is due to the mixture of magnets from the 3 producers.
Training quenches are due to frictional energy from coil movements.

## Slide 108: Electron cloud mitigation
With 50 ns spacing e-clouds are much weaker than for 25 ns spacing !
 To ease life during Run 1, bunch spacing was reduced to 50 ns
Vacuum chamber in 2012 run
Strong dependence of e-clouds on bunch spacing.
Conditioning of the vacuum chamber by beam-induced electron bombardment (“scrubbing”): progressive reduction of the SEY
Conditioning is performed at 450 GeV where fresh beams can be injected easily.
One must condition with a beam that is more powerful ( more electron could generation) that the beam one plans to use for operation.

## Slide 109: Scrubbing for 50 ns operation
50 ns
Scrubbing
25 ns Scrubbing
50 ns physics
e-cloud free 
25 ns beam
~2800 bunches
1.15 x 1011 p/b
50 ns beam
~1400 bunches
1.7 x 1011 p/b
During the first scrubbing run for 50 ns operation, a 25 ns beam is used to condition the vacuum chamber.

## Slide 110: (Second) 2015 scrubbing run
Beam1 intensity
Beam2 intensity
Scrubbing with 25 ns beams
At the end, machine conditions were reasonable for ~1200 bunches operation (max. possible 2800). Number of bunches limited by high vacuum pressures at injection on some absorbers and cryogenic heat load
Heat load in cryogenic system

## Slide 111: 25 ns beam quality
The 25 ns beams are operated with trains of 48, 72 or 144 bunches (nominal 288), the signature of electron clouds is visible:
Intensity along the trains.
Blown up bunches.
Scrubbing has not completely removed e-clouds. The conditioning has to continue in parallel to physics operation.
Bunch
intensity
Bunch emittance (mm)
Trains of 72 bunches

## Slide 112: UFOs at LHC

## Slide 113: Surprising ‘Unidentified Falling Objects’
Very fast localized beam losses are observed when the LHC beam intensity is increased.
The beam losses were traced to dust particles entering into the beam – ‘UFO’.
Losses too high => beams dumped to avoid a quench, but sometimes magnets quench
2015: 2 UFO quenches (vs. >10 beam dumps due to UFOs in the arc + 2 in LSS)
Conditioning of the UFO-rate expected
100µm
10µm
In one accelerator component UFOs were traced to Aluminum oxide particles.
time
Rate (/hour)
25ns scrubbing

## Slide 114: 2015 Overview
50 ns scrubbing run
25 ns scrubbing run
50 ns
25 ns

## Slide 115: 2015 Overview
50 ns scrubbing run
25 ns scrubbing run
50 ns
25 ns

## Slide 116: Run 1 versus Run 2
The start-up of Run 2 was faster then for Run 1, but we are still far from the Run 1 performance. We are still in the learning phase for 25 ns.
Operation with 50 ns beams is easier !

## Slide 117: Luminosity projections
Beam | k | Nb [1011 p] | e [mm] | b* [m] | Peak L [1034 cm-2s-1] | Event pile-up | Int. L(*) [fb-1]
25 ns – 2015 | ~1500 | 1.1 | 3.5 | 0.8 | 0.31 | 14 | ~2
25 ns – standard | ~2700 | 1.2 | 3.0 | 0.8 | 0.78 | 21 | ~20
25 ns – pushed | ~2500 | 1.2 | 2.0 | 0.4 | 1.7 | 51 | ~40-50
50 ns | 1360 | 1.6 | 2.2 | 0.4 | 1.65 | 90 | ~30
Some scenarios @ 6.5 TeV
(*): per year

## Slide 118
The next 20 years
LHC
and
High Luminosity-LHC (HL-LHC)

## Slide 119: LHC - the next years
Long Shutdown 1
LHC Run 2 Physics at 6.5 TeV
“Ultimate” Physics
High Luminosity LHC
Deliver 300 fb-1 at ≥ 6.5 TeV/c
LHC Run 1
Long Shutdown 2
Long Shutdown 3
At 4 TeV/c, demonstrated LHC potential, integrated luminosity of 30 fb-1
Deliver 3000 fb-1 at ≥ 6.5 TeV/c

## Slide 120: Horizon 2025: LHC High Luminosity Upgrade
Motivation
Very ambitious target for : 200 – 300 fb-1/y (×10 today)
Radiation damage limit of existing sc quadrupoles close to experiments
Past experience from 2010-2012 operating with 50 ns bunch spacing
Operation with large bunch intensity possible (no serious limitation)
Single bunch with > 3x1011 protons per bunch with 2.5 um emittance provided by injector complex
Operation with very small beams (low β* optics) successfully tested in injector complex
Pile-up/pile-up density HL-LHC beam physics constraint  bunch spacing of 25 ns and luminosity leveling required for 2015 and later
Total current: collimation efficiency, upper limits from: beam dump, vacuum, machine protection, radiation protection, …
Electron cloud

## Slide 121: Integrated Luminosity increase by levelling
t [h]
Too many events per bunch crossing, pile-up too high for experiment
Increase of with Luminosity levelling
L [1034 cm-2s-1]
increase by increasing not feasible (pile up too high): Luminosity levelling can increase
High availability is required (optimise length of fills)
No way to achieve for HL-LHC

## Slide 122: Luminosity parameters with crossing angle
Head-on collision…..
…..not an option for HL-LHC

## Slide 123: Luminosity parameters with crossing angle
HL-LHC: Bunches collide with smaller beams and a larger crossing angle as in LHC: reduction of luminosity
Tilt bunches before collisions with crab cavities: recovering luminosity => R ~1
Angle crossing (ineffective overlap):
L =
reduction factor

## Slide 124: Hardware for the Upgrade
Main modifications of LHC
  New high field/larger aperture interaction region sc magnets
  Crab Cavities to take advantage of the small b*
  New collimators (lower impedance)
  Cryo-collimators and high field 11 T dipoles in cold part of LHC
  Additional cryo plants for magnets and RF (P1, P4, P5)
  Superconducting links to allow power converters to be moved to protected areas (availability)

## Slide 125: LHC operational cycle
Stable beams: Luminosity production (~10 h)
Machine setup: (Optimum turnaround time ~2h 20m)
Beam dump due to a failure implies on average 5.5 hours of turnaround – impacting availability for physics significantly!
Time
Energy
Beam Intensity

## Slide 126: Integrated Luminosity and Availability
Turnaround
Stable Beams
Fault
  Machine Failure Rate (MFR) = fraction of premature beam dumps due to a failure = 70 %
Monte Carlo model for integrated luminosity:
  Based on observed failure distributions
  The model accurately reproduces 2012 operation
  Extrapolated distributions for future LHC runs and HL-LHC
Turnaround
Stable
Beams
Turnaround
Turnaround
5.5 h
6.1 h
6.9 h
30 %
70 %
Stable
Beams
A. Apollonio

## Slide 127: Availability for HL-LHC
SCENARIO 1
HL TARGET
SCENARIO 2
To achieve HL-LHC parameters, challenging upgrades to achieve availability is required
2012 AVAILABILITY
A. Apollonio

## Slide 128: LHC High Luminosity Upgrade
M. Lamont

## Slide 129
First ideas for LHC presented in 1984
Physics operation started 25 years later
Preparing for the next 50 years FCC Study – Proton collisions at a c.m. energy of 100 TeV

## Slide 130: C.M. energy evolution
Hadron collider c.m. energy evolution [GeV vs. year]
Chart: 
| 1971 | 1981 | 1986 | 1992 | 2000 | 2009 | 2015 | 2035 | 2040
 | 63 | 630 | 1980 | 319 | 500 | 7000 | 14000 | 50000 | 100000
30 years
10 x energy
25 years
7 x energy

## Slide 131: FCC Study Scope
Conceptual Design Report (CDR) and cost review for the next European Strategy Update in 2018:
pp-collider (FCC-hh)
  ~16 T-> 100 TeV c.m. pp in 100 km
  ~20 T-> 100 TeV c.m. pp in 80 km
e+e- collider (FCC-ee) as potential intermediate step
p-e collider (FCC-he) option
Requires a 80-100 km infrastructure in Geneva area

## Slide 132: SSC
SSC (Superconducting Super Collider): particle accelerator complex under construction in the vicinity of Waxahachie, Texas, to be the world's largest and most energetic Hadron Collider 87.1 km and an c.m. energy of 40 TeV.
When the project was cancelled in 1993, 22.5 km of tunnel and 17 shafts to the surface were already dug, nearly two billion dollars had already been spent on this facility.
Green field: no lab, no injectors, area moderately attractive….. and no working LHC
Crazy ?

## Slide 133: Luminosity evolution
Hadron collider peak luminosity evolution per Interaction Point [x 1030 cm-2s-1]
Chart: 
| 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
protons-proton and proton-antiprotons collisions | 5 | 10 | 20 | 30 | 35 | 40 | 45 | 65 | 75 | 100 | 120 | 140
 | 0.001 | 200 | 3700 | 7730
 | 2.1 | 3.575 | 5.05 | 6.525 | 8 | 9.9 | 18 | 23 | 24 | 10 | 38 | 52 | 105 | 170 | 260 | 295 | 360 | 360 | 402.4 | 430
 | 2 | 6 | 8.5 | 15 | 28 | 31.749 | 36 | 92 | 123.2071 | 165 | 184 | 267
ion-ion collisions | 1 | 15.5236 | 21.5518 | 27.58 | 58.2135 | 94.8591 | 105.0912 | 116.427 | 120.17 | 145.3494 | 175.8048 | 205.6877 | 161.343 | 232.0548 | 333.7574
 | 1.2979 | 22.0646 | 26 | 26
 | 0.05 | 0.21 | 0.35 | 0.35 | 0.4 | 0.4 | 3 | 4 | 7
lepton-proton and lepton-ion collisions | 0.6 | 2.9 | 4.2 | 7 | 14 | 14.6 | 15.2 | 17 | 3.8 | 26.8 | 38 | 51.2 | 51.2 | 51.2
 | 6.4 | 5.6 | 4.8 | 4 | 3.24
 | 300 | 1000 | 1800 | 3060 | 4896 | 6854.4 | 8225.28 | 9047.808 | 9952.5888

 | 10000 | 17000 | 19000 | 20000 | 20000 | 20000 | 30000 | 40000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 85000 | 136000 | 190400 | 209440 | 209440 | 209440 | 209440 | 209440 | 209440 | 209440 | 209440 | 209440 | 209440 | 209440

## Slide 134: FCC-hh parameter (other parameter sets exist)
parameter | FCC-hh | LHC nominal
Energy | 100 TeV c.m. | 14 TeV c.m.
Dipole field | 16 T | 8.33 T
Number of IP | 2 main + 2 | 4
Normalized emittance | 2.2 mm | 3.75 mm
Luminosity / IPmain | 5 x 1034 cm-2s-1 | 1 x 1034 cm-2s-1
Energy stored in each beam | 8.4 GJ | 0.36 GJ
Synchrotron radiation | 28.4 W/m/aperture | 0.17 W/m/aperture
Bunch spacing | 25 ns (5 ns) | 25 ns

## Slide 135: FCC-hh design targets
Pushing the energy frontier by maximizing the energy reach
Hadron collider only option for exploring energy scale at tens of TeV
x 3.7
x 2
LHC nominal
FCC
Ph. Lebrun

## Slide 136: Advanced superconductors to reach high fields
Chart: Applied Field (T)
| 0 | 5 | 15 | 20 | 25 | 30
YBCO: Parallel to tape plane, 4.2 K | 4144.6766 | 3507.9375 | 3148.3332 | 2909.0554 | 2090.4933 | 1888.9952
YBCO: Perpendicular to tape plane, 4.2 K | 4144.6766 | 1445.8386 | 975.0997 | 767.7508 | 655.6687 | 571.6114 | 526.7777 | 481.944 | 442.7183 | 428.1462 | 403.4904 | 386.6773 | 364.2626 | 341.8457 | 328.3952 | 319.4289 | 318.3073
2212: Round wire, 4.2 K | 1265.6716 | 1257.7114 | 1257.7114 | 1225.8706 | 1181.0945 | 1126.3682 | 1040.796 | 973.1343 | 929.3532 | 835.8209 | 780.0995 | 704.4776 | 623.8806 | 577.7114 | 529.3532 | 513.4328 | 509.4527 | 489.5522 | 469.6517 | 453.7313 | 435.8209 | 416.9154 | 398.01 | 380.0995 | 364.1791 | 347.2637 | 330.3483 | 315.4229 | 298.5075 | 282.5871 | 265.4726
Nb3Sn: High Energy Physics, 4.2 K | 1754.8557 | 1454.9349 | 1190.9814 | 1072.6374 | 957.7741 | 855.0933 | 757.6336 | 268.0143 | 190.8587 | 118.9241 | 65.5533 | 28.3097
Nb-Ti (LHC) 1.9 K | 1430 | 1195.7692 | 950.7692 | 703.4615 | 475.7692
Nb-Ti
Nb3Sn
HTS
400
Ph. Lebrun

## Slide 137: FCC-hh Challenges: Magnets
FCC-hh baseline: 16 T Nb3Sn technology for 100 TeV in 100 km
  Develop Nb3Sn-based 16 T dipole technology
  With sufficient aperture of ~40 mm (LHC = 56 mm) and accelerator features (field quality, ability to protect, cycling operation).
  Learn from Nb3Sn magnets in the LHC (HL-LHC 11 T dipoles).
  Technology push to achieve duplication of critical current density of Nb3Sn
  Possible goal: 16 T short dipole models by 2018 (in collaboration with America, Asia, Europe).
  In parallel HTS development targeting 20 T
  HTS insert, generating 5 T additional field, ~40mm aperture and accelerator features.
  R&D goal: demonstrate HTS/LTS technology for building magnets with a field of 20 T.

## Slide 138: FCC-hh challenges Stored beam energy
Stored energy 8 GJ per beam
  20 times higher than LHC, equivalent to A380 (560 t) at nominal speed (850 km/h)
  Collimation, control of beam losses and radiation effects (shielding) important
  Injection, beam transfer and beam dump very critical
Damage of a beam with an energy of 2 MJ
Machine protection issues to be addressed early on!

## Slide 139: FCC-hh Challenges
High synchrotron radiation load on beam pipe (up to 26 W/m/aperture in arcs, total of ~5 MW)
  Heat extraction: photon stop, beam screen design, cryo load, ….
Synchrotron radiation damping
  Beams shrinking, controlled blow up, luminosity levelling, etc…
Impedances, instabilities, feedbacks
  Beam-beam, e-cloud, resistive wall, feedback systems design
Optics and beam dynamics
  IR design, dynamic aperture studies, SC magnet field quality

## Slide 140: FCC study Status
Study launched at FCC kick-off meeting in February 2014
Presently forming a global collaboration based on general MoUs between CERN and individual partners + specific addenda for each participant
First International Collaboration Board meeting on 9-10 September 2014 at CERN, chaired by Prof. L. Rivkin (PSI/EPFL)
Design study proposal: EU support in the Horizon 2020 program approved

## Slide 141: Scope of FCC study
Main emphasis of the conceptual design study: long-term goal of a hadron collider with a centre-of-mass energy of the order of 100 TeV in a new tunnel of 80 - 100 km circumference.
Conceptual design study shall also include a lepton collider and its detectors, as a potential intermediate step towards realization of the hadron facility. Potential synergies with linear collider detector designs should be considered.
Options for e-p scenarios and their impact on the infrastructure shall be examined at conceptual level.
The study shall include cost and energy optimisation, industrialisation aspects and provide implementation scenarios, including schedule and cost profiles

## Slide 142: FCC study 49 FCC collaboration members, 27 Feb. 2015 (now >60)
ALBA/CELLS, Spain
U Bern, Switzerland
BINP, Russia
CASE (SUNY/BNL), USA
CBPF, Brazil
CEA Grenoble, France
CIEMAT, Spain
CNRS, France
Cockcroft Institute, UK
U Colima, Mexico
CSIC/IFIC, Spain
TU Darmstadt, Germany
DESY, Germany
TU Dresden, Germany
Duke U, USA
EPFL, Switzerland
GWNU, Korea
U Geneva, Switzerland
Goethe U Frankfurt, Germany
GSI, Germany
Hellenic Open U, Greece
HEPHY, Austria
IFJ PAN Krakow, Poland
INFN, Italy
INP Minsk, Belarus
U Iowa, USA
IPM, Iran
UC Irvine, USA
Istanbul Aydin U., Turkey
JAI/Oxford, UK
JINR Dubna, Russia
FZ Jülich, Germany
KEK, Japan
KIAS, Korea
King’s College London, UK
KIT Karlsruhe, Germany
Korea U Sejong, Korea
MEPhI, Russia
MIT, USA
NBI, Denmark
Northern Illinois U., USA
NC PHEP Minsk, Belarus
U. Liverpool, UK
PSI, Switzerland
Sapienza/Roma, Italy
UC Santa Barbara, USA
U Silesia, Poland
TU Tampere, Finland

## Slide 143: Conclusions
LHC demonstrated that an ultra-complex accelerator can operate reliably, achieve high luminosity and produce excellent physics
The next step is HL-LHC – with an increase of integrated luminosity by one order of magnitude
Reaching a luminosity an order of magnitude above 1034 [cm-2s-1] and operating reliably is a formidable challenge
Today, the only realistic option to collide particles at a c.m. energy in the range of 100 TeV are circular proton colliders
We will learn from HL-LHC as a preparation for FCC
There are a number of very interesting challenges for the realisation of such collider, and scientists who are interested in such R&D are very welcome to join!

## Slide 144
Plumber visiting Freudenstadt
Thanks for your attention
Thanks a lot for slides from several colleagues, in particular G.Arduini, M.Lamont and J.Wenninger

## Slide 145: Literature
The Physics of Particle Accelerators: An Introduction, Klaus Wille, Oxford, 2000
Proceedings of CERN ACCELERATOR SCHOOL (CAS), Yellow Reports, many topics, General Accelerator Physics, and topical schools on Vacuum, Superconductivity, Synchrotron Radiation, Cyclotrons, and others… http://cas.web.cern.ch/cas/
5th General CERN Accelerator School, CERN 94-01, 26 January 1994, 2 Volumes, edited by S.Turner
A.Wolski, Beam Dynamics in High Energy Particle Accelerators, Imperial College Press
Superconducting Accelerator Magnets, K.H.Mess et al., WorldScientific 1996
Handbook of Accelerator Physics and Engineering, A.W.Chao and M.Tigner, World Scientific, 1998
A.Sessler, E.Wilson: Engines of Discovery, World Scientific, Singapur 2007
Conferences and Workshops (EPAC, PAC, IPAC, …) – http://www.jacow.org

## Slide 146: Comment: Screen
Beam dump scintillating screen: Alumina doped with 0.5% chrome sesquioxide and at room temperature two principal lines of luminescence at 692.9 and 694.3 nm are generated with a decay time of 3.4 ms.

## Slide 147: Comment: Extraction kicker magnet
Kicker magnet (LHC) : one turn for the current (low inductance), HV, field, kick strength per magnet 0.428 Tm, length 1.4 m
L. DUCIMETIERE

## Slide 148: Comment: LHC Beam Screen
Vacuum chamber 1.9 K (stainless steel)
Beam screen (stainless steel + copper)
Helium tubes 4-40 K