## Slide 2: CLIQ on MB
Gaelle Dib, Alejandro Fernandez, Emmanuele Ravaioli, Gerard Willering
We would like to acknowledge the work of and the fruitful collaboration with the various teams in making the tests possible, in particular the following sections:
TE-MPE-EE, TE-MPE-PE, TE-MSC-LMF, TE-MSC-MDT, TE-MSC-TF, TE-CRG and TE-EPC-MPC.
TE-MPE-PE
01.10.2015
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 3: Outline
CLIQ
Measurements
Simulations
Differential inductance
Conclusions

## Slide 4
CLIQ

## Slide 5: CLIQ (Coupling-Loss Induced Quench)
s
Current change
Magnetic field change
Coupling losses (Heat)
QUENCH
Temperature rise

## Slide 6: CLIQ configurations
1-CLIQ Not Optimized
2-CLIQ Optimized
1-CLIQ Optimized
Higher dI/dt, More efficient dB/dt

## Slide 7: Pics – Addition of CLIQ leads in B180

## Slide 8: Pics – Magnet test station in SM18

## Slide 9: CLIQ behavior

## Slide 10
Measurements

## Slide 11: Typical CLIQ discharge

## Slide 12: Typical CLIQ discharge

## Slide 13: Quench heaters configuration
Aperture 1
Aperture 2

## Slide 14: CLIQ and QH at every current level

## Slide 15: 3 kA: CLIQ-QH comparison

## Slide 16: 3 kA: All tests
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 17: 6 kA: CLIQ-QH comparison
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 18: 6 kA: All tests
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 19: 9 kA: CLIQ-QH comparison
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 20: 9 kA: CLIQ configurations
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 21: 11.85 kA: All tests
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 22: 12.7 kA: All tests
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 23: 2-CLIQ, 1-CLIQ comparison at 6 kA
CLIQ on MB
E. Ravaioli and A. Fernandez
1-CLIQ
2-CLIQ

## Slide 24: Quench load and hot-spot temperature
CLIQ on MB
E. Ravaioli and A. Fernandez
Assumptions: RRR=187; Magneto-resistivity=6E-11 Ohm m/T; Quench detection + validation time: 15 ms.
Calculated from t=0
(quench detection card triggered)

## Slide 25
Simulations

## Slide 26: Parameters of the models
Parameter | Set 1 | Set 2 | Set3
Number of blocks | 204 | 204 | 264
RRR | 150 (All poles) | 200 (1U) 150 (1L) 100(2U) 125 (2L) | 194 (1U) 187 (1L) 192(2U) 192 (2L)
Magneto resistivity [Ohm*m/T] | 4.2E-11 (All poles) | 6E-11 (All poles) | 5E-11 (1U) 6E-11 (1L) 7E-11 (2U) 5E-11 (2L)
Effective transverse resistivity factor | 2 | 1 | 0.9
Helium fraction [%] | 5 | 5 | 4.5
Resistance of the CLIQ leads [mOhm] | 20 | 15 | 10
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 27: 3 kA: Simulations
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 28: 6 kA: Simulations
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 29: 9 kA: Simulations
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 30: 9 kA: Simulations
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 31: 11.85 kA: Simulations
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 32: 11.85 kA: Simulations
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 33: Quench load and hot spot-temperature
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 34: Temperature profile at nominal current
2xCLIQ + 1xQH
CLIQ on MB
E. Ravaioli and A. Fernandez
2xQH

## Slide 35
Differential inductance

## Slide 36: Differential inductance
CLIQ on MB
E. Ravaioli and A. Fernandez
The differential inductance of the CLIQ discharge circuit is influenced by
Mainly coil geometry (without the other effects, differential inductance = nominal)
Magnetization (persistent currents in the filaments)
Coupling currents
Iron yoke saturation
Eddy currents in the copper of the cables

## Slide 37: Three tested conditions (more possible)
CLIQ on MB
E. Ravaioli and A. Fernandez
Effect on the differential inductance | Superconducting After magnetic cycle | Superconducting After warm up | Resistive (~14 K)
Coil geometry | YES | YES | YES
Magnetization in the SC | YES | NO | NO
Coupling currents | YES | YES | NO
Iron yoke saturation | YES | YES | YES
Eddy currents in the cable | NO | NO | YES
Others…? | ? | ? | ?

## Slide 38: CLIQ current – 80 mF, 500 V
CLIQ on MB
E. Ravaioli and A. Fernandez
 | f [Hz] | Ipeak [A] | % Leq | Req [Ω]
80mF after MagCycle | 11.30 | 2446 | 68% | 0.0366
80mF after WarmUp | 10.55 | 2305 | 78% | 0.0368
80mF resistive | 10.22 | 2277 | 83% | 0.0322

## Slide 39: CLIQ current – 40 mF, 500 V
CLIQ on MB
E. Ravaioli and A. Fernandez
 | f [Hz] | Ipeak [A] | % Leq | Req [Ω]
40mF after MagCycle | 16.95 | 1830 | 60% | 0.051
40mF after WarmUp | 15.77 | 1735 | 70% | 0.047
40mF resistive | 14.49 | 1649 | 83% | 0.038

## Slide 40: Frequency transfer functions – |Z|
CLIQ on MB
E. Ravaioli and A. Fernandez
CLIQ 80 mF
CLIQ 40 mF
Simple calculation with nominal parameters

## Slide 41: Frequency transfer functions – phase
CLIQ on MB
E. Ravaioli and A. Fernandez
CLIQ 80 mF
CLIQ 40 mF
Simple calculation with nominal parameters

## Slide 42: Conclusions
CLIQ successfully tested on a full-scale LHC main dipole magnet
Model predicted the measured transients with reasonable accuracy
CLIQ can discharge more quickly even this long coil (quench load -20%, hot-spot T -150 K)
Wealth of information acquired to further improve the available magnet models (for example operating conditions, CLIQ configurations, differential inductance,…)

## Slide 43: Annex

## Slide 44: 3 kA: Simulations
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 45: 6 kA: Simulations
CLIQ on MB
E. Ravaioli and A. Fernandez

## Slide 46: 9 kA: All tests
CLIQ on MB
E. Ravaioli and A. Fernandez