## Slide 1
Quench Simulation in COMSOL
Deepak Paudel
August 2015, Geneva
Supervisor:
Bernhard Auchmann

## Slide 2
Outline
1D FEM model of magnet coil
Mesh Adaptation
Implementation of helium non-linear cooling behavior
Performance Analysis
Outlook.

## Slide 3
1D FEM model of magnet coil
Single 1D 2.25 km long line model representing LHC dipole magnet. I = 4200 A , B = 2.88 T
Heat conduction along cable was calculated using COMSOL default heat diffusion equation.
The joule heat generation and turn to turn heat conduction was calculated by defining function in COMSOL GUI which was than applied as body loads to the model.
Model Characteristics
Adaptive time stepping (Δt = 10 - 100 μs)
Adaptive mesh (h = 1 mm - 15 cm )
Total simulation time = 1 s
Total computation time = 5 hours
No of elements (15000 - 20000)
Without adaptive mesh (2e6, ~ 100 times faster)

## Slide 4
Mesh Adaptation
QP3 like model with mesh adaptation feature.
Results in much fast performing model while accuracy remaining same as fixed mesh model.
For 1 m long model we don’t benefit from mesh adaptation feature.
However, for large model size, the computation time reduces significantly.
(In reference to slide 3)

## Slide 5
Implementation of helium cooling dynamics
Same geometry - Two field variables (Ts,THe)
Strand domain
S = Joule(Ts) - aHe/(aCu*L)*hHe(Ts, THe, hHe) [W/m3]
y
Heat diffusion equation
Initial condition
Gaussian shape temperature profile representing heat pulse
Helium domain
Heat diffusion equation
S = hHe(Ts, THe, hHe)*aHe/vHe [W/m3]
Initial condition
1.9 K
(assumed)
sink
source

## Slide 6
Performance analysis
QP3 like 1D strand model
I = 150 A B = 2.88 T
Approximation fun. order
QP3 - Linear
ANSYS - Linear (was used)
Requires discretization in the scale less than 1 mm
In COMSOL Convergence achieved with discretization scale of 1 cm (Cubic order approximation )
n = 1000 Linear, Compu time = 110 s (QP3 )

## Slide 7
Coil Geometry
CAD
ROXIE
Turn2turn Mapping
1D FEM Model
Physics
Coil | Helium
Solver






Coil geometry
Winding direction
1D FEM Coil Model Development Workflow

## Slide 8: SMC with mech. structure
Heaters
Central Post
Wedges
Mid-plane insulation
Interlayer insulation
Entire cold-mass

## Slide 9
Coil Geometry
CAD
ROXIE
Turn2turn Mapping
1D FEM Model
Physics
Magnet, Helium
Solver
Coil Geometry
CAD
ROXIE
Automatic detection of thermal contacts
3D FEM Model
Unstructured | Structured
Physics
Heat Exchange| Magnet, Helium
Solver
Additional elements
Heaters
Central Post
Wedges
Mid-plane insulation
Interlayer insulation
Entire cold-mass
Water Heat Exchange
Coil geometry
Winding direction
3D FEM Coil Model Development Workflow

## Slide 10: 3D FEM Coil Model Development Workflow - Questions
Coil Geometry
CAD
ROXIE
Automatic detection of thermal contacts
3D FEM Model
Unstructured | Structured
Physics
Heat Exchange| Magnet, Helium
Solver
Additional elements
Heaters
Central Post
Wedges
Mid-plane insulation
Interlayer insulation
Entire cold-mass
Water Heat Exchange
Coil geometry
Winding direction
#1 How to adaptively mesh 3D to get 1D performance?
#2 How to script entire process? (COMSOL API)
#3 Performance optimisation
#4 Tips on how to read geometry from CAD

## Slide 11
Electro thermal
Electromagnetic
Electrical
SPICE
Simulations Coupling
CAD
ROXIE
Coil geometry
Winding direction
Outlook 1/2 Co-simulation

## Slide 12: Outlook 2/2 – extendibility
Electro thermal
Electromagnetic
Electrical
SPICE
Simulations Coupling
Electro thermal
CAD
ROXIE
CFD
Open Foam
Coil geometry
Winding direction

## Slide 13
3D Magnet Coil
ANSYS SMC 11 T
Quench Propagation
Hexahedral mesh, no mesh adaption for time dependent solver.

## Slide 14
3D COMSOL models
SMC 11T
3D Strand Mesh adaptation
Tetrahedral Mesh adaptation
Quench Propagation

## Slide 15
What has been accomplished
A 3D quench propagation model which takes into consideration non-linear material property and non-linear helium cooling behaviour.
What we would like to achieve
A quench propagation model representing actual 3D model of the magnet coil, with non-linear helium cooling behaviour taken into consideration.
Issue
Magnet are usually large (15 m) and proper calculation needs fine discretization which can be computationally expensive.
Mesh adaption feature
COMSOL GUI provides this feature which is not efficient enough for our problem. We need to have knowledge of using COMSOL scripts which would allows us to define our own mesh adaptive algorithms.
Domain decomposition solver (and Cluster computing)
In order to solve large problems more efficiently on multiple processors. Dividing the modelling domain into subdomains where each PDE in the subdomain is easier to solve.
Model performance optimization
Outlook