## Slide 1
Machine Protection
Rüdiger Schmidt, CERN
CAS on Intensity Limitations in Particle Beams
Geneva, November 2015

## Slide 2
Copper part of a target at a depth of 0.6 m, irradiated with one SPS beam pulse (1.5 MJ, 7 µs, 450 GeV, 0.2 mm)
0. 6 m

## Slide 3: Outline
Particle beams and damage mechanisms
Hazards and Risks
Hazards when operating with particle beams
Worst case scenario
Machine Protection and Interlocks
See also material in Joint International Accelerator School on
"Beam Loss and Accelerator Protection"
http://uspas.fnal.gov/programs/JAS/JAS14.shtml Proceeding to be published by 2016

## Slide 4: Protection from Energy and Power
Risks come from Energy stored in an accelerator (Joule), and Power when operating an accelerator (Watt)
  “Very powerful accelerator” … the power flow needs to be controlled
Particle accelerators use large amount of power (few to many MW)
  Where does the power go in case of failure?
An uncontrolled release of energy or power flow can lead to unwanted consequences
  Damage of equipment and loss of time for operation
  Risk of activation of equipment when operating with particle beams
This is a particular challenge for complex systems such as accelerators

## Slide 5: Direct energy transfer from beam to equipment
Regular particle losses during operation
  Particle losses due to residual gas
  Particle losses due to collisions (in a collider)
  Particles losses at the aperture (e.g. due to emittance growth and other effects)
  Particle beams directed onto a target
Accidental particle losses - due to a large number of possible failure mechanisms
  Particles can be deflected into the aperture
  Targets, collimators and beam dumps: beam characteristics not matching the target, e.g. beam size at a spallation target too small
Machine protection is essentially to prevent consequences of accidental beam losses

## Slide 6: Indirect energy transfer from beam to equipment
Power deposited by electromagnetic interaction between beam and environment (RF, beam instrumentation, vacuum chamber, kicker magnets, …)
  Depends on the beam intensity and bunch structure
  Depends on the impedance
Power of synchrotron radiation emitted by the beam
  For electron / positron accelerators
  The power increases with the particle energy:
  The power of synchrotron radiation can be very high (10s of MW)
  The radiation can be very focused
  Wiggler and undulator magnets can increase the power by orders of magnitude (e.g. for FELs)
  Normally, this is considered in the design of the accelerator and experiments – however, there are a number of failure scenario that can lead to accidents
The metallic coating on the fingers had melted, temperature had reached more than 800 C.
B.Salvant

## Slide 7: Particle losses and consequences

## Slide 8: Beam loss and consequences
Charged particles moving through matter interact with electrons of atoms in the material, exciting or ionizing the atoms => energy loss of traveling particle described by Bethe-Bloch formula.
If the particle energy is high enough, it leads to particle cascades in materials, increasing the deposited energy
  The maximum energy deposition can be deep in the material at the maximum of the hadron / electromagnetic shower
The energy deposition leads to a temperature increase
  Superconducting magnets could quench (beam loss of ~mJ to J)
  Superconducting cavities performance degradation by some 10 J
  Material can vaporise, melt, deform or lose its mechanical properties
  Risk to damage sensitive equipment for less than one kJ, risk for damage of any structure for some MJ (depends on beam size)
  Activation of material, risk for hand-on-maintenance
  Single event upsets in electronics equipment

## Slide 9: Energy loss: example for one proton in iron (stainless steel, copper very similar)
Low energy few MeV, beam transport, RFQ for many machines
SNS - ESS 1 – 3 GeV
LHC 7 TeV
From Bethe-Bloch formula.
Energy loss for a high energy particle entering a target

## Slide 10: Heating of material with high energy protons
Nuclear inelastic interactions (hadronic shower)
  Creation of pions when going through matter
  Causes electromagnetic shower through decays of pions
  Exponential increase in number of created particles
  Final energy deposition to by a large number of electromagnetic particles
  Scales roughly with total energy of incident particle
  Energy deposition maximum deep in the material
  Energy deposition is a function of the particle type, its momentum and parameters of the material (atomic number, density, specific heat)
  No straightforward expression to calculate energy deposition
  Calculation by codes, such as FLUKA, GEANT or MARS
http://williamson-labs.com/ltoc/cbr-tech.htm

## Slide 11: Proton energy deposition for different energies
7 TeV
450 GeV
50 MeV
40 TeV
26 GeV
1 GeV
100 MeV
200 MeV
F.Burkart + V.Chetvertkova
Simulations with FLUKA, beam impact on a copper target

## Slide 12: Beam loss and consequences
Proton beam travels through a thin window of thickness
Assume a beam area of 4 , with rms beam sizes (Gaussian beams)
Assume a homogenous beam distribution
The energy deposition can be calculated, mass and specific heat are known
The temperature can be calculated (rather good approximation), assuming a fast loss and no cooling

## Slide 13: Heating of material with low energy protons (3 MeV)

## Slide 14: Damage of a pencil 7 TeV proton beam (LHC)
Copper
graphite
copper
graphite

## Slide 15: Beam loss and consequences
Calculate the response of the material (deformation, melting, …) to beam impact (mechanical codes such as ANSYS, hydrodynamic codes such as BIG2 and others)
Beams at very low energy have limited power…. however, the energy deposition is very high, and can lead to (limited) damage in case of beam impact
  Issue at the initial stage of an accelerator, after the source, low energy beam transport and RFQ
  Limited impact (e.g. damaging the RFQ) might lead to long downtime, depending on spare situation
Beams at very high energy can have a tremendous damage potential
  For LHC, damage of metals for ~1010 protons at top energy (7 TeV)
  One LHC bunch has about 1.5∙1011 protons, in total up to 2808 bunches
  In case of catastrophic beam loss, possibly damage beyond repair

## Slide 16: What accelerators?

## Slide 17: Energy versus momentum
Chart: Momentum [GeV/c]
| 250 | 900 | 450 | 920 | 26 | 450 | 4000 | 7000 | 40000 | 45 | 7000 | 7000 | 40000 | 40000 | 40000
Stored Energy MJ | 0.9 | 1.6 | 2.5 | 2.67 | 3 | 25 | 142 | 362 | 8000 | 21.6 | 8800 | 1100 | 160000 | 32000 | 50000

## Slide 18: High Intensity Proton Accelerators
P=1MW

## Slide 19: What does it mean ……… MJoule ?
360 MJ: the energy stored in one LHC beam corresponds approximately to…
90 kg of TNT
8 litres of gasoline
15 kg of chocolate
It matters most how easy and fast the energy is released !!
The energy of an 200 m long fast train at 155 km/hour corresponds to the energy of 360 MJ stored in one LHC beam.

## Slide 20: Hazards and Risks Synchrotrons Linear accelerators

## Slide 21: Hazard and Risk
Hazard: a situation that poses a level of threat to the machine. Hazards are dormant or potential, with only a theoretical risk of damage. Once a hazard becomes "active“: incident / accident.
Consequences and Probability of an accident create Risk:
Risk = Probability ∙ Consequences
Related to complex research instruments
Consequences of a failure in a hardware systems or uncontrolled beam loss (in €, downtime, radiation dose to people, reputation)
Probability of such event
The higher the Risk, the more Protection is required
Notes: 21

## Slide 22: Hazards related to particle beams
Accidental beam losses due to failures: understand hazards, e.g. mechanisms for accidental beam losses
  Hazards become accidents due to a failure, machine protection systems mitigate the consequences
Understand mechanisms for damage of components by direct beam loss
Regular beam losses during operation
  To be considered since this leads to activation of equipment and possibly quenches of superconducting magnets
  Radiation induced effects in electronics (Single Event Effects)
Understand effects from electromagnetic fields and synchrotron radiation that potentially lead to damage of equipment

## Slide 23: Luminosity fill in 2011 (18 hours)
Beam dump
3.5 TeV / 100 MJoule
0.45 TeV / 13 MJoule
Energy ramp
Luminosity: start collisions
Injection of 1380 bunches per beam in batches of 144 bunches

## Slide 24: Layout of beam dump system in IR6
24
LHC Layout
eight arcs (sectors)
eight long straight section (about 700 m long)
IR6: Beam dumping system
IR4: RF + Beam instrumentation
IR5:CMS
IR1: ATLAS
IR8: LHC-B
IR2: ALICE
IR3: Moment Beam Cleaning (warm)
IR7: Betatron Beam Cleaning (warm)

## Slide 25: Layout of beam dump system in IR6
25
Injection of batches with up to 288 bunches, 2 MJ
IR6: Beam dumping system
IR4: RF + Beam instrumentation
IR5:CMS
IR1: ATLAS
IR8: LHC-B
IR2: ALICE
Injection
Injection
IR3: Moment Beam Cleaning (warm)
IR7: Betatron Beam Cleaning (warm)
Beams from SPS

## Slide 26: Layout of beam dump system in IR6
26
Operation with stored beam, up to 362 MJ per beam
IR6: Beam dumping system
IR4: RF + Beam instrumentation
IR5:CMS
IR1: ATLAS
IR8: LHC-B
IR2: ALICE
IR3: Moment Beam Cleaning (warm)
IR7: Betatron Beam Cleaning (warm)
Detection of beam losses with >3600 monitors around LHC
Many other systems can detect failures

## Slide 27: Layout of beam dump system in IR6
27
Extraction of the beam into the beam dump blocks, after the end of a luminosity run, and in case of failure
IR6: Beam dumping system
IR4: RF + Beam instrumentation
IR5:CMS
IR1: ATLAS
IR8: LHC-B
IR2: ALICE
IR3: Moment Beam Cleaning (warm)
IR7: Betatron Beam Cleaning (warm)
Beam dump blocks
Signal to kicker magnet

## Slide 28: Protection at injection
LHC circulating beam
Circulating beam in LHC
LHC vacuum chamber
Transfer line vacuum chamber

## Slide 29: Protection at injection
LHC circulating beam
Beam injected from SPS and transfer line
Beam from SPS
Injection Kicker
LHC injected beam

## Slide 30: Protection at injection
LHC circulating beam
Kicker failure (no kick)
Beam from SPS
Injection Kicker
Major damage to superconducting magnets, vacuum pipes, possibly LHCb / Alice experiments

## Slide 31: Protection at injection
LHC circulating beam
Beam absorbers take beam in case of kicker misfiring Transfer line collimators ensure that incoming beam trajectory is ok
Beam from SPS
Injection Kicker
Set of transfer line collimators (TCDI) ~5σ
Injection absorber
(TDI) ~7σ
phase advance 900

## Slide 32: Protection at injection
LHC circulating beam
Beam absorbers take beam in case of kicker misfiring on circulating beam
Injection Kicker
Injection absorber
(TDI) ~7σ
Circulating beam – kicked out
phase advance 900
LHC circulating beam
Set of transfer line collimators (TCDI) ~5σ
This type of kicker failure happened several times: protection worked

## Slide 33: Layout of beam dump system in IR6
Beam 2
Beam dump block
Kicker magnets to paint (dilute) the beam
about 700 m
about 500 m
15 fast ‘kicker’ magnets deflect the beam to the outside
To get rid of the beams (also in case of emergency!), the beams are ‘kicked’ out of the ring by a system of kicker magnets send into a dump block !
Septum magnets deflect the extracted beam vertically
quadrupoles
The 3 ms gap in the beam gives the kicker time to reach full field.
Ultra-high reliability system !!

## Slide 34: Beam dump line
700 m long tunnel to beam dump block- beam size increases
Beam dump block

## Slide 35: Beam dump with 1380 bunches
Beam spot at the end of the beam dumping line, just in front of the beam dump block

## Slide 36: ESS Lund / Sweden – 5 MW beam power
Example for a high intensity linear accelerator (similar to SNS and J-PARC)
Power of
5000 kW
Drift tube linac with
4 tanks
Low energy beam transport
Medium energy beam transport
Super-conducting cavities
High energy beam transport
RFQ
352.2 MHz
75 keV
3 MeV
78 MeV
200 MeV
628 MeV
2500 MeV
Source
LEBT
RFQ
MEBT
DTL
Spokes
High β
Medium β
HEBT & Upgrade
Target
2.4 m
4.0 m
3.6 m
32.4 m
58.5 m
113.9 m
227.9 m
352.21 MHz
704.42 MHz
~ 500 m
Operating with protons
Operation with beam pulses at a frequency of 14 Hz
Pulse length of 2.86 ms
Average power of 5 MW
Peak power of 125 MW
One pulse = 357 kJ

## Slide 37: ESS Lund / Sweden – 5 MW beam power
Operating with protons
Operation with beam pulses at a frequency of 14 Hz
Pulse length of 2.86 ms
Average power of 5 MW
Peak power of 125 MW
One pulse = 357 kJ
The energy stored in the beam at a given moment is relatively small
Low energy part
Medium energy part
High energy part
In case of a failure, the beam needs to be switched off at the source
Power of
5000 kW
Drift tube linac with
4 tanks
Low energy beam transport
Medium energy beam transport
Super-conducting cavities
High energy beam transport
RFQ
352.2 MHz
75 keV
3 MeV
78 MeV
200 MeV
628 MeV
2500 MeV
Source
LEBT
RFQ
MEBT
DTL
Spokes
High β
Medium β
HEBT & Upgrade
Target
2.4 m
4.0 m
3.6 m
32.4 m
58.5 m
113.9 m
227.9 m
352.21 MHz
704.42 MHz
~ 500 m

## Slide 38: ESS Lund / Sweden – 5 MW beam power
In between two pulses (about 70 ms), ensure that the parameters of the accelerator allow for correct beam transmission – or do not start with the next pulse.
If something is wrong and not detected before the pulse by monitors, stop beam as soon as possible
Power of
5000 kW
Drift tube linac with
4 tanks
Low energy beam transport
Medium energy beam transport
Super-conducting cavities
High energy beam transport
RFQ
352.2 MHz
75 keV
3 MeV
78 MeV
200 MeV
628 MeV
2500 MeV
Source
LEBT
RFQ
MEBT
DTL
Spokes
High β
Medium β
HEBT & Upgrade
Target
2.4 m
4.0 m
3.6 m
32.4 m
58.5 m
113.9 m
227.9 m
352.21 MHz
704.42 MHz
~ 500 m
Operating with protons
Operation with beam pulses at a frequency of 14 Hz
Pulse length of 2.86 ms
Average power of 5 MW
Peak power of 125 MW
One pulse = 357 kJ

## Slide 39: Example for a failure at ESS
Bending magnet in an accelerator deflecting the beam
Assume that the power supply for the bend in HEBT-S2 fails and the magnets stops deflecting the beam
  Probability: MTBF for power supply is 100000 hours = 15 years
The beam is not deflected and hits the vacuum chamber
  Consequences: what is expected to happen? Damage of magnet, vacuum pipe, possibly pollution of superconducting cavities
5 MW Beam
~ 160 m following the sc cavities
HEBT-S2

## Slide 40: Accelerators that require protection systems I
Hadron synchrotrons with large stored energy in the beam
  Colliders using protons / antiprotons (RHIC, LHC, FCC)
  Synchrotrons accelerating beams for fixed target experiments (SPS)
High power proton accelerators (e.g. spallation sources) with beam power of some 10 kW to above 1 MW
  Risk of damage and activation
  Spallation sources, up to (and above) 1 MW beam power (SNS, ISIS, PSI cyclotron, JPARC, and in the future ESS, FRIB, MYRRHA and IFMIF)
Synchrotron light sources and FELs with high intensity beams and secondary photon beams
  LCLS, FLASH 90 kW, European XFEL 600 kW, JLab FEL 1.5 MW,
Energy recovery linacs
  Daresbury prototype: one bunch train cannot damage equipment, but next train must not leave the (injector) station
Notes: 40

## Slide 41: Accelerators that require protection systems II
Linear e+e- colliders / accelerators with very high beam power densities due to small beam size
  High average power in linear accelerators: ILC 11 MW, CLIC
  One beam pulse can lead already to damage
“Any time interval large enough to allow a substantial change in the beam trajectory of component alignment (~fraction of a second), pilot beam must be used to prove the integrity” from Next Linear Collider paper 1999
Notes: 41

## Slide 42: Worst case accidents Proton collider

## Slide 43: Hydrodynamic tunnelling
The beam impacts on a target, e.g. due to a failure of the injection of extraction kicker
For LHC, bunches arrive every 25 or 50 ns
The time structure of the beam plays an essential role
The first bunches arrive, deposit their energy, and lead to a reduction of the target material density
Bunches arriving later travel further into the target since the material density is reduced (predicted already for SSC, N.Mokhov et al.)
Copper or carbon target

## Slide 44: How to perform calculations?
Assume LHC Beam impacts on Solid Cylindrical Target
  2808 bunches withprotons, , 25 ns bunch distance, target length of 6 m, Radius = 5 cm, Density = 2.3 g/cm3
The energy deposition for few bunches is calculated with FLUKA
The hydrodynamic code BIG2 uses the 3d energy deposition to calculate temperature, pressure and density of the target
The programs are run iteratively
  FLUKA 3d energy loss data is used as input to BIG2
  BIG2 3d density data is used as input for FLUKA
The modified density distribution is used in FLUKA to calculate the energy loss corresponding to this new density distribution
The new energy loss distribution is used in BIG2 which is run for time step
LHC: tunnelling of the beam through about 30 m is expected

## Slide 45: FCC: Temperature profile
90.400 K
120.000 K
FCC 100 km long accelerator.
Particle energy of 40 TeV.
Copper, Length = 5 m, Radius = 2 cm.
The simulation took about 15 months.
Naeem Tahir, Florian Burkart

## Slide 46: Density profile
3.5 g/cc
0.83 g/cc

## Slide 47: Density profile on axis
tbeam = 270 µs
L = v * tbeam = 297m (40 TeV protons)

## Slide 48: Principle of the code validation experiment using a copper target
Target 1
Target 2
Target 3
Target 1: 144 bunches ~1.9E11@50ns, 2.0mm  -> no tunnelling expected
Target 2: 108 bunches ~1.9E11@50ns, 0.2mm  -> tunnelling expected
Target 3: 144 bunches ~1.9E11@50ns, 0.2mm  -> tunnelling expected
Copper Target length of about 2 m
beam
beam
beam
Juan Blanco, Florian Burkart, et al.

## Slide 49: Copper target before the experiment
The range of the beam in target 3 is larger than in target 1 and 2
Clear indication for tunnelling

## Slide 50: Machine Protection

## Slide 51: Analysing need for machine protection
Is protection required?
YES
Great, nothing needed, simplifies life and increases system availability
NO
Is protection possible?
YES
NO
Is the risk acceptable?
YES
NO
Back to drawing board
Start design of the protection system
Identify hazard and estimate risk
Transverse deflecting devices in an accelerator that can deflect the beam by a large angle within about one turn
Superconducting magnet coils with too little copper to NbTi ratio

## Slide 52: Classification of failures
Type of the failure
  Hardware failure (power converter trip, magnet quench, AC distribution failure such as thunderstorm, object in vacuum chamber, vacuum leak, RF trip, kicker magnet misfires, .…)
  Controls failure (wrong data, wrong magnet current function, trigger problem, timing system, feedback failure, ..)
  Operational failure (chromaticity / tune / orbit wrong values, …)
  Beam instability (due to too high beam current / bunch current / e-clouds)
Failures in the injectors and transfer lines to be considered
Parameters for the failure
  Probability for the failure
  Damage potential
  Time constant for beam loss
Risk = Probability * Consequences

## Slide 53: Multi passage beam loss in a synchrotron
Very fast beam loss (few ms)
  Large number of possible failures, mostly in the magnet powering system, with a typical time constant of some ms to many seconds
Fast beam loss (some 10 ms to seconds)
  Beam instabilities
Slow beam loss (many seconds)
Detect failure and trigger beam dump
Notes: 53

## Slide 54: Single passage beam loss
Single-passage beam loss in an accelerator complex (ns - s)
Linear accelerators
  Beam is injected, but there is a failure present in the accelerator
  Before a pulse, ensure that the parameters of the accelerator allow for correct beam transmission
  If something is wrong and not detected before the pulse, stop beam as soon as possible at the source
Transfer lines between accelerators (e.g. SPS to LHC)
  Before a transfer, ensure that the parameters of the accelerator allow for correct beam transmission
  Use beam absorbers to capture mis-steered beam
Failures of kicker magnets (injection, extraction, special kicker magnets, for example for diagnostics)
  Use beam absorbers to capture mis-steered beam
Notes: 54

## Slide 55: Active and Passive Protection
Active protection
A sensor detects a dangerous situation
An action is triggered by an actuator
The energy stored in the system is safely dissipated
Passive protection
Preferred if possible to operate without active protection
Active protection not possible, e.g. the reaction time is too short
Monitors fail to detect a dangerous situation (redundancy)

## Slide 56: Passive protection
Passive protection
Is always necessary when the time required for the response is too short (…remember the limitation of the speed of light)
One example is the fast injection of a high intensity beam into a synchrotron with a fast kicker magnet
  If beam can damage hardware, protection absorbers are required
  For movable absorbers: need to be made sure that they are at the correct position of the absorber with respect to the beam during injection

## Slide 57: LHC strategy for machine protection
Beam Cleaning System
Beam Loss Monitors
Other Beam Monitors
Beam Interlock System
Powering Interlocks
Fast Magnet Current change Monitor
Beam Dumping System
Stop beam at source
Collimator and Beam Absorbers
Early detection of equipment failures generates dump request, possibly before beam is affected.
Active monitoring of the beams detects abnormal beam conditions and generates beam dump requests down to a single machine turn.
Reliable transmission of beam dump requests to beam dumping system. Active signal required for operation, absence of signal is considered as beam dump request and injection inhibit.
Reliable operation of beam dumping system for dump requests or internal faults, safely extracting beams onto the external dump blocks.
Passive protection by beam absorbers and collimators for specific failure cases.
Definition of aperture by collimators.

## Slide 58: Three Principles for Machine Protection
Protect the equipment (machine protection systems + interlock systems)
Protect the process (high availability systems)
  Machine protection systems will always contribute to downtime
  Protection action ONLY if a hazard becomes active (e.g. something went wrong threatening to damage equipment)
Provide the evidence (post mortem, logging of data)
  Provide post mortem buffers in equipment (record data, and stop after protection action kicks in) – 70% of LHC luminosity fills dumped prematurely
  Synchronisation of different systems is ultra – critical, to understand what happened
  Post operational checks by the controls system

## Slide 59
RF contacts for guiding image currents
Beam spot
2 mm
View of a two sided collimator
about 100 collimators are installed in LHC
Ralph Assmann, CERN
length about 120 cm

## Slide 60: Betatron beam cleaning
Cold aperture
Cleaning insertion
Arc(s)
IP
Circulating beam
Illustration drawing
Arc(s)
Primary collimator
Secondary collimators
Tertiary beam halo + hadronic showers
Shower absorbers
Tertiary collimators
SC Triplet
About 99.99% of the particle lost are captured in the cleaning insertion

## Slide 61: Beam Loss Monitors
Ionization chambers to detect beam losses:
  Reaction time ~ ½ turn (40 s)
  Very large dynamic range (> 106)
There are ~3600 chambers distributed over the ring to detect abnormal beam losses and if necessary trigger a beam abort !
Very important beam instrumentation!

## Slide 62: BLM system: beam losses before collisions
CMS Experiment
ATLAS Experiment
LHCb Experiment
ALICE Experiment
MomentumCleaning
RF and
BI
Beam
dump
Betatron Cleaning

## Slide 63: Continuous beam losses during collisions
CMS Experiment
ATLAS Experiment
LHCb Experiment
ALICE Experiment
MomentumCleaning
RF and
BI
Beam
dump
Betatron Cleaning

## Slide 64: Accidental beam losses during collisions
CMS Experiment
ATLAS Experiment
LHCb Experiment
ALICE Experiment
MomentumCleaning
RF and
BI
Beam
dump
Betatron Cleaning

## Slide 65: Accidental beam losses : UFOs

## Slide 66: High power accelerators …
Operate with beam power of 1 MW and more
SNS – 1 MW, PSI cyclotron – 1.3 MW, ESS – planned for 5 MW, FRIB (ions) – planned for 0.4 MW
ESS (4 % duty cycle): in case of an uncontrolled beam loss during 1 ms, the deposited energy is up to 130 kJ, for 1 s it is up to 5 MJ
Inhibit the beam after detecting uncontrolled beam loss – how fast?
The delay between detection and “beam off” to be considered

## Slide 67: Example for ESS
source
dT = dT_detect failure + dT_transmit signal + dT_inhibit source + dT_beam off
inhibit beam interlock signal
Example:
After the DTL normal conducting linac, the proton energy is 78 MeV. In case of a beam size of 2 mm radius, melting would start after about 200 µs.
Inhibiting beam should be in about 10% of this time.
L.Tchelidze
Time to melting point
Time to melting point [µs]

## Slide 68: Interlock Systems

## Slide 69: LHC Interlock Systems and inputs
Beam Interlock System
PIC essential
+ auxiliary
circuits
WIC
QPS
(several 10000)
Power
Converters
~1800
AUG
UPS
Power Converters
BLM
Vacuum
System
Vacuum
Valves
(~300)
Access
System
BPM in IR6
Access
Safety
Blocks
RF /e-Stoppers
Magnets
Doors
EIS
Beam
Dumping System
FMCM
Cryo
OK
Injection BIS
Monitors
aperture limits
(some 100)
Monitors in arcs
(several 1000)
CCC
Operator Buttons
Transverse Feedback
Movable Devices
Beam
Aperture
Kickers
SMP
Experiments
BCM
Beam Loss
Experimental Magnets
RF
System
FBCM
Lifetime
Collimation
System
Collimator
Positions
Environmental
parameters
BTV
BTV screens
Software
Interlocks
LHC
Devices
Timing System
(PM)
SEQ via
GMT
LHC
Devices
LHC
Devices
Timing
Safe
Beam
Flag
MKI
Mirrors
32
8
12
In total, several 10k interlock channels

## Slide 70: Beam Interlock Systems
Beam Interlock System
PIC essential
+ auxiliary
circuits
WIC
QPS
(several 10000)
Power
Converters
~1800
AUG
UPS
Power Converters
BLM
Vacuum
System
Vacuum
Valves
(~300)
Access
System
BPM in IR6
Access
Safety
Blocks
RF /e-Stoppers
Magnets
Doors
EIS
Beam
Dumping System
FMCM
Cryo
OK
Injection BIS
Monitors
aperture limits
(some 100)
Monitors in arcs
(several 1000)
CCC
Operator Buttons
Transverse Feedback
Movable Devices
Beam
Aperture
Kickers
SMP
Experiments
BCM
Beam Loss
Experimental Magnets
RF
System
FBCM
Lifetime
Collimation
System
Collimator
Positions
Environmental
parameters
BTV
BTV screens
Software
Interlocks
LHC
Devices
Timing System
(PM)
SEQ via
GMT
LHC
Devices
LHC
Devices
Timing
Safe
Beam
Flag
MKI
Mirrors
32
8
12
In total, several 10k interlock channels

## Slide 71: Powering Interlock Systems
Beam Interlock System
PIC essential
+ auxiliary
circuits
WIC
QPS
(several 10000)
Power
Converters
~1800
AUG
UPS
Power Converters
BLM
Vacuum
System
Vacuum
Valves
(~300)
Access
System
BPM in IR6
Access
Safety
Blocks
RF /e-Stoppers
Magnets
Doors
EIS
Beam
Dumping System
FMCM
Cryo
OK
Injection BIS
Monitors
aperture limits
(some 100)
Monitors in arcs
(several 1000)
CCC
Operator Buttons
Transverse Feedback
Movable Devices
Beam
Aperture
Kickers
SMP
Experiments
BCM
Beam Loss
Experimental Magnets
RF
System
FBCM
Lifetime
Collimation
System
Collimator
Positions
Environmental
parameters
BTV
BTV screens
Software
Interlocks
LHC
Devices
Timing System
(PM)
SEQ via
GMT
LHC
Devices
LHC
Devices
Timing
Safe
Beam
Flag
MKI
Mirrors
32
8
12
In total, several 10k interlock channels

## Slide 72: Software Interlock System
Beam Interlock System
PIC essential
+ auxiliary
circuits
WIC
QPS
(several 10000)
Power
Converters
~1800
AUG
UPS
Power Converters
BLM
Vacuum
System
Vacuum
Valves
(~300)
Access
System
BPM in IR6
Access
Safety
Blocks
RF /e-Stoppers
Magnets
Doors
EIS
Beam
Dumping System
FMCM
Cryo
OK
Injection BIS
Monitors
aperture limits
(some 100)
Monitors in arcs
(several 1000)
CCC
Operator Buttons
Transverse Feedback
Movable Devices
Beam
Aperture
Kickers
SMP
Experiments
BCM
Beam Loss
Experimental Magnets
RF
System
FBCM
Lifetime
Collimation
System
Collimator
Positions
Environmental
parameters
BTV
BTV screens
Software
Interlocks
LHC
Devices
Timing System
(PM)
SEQ via
GMT
LHC
Devices
LHC
Devices
Timing
Safe
Beam
Flag
MKI
Mirrors
32
8
12
In total, several 10k interlock channels

## Slide 73: MP systems: design recommendations
Avoid (unnecessary) complexity for protection systems
Failsafe design
  Detect internal faults
  Possibility for remote testing, for example between two runs
Critical equipment should be redundant (possibly diverse)
Critical processes not by software and operating system
No remote changes of most critical parameters
Calculate safety / availability / reliability
  Use methods to analyse critical systems and predict failure rate
Managing interlocks
  Bypassing of interlocks is common practice (keep track!)
  LHC: bypassing of some interlocks possible for “setup beams”
Time stamping for all system with adequate synchronisation

## Slide 74: Summary
Machine protection…….
requires the understanding of many different type of failures that could lead to beam loss
requires comprehensive understanding of all aspects of the accelerator (accelerator physics, operation, equipment, instrumentation, functional safety)
touches many aspects of accelerator construction and operation
includes many systems
is becoming increasingly important for future projects, with increased beam power / energy density (W/mm2 or J/mm2 ) and increasingly complex machines