## Slide 1: LHC Fault Tracking Project
or LHC failure studies progress

## Slide 2: Motivation
Intention
1. Illustrating the project goals
2. Present failure data sources
  3. Discuss methods of how to process the data to reach the goals

## Slide 3: Project goals
General: Find weak spots to improve the systems
Sort and assign the occured failures
Observe failure patterns and key dependencies
Failure behaviour for different intensities and beam parameters (some systems independent)
Weibull distributions (aging factor)
Calculate system availability for future goals of the LHC (High Luminosity)

## Slide 4: Downtime distributions
2015
Difference: shadows

## Slide 5: Failure data sources - AFT
  Details:
    High level description (Hardware, Controller)
    Imports data from logbook

## Slide 6
Failure data sources - COMS
Details:
  Since 2012
  Including minor failures (not affecting operation)
  Time assignment not precise

## Slide 7
Failure data sources - Piquet
Details:
  only failures requiring piquet
  Mostly QPS

## Slide 8
Failure data sources - logbook
Details:
  Before „failure reviews“ (by availability workgroup since 2015), sometimes wrongly assigned or incomplete failure data
  Provides data for the Cardiogram
Colorful line:
Correlation to
operational mode
(e.g. Scrubbing)

## Slide 9: Failure studies – Powering circuits
Possible division
of 600 A EE circuit:
QPS is the first analysed system of the failure studies
(System of MPS + many failures to observe ;-))

## Slide 10: Failure studies - Recurring
Family | Failure | # faults
600 A EE | Switch | 11
600 A no EE | RCBXV2.R1 RQSX3.L8 | 2 3
600 A no EE crowbar | RQT12.R3B1 | 2
IPQ | RQ4.R8 RQ7.R4 RQ4.L1 | 2 2 5
IT | RQX.L8 | 4
MAIN QUAD | 13 kA earth FIP comm lost FIP comm lost | 3x same day 3x same day 2x MQ9.L7
MAIN DIPOLE | RB.A67 EE 13 kA FLT timeout RB.A45 nQPS | 3x in 2 weeks 2x same day
Recurring failures in 2012 (source: Piquet data)

## Slide 11: Failure studies - Sectors
Sector | Dipole | Quadrupole
12 | 3 | 6
23 | 1 | 3
34 | 1 | 0
45 | 8 | 3
56 | 0 | 1
67 | 7 | 3
78 | 1 | 1
81 | 8 | 0
 | 29 | 17
Sector comparison: Dipoles and Quadrupoles failures 2012

## Slide 12: Failure studies - Weibull
Data sources: AFT + COMS
Time period: 01.05.2012 – 25.06.2012

## Slide 13: Failure studies
Questions:
What data to use? (minors, shadows, access, child, ...)
How to process the data? (Methods)
How to structure?
Future tasks:
Intensity and beam parameters studies
Calculating Availability budgets (In cooperation with University of Stuttgart)

## Slide 14
Thank you for your attention

## Slide 15: Failure studies - Circuits
Cicuit family | #
MAIN DIPOLE | 8
MAIN QUADRUPOLE | 16
IT | 8
IPQ | 78
IPD | 16
600 A EE | 202
600 A no EE | 72
600 A no EE crowbar | 136
80-120 A | 284
60 A | 752
WARM | 35
EXPERIMENTS | 12
1612 in total

## Slide 16: Basic Layout
Motivation:
Measuring of the transversal magnetic field
Magnetic needle with attached mirror
Laser for measuring offset
Control circuit for balancing the offset with secendary magnetic field

## Slide 17: Modeling

## Slide 18: Modeling
Modeling
Components magnetic needle:
  Mirror
  Magnets
  Iron parts
  Nylon string
  Brass screws
Important properties:
  Centre of mass
  Moment of inertia
  Maximum angle
Upcoming:
  Assembling the components (glue)
  Balancing needle with screws
  Testing the setup
Designed parts are in production and screws are ordered ✔