## Slide 1
Michael Benedikt
CERN
23 June, 2015
Study Overview & Status

## Slide 2: Motivation for global FCC study:
European Strategy for Particle Physics 2013:
  “…to propose an ambitious post-LHC accelerator project….., CERN should undertake design studies for accelerator projects in a global context,…with emphasis on proton-proton and electron-positron high-energy frontier machines..…”
US P5 recommendation 2014:
  ”….A very high-energy proton-proton collider is the most powerful tool for direct discovery of new particles and interactions under any scenario of physics results that can be acquired in the P5 time window….”
Goal:
Conceptual Design Report by end of 2018 in time for next European Strategy Update

## Slide 3: Scope: Accelerator & Infrastructure
FCC-hh: 100 TeV pp collider as long-term goal  defines infrastructure needs
FCC-ee: e+e- collider, potential intermediate step
FCC-he: integration aspects of pe collisions
Tunnel infrastructure in Geneva area, linked to CERN accelerator complex
Site-specific, requested by European strategy
Push key technologies in dedicated R&D programmes e.g.
16 Tesla magnets for 100 TeV pp in 100 km
SRF technologies and RF power sources

## Slide 4: Scope: Physics & Experiments
Elaborate and document
- Physics opportunities
- Discovery potentials
Experiment concepts for hh, ee and he
Machine Detector Interface studies
Concepts for worldwide data services
Overall cost model
Cost scenarios for collider options
Including infrastructure and injectors
Implementation and governance models

## Slide 5: CERN Circular Colliders + FCC
Constr.
Physics
LEP
Construction
Physics
Proto
Design
LHC
Construction
Physics
Design
HL-LHC
Physics
Construction
Proto
Design
Future Collider
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2035
20 years

## Slide 6: Key Parameters FCC-hh
Parameter | FCC-hh | LHC
Energy [TeV] | 100 c.m. | 14 c.m.
Dipole field [T] | 16 | 8.33
# IP | 2 main, +2 | 4
Luminosity/IPmain [cm-2s-1] | 5 - 25 x 1034 | 1 x 1034
Stored energy/beam [GJ] | 8.4 | 0.39
Synchrotron rad. [W/m/aperture] | 28.4 | 0.17
Bunch spacing [ns] | 25 (5) | 25

## Slide 7: FCC-hh Luminosity Goals
Two parameter sets for two operation phases:
  phase 1 (baseline): 5 x 1034 cm-2s-1 (peak), 250 fb-1/year (averaged)
  phase 2 (ultimate): ~2.5 x 1035 cm-2s-1 (peak), 1000 fb-1/year (averaged)
   total luminosity a few 10’s of ab-1
  over ~25 years of operation
OK for physics

## Slide 8: FCC-hh luminosity evolution 24 h
phase 1: b*=1.1 m, DQtot=0.01, tta=5 h
phase 2: b*=0.3 m, DQtot=0.03, tta=4 h
  for both phases:
  beam current 0.5 A unchanged!
  total synchrotron radiation power ~5 MW.
radiation damping: t~1 h

## Slide 9: Key Parameters FCC-ee
Parameter | FCC-ee |  |  | LEP2
Energy/beam [GeV] | 45 | 120 | 175 | 105
Bunches/beam | 13000- 60000 | 500- 1400 | 51- 98 | 4
Beam current [mA] | 1450 | 30 | 6.6 | 3
Luminosity/IP x 1034 cm-2s-1 | 21 - 280 | 5 - 11 | 1.5 - 2.6 | 0.0012
Energy loss/turn [GeV] | 0.03 | 1.67 | 7.55 | 3.34
Synchrotron Power [MW] | 100 |  |  | 22
RF Voltage [GV] | 0.2-2.5 | 3.6-5.5 | 11 | 3.5
Dependency: crab-waist vs. baseline optics and 2 vs. 4 IPs

## Slide 10: FCC-ee: Luminosity vs. Energy
Chart: c.m. energy [GeV]
| 91 | 160 | 240 | 350
baseline 4 IPs | 84 | 42 | 21 | 6
baseline 2 IPs | 54 | 26 | 14 | 3.8
crab wais 4 IPs | 860 | 152 | 35 | 8.4
crab waist 2 IPs | 454 | 76 | 22 | 5.2
Baseline 2 IP
Baseline 4 IP
Crab waist 2 IP
Crab waist 4 IP
H?
with mono-chromatization

## Slide 11: Geology Studies – Example 93 km
90 – 100 km fits geological situation well, better than a smaller ring size
LHC suitable as potential injector

## Slide 12: FCC-ee preliminary layout

## Slide 13: Key Technology R&D - HFM
Increase critical current density
Obtain high quantities at required quality
Material Processing
Reduce cost
Develop 16T short models
Field quality and aperture
Optimum coil geometry
Manufacturing aspects
Cost optimisation
First demonstrator in 2016?
Conductor R&D
Nb3Sn
Magnet Design
16 T

## Slide 14: Key Technology R&D - RF
Cavity R&D for large , high gradient, acceptable cryo power
Multilayer additive manufacturing combining Cu and LTS materials
High quality over large surfaces
Push Klystrons far beyond 70% efficiency
Increase power range of solid-state amplifiers
High reliability for high multiplicity
Superconducting RF
Beyond
Nb
Power Conversion
Efficiency

## Slide 15: FCC Study timeline
2014 |  |  |  | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Explore options
“weak interaction”
Report
Study plan, scope definition
FCC Week 2018
 contents of CDR
CDR ready
FCC Week 2015:
work towards baseline
conceptual study of baseline “strong interact.”
FCC Week 17 & Review Cost model, LHC results  study re-scoping?
Elaboration,
consolidation
FCC Week 2016
Progress review

## Slide 16: FCC Collaboration Status
51 institutes
19 countries
EC participation

## Slide 17: FCC Week 2016 Rome, 11 – 15 April 2016