## Slide 1: Accelerator R&D status in cooperation with CERN and KEK
BSM, BHM (T. Mitsuhashi)
2. Crab Cavity (Y. Morita)
3. X-band Acc. Structure (T. Higo)
10th Meeting of the CERN-KEK Committee
30th July, 2015, at CERN
Seiya Yamaguchi, KEK

## Slide 2
BSM by SR interferometry
LHC beam size measurement at 6.5TeV
World first interferogram from proton beam!
Vertical beam size via Fourier transform 230μm
Spatial coherence as a function of double slit separation
d=3mm
d=6mm
d=9mm
d=18mm

## Slide 3
Source
Objective lens
Lyot stop
Field lens
Relay lens
Opaque disk for eclipse
Coronagraph for beam halo measurement
Square slits
defining the aperture
Objective lens
Obstacle blocking the
Beam core
Field lens
Lyot stop
Relay lens
Magnifier
lens
Setup of the coronagraph at B1

## Slide 4
Schedule hereafter
Interferometer
remaining issues;
Install automatic double slit.
Calibration with Hartmann mask.
Test for horizontal beam size measurement.
Coronagraph
Construct the first coronagraph (104 contrast) until end of October.
Optical testing in November.
Install to B1 in December.
Budget in JFY2015: 0.30MJPY for lenses

## Slide 5: CERN-KEK collaboration on the crab cavity development
Objectives:
Based on research and development on crab cavities for the LHC luminosity upgrade progressed, as a cooperative work between KEK and CERN, this agreement, Appendix 16, aims to develop state of the art surface treatment techniques for high field superconducting crab cavities that deflect beam bunches in order to realize the crab crossing for the LHC accelerator luminosity upgrade.
KEK responsibilities for:
Development of a vertical electro-polishing (VEP) system,
Application of VEP to crab cavities,
Fundamental studies on vertical electro-polishing conditions,
CERN responsibilities for:
Necessary technical information and requirements for LHC crab cavities,
Support for the research activities in 3.1, such as experimental evaluation for electro-polishing and cavity performances,
Valid initially until 31 March 2017
Crab Cavity
・ Type : DQW (400 MHz)
・ Used at ATLAS and CMS

## Slide 6: Crab cavities for HL-LHC
LHC Crab Cavity
Compact and complicated cavity structure to meet space requirements
High fields are required to sufficiently deflect beam bunches
  3.4 MV per cavity at 400 MHz with Q=1010,T=2K
  14 MV per interaction point using 4 crabs
  (KEKB crab: 1.4 MV at 509MHz with Q=109,T=4.4K)
Surface treatment is one of important issues
  CP(Chemical polishing) has been used so far
EP (Electro-polishing)
Developed for TRISTAN SC cavities
Horizontally rotating technique
Smoother surface than CP
Standard treatment method for high field cavities
VEP (Vertical EP)
We proposed an R&D on application of EP to LHC crab cavities
Horizontally rotating EP system can not be used
Vertical positioning EP at our EP facility
Our EP apparatus for 500 MHz cavity
BNL DQW cavity
Horizontally rotating EP system developed for TRISTN SC cavities

## Slide 7: Vertical EP apparatus
Drain port
Electrolyte outlet
N2 outlet
N2 inlet
Teflon cathode bag
Al electrode
Electrolyte inlet
Upper Teflon box
Lower Teflon box

## Slide 8: Timetable for Vertical EP at KEK
Item | July 2015 | Aug. | Sep. | Oct. | Nov. | Dec. | Jan. 2016
Electrode |  |  |  |  |  |  | 
Teflon box |  |  |  |  |  |  | 
Rotation jig |  |  |  |  |  |  | 
Ozone rinsing jig |  |  |  |  |  |  | 
Dummy cavity |  |  |  |  |  |  | 
Fitting check |  |  |  |  |  |  | 
Vertical EP |  |  |  |  |  |  | 
SRF operation for SuperKEKB |  |  |  |  |  |  | 
Fabrication
Fabrication
Fabrication
Fabrication
Fabrication
Coupler conditioning
at room temperature
Start up
for SuperKEKB

## Slide 15
E30・tp5
BDR
=const.
E*
Normalized gradient is increasing smoothly with pulse number.
BDR is roughly decreasing linearly with pulse number.

## Slide 20: end