## Slide 1: Performance Comparison of Interleaved Sextupole Schemes + New Racetrack Lattice
Bastian Haerer (CERN, Geneva; KIT, Karlsruhe) for the FCC-ee lattice design team

## Slide 2: 1) Chromaticity Correction
Systematic investigation of chromaticity correction schemes for FCC-ee:
Interleaved sextupole scheme using Montague Formalism  LEP-like IRs
Comparison 4 IPs and 2 IPs (90°/60°)
Phase advance 0.249/0.166
(Direct matching of chromaticities)

## Slide 3: 12-fold lattice
Circumference: 100 km
Arc length: 6.8 km
Straight section length: 1.5 km
4 LEP-like mini-beta insertions (IR)!
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
IR
IR
IR
IR
S
B
Q
Q
B
B
B
S
Q
S
S
B = bending magnet, Q = quadrupole, S = sextupole

## Slide 4: Both W functions in the 1st quarter
Arc 1
Arc 2
Arc 3
s in km
IP
IP

## Slide 5: Corrected Chromaticity
 | Symmetric FODO |  | 
 | Natural Chromaticities | Corrected Chromaticities | ΔQ (δ=0.05 %)
Qx | 506.16 | 509.08 | 
Qx’ | -629.88 | -4.20 | -2.10e-03
Qx’’ | -1.6e+04 | 6.6e+03 | 8.19e-04
Qx’’’ | -2.7e+08 | -1.5e+07 | -3.13e-04
Qx’’’’ | -4.1e+12 | -2.9e+10 | -6.73e-05
Qy | 334.28 | 334.28 | 
Qy’ | -2059.23 | 6.7e-02 | 3.36e-05
Qy’’ | -8.6e+06 | -9.8e+03 | -1.22e-03
Qy’’’ | -2.0e+11 | -2.5e+09 | -5.11e-02
Qy’’’’ | -6.7e+15 | -1.5e+12 | -3.92e-03

## Slide 6: New procedure
Before:
Matching W functions first in one plane then in another
Now:
Matching W functions of both planes at the same time in sector wise
 1st arc, 2nd arc, 3rd arc, all arcs, all arcs (periodic)
Optimised phase advance between FD and Arc

## Slide 7: Sectors
s in km
Sector 1
Sector 2
Sector 3
Match W functions < 5
Match W function = 0
at the IP
Match first order
chromaticity

## Slide 8: 4 IPs: Horizontal W function

## Slide 9: 4 IPs
[-0.08%, 0.06%]
[-0.22%, 0.06%]
integer
half-integer

## Slide 10: 2 IPs: Horizontal W function
Sextupole strengths: Arc2 = Arc5
Arc3 = Arc4

## Slide 11: 2 IPs
[-0.15%, 0.06%]
[-0.20%, 0.06%]
half-integer

## Slide 12: 3rd order chromaticity
Anton Bogomyagkov
~W2
Octupoles
Put Sextupole
where
b2 is large

## Slide 13: Comparison chromaticities
4 IPs (90°/60°):
2IPs (90°/60°):

## Slide 14: Detuning the Arc Cells
(90°/60°)
(0.249/0.166)
K2SF = 0
K2SD11= -35
K2SF = 0
K2SD11= -35

## Slide 15: Matching of the phase advance between Final Doublet and Arc
μx = 5.05907
μy = 3.04280
W function is
minimal here

## Slide 16: 4 IPs (0.249, 0.166)
[-0.24%, 0.22%]
half-integer

## Slide 17: Next steps
Repeat Matching of W functions for Racetrack Layout (get a set of comparable cases to analyse)
 Start DA studies with Luis
Need to get 3rd order chroma under control
 Analyse higher order derivatives of β functions
 Change weights in matching routine
( Introduce octupoles)
Try direct matching of chromaticities
Try 60°/60° optics
Try non-interleaved schemes

## Slide 18: 2) New Baseline Layout (V17)
P. Lebrun & J. Osborne
Exp.
Exp.
no DS
no DS
no DS
no DS
100 km
circumference
Longer arcs
(before ≈95 km)
No Technical
Straight Sections
(TSS)

## Slide 19: Lattice Modules
*P. Lebrun et al.: FCC layout: naming, numbering, lengths, preliminary siting,
FCC Infrastructure & Operation, Meeting, 22 October 2014
 | Number | Length Lebrun & Osborne* | Length FCC-ee V17
LSS | 6 | 1400 m | 1400 m
ESS | 2 | 4200 m | 4200 m
DS | 16 | 400 m | 100 m
SARC | 4 | 3200 m | 4200 m
LARC | 8 | 8000 m | 8100 m
DS-SARC-DS: 400 m longer than proposed by Lebrun & Osborne
Required for nice arrangement of sextupole families
CEA: no problem for FCC-hh lattice