## Slide 1: Electronics for the SPS BWS prototype
J. Emery for the BWS electronics team
Aleksander Cudny, Bernd Dehning, Pierre-Jean Lapray, Emiliano Piselli, Jose Sirvent, Luca Timeo
Contributions: Julien De Freitas, Kamil Florek, Colin Grosjean, Henzer Kevin, Mohamed Koujili, Matteo Macchini, Carlos Daniel Morais Pereira, Cantin Simon.
Electronics for the SPS BWS prototype

## Slide 2: Outlook
System overview
Prototype setup 2015
Calibration setup
Electronics for the SPS BWS prototype
Development status

## Slide 3: links
BWS review 2013 http://indico.cern.ch/event/229959/timetable/#20130418
BWS control electronics specification (references list at the end): https://edms.cern.ch/document/1318827
“A fast and accurate wire scanner instrument for the CERN accelerators to cope with severe environmental constraints and an increased demand for availability” 2014 IEEE Conference on Control Applications (CCA) http://ieeexplore.ieee.org/xpl/articleDetails.jsp?arnumber=6981482
“Secondary particle acquisition system for the CERN beam wire scanners upgrade” 2014 Topical Workshop on Electronics for Particle Physics http://dx.doi.org/10.1088/1748-0221/10/04/C04021
Electronics for the SPS BWS prototype

## Slide 4: Electromechanical view
Motor
Magnetic Brake
Resolver
RF shielding chamber (not present in SPS Proto)
Shaft
Fork
Wire
Glass disk
Optical fibre light focuser
Electronics for the SPS BWS prototype

## Slide 5: Control and Acquisition electronics
Secondary particles shower acquisition
Scanner control, monitoring and supplies “Intelligent drive”
Acquisition and supervision
CPU
T IMING
BST receiver
Fast integration secondary shower
SFP Ethernet
SFP Optical link
SFP Optical link
Long range resolver interface
3-phases PWM
Magnetic brake
External temperature and vibration
Optical encoder interface
Wire resistivity & Strain gauge
HV
CTRL
Optical encoder interface
Electronics for the SPS BWS prototype

## Slide 6: Connections to external systems
TCP/IP
SFP Optical link
Long range resolver interface
Wire resistivity & Strain gauge
3-phases PWM
Magnetic stopper
External temperature and vibration
Optical encoder interface
Intelligent drive
SFP Optical link
Acquisition and supervision
CPU
Trigger input
T IMING
General Machine Timing (GMT)
Low jitter < 1ns Granularity: 1ms
Control room
Expert monitoring
Logging storage Long term storage offline analysis
Trigger input
Trigger output
BST receiver
Beam Synchronous timing (BST): - Bunch synchronisation => 25 ns accurate clock - Revolution frequency synchronisation => for LHC 89us pulse period
Triggers: Wire-scan trigger, post-mortem, acquisition
- Granularity: 89us, low jitter < 1ns
- Scan trigger at ms scale use serial data link
- If we need ns scale, use of dedicated line
Beam Energy and Intensity
CISV? BCT?
CISV receiver
Electronics for the SPS BWS prototype

## Slide 7: Goals for this year prototyping
Experts development & debugging
Beam tests of control electronics & Diamond acquisition
Diamond vs PM+IBMS comparison
Accuracy and reproducibility of mechanics & control with the calibration bench (But without secondary particle acquisition)
Electronics for the SPS BWS prototype

## Slide 8: BWS SPS PROTOTYPE - SETUP 2015
CPU
CTR
V
BOBR
I BMS
HV
Acquisition crate
HV power supply
Back-end receiver
Filter crate
Sin wave filter
I & V Measures
Control crate
Motor drive crate
3-phases PWM
I & V Measures, DC BUS, etc.
Optical encoder interface
Wire resistivity
Long range resolver interface
Start scan trigger
Acquisition trigger
VME boards configuration Machine Synchro triggers PMT acquisition
Feedback optimisation Profiles generation Electronics boards expert Prototype control Calibration
Front-End A/D
Electronics for the SPS BWS prototype

## Slide 9: Control crate prototype
Electronics hardware for control ok
Crate finalisation foreseen for September
Matlab interface ok
Firmware code on-going and well advanced
First movement already performed
Will be ready for machine test foreseen for November-December 2015
FPGA board Firmware development platform
Interface board Scanner actuator control and measurements
Electronics for the SPS BWS prototype

## Slide 10: Firmware block diagram
SDRAM MEMORIES
Hard SDRAM controller
Digitalisations (~20 MHz)
Digitalisations of the currents, voltages. Controls of the wire, lasers. RDC
Aux IN/OUT
2x Digial in
2x Digial out
Monitoring (TCP/IP)
To VME crate & CPU control
Triggers
CTRL POWER
PWM
Slow interfaces
Fast interfaces
Current Speed Position Feedback
Condition Monitoring online fault diagnosis
VFC
Check procedures
Movement sequencer Safety procedures
Detection Identification
HWR PROTOCOL
HPS EMAC
HW bridge Internal bus
SW bridge to Internal bus
Memory loggers
Electronics for the SPS BWS prototype

## Slide 11: Control feedback model (2013)
Position
Position Profile
Currents
Speed
Pos
Park/Clarke
PWM
Electronics for the SPS BWS prototype

## Slide 12: Feedback data monitoring using TCP/IP and MatLab GUI
Electronics for the SPS BWS prototype

## Slide 13: Feedback data acquisition on SDRAM download by MatLab GUI (TCP/IP)

## Slide 14: Drive crate prototype
Electromechanical design well advanced
It can satisfy lab test setup and optimised version
Board for measures, relays and identification design on-going
3 phases power driver
Motor and control connectors
Voltages supplies LV and 400V
measures board design on-going
Electronics for the SPS BWS prototype

## Slide 15: Drive crate schematic
Electronics for the SPS BWS prototype

## Slide 16: Sin wave filter crate
Electromechanical integration foreseen 09.2015
Will use the same board as the motor drive crate
Some experiments foreseen with other types of filters, lower PWM periods September-October
Electronics for the SPS BWS prototype

## Slide 17: Diamond acquisition
Scope measurements on SPS 517 scanner (June 2015)
Second diamond install planned to study noise source
Tunnel digitalisation should be installed in next SPS TS
Diamond system will probably be moved to the prototype
Electronics for the SPS BWS prototype

## Slide 18: Diamond acquisition setup
pCVD
DD_1
pCVD
DD_2
Amplif.
+
Split
Amplif.
+
Split
To Surface (~80m)
CK50
CK50
CB50
CB50
CBH50
SMF
CBH50
Beam Pipe
HV_1
HV_2
-12V
+12V
Sig_1
Sig_2
Igloo2 Dev. Kit
GBT Core
SDRAM Storage
PC Communication
Power Supply Instrumentation
Scope
Bi-directional GBT optical link @ 4.8Gbps
(Data transfer, Synchronization & Control)
Digital Front-End Prototype
Power (FEASTMP)
ICECAL or QIE10
Mezzanine
Igloo2_Umd
Mezzanine Board
(from CMS ngCCM)
VTRx
Electronics for the SPS BWS prototype

## Slide 19: Prototype accuracy & reproducibility determination with the calibration bench
Photodiode
2x Picoscopes @ 14 bits
C-Wire / Strain Gauges
2x Optical encoder
Laser
Photodiode
Digital output
Scan start trigger
2x USB interfaces
Position
Power
Embedded
control
Electronics for the SPS BWS prototype

## Slide 20: Labview calibration application
Electronics for the SPS BWS prototype

## Slide 21: Summary
Electronics system
BWS SPS prototype setup
Development status
Beam tests foreseen for Nov-Dec
2016: Development of the remaining electronics
2016: SPS Beam tests with modified electronics?
2016: Prototype install in the PS or PSB?
Electronics for the SPS BWS prototype
Control of the prototype with DSpace @ 140 rad/s

## Slide 22: Additional slides

## Slide 23: Operational system layout for all scanner types since 2009 (2012 for SPS)
SURFACE INSTALLATION
UNDERGROUND (radioactive)
Up to 270m !
BST master
MTG master
CCC & databases
Motion control board
CPU
R IO3
HV
CTRL
DAB+
I BMS
T IMING
BOBR
Power amplifier behind the VME
Step motor control
Multiplexers
Power
Position

## Slide 24: Specification
Nominal speed @ beam-wire interaction position ≥ 20 [m/s]
Forks angular position measurement accuracy ≤ 5 [µm]
Mechanical bellow removed => All mobile part under vacuum
Large dynamic range => New secondary shower detector chain design
Movement limited to [rad] => Nominal speed reached in π/3
IN
INTERACTION
IN movement
OUT movement
HOME

## Slide 25: Design guidelines
Minimisation of complexity - As less as possible electrical connections - Avoid multiplexing channel - Settings and parameters (control and acquisition)
Separate critical and non-critical functions - Instrument safety in the low level hardware - High level software configure, analyse and record the measurements
Early failure detection - Constant hardware Condition Monitoring (CM) - Programmed maintenance

## Slide 26: Wire Scanner locations
Accelerator | Number of Systems | Measurement cycles in 2012 | Scanner characteristics |  | 
 |  |  | Type | Speed | Precision
LHC | 8 | 16 k | Linear | 1 m·s-1 | 15 mm
SPS | 6 | 26 k | Rotating long | 6 m·s-1 | 40 mm
SPS | 4 | 400 | Linear | 1 m·s-1 | 15 mm
PSB | 8 | 55 k | Rotating fast | 20 m·s-1 | 100 mm
PS | 5 | 32 k | Rotating fast | 20 m·s-1 | 100 mm

## Slide 27: Operational system failures for all scanner types since 2009
Multiplexers
Step motor control
Power amplifier behind the VME
Cabling / Electronic
VME cards / crate
Affected Component | machine | Occurrences | Failure source | Mitigation | System under design
Linear Power Amplifier | All & lab | 16 (2 in 2012) | Electrical glitch to unprotected outputs, Use of componant (PA50) on the limit of its specification | Replacement of supplies | Use of switch mode power supplies and filters
Multiplexers | LHC, PS | 3 | Mechanical relay failure in the tunnel | Replacement of relays | Use dedicated cables and control electronics
Step motor controler | PSB, LHC | 2 | Electronic board aging | End of life electronics to be upgraded | Avoid filter wheel by the use of high dynamic detector
Motion control | PS | 1 | VME bus access switch off VME | Replacement of the card | Motion control in the power supply disconected from the VME
CPU RIO 3 | SPS | 1 | Unexpected reboot | Replacement of the card | 
PA50A
BWS Power amplifier
Transformer
DC power storage units (Capacitors)
±32V
motor
AOP
AOP
150m

## Slide 28: Switch mode output filter principle
Results: Reduction of Electromagnetic Interferences (EMI) Better compatibility with signal cables nearby this cable
No overvoltage at motor side
Shielded power cable 6mm2

## Slide 29: Incremental Optical Angular Sensor
laser
Optical fibre
feedthrough
lens
photodiode
10 mm
disk

## Slide 30: Interface to the wire resistivity, thermionic and RF induced current
PSB Ring 1 H at 15 m/s
Wire resistivity variation during a movement due to mechanical constraints (See Juan’s talk)
SPS 416 H at 6 m/s
Wire current variation when interacts with beam (thermionic effect)
SPS 416 H at 6 m/s
Wire current variation induced by the beam exitating RF modes inside a cavity (BWS tank)