Title
ATLAS Preparation for LHC Phase-1 Upgrade
Conditions
B-layer
Other changes

---
Overview
It was always expected to replace ATLAS B-layer before other detectors
Life expected to be <~ 300 fb-1
Realised during assembly that quantity and complexity of services mean any replacement is a long and delicate process
  - Longer than a standard winter shutdown (In fact more like a year)
ATLAS set up a Task Force (“B-Layer Task Force”, BLTF) to look into options and recommend best way forward; reported at Bern ATLAS week and now to EB
  - Will cover this here
Since Phase-1 plans unveiled and LHCC agreement on beam conditions we are beginning a review of all detector systems
  - evaluate performance in all expected conditions and decide on changes needed; status so far covered here
ATLAS planned for 2e34 and 700 fb-1
  - Phase-1 is 50 % increase on peak rate and no change integral
    - don't expect major changes to be needed
  - But some items need improvement anyway, will also cover these where known

---
Conditions for Phase-1
From LHCC/LHC/Atlas/CMS agreement (Garoby talk):
  - Peak luminosity rising to 3x1034 cm-2 s-1 for a year or two
    - This is slightly higher than “Ultimate” and 50 % higher than the 2x1034 that many systems worked to
  - Integrated luminosity ~100 fb-1 at 6-8 month shutdown end 2012
  - Further ~550 fb-1 to end 2016 and long shutdown for Phase-2
    - Total ~650 fb-1 is roughly what was designed for e.g. 730 fb-1 for SCT)

---
Basic expectations
Collimation phase 2
Linac4 + IR upgrade phase 1
New injectors + IR upgrade phase 2
Normal Ramp
No phase II
Year
Peak Lumi (x 1034)
Annual Integrated
(fb-1)
Total Integrated
(fb-1)
Peak Lumi (x 1034)
Annual Integrated
(fb-1)
Total Integrated
(fb-1)
2009
0.1
6
6
0.1
6
6
2010
0.2
12
18
0.2
12
18
2011
0.5
30
48
0.5
30
48
2012
1
60
108
1
60
108
2013
1.5
90
198
1.5
90
198
2014
2
120
318
2
120
318
2015
2.5
150
468
2.5
150
468
2016
3
180
648
3
180
648
2017
3
0
648
3
0
648
2018
5
300
948
3
180
828
2019
8
420
1428
3
180
1008
2020
10
540
2028
3
180
1188
2021
10
600
2628
3
180
1368
2022
10
600
3228
3
180
1548
2023
10
600
3828
3
180
1728
2024
10
600
4428
3
180
1908
2025
10
600
5028
3
180
2088

---
ATLAS B-layer Plans
Ref. Bern ATLAS week, Thursday afternoon http://indico.cern.ch/materialDisplay.py?contribId=69&sessionId=26&materialId=slides&confId=20501
ATLAS Pixel package = pixel detector + services to ~3 m + beampipe, inside a CF support tube
  - Inserted as one piece
First realisation: cannot repair/replace beam-pipe (e.g. vacuum leak)
  - ...order new spare beampipe which can be inserted
  - ...develop method to replace old one (cut at z = 0?)

---
B-layer
Lifetime: should last beyond 2012, but not until 2017
  - Irradiation damage
    - HV limited so eventually cannot fully deplete
      - Leeds to signal loss and inefficiency
      - “Soft failure”
  - Some possible other failures (leaks, opto packages...) - “hard failures”
Rate capability:
  - Inefficiencies become significant but OK at 2.1034
  - Very bad at 3 x nominal
B-layer has to be renewed
Only time is longer shutdown 2012-13
Hit prob. / DC
LHC
3xLHC
sLHC
inefficiency
FEI3 inefficiencies
pile-up
busy/waiting
late copy
total inefficiency

---
Insertable B-Layer IBL
Time to remove pixel package, open up, remove B-layer, put in a new one is ~ 1 year. BLTF set up to find best way to avoid ATLAS running a year without pixels
Many options considered
Only one survived scrutiny:
  - Insert a new B-layer inside the current pixel detector
  - leave the old (partially functioning) B-layer in place
  - New, smaller beam-pipe to make space
  - Cost not known, but ~5 – 7 MCHF components
Performance has been evaluated (shown last meeting):
  - Moving to smaller R and shorter pixels gains
  - Extra material loses
  - Net effect is beneficial, especially if old B-layer is working at > 70 % efficiency

---
Current Expectations
Need careful evaluation, subject to change
Beam-pipe 50 mm diam
B-layer sensors centred at 37 mm radius
Planar sensors, probably n-in-n, maybe thinned; or 3D
FE-I4 chip: well under development
  - 130 nm cf 250; smaller pixels (50 x 250 cf 50 x 400 micron)
  - hits stored in pixels until LVL1 (cf all data to end of column) – allows high efficiency eventually to 10 times nominal
Evaporative CO2 cooling (cf C3F8)
  - Smaller pipes, lower coolant T: freedom in design
Powering: serial or DC-DC/charge pump or buck converter
Readout: electrical to z = 3 m, r = 1 m
Services: needs new services to racks!

---
Pixel installation
Integrate new B-ayer and its services with a new Be beampipe
Cut old beam pipe at z ~ 0 and remove, managing cable supports
  - Solution under investigation; sketches show it is possible
  - Cutting activated poisonous Be
Insert complete new package, but locate B-layer on old pixel detector
  - Must not move relative to rest of pixels! beam pipe expands and contracts too much to use as locator

---
Organisation
Needs major effort now
Involves pixel group, beam-pipe (machine), cooling, services ...
Should fit in with Phase-II Upgrade:
  - FE-I4, sensors, CO2 cooling as pilot projects for Phase-II
Use Pixel group, USG, PO, TC

---
Other Phase-1 Changes

---
Beam-pipe
Beam-pipe at large z (z > 3 m) is SS
Generates large background in muon system
Gets activated, making maintenance difficult
Two Upgrade stages proposed:
  - SS -> Al
  - Al -> Be
Be compared to SS reduces BG factor 2 in muon system
  - In fact, a factor 3 in worst regions

---
Other ATLAS Detectors
Have started an evaluation of how each system will perform in Phase-I, and what changes are needed (if any), and whether R&D is needed now
Report back by Christmas
For each detector evaluate:
  - Sensitive detector resolution and efficiency
    - E.g. space charge, occupancy/dead-time fraction, tracking efficiency
    - Effect on jet, gamma, or track resolution
  - Data loss during transmission at peak rate
  - Total dose effects
  - What action is needed
  - What R&D is needed now
USG will coordinate and produce a report (ATLAS EB Action to do this)
Now go through (briefly) each sub-system...

---
Inner Tracker
Rest of Pixel outside the B-Layer:
  - Should be OK: the data rate is much less than in the B-layer; integrated dose is OK. There will be slight increase of lost hits, but tolerable.
SCT
  - Zero suppressed data. Readout will lose about 1 % of hits at 3 times nominal
  - max occupancy at nominal is 0.6 %, so expect 1.8 % at Phase-I
    - Should be OK for pattern recognition (usually like to keep below 1 %)
  - Total dose OK (as designed)
TRT
  - Fixed data length (no zero suppression) so no extra data losses to ROD
    - But after ROD it is zero suppressed; investigate
  - Long drift time and large area of straws gives high dead fraction
    - Needs detailed assessment
  - ion build up etc.
  - R&D to different gasses? E.g. drop TR detection, get faster gas

---
Inner Tracker Cooling
Current evaporative C3F8 has several problems:
  - Large pressure drop in return pipes so cannot reach the required -25 degC needed after irradiation
  - Heaters mostly working, but still control problems for some orientations
  - Compressors: low input P due to pressure drops; high output P to avoid need for liquid pumps
    - Compressors are working at their maximum: rapid wear (oiless pistons) and reliability questions – already had major failure
Solutions to investigate:
  - Change BPR to something with lower dP
    - E.g. accumulator solution used at LHCb (zero dP), vacuum pump in line, bigger BPRs...
  - Do condensing at surface and use static head to get to high P in pit. This gives compressor lower output P since gas has less static head
  - And other ideas

---
Calorimeters
LAr
  - Fixed data length: no data loss
  - Pile-up increases, acts as a noise, grows slowly (sqrt(L/L0))
    - Filtering to be optimised
  - Boiling not a problem at 3x1034
  - HV drops, ion build OK in most of eta, but needs chacking in FCAL
Tiles
  - Fixed data length so no data loss
  - Don't expect any changes except maybe crack scintillator
  - But maintenance issues and back-ups needed in several places
  - Plus monitor rate of light-output decline with time and radiation

---
Muons
Depends on BG!
We need to urgently measure the background relative to the luminosity
Separate n and gamma
Need to follow up and check all radiation monitoring sensors (~7 varieties); joint group to do this
R&D project for this was among the first approved
See how much of safety factor 5 is used up
Consider selective readout
  - Only readout at LVL1 in RoI
Need to simulate trigger effects, and tune trigger
Shielding: look at improving JF shielding (rest has no space and all is fully optimised already)
Beam-pipe already mentioned

---
Electronics
Several detectors use same technologies and these need monitoring
E.g. D-Mill bi-polar transistors suffer n damage
beta could drop from 120 to ~40
Can power supplies compensate etc.?
Needs monitoring

---
Trigger
Difficult to change LVL1 (latency, rate)
Investigate “topological” cuts e.g. isolated muon
Can raise thresholds
  - ...needs evaluation
High Level Trigger and Event storage:
  - Can keep improving as processor costs reduce
  - Can improve algorithms
  - Is accessible: decoupled from cavern

---
Summary
Fixing the anticipated LHC evolution helps greatly to focus discussions
Main necessity at ATLAS is Insertable B-Layer
  - Difficult but Doable
Evaluation of other changes needed has begun
  - Seems manageable